IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Task Group 4a for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Calculating parameter macAckWaitDuration for the UWB PHY types |
| Date Submitted | 12 June 2006 (rev 1) |
| Source | [Ben Rolfe] [ ] [ ] | Voice: [408-395-7207] Fax: [] E-mail: [ben@blindcreek.com] |
| Re: | 802.15.4a Draft 2 Comment Resolution |
| Abstract | Formula for calculating macAckWaitDuration for UWB PHY, at mandatory and optional data rates. |
| Purpose | Resolve comments on Draft 2 regarding missing definition of macAckWaitDuration |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

Calculating parameters macAckWaitDuration and macMaxFrameTotalWaitTime for the UWB PHY types

Author: Ben Rolfe   Date: 30-April-2006

In draft 2 of 15.4a, macAckWaitDuration and macMaxFrameTotalWaitTime are used and defined in principle but no value is given. To calculate the macAckWaitDuration depends on the maximum frame duration which for UWB depends on several PHY parameters which are not all constant, for example, depends on the data rate.  This note is about calculating the frame length for the 15.4a UWB PHY. Based initially on "Vern's notion of the frame length" email thread by Vern Brethour <vern.brethour@timedomain.com>.

The preamble and PHY header may be sent at a different data rate than the body. Shown here in three parts: the preamble and PHR separate for clarity:

The values for  Tpsym and Tdsym are given in the referenced tables (referring to D2).  The PHY parameter SHRDuration is given by the above eqn as

SHRDuration = Tpreamble + TPHR

# Proposed Text Changes

Add to section 7.4.2 (reference 4bD3):

For the UWB PHY, where there the CCA method is ALOHA, the formula for macAckWaitDuration reduces to

macAckWaitDuration = aTurnaroundTime phy + SHRDuration + ceil(6* phySymbolsPerOctet);

Where SHRDuration is calculated as shown in section <6.8a.xx where above formula is given>.

For UWB PHY types, maxMaxBE, macMaxCSMABackoffs  amd m in eqn 16 become zero, so the forumula becomes

macMaxFrameTotalWaitTime  = phyMaxFrameDurationUs

As given in section <6.8a.xx where above formula is given>.