IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Task Group 4a for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Calculating parameter macAckWaitDuration and attributes phyMaxFrameDuration, phySHRDuration for the UWB PHY types |
| Date Submitted | 21 June 2006 (rev 2) |
| Source | [Ben Rolfe] [Zhen Bin] | Voice: [+1 408 395 7207] E-mail: [ben@blindcreek.com] Voice: [+81 46 847 5445] E-mail: [zhen.bin@nict.go.jp] |
| Re: | 802.15.4a Draft 2 Comment Resolution |
| Abstract | Formula for calculating macAckWaitDuration and the PHY PIB attributes it depends on for UWB PHY, at mandatory and optional data rates. |
| Purpose | Resolve comments on Draft 2 regarding missing definition of macAckWaitDuration |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

Calculating parameters macAckWaitDuration and macMaxFrameTotalWaitTime for the UWB PHY types

Author: Ben Rolfe, Zhen Bin

Date: 21 June 2006

# Introduction and Background

In draft 2 of 15.4a, macAckWaitDuration and macMaxFrameTotalWaitTime are used and defined in principle but no value is given for the UWB PHY, which will be different than for existing 802.15.4 PHYs. The calculation of macAckWaitDuration depends on the maximum frame duration, which for UWB depends on several PHY PIB attributes which varry depending on operating mode.  As it happens, these PIB parameters (phyMaxFrameDuration, phySHRDuration) are a bit more involved to determine for the UWB PHY than for the other PHY types.  To clarify this in 4a draft three, this submission proposes to modify the existing text in MAC section 7.4.2, modify the PIB table and add a sub-clause to the PHY PIB section to clarify determination of the affected PIB attributes.

This note is based initially on "Vern's notion of the frame length" email thread by Vern Brethour <vern.brethour@timedomain.com>.

# Proposed Text Changes

Add to section 7.4.2 (reference 4bD3):

For the UWB PHY, where there the CCA method is ALOHA, the formula for macAckWaitDuration reduces to

macAckWaitDuration = aTurnaroundTime phy + SHRDuration + ceil(6* phySymbolsPerOctet);

Where SHRDuration is calculated as shown in sub-clause 6.4.2.1.  This form also works for the UWB PHY with optional CCA mode, as explained in 6.4.2.1.

For UWB PHY types, macMaxBE, macMaxCSMABackoffs  amd m in eqn 16 become zero, so the forumula reduces to:

macMaxFrameTotalWaitTime  = phyMaxFrameDurationUs

where phyMaxFrameDuationUs is also given in section 6.4.2.1

6.4.2 Change rows in table Table 23—PHY PIB attributes

| Attribute | Identifier | Type | Range | Description |
| --- | --- | --- | --- | --- |
| phyMaxFrameDuration† | 0x05 | Integer | 53, 206, 258, 1032 | The maximum number of symbols in a frame. For all non-UWB PHY ypes: = phySHRDuration + ceiling([aMaxPHYPacketSize + 1] * phySymbolsPerOctet) For UWB PHY types, see subclause 6.4.2.1 |
| phySHRDuration† | 0x06 | Integer | 3, 7, 10, 40 | The duration of the synchronization header (SHR). For non-UWB PHYs types, constant in symbols for the current PHY. For UWB PHY types |

Add sub-clause to 6.4.2

6.4.2.1  PID values phyMaxFrameDuration, phySHRDuration  for UWB

For the UWB PHY types, the values for these PIB attributes varies depending upon the UWB PHY operating mode.  The symbol duration varies by data rate and is different for preamble symbols and body symbols. Also note that the preamble and PHY header are sent at a different data rate than the body.

The values for Tpsym and Tdsym are given in tables 39a and 39c in picoseconds, expressed above as Tdsymμs  and Tdsymμs in microseconds. The value of T_d_CCAsym is the nominal data rate of 1Mbps which is listed as follows (from Table 39a), in microseconds.

| Channel number | Data symbol duration Tdsym (ns) | Symbol Rate (Mbps) |
| --- | --- | --- |
| {0:3, 5,6, 8:10, 12:14} | 1025.64 | 0.98 |
| 4, 11 | 769.23 | 1.30 |
| 7 | 946.75 | 1.06 |
| 15 | 755.74 | 1.32 |

The PHY parameter SHRDuration is given by the above formula as

SHRDuration = Tpreamble + TPHR