| Project | IEEE 15.4a |
| --- | --- |
| Title | Suggested changes for the 4a draft regarding the multiplexed preamble for CCA |
| Date Submitted | [June, 2006] |
| Source | [Yihong Qi, Bin Zhen, Huan-bang Li and Ryuji Kohno] [NiCT, 3-4 Hikarino-oka, Yokosuka, 239-0847, Japan] | Voice: [+81-46-847-5092] Fax: [+81-46-847-5431] E-mail: [yhqi@nict.go.jp] |
| Re: |  |
| Abstract | The changes regarding the multiplexed preamble for CCA are to accommodate the recent 4a draft modification for ballot resolution |
| Purpose | [] |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

6.8a.13 Extended preamble for the optional UWB CCA mode

The PHY may provide the capability to perform the optional UWB CCA mode 6 (see 6.9.9). This CCA mode shall be supported by the modified frame structure where preamble symbols are multiplexed with the data symbols in the PHR and the PSDU of a frame.

Figure 27b shows the modified frame structure with multiplexed preamble symbols. One preamble symbol is inserted after each PHR and PSDU segment. The inserted preamble symbol should be same as the symbol used in the SHR (see 6.8a.2) of the same frame. The time duration of each PHR or PSDU segment is fixed to 4 symbol periods, where the symbol period is defined according to the nominal data rate of 1Mbps in each channel group, as listed in Table 39c with data rate field index R1-R0=01. Distinguished from the CCA in narrowband systems, which is to detect the energy of carrier waveforms, the UWB CCA based on the frame with multiplexed preamble is to detect the presence of preamble symbols. The processing gain can be enhanced by exploiting the spreading characteristics and repetition of the preamble symbols.

Figure 27o Illustration of the modified frame structure with multiplexed preamble

The PAN coordinator of a piconet shall guarantee the availability of all nodes in the piconet before the UWB CCA mode 6 is enabled. The modified frame structure with multiplexed preamble shall only be applied to a data frame and a MAC frame in the CAP when the PHY PIB attribute phyCCAmode indicates the UWB CCA mode 6.

The CCA detection window shall capture at least 8 (multiplexed) preamble symbols.

In addition to enable the UWB CCA mode 6, the multiplexed preamble symbols can help to improve ranging accuracy, or assist data demodulation. Such use is similar to that of the pilot tone in narrowband systems.

For Table 39c UWB PHY frame-dependent parameters

Please add the following one parameter:

| parameter | Description | value | … | value |
| --- | --- | --- | --- | --- |
|  | Time interval between two neighboring multiplexed preamble symbols |  |

For Table 23 PHY PIB Attributes

Please add the following attribute

| Attribute | Identifier | Type | Range | Description |
| --- | --- | --- | --- | --- |
| phyUWBInsertedPreambleInterval | 0x1D | Enumeration | Channel group 1-5 | Time interval between two neighboring inserted preamble symbols (see 6.8a.13) |