| Project | IEEE 15.4a |
| --- | --- |
| Title | CSS updates for D3 |
| Date Submitted | 28 June 2006 |
| Source | [Rainer Hach] [Nanotron Technologies GmbH Alt-Moabit 61, 10555 Berlin, Germany] [Kyung-Kuk Lee ] [Orthotron Co., Ltd. 709 Kranz Techno, 5442-1 Sangdaewon-dong, Jungwon-gu, Sungnam-si, Kyungki-do, Korea 462-120] | Voice : [+49 30 399 954 0] Fax : [+49 30 399 954 288] E-mail : [r.hach@nanotron.com] Voice : [+82 31 777 8198] Fax : [+82 31 777 8199] E-mail : [kyunglee@orthotron.com] |
| Re: | [] |
| Abstract | This document list changes to be made for the next revision of 15.4a regarding CSS |
| Purpose | Provide information on on Coexistence performance of CSS at 2450 MHz |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

# Add the following text and figue at the end of subclause “6.3 PPDU format”

# The format of the PHR is shown in figure 16c

# Figure 16c- Format of CSS PHR

Replace the subclause 2.7 DQPSK - to - DQCSK modulation by the following:

2.7 DQPSK - to - DQCSK modulation

The stream of DQPSK symbols shall be modulated onto the stream of sub-chirps which is generated by the

CSK Generator. The effect of the DQCSK modulation shall be that each sub chirp is multiplied with a DQPSK value which has unit magnitude and has constant phase for the duration of the sub chirp.

In “6.5a.2.9 Bit interleaver” insert the following on page 40, at line 20:

The memory of the interleaver shall be initialized with zeros before the reception of a packet.

The data stream going into the interleaver shall be padded with zeros if the number of octets to be transmitted does not align with the bounds of the interleaver blocks.

# Text boxes

2412   2417  2422   2427  2432   2437  2442   2447  2452  2457  2462   2467  2472         2484