| Project | IEEE 15.4a |
| --- | --- |
| Title | CSS updates for D3 |
| Date Submitted | 29 June 2006 |
| Source | [Rainer Hach] [Nanotron Technologies GmbH Alt-Moabit 61, 10555 Berlin, Germany] [Kyung-Kuk Lee ] [Orthotron Co., Ltd. 709 Kranz Techno, 5442-1 Sangdaewon-dong, Jungwon-gu, Sungnam-si, Kyungki-do, Korea 462-120] | Voice : [+49 30 399 954 0] Fax : [+49 30 399 954 288] E-mail : [r.hach@nanotron.com] Voice : [+82 31 777 8198] Fax : [+82 31 777 8199] E-mail : [kyunglee@orthotron.com] |
| Re: | [] |
| Abstract | This document lists changes to be made for the next revision of 15.4a regarding CSS |
| Purpose | Provide information on on Coexistence performance of CSS at 2450 MHz |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

# Note: All references are relating to d3P802-15-4a_Draft_Standard review 1.pdf

# Clause 6.5a.2.1

# Move “Table 23-PHY PIB attributes” to the appropriate position in the document

# Clause 6.5a.2.7

Replace the content of 6.5a.2.7 DQPSK - to - DQCSK modulation by the following:

The stream of DQPSK symbols shall be modulated onto the stream of sub-chirps which is generated by the CSK Generator. The effect of the DQCSK modulation shall be that each sub chirp is multiplied with a DQPSK value which has unit magnitude and has constant phase for the duration of the sub chirp. An example of this operation can be found in 6.5a.4.6.

# 6.5a.2.9 Bit interleaver

Insert the following on page 47 at the end of line 38:

The memory of the interleaver shall be initialized with zeros before the reception of a packet.

The data stream going into the interleaver shall be padded with zeros if the number of octets to be transmitted does not align with the bounds of the interleaver blocks.

# Clause 6.5a.3

# I would like to restrcuctue and split up this clause. Therfor please:

# Insert “6.5a.3 CSS Frame format” right before “6.5a.3 Preamble”

# Change “6.5a.3 Preamble” to “6.5a.3.1 Preamble”

# Insert the following after subclause “6.5a.3.1 Preamble”:

# 6.5a.3.2 Start of frame delimiter

# The SFD field for CSS is defined in 6.3.2

# 6.5a.3.3 PHY header

# The format of the PHR is shown in figure XX

# Figure XX- Format of the CSS PHR

# Clause 6.5a.4.3

# page 51, line 6:

# Insert “average” before the first appearance of “duration”

# (So that the sentence reads:

It is determined by Tchirp which is the average duration of a chirp symbol and by Tsub which is the duration of a sub chirp signal.)

# page 51, line 22:

# Insert

# (but is not identical to) after “determines”.

# page 51, line 23:

# replace “the previous and the actual sub-chirp sequence” by “two subsequent sub-chirp sequences”

# remove “and Table 26f”

# It should then read:

The constant τm is either added or subtracted and thus determines (but is not identical to) the time-gap which was applied between two subsequent sub-chirp sequences as shown in Figure 20d.

# First column of Table 26g:

# Replace Tchirp by Tchirp

# Replace Tsub by Tsub

# Replace {}1 by τ1

# Replace {}2 by τ2

# Replace {}3 by τ3

# Replace {}4 by τ4

# Insert new subclause

“6.5a.4.6 Example of CSK signal generation ”

An example for the modulation of one chirp symbol is provided, illustrating each step from DEMUX to the output of the reference modulator as shown in Figure 20b. The scenario parameters are as follows:

1) The initial values of all 4 feedback memory stages of the differential encoder is set .

2) Data bit-rate is 1 Mb/s.

Input binary Data

1 1 0 10 0

De-Multiplexer (Demux)

I-path: 1 0 0

Q-path : 1 1 0

Serial to parallel mapping

I-path: {1 0 0}

Q-path: {1 1 0}

Bi-orthogonal Mapping (r=3/4)

I-path: -1 -1 -1 -1

Q-path: -1 -1 1 1

P/S and QPSK symbol mapping

Mapper Input: (-1-j), (-1-j), (-1+j), (-1+j)

QPSK Output Phase: π, π, -π/2, -π/2

D-QPSK Coding:

Initial phase of 4 feedback memory for D-QPSK are all π/4

D-QPSK Coder Output Phase: -3π/4, -3π/4, -π/4, -π/4

D-QPSK to D-QCSK Modulation Output:

Sub-chirp sequence of D-QCSK output:

[exp(-j3π/4) * subchirp(k=1), exp(-j3π/4) * subchirp(k=2), exp(-jπ/4) * subchirp(k=3), exp(-jπ/4) * subchirp(k=4)]

# Text boxes

2412   2417  2422   2427  2432   2437  2442   2447  2452  2457  2462   2467  2472         2484