## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Beacon Request Modifications
Date Submitted: 14 July 2009
Source: Skip Ashton, Andy Summers, Ember
Address: 47 Farnsworth St Boston MA 02210
Voice: (617) 951 1201 , FAX: [], E-Mail: skip.ashton@ember.com, andy.summers@ember.com
Re: [802.15.4e] TG4e MAC Modifications
Abstract: This presentation discusses several use cases noted within ZigBee that could be improved with modifications to the beacon request frame within 15.4.
Purpose: Technical Proposal to be discussed by IEEE 802.15 TG4e
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Beacon Request Modifications
Skip Ashton, Andy Summers
July 2009

## Slide 3: Introduction
Beacon frame format defined in 7.2.2.1 and provides variable payload.
  ZigBee as an example then specifies this payload in section 3.6.7 of the ZigBee Specification to include protocol ID, stack profile, extended PANID etc to provide indication to joining device of what network it should join
Beacon request command defined in section 7.3.7 of 15.4 has no payload and is sent to the broadcast PAN with a broadcast short address for destination
When a beacon request is received, a single beacon frame is transmitted using unslotted CSMA-CA with a random backoff (for ZigBee configuration)

## Slide 4: Field Problems Identified
Dense network – (typically more than 30 devices within range)
  Ability to receive beacons is limited due to collision of beacons
  Limited number of back off slots results in multiple devices picking the same slot and then colliding
  ZigBee moved to 2006 backoff definitions (from 15.4-2003) which provided some improvements
Network Joining or Steering
  Current mechanism has joining device select a network based on what information is provided in beacon
  Would also like to steer a joining device to a network based on the joining device knowing some piece of information
Often the joining device knows more about what it wants to do than the devices sending the beacon – but this information cannot be used with the current beacon request command

## Slide 5: Simple Cases for Beacon Request
Always allow beacon as it is today, but allow beacon request to limit beacon responses from devices within range
For example
  Only those device with permit joining on respond
  Send beacon request to particular short or long PANID
  Send a beacon request with a particular RSSI level – only devices with that level or higher will respond
  Send a beacon request and ask a random percentage of devices to respond (this stops beacon storms in dense networks)
  Allow for other higher level capabilities (for ZigBee this could be application profile, security level etc) to discriminate the networks the device can join
  Send some combination of the above items to allow steering a device
This cannot be done without changes to frame format within 15.4
Beacon frame has variable payload that higher levels can define but beacon request is a fixed frame

## Slide 6: Proposed Changes
Change wording in beacon request command (section 7.3.7) to allow sending to specific PAN and not just broadcast PAN
Provide a means for beacon request to have a variable payload to allow higher levels to specify items within the beacon request.
Modify wording on when to send a beacon response to a beacon request to allow for devices to not respond if some level of application discrimination is on
  Older devices without this would still respond with beacon so new devices would need to be aware of this