## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG 4f, 4g, 6 Unified Narrowband PHY]
Date Submitted: [11 September 2009]
Source: [Ed Callaway] Company [Sunrise Micro Devices]
Address [9181-125 Glades Road, Boca Raton, FL 33434 USA]
Voice:[+1-954-608-7537], E-Mail:[ed@sunrisemicro.com ]
Re: [TG4f, TG4g, and TG6 PHY proposals]
Abstract: [I propose a unified narrowband PHY for TGs 4f, 4g, and 6.]
Purpose: [Encourage a unified narrowband PHY option be adopted for TGs 4f, 4g, and 6.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Doc.:IEEE 802.15-09-0612-01-wng0

## Slide 2: A Unified Narrowband PHY for TGs 4f, 4g, and 6
Ed Callaway
Sunrise Micro Devices
ed@sunrisemicro.com
Doc.:IEEE 802.15-09-0612-01-wng0

## Slide 3: Déjà Vu
Presentations at TG 4f, TG 4g, and TG 6 meetings in San Francisco left one visitor with a profound sense of having heard something before…
Doc.:IEEE 802.15-09-0612-01-wng0

## Slide 4: 433 MHz Channel Parameters
Parameter | Value
Frequency Band | 433.05 MHz – 434.79 MHz
Number of Channels | 1
Channel Bandwidth | 540 kHz
Data Rate | 250 kb/s
Modulation | Minimum Shift Keying (MSK)
Pathloss | 10m = 45dB, 100m = 65dB
Doc.:IEEE 802.15-09-0500-00-004f
Dalibor Pokrajac,
802.15-09-0500-00-004f

## Slide 5: FSK and GFSK
Depends on band requirements
  GFSK for reduced adjacent-channel and adjacent-band emissions,
    well suited to ‘tighter’ bands
  FSK better dB
    Well suited to 902-928, 2.4GHz bands
Different optimizations for different situations
  Cheap, simple flexibility
Both GFSK and FSK work!
Doc.:IEEE 802.15-09-0477-01-004g
B. Rolfe, C. Powell, et al.,
802.15-09-0477-01-004g

## Slide 6: Proposed Data Rate and Modulation
Power efficient FSK Modulation
Band limited gaussian pulse shape filter
  Improve spectrum efficiency at the cost of increased ISI
  Cause elevated BER compared with a typical FSK
FEC for compensating the elevated BER
      Outer RS(15,13) in GF(24)
      Inner CC code, with constraint length 3, rate ½ [5 7]
Frequency Band | Channel/BW | Data rate | Modulation | FEC | Pulse shape Filter
402-405 MHz MICS | 10 (300KHz/CH) | 150 Kbps / 500 Kbps1) | 2FSK/ 4FSK | RS+CC Header (5,3) Payload (15,13) | Gaussian Filter (Modulation index = 0.5, BT = 0.5)
500 kbps is a minimum transmission data rate for 8bit RGB 256x256 pixel color image with 1 fps and 4:1 image compression ratio
JPEG compression ratio is typically 4:1 for CT and MR.
32 channel ECG need minimum 192 kbps and 2 channel EMG needs 256 kbps.
Doc.:IEEE 802.15-09-0573-00-0006
Ismail Lakkis, et al., 802.15-09-0573-00-0006

## Slide 7: Observations
250 kb/s GFSK with h = 0.5 or 1 is common to all three narrowband proposals.
A common narrowband PHY would enable each application to ride on the chip volumes of the others, advancing the market for all.
New, cross-TG applications may also be enabled.
Doc.:IEEE 802.15-09-0612-01-wng0

## Slide 8: Proposal
TG4f, TG4g, and TG6 should develop common draft text for a “universal” narrowband PHY.
Doc.:IEEE 802.15-09-0612-01-wng0

## Slide 9: Suggested Common Denominator
Data Rate
  Common data rate, 250 kbps
Modulation
  FSK/GFSK
  Multiple modulation index support: h = 0.5, 1.0, 2.0 (trade BW efficiency for robustness)
  Gaussian filtering (BT selected per spectral requirements)
Demodulator
  Compatible: A single FM receiver can receive all options
  Flexible: Coherent, differential, non-coherent choices (can optimize for application)
  Proven: Existing chips typically support several configurable FSK/ASK modes
Doc.:IEEE 802.15-09-0612-01-wng0
Plus other, TG-specific modes …