IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Multiple clock support documentation |
| Date Submitted | [17 January, 2010] |
| Source | [Sridhar Rajagopal, Sang-Kyu Lim, Taehan Bae, Dae Ho Kim, Jaeseung Son, Ill Soon Jang, Doyoung Kim, Dong Won Han, Ying Li, Atsuya Yokoi, J.S. Choi, D.K. Jung, H.S.Shin, S.B.Park, K.W.Lee, Shadi Abu Surra, Eran Pisek, Farooq Khan, Tae Gyu Kang, E.T. Won] [Samsung Electronics, ETRI] | Voice:[] Fax: [ ] E-mail:[srajagop@sta.samsung.com] |
| Re: | [] |
| Abstract | [Documentation for multiple clock support ] |
| Purpose | [Description of what the authors wants P802.15 to do with the information in the document.] |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

# Clock rate selection:

The standard supports multiple optical clock rates in order to accommodate a wide variety of optical sources and receivers.  The standard also supports the use of asymmetric clock rates between the transmitter and the receiver since the transmitter and receiver are independent chains and may support different clock rate ranges. The multiple clocks used for both PHY types are as shown in Tables xx and yy.

Support for minimum clock rate for a given PHY type shall be mandatory for TX and RX for all devices. All specified clock rates less than the maximum supported clock rate in a given device shall also be supported in that device. If a clock rate is supported, all data rates associated with that clock rate shall be supported. The preamble, header and payload in the PHY shall have the same clock rate The header shall be sent at lowest data rate for the chosen clock rate. The payload can choose any data rate belonging to the chosen clock rate.

## Clock rate selection for P2P topology:

Let us assume that Device 1 supports the following clock rates at the transmitter (C1, C2, … Ct1), where Ct1 is the maximum clock rate supported at the transmitter at device 1. Also, C1 < C2 < .. < Ct1  The clock rates are also integral multiples of each other to make the clock generation and selection simple at the transmitter i.e. Ci+1/Ci = m Є Z. The receiver may support more or less clock rates than the transmitter since the receiver circuit is physically independent of the transmitter clock. The transmitter clock is restricted to the clock supported by the optical source while the receiver clock is restricted by the photodiode.  Let the clocks supported by the receiver of device 1 be C1, C2, … Cr1, where Cr1 is the maximum clock rate supported at the receiver of device 1. Similarly, let Ct2 and Cr2 be the maximum clock rates supported by the device 2. Support for the lowest clock rate C1 is mandatory at both the transmitter and receiver for all devices i.e. t1, t2, r1, r2 ≥ 1. For every clock rate, there is associated set of data rates at the physical layer. This data rate is dependent on the modulation, line coding and FEC used at the physical layer for a given clock rate. Let the data rate be represented by rate{Ci,p}, where Ci is the chosen clock rate and 1 ≤ p ≤ N(Ci), where N(Ci) is the number of physical layer rates associated with clock rate Ci.

In Figure 1, Device 1 sends the association request at the lowest clock C1 at a physical layer data rate rate{C1,k}.  The data rate index ‘k’ is typically is chosen to be the lowest data rate to guarantee maximum range and reliability for the given clock rate. In this association request, the device 1 also informs the other device of the maximum clock rate supported by its transmitter and receiver (Ct1, Cr1). Device 2 receives the association request and compares the received information about the supported clocks at device 1 and compares it with its supported clocks. In order for it to communicate, it must select a clock rate Csel2 that is equal to or lower than maxCsel2, which is the minimum of its maximum transmitter clock and the maximum receiver clock supported by device 1.  The decision to use clock rates lower than maxCsel1 and maxCsel2 at device 1 and device 2 for transmission depends on the performance and throughput needs of the devices. The receiver also sends an association grant back to the transmitter at the same lowest clock rate C1 supported by all devices. The devices then exchange the selected clock frequencies for future communication before they switch to the selected clock frequencies. The devices may also decide to change the clock rate anytime in future communication for performance or throughput, as long as it is below maxCsel1 and maxCsel2 for transmission at devices 1 and 2 respectively.

Figure 1 Clock rate selection for P2P topology (explicit notification)

It is also possible for Device 2 to send the association grant at the new clock rate Csel2 and not have to explicitly exchange notification information, if device 1 has the capability to detect all clock rates less than its maximum receive clock rate. In this case, communication can occur without overhead for explicit notification.

Figure 2 Clock rate selection for P2P topology (without explicit notification)

## Clock rate selection for Star topology:

Figure 3 shows the clock rate selection for a star topology. In this case, let us assume Device 1 to be a co-ordinator. The co-ordinator will send a broadcast message via a beacon to all nodes such as Devices 2 and 3 and inform them of its supported clock rates. The CAP always uses the lowest clock rate C1 for uplink contention. The co-ordinator and the devices communicate the selected clock frequencies during the CFP using clock rate C1 before switching to the selected clock frequencies.

Figure 3 clock rate selection for star topology (explicit notification)

Similar to the P2P topology, the clock rate selection for the star topology can also occur without explicit notification as shown in Figure 4.

Figure 4 clock rate selection for star topology (without explicit notification)

## Clock rate selection for Broadcast/Multicast topology:

Figure 5 and Figure 6 show the clock rate selection for broadcast/multicast topologies assuming bi-directional communication. For unidirectional broadcast, the co-ordinator should use the lowest clock rate for broadcasting to ensure all devices can receive the information.

Figure 5 Clock rate selection for broadcast/multicast (assuming bi-directional communication)

Figure 6 clock rate selection for broadcast/multicast (bi-directional communication and no explicit notification)

# Changes to support multiple clock rate selection

Table 1 Capability field

| Bit | Attribute | Description |
| --- | --- | --- |
| 0 | Traffic support | 0 = unidirectional (broadcast only) 1 = bi-directional |
| 1-2 | Topology | 00 = reserved 10 = P2P only 01 = P2MP support 11 = both |
| 3-4 | Device type | 00 = infrastructure 01 = mobile 10 = vehicle 11 = reserved |
| 5 | Beacon capability | 1 = capable |
| 6 | Visibility support | 1= support |
| 7 | Dimming support | 1 = support |
| 8 | Co-ordinator support | 1 = support, can act as co-ordinator for VLAN |
| 9-11 | Max supported TX clock | 000 – lowest clock rate, 001 – next highest clock, … |
| 12-14 | Max supported RX clock | 000 – lowest clock rate, 001 – next highest clock, … |
| 15 | Explicit clock notification request | 1 = needs explicit clock notification at receiver |

Table 2 Command frame notification

| Command frame identifier | Command name |
| --- | --- |
| 0x01 | Association request |
| 0x02 | Association response |
| 0x03 | Disassociation notification |
| 0x04 | Data request |
| 0x05 | PAN ID conflict notification |
| 0x06 | Orphan notification |
| 0x07 | Beacon request |
| 0x08 | Coordinator realignment |
| 0x09 | GTS request |
| 0x0a | Blinking notification |
| 0x0b | Dimming notification |
| 0x0c | Fast link recovery signaling |
| 0x0d | Mobility notification |
| 0x0e | Information element exchange |
| 0x0f | Clock rate change notification |
| 0x10–0xff | Reserved |

Table 3 Clock rate change notification format

| octets: | 1 | 1 |
| --- | --- | --- |
| MAC Header fields | Command Frame Identifier | New clock rate for future TX |