## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Considerations for Non-Coherent UWB Receivers Operating in Long Range Mode]
Date Submitted: [17 March, 2010]
Source: [Adrian Jennings] Company [Time Domain]
Address [330 Wynn Drive, Suite 300, Huntsville, AL. 35805. USA]
Voice:[+1 256 759 4708], FAX: [+1 256 922 0387], E-Mail:[adrian.jennings@timedomain.com]
Re: [Packet structures to aid non-coherent UWB receivers]
Abstract: [This document proposes two remedies to help non-coherent UWB receivers receive and demodulate Long Range Mode packets intended primarily for coherent receivers]
Purpose: [To resolve outstanding issues on the current baseline proposal]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Considerations for Non-Coherent UWB Receivers Operating in Long Range Mode
Adrian Jennings
adrian.jennings@timedomain.com
+1 256 759 4708

## Slide 3: Background
The current draft of the 802.15.4f standard includes a long range mode for the UWB PHY
  Intended primarily for use by a coherent receiver
  Uses many (m) pulses per bit to enable pulse integration
This mode must also be received and demodulated by a non-coherent receiver
Two potential problems arise
  The long SFD is not ideal for synchronization
  Any long periods of zeros will cause loss of synchronization
Item #2 is also problematic for the coherent receiver when using OOK modulation

## Slide 4: Attaining Alignment

## Slide 5: Preamble Proposal
It is proposed that the Long Range Mode preamble include the 1 pulse per symbol SFD as the last 16 pulses
This provides a sync marker for the non-coherent receiver at the expense of slightly reduced preamble energy for the coherent receiver

## Slide 6: Proposed Preamble Diagram
Preamble
SFD
Key:
Long Range Mode
(2 MHz)
Base Mode
(1 MHz)
1111111111111111
0001010010011101
1111
0000
1111
1111
1111
1111
1111
1111
1111
1111
1111
1111
1111
0001
0000
0000
1111
0000
1111
0000
0000
0100
1001
1101
Etc.
1:1 SFD
1:1 SFD
4:1 SFD
Using 4 pulses per symbol for illustrative purposes only:

## Slide 7: Energy Lost in Preamble
Preamble Length | Pulses per symbol |  |  | 
 | 8 | 16 | 32 | 64
16 | -0.63 | -0.31 | -0.15 | -0.08
32 | -0.31 | -0.15 | -0.08 | -0.04
48 | -0.21 | -0.10 | -0.05 | -0.03
64 | -0.15 | -0.08 | -0.04 | -0.02
Energy loss in dB
A minimal effect given the gain in interoperability

## Slide 8: Maintaining Alignment

## Slide 9: The Issue
For an OOK system, no energy is received for a zero data value
Long stretches of zeros therefore provide no reference to correct for clock drift during a packet
We must ensure that the modulation scheme allows this “sync on data” functionality in all modes
This is of particular concern in the Long Range mode which has a much higher likelihood of long sequences of zeros

## Slide 10: Modulation Proposal
It is proposed that the modulation scheme be modified to ensure a maximum length to any run of zero pulse positions
This means inserting a data 1 after a defined run of data 0’s
How many 0’s can be tolerated?

## Slide 11: Long Range Mode Tx, Base Mode Rx
Assumptions
  100MHz Rx clock, which can make 10ns pulse windows
  20ppm crystal in Rx per the UWB 4a PHY
  2ppm crystal in Tx per 4f Long Range spec
  64 pulses per bit per 4f Long Range spec
  Goal is to drift no more than one window before receiving a pulse
Calculations
  Worst case link drift is 2+20ppm = 22ppm
  Time to drift 10ns @ 22ppm = 454.5ms
  # pulses @ 2MHz in 454.5ms = 909
  # whole bits at 64 pulses per bit = 14

## Slide 12: Base Mode Tx, Base Mode Rx
Assumptions
  100MHz Rx clock, which can make 10ns pulse windows
  20ppm crystal in Rx per the UWB 4a PHY
  20ppm crystal in Tx per the UWB 4a PHY
  1 pulse per bit per 4f Base Mode spec
  Goal is to drift no more than one window before receiving a pulse (which is a data 1)
Calculations
  Worst case link drift is 20+20ppm = 40ppm
  Time to drift 10ns @ 40ppm = 250ms
  # pulses @ 1MHz in 250ms = 250
  # whole bits at 1 pulse per bit = 250

## Slide 13: Long Range Mode Tx, Long Range Mode Rx
Assumptions
  100MHz Rx clock, which can make 10ns pulse windows
  2.3ppm total system, drift
  64 pulses per bit per 4f Long Range Mode spec
  Goal is to drift no more than one window before receiving a pulse (which is a data 1)
Calculations
  Link drift is 2.3ppm
  Time to drift 10ns @ 2ppm = 4.348ms
  # pulses @ 2MHz in 4.348ms = 8,696
  # whole bits at 64 pulses per bit = 136

## Slide 14: Discussion
 | Base Mode Tx | Long Range Tx
Base Mode Rx | 250 | 14
Long Range Rx | - | 136
# Allowable 0 symbols
However, the Base Mode receiver could be further helped by inserting a single pulse in the Long Range 0 symbol
This replaces the need to insert a 1 symbol as often as every 14 symbols in the Base Rx/Long Range Tx case

## Slide 15: Modified Table
These numbers are close enough to allow a single modulation modification which works in all modes
For ease of implementation, the number 128 is preferred
 | Base Mode Tx | Long Range Tx
Base Mode Rx | 250 | -
Long Range Rx | - | 136
# Allowable 0 symbols

## Slide 16: Modulation Modification
All tags must implement the following modulation modification
  Insert a redundant data “1” after a run of 128 data “0”s
All receivers must implement the following demodulation modification:
  Ignore any “1” following a run of 128 “0”s
The Long Range 0 symbol must be modified to include a single pulse and 63 empty pulse positions

## Slide 17: Summary
Interoperability between Long Range tags and Base Mode receivers can be significantly improved with little cost
Proposal Summary
  Insertion of 1:1 mapped SFD as last 16 pulses of Long Range preamble
  Modification of data modulation as follows:
    Insert redundant one after 128 zeros
    Insert single pulse in Long Range 0 symbol
  Note: Enhance Mode should be treated the same way as Base Mode