IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | MAC Rejoin Comment Resolution Proposal |
| Date Submitted | [15 May 2010] |
| Source | [Philip Beecher, BCC] [16 Saxon Road, Hove, BN3 4LE, UK] | Voice: [ ] Fax: [ ] E-mail: [ pbeecher@ieee.org ] |
| Re: | TG4e Letter Ballot Comment Resolution |
| Abstract | Recommended solution to MAC rejoin comment |
| Purpose | Proposal to TG4e for resolution to comment submitted during LB53 |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

MAC Rejoin commands

Context

The following type of information is potentially needed in the frame:

- Network ID (if known)

- Type of network device is seeking to join

- Indication if joining or rejoining

- Capability information of the joining device (15.4 specifies capability information but we potentially also need additional information such as router or host, services offered)

- Security capabilities

This information is required by the NHL so, rather than specify the values in 15.4, they will be provided like the beacon payload which is a MAC PIB value set by the higher layers to be included in the rejoin command payload.  The MAC then does not need knowledge of the payload fields; it just included them in the packet.

(Note - the text below is a proposed addition for IEEE 802.15.4e)

- Use of a MAC commands frame requires updating of the existing command frame table (Table 82 page 149) to include new lines:

| Command Frame Identifier | Command Name | RFD Tx | RFD Rx | Subclause |
| --- | --- | --- | --- | --- |
| 0x0A | MAC Rejoin request | X |  | 7.3.10 |
| 0x0B | MAC Rejoin response |  | X | 7.3.11 |

- A new item should be added to the MAC PIB (Table 86) as follows:

| Attribute | Identifier | Type | Range | Description | Default |
| --- | --- | --- | --- | --- | --- |
| macRejoinPayload | 0xXX | Set of octets | ---- | The contents of the rejoin payload | NULL |

- A new section 7.3.10 and 7.3.11 would need to be added as follows:

7.3.10 MAC Rejoin Request command

The rejoin request command allows a device to request rejoining with a PAN through the PAN coordinator or an FFD.

An associated device that has lost contact with its PAN and wishes to rejoin with a PAN may send this command. A device shall only rejoin with a PAN through the PAN coordinator or an FFD, as determined through the scan procedure.

All devices shall be capable of transmitting this command, although an RFD is not required to be capable of receiving it.

The rejoin request command shall be formatted as illustrated in Figure XX.

| Octets (see 7.2.2.4) | 1 | 1 | variable |
| --- | --- | --- | --- |
| MHR fields | Command Frame Identifier (see Table 82) | Capability Information | payload |

7.3.10.1 MHR fields

The Source Addressing Mode subfield of the Frame Control field shall be set to three (64-bit extended addressing). The Destination Addressing Mode subfield shall be set to the same mode as indicated in the beacon frame to which the rejoin request command refers.

The Frame Pending subfield of the Frame Control field shall be set to zero and ignored upon reception, and the Acknowledgment Request subfield shall be set to one.

The Destination PAN Identifier field shall contain the identifier of the PAN to which to rejoin. The Destination Address field shall contain the address from the beacon frame that was transmitted by the coordinator to which the rejoin request command is being sent. The Source PAN Identifier field shall contain the broadcast PAN identifier (i.e., 0xffff). The Source Address field shall contain the value of aExtendedAddress.

The payload shall contain the set of octets from amacRejoinPayload

7.3.10.2 Capability Information field

The Capability Information field shall be formatted as illustrated in Figure XY.

| Bits: 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Alternate PAN Coordinator | Device type | Power source | Rx on when idle | Reserved | Rejoin | Security capability | Allocate address |

The Alternate PAN Coordinator subfield is 1 bit in length and shall be set to one if the device is capable of becoming the PAN coordinator. Otherwise, the Alternate PAN Coordinator subfield shall be set to zero.

The Device Type subfield is 1 bit in length and shall be set to one if the device is an FFD. Otherwise, the Device Type subfield shall be set to zero to indicate an RFD.

The Power Source subfield is 1 bit in length and shall be set to one if the device is receiving power from the alternating current mains. Otherwise, the Power Source subfield shall be set to zero.

The Receiver On When Idle subfield is 1 bit in length and shall be set to one if the device does not disable its receiver to conserve power during idle periods. Otherwise, the Receiver On When Idle subfield shall be set to zero.

The Rejoin subfield is 1 bit in length and shall be set to one if the device is rejoining the network.

The Security Capability subfield is 1 bit in length and shall be set to one if the device is capable of sending and receiving cryptographically protected MAC frames as specified in 7.5.8.2; it shall be set to zero otherwise.

The Allocate Address subfield is 1 bit in length and shall be set to one if the device wishes the coordinator to allocate a 16-bit short address as a result of the association procedure. Otherwise, it shall be set to zero.

7.3.11 Rejoin response command

The rejoin response command allows the PAN coordinator or a coordinator to communicate the results of a rejoin attempt back to the device requesting rejoin.

This command shall be sent by the PAN coordinator or coordinator to a device that is currently trying to rejoin.

All devices shall be capable of receiving this command, although an RFD is not required to be capable of transmitting it.

The rejoin response command shall be formatted as illustrated in Figure XZ.

| Octets (see 7.2.2.4) | 1 | 2 | 1 |
| --- | --- | --- | --- |
| MHR fields | Command Frame Identifier (see Table 82) | Short Address | Rejoin Status |

7.3.2.1 MHR fields

The Destination Addressing Mode and Source Addressing Mode subfields of the Frame Control field shall each be set to three (i.e., 64-bit extended addressing).

The Frame Pending subfield of the Frame Control field shall be set to zero and ignored upon reception, and the Acknowledgment Request subfield shall be set to one.

The PAN ID Compression subfield of the Frame Control field shall be set to one. In accordance with this value of the PAN ID Compression subfield, the Destination PAN Identifier field shall contain the value of macPANId, while the Source PAN Identifier field shall be omitted. The Destination Address field shall contain the extended address of the device requesting association. The Source Address field shall contain the value of aExtendedAddress.

7.3.2.2 Short Address field

If the coordinator was not able to rejoin this device to its PAN, the Short Address field shall be set to 0xffff, and the Association Status field shall contain the reason for the failure. If the coordinator was able to rejoin the device to its PAN, this field shall contain the short address that the device may use in its communications on the PAN until it is disassociated.

A Short Address field value equal to 0xfffe shall indicate that the device has been successfully associated with a PAN, but has not been allocated a short address. In this case, the device shall communicate on the PAN using only its 64-bit extended address.

7.3.2.3 Association Status field

The Rejoin Status field shall contain one of the non-reserved values listed in Table XA.

| Rejoin Status | Description |
| --- | --- |
| 0x00 | Rejoin successful |
| 0x01 | PAN at capacity |
| 0x02 | PAN access denied |
| 0x03 – 0x7f | Reserved |
| 0x080 – 0xff | Reserved for MAC primitive enumeration values |