## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Comments Resolution for issues related to data flow processing for MR-FSK PHY]
Date Submitted: [May, 2010]
Source: [Daniel Popa, Hartman Van Wyk] Company [Itron, Inc.]
Address [76 Avenue Pierre Brossolette, 92240 Malakoff, France]
Voice: [+33 158351760], E-Mail:[daniel.popa@itron.com]
Re: []
Abstract: []
Purpose: [Proposed resolution for comments on data flow processing. Presented to the 802.15.4g SUN Task Group for consideration.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15<doc 15-10-0356-02-004g>

## Slide 2
This proposal provides a resolution to the following comments: 1233, 1264, 1273.
doc.: IEEE 802.15<doc 15-10-0356-02-004g>

## Slide 3: Comments
Comment ID 1233 – Classified as FSK subgroup
  Block diagram in Figure 65a is incomplete, since FEC and Data Whitening are missing.
  Resolution required by the commenter: Add boxes for FEC and Data Whitening to Figure 65a.
Assigned to Alina Liu
doc.: IEEE 802.15<doc 15-10-0356-02-004g>

## Slide 4: Comments
Comment ID 1264 – Classified as Scrambling subgroup
  Comment content: The order of data whitening relative to FEC encoding is unclear.
  Resolution proposed by the author Clarify that, at the transmitter, when FEC is not used, data whitening is applied to the uncoded PSDU data bits. When FEC is used, data whitening is applied to the coded PSDU data bits following FEC encoding.
Assigned to James Gilb.
doc.: IEEE 802.15<doc 15-10-0356-02-004g>

## Slide 5: Comments
Comment ID 1273 – Classified as FSK subgroup
  Comment content: In case of FEC being enabled, is data whitening to be applied to the raw PSDU info bits or to the bits at the output of the FEC and possibly interleaver?
  Resolution proposed by the commenter: Specify the order of whitening in conjunction with FEC and interleaving.
Assigned to James Gilb.
doc.: IEEE 802.15<doc 15-10-0356-02-004g>

## Slide 6
Create a new subsection within the MR-FSK PHY Clause (6.12), as follows:
  Sub-section 6.12a.1 “Reference data flow processing diagram”, and
  inserts it before the existing subsection 6.12a.1, called “Reference Modulator Diagram”.
  Use the diagram from the following slide
Renumber all the following subsections.
doc.: IEEE 802.15<doc 15-10-0356-02-004g>

## Slide 7
doc.: IEEE 802.15<doc 15-09-xxx-xx-004g>
doc.: IEEE 802.15<doc 15-10-0356-02-004g>
* When forward error coding is enabled PHR and PSDU shall be processed for coding as a single block of data, as described in <Insert correct sub-clause number>
Forward Error
Coding*
PSDU
PHR
SHR
coded PHR
coded PSDU
uncoded PSDU
uncoded PHR
Controlled by
phyFSK_FEC
Controlled by phyScramblePSDU
Concatenater
Data
Whitener
CRC
MR-FSK Modulator