## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Comments Resolution for issues related to Reference Modulator Diagram for MR-FSK PHY]
Date Submitted: [July, 2010]
Source: [Daniel Popa, Hartman Van Wyk] Company [Itron, Inc.]
[Alina Lu, Hiroshi Harada] Company [NICT]
Address [76 Avenue Pierre Brossolette, 92240 Malakoff, France]
Voice: [+33 158351760], E-Mail:[daniel.popa@itron.com]
Re: []
Abstract: []
Purpose: [Proposed resolution for comments on data flow processing. Presented to the 802.15.4g SUN Task Group for consideration.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15<doc 15-10-0356-04-004g>

## Slide 2
This proposal provides a resolution to the following comments:
1233, 1264, 1273.
doc.: IEEE 802.15<doc 15-10-0356-04-004g>

## Slide 3: Comments
Comment ID 1233 (FSK subgroup)
  Block diagram in Figure 65a is incomplete, since FEC and Data Whitening are missing. Add boxes for FEC and Data Whitening to Figure 65a.
Response: Accept.
Proposed resolution: see document xx-0356-04-xx, pp 7-8.
doc.: IEEE 802.15<doc 15-10-0356-04-004g>

## Slide 4: Comments
Comment ID 1264 (Scrambling subgroup)
  - The order of data whitening relative to FEC encoding is unclear.
  - Clarify that, at the transmitter, when FEC is not used, data whitening is applied to the uncoded PSDU data bits. When FEC is used, data whitening is applied to the coded PSDU data bits following FEC encoding.
Response: Accept.
Proposed resolution: see document xx-0356-04-xx, pp 7-8.
doc.: IEEE 802.15<doc 15-10-0356-04-004g>

## Slide 5: Comments
Comment ID 1273 (FSK subgroup)
  In case of FEC being enabled, is data whitening to be applied to the raw PSDU info bits or to the bits at the output of the FEC and possibly interleaver?
  Specify the order of whitening in conjunction with FEC and interleaving.
Response: Accept.
Proposed resolution: see document xx-0356-04-xx, pp 7-8.
doc.: IEEE 802.15<doc 15-10-0356-04-004g>

## Slide 6
Proposed resolution:
  In Subsection 6.12a.1 “Reference Modulator Diagram”, replace Figure 65.a with Figure X.X provided in document xx-0356-04-xx”, page 7.
  Insert text provided in document xx-0356-04-xx, page 8.
doc.: IEEE 802.15<doc 15-10-0356-04-004g>

## Slide 7
doc.: IEEE 802.15<doc 15-09-xxx-xx-004g>
doc.: IEEE 802.15<doc 15-10-0356-04-004g>
Forward Error Correction
Coding Block
(Insert reference to section describing this functionality)
Binary {PSDU, PHR}
Controlled by phyFSKFEC
Concatenator
Data
Whitening Block
(Insert reference to section describing this functionality)
Controlled by phyScramblePSDU
PHR
PSDU
Figure X.X: Forward error correction, data whitening and modulator functions.
SHR Generation Block
(Insert reference to
section describing SHR)
Bit-to-symbol mapping Block
(Insert reference to section describing this functionality)
FSK/GFSK Modulation Block
(Insert reference to section describing this functionality)
Modulated Signal
RF

## Slide 8
doc.: IEEE 802.15<doc 15-09-xxx-xx-004g>
doc.: IEEE 802.15<doc 15-10-0356-04-004g>
Instructions to editors: Insert the following paragraphs after the new Figure 65.a:
The functional block diagram in Figure X.X is provided as a reference for specifying the MR-FSK PHY data flow processing functions. The number in each block refers to the subclause that describes that function. Each bit in the PPDU shall be processed through concatenator, FEC, data whitening and modulation functions using bit order rules defined in <Insert reference to clause that defines 4g bit order rules for data processing of PPDU (today Clause 6.3)>.
When forward error coding is enabled, PHR and PSDU shall be processed for coding as a single block of data, as described in <Insert correct sub-clause number>. When Data Whitening is enabled, the scrambling shall be only applied over the PSDU, as described in <Insert correct sub-clause number>.