IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Baseline Mode for SUN |
| Date Submitted | July 2010 |
| Source | Mark Wilbur | Voice: 01 440 528 7471 Fax: 01 440 528 7199 E-mail: mwilbur@aclara.com |
| Re: |  |
| Abstract | IEEE 802.15 Task Group TG4g Comment Resolution |
| Purpose | Define Baseline Mode for SUN |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

The document provides resolution for the following comments:

80, 82, 83, 88, 90-94, 98-102, 115, 131-134, 146-150, 152, 254, 255, 257

1595-1617, 1618-1626, 1628-1636, 1759, 1760-1765

Editorial note: replace existing 5.2a with text below

5.2a Baseline Mode

Several orthogonal PHY’s have been defined within this standard that will potentially operate within the same shared spectrum. The baseline mode is used to support communications between otherwise orthogonal devices sharing the same spectrum. Should the next higher layer determine that the primary baseline mode has been compromised the alternate baseline modes defined in 6.2a may be utilized.

Editorial note: add the 5.3.9b text below

5.5.3.1b Enhanced Beacon Request (EBR)

The EBR defined in 7.3.7a provides a discovery mechanism that can be used by an unassociated device to make itself known to all coordinators in range that are currently monitoring the baseline mode. The EBR is an information request transmitted by an unassociated device in order to communicate with a neighboring network associated coordinator.

Editorial note: add the5.3.9a text below

5.5.3.1a Enhanced Beacon (EB)

The EB defined in 7.2.2.1a is transmitted by a network associated coordinator when the EBR response criteria defined in 7.3.7a has been met. The device could use the information contained within the EB payload to perform any number of actions such as, avoidance of orthogonal networks sharing the spectrum or facilitation of the network association process for frequency hopping devices. The use of a pseudorandom EB transmission delays may be utilized to limit the number of simultaneous responses from neighboring nodes. Figure 103c shows an example of an EBR/EB packet sequence utilizing the baseline mode.

Editorial note: add the text and table 6.2a text below

6.2a Baseline Modes

Smart utility network (SUN) devices operating in shared spectrum bands shall be capable of communications using the baseline mode defined in table 6.2a.

Monitoring the baseline mode is optional. The baseline modes may be used for network traffic in bands where bandwidth is limited.

| Baseline | Modulation | Modulation Index / Rate | Channel Spacing (kHz) | Data Rate (kbps) | Channel Number |
| --- | --- | --- | --- | --- | --- |
| Primary Alt-1 Alt-2 | FSK FSK FSK | 1 1 1 | 200 200 200 | 50 50 50 | FLOOR (TCB*0.75) FLOOR (TCB*0.25) FLOOR (TCB*0.50) |

Table 6.2a

TCB=Total number of Channels defined for the Band of operation

The floor function takes a floating point number and returns the first integer which is less than or equal to that number.

Editorial note: remove entire sections 7.5.8a and 7.5.8b

7.3 MAC command frames

Editorial note: Change Table 123 (the entire table is not shown) as indicated:

Change the second paragraph of 7.3 as indicated

How the MLME shall construct the individual commands for transmission is detailed in 7.3.1 through7.3.9 7.3.9b. MAC command reception shall abide by the procedure described in 7.5.6.2.

Editorial note: replace existing 7.3.9a with text below

7.3.7a Enhanced Beacon Request (EBR) command

The EBR command is formatted as illustrated in Figure 103a.

| octets: (see 7.2.2.4) | 1 | 1 |
| --- | --- | --- |
| MHR fields | Command Frame Identifier (see Table 123) | Response Filter 0=ALL Coordinators respond 1=Only SUN Coordinators respond 2=Only Frequency Hopping Coordinators respond |

Figure 103a—EBR command format

7.3.7a MHR fields

The source addressing mode subfield of the frame control field shall be set to three ( 64-bit extended addressing). The destination addressing mode subfield of the frame control field shall be set to two (i.e.,16-bit short addressing).The frame pending subfield of the frame control field shall be set to zero on transmission and ignored upon reception. The acknowledgment request subfield and security enabled subfield shall be set to zero. The destination PAN identifier field shall contain the broadcast PAN identifier (i.e., 0xffff). The destination address field shall contain the broadcast short address (i.e., 0xffff).  The Source Address field shall contain the value of aExtendedAddress

Editorial note: replace existing 7.3.9b with text below

7.2.2.1a Enhanced Beacon (EB)

The EB command is formatted as illustrated in Figure 103b.

| octets: (see 7.2.2.4) | 1 | 4 | 2 | *Variable |
| --- | --- | --- | --- | --- |
| MHR fields | Command Frame Identifier (see Table 123) | phyCurrentSUNPageEntry (see Tab. 3. 31) | phyCurrentChannel (see Tab. 3. 31) | Necessary FreqHopping parameters |

Figure 103b—EB command format

*Frequency hopping parameters are only included in the beacon when responding to a EBR with the response filter set to (Only Frequency Hopping Coordinators respond)

7.2.2.1a MHR fields

The source addressing mode and destination addressing mode subfields of the frame control field shall both be set to three (i.e., 64-bit extended addressing).The frame pending subfield of the frame control field shall be set to zero and ignored upon reception. The acknowledgment request subfield and security enabled subfield shall be set to zero.. The PAN ID compression subfield of the frame control field shall be set to 1 and the Destination PAN shall contain the broadcast PAN ID (0xFFFF). The destination address field shall contain an extended address equal to the source address of the received EB command. The Source Address field shall contain the value of aExtendedAddress.

Editorial note: replace existing figure 103c with figure below

Figure 103c example of EBR/EB sequence