## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [802.15.4g Bit Order Resolution]
Date Submitted: [ “30 JUne, 2010”]
Source: [Daniel Popa], Company [Itron, Inc], Address [76 Avenue Pierre Brossolette, 92240 Malakoff, France], E-Mail:[daniel.popa@itron.com]
[J.L.Taylor], Company [DTC (UK)], Address [UK], E-Mail:[larry.taylor@discretetime.com]
Re: [LB51 Comment Resolution]
Abstract: [This contribution proposes a resolution to bit order representation for the 4g amendment]
Purpose: [LB#51 Comment Resolution]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 15-10-0445-00-004g

## Slide 2: Text Change Suggestion - Update the 3rd paragraph of 6.3 to say:
Slide 2
May 2010
  Delete “When the transmission order differs from this convention, it is described in the appropriate sub-clause” at the end of the 1st paragraph of 6.3
  Change 3rd paragraph in 6.3 as follows
  “In general, a PPDU packet consists of the following basic components:
    A synchronization header (SHR), which allows….
    A PHY header (PHR), which contains..
    A variable length payload (PSDU), which carries…
  Insert after the last bullet of the 3rd paragraph of 6.3
  For SUN PHYs (MR-FSK, MR-O-QPSK and OFDM) each component is treated as a bit string of length n, numbered b0 on the left and bn-1 on the right. When transmitted, the PPDU components are processed in the order SHR, PHR, PSDU and each component is processed b0 first to bn-1 last without regard to its content or structure as shown in Figure xx
Bit order processing at transmitter/receiver
Octet string index | 0 |  |  |  |  |  |  |  | 1 |  |  |  |  | 
Bit string index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | Component name |  |  |  |  |  |  |  |  |  |  |  |  | 
Figure xx: Example of bit order processing for a 4g PHY component; the number of octets {m = (k+1)} forming a PHY component is not necessarily an integer value.
Note: Changes are in bold italics
“In general..” is added since the
MSF PPDU has no PSDU
 | K |  |  |  |  |  |  | 
 | 8(k+1)-8 | 8(k+1)-7 | 8(k+1)-6 | 8(k+1)-5 | 8(k+1)-4 | 8(k+1)-3 | 8(k+1)-2 | 8(k+1)-1
 | Component name (cont’d) |  |  |  |  |  |  | 
doc.: IEEE 15-10-0445-00-004g

## Slide 3: 4g MR-FSK PHY: Mapping between bit string and PHR fields; each multi-bit field is processed MSB first
Slide 3
May 2010
MS = Mode Switching
RFU = Reserved for further use
FCS = FCS length
DW = Data Whitening
Bit string index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Bit Mapping | MS | R1 | R0 | FCS | DW | L10 | L9 | L8 | L7 | L6 | L5 | L4 | L3 | L2 | L1 | L0
Field Name |  | RFU |  |  |  | Payload Length |  |  |  |  |  |  |  |  |  | 
Delete 1st sentence of 6.3.2a as it is already defined in figure 26a
Replace figure 27a with the following
Figure 27a: MR-FSK PHR component
doc.: IEEE 15-10-0445-00-004g

## Slide 4: 4g MR-FSK PHY: Mapping between bit string and MSF fields; each multi-bit field is processed MSB first
Slide 4
May 2010
MS = Mode Switching
MSPE = mode Switch Parameter Entry
FEC = new mode FEC field
Bit string index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Bit Mapping | MS | M1 | M0 | FEC | N6 | N5 | N4 | N3 | N2 | N1 | N0 | F4 | F3 | F2 | F1 | F0
Field Name |  | MSPE |  |  | New Mode |  |  |  |  |  |  | Mode Switch FEC |  |  |  | 
Replace figure 27c with the following
Figure 27c: MR-FSK Mode Switching Frame PHR component
doc.: IEEE 15-10-0445-00-004g

## Slide 5
Slide 5
May 2010
PC = Parity Check
RM = Rate Mode
RFU = Reserved for further use
4g MR-O-QPSK PHY: Mapping between bit string and PHR fields; each multi-bit field is processed MSB first
Bit string index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Bit Mapping | P1 | P0 | RM1 | RM0 | RFU | L10 | L9 | L8 | L7 | L6 | L5 | L4 | L3 | L2 | L1 | L0
Field Name | PC |  | RM |  |  | Payload Length |  |  |  |  |  |  |  |  |  | 
Delete 1st sentence in 6.3.2b
Replace figure 27b with the following
Figure 27b: MR-O-QPSK PHR component
doc.: IEEE 15-10-0445-00-004g

## Slide 6
Slide 6
May 2010
RFU = Reserved for further use
S = Scrambler
HCS = Header Check Sequence
4g OFDM PHY: Mapping between bit string and PHR fields; each multi-bit field is processed MSB first
Bit string index | 0 - 4 | 5 | 6 - 16 | 17 - 18 | 19 - 20 | 21 | 22 - 29 | 30 – 35
 | R4 ……..R0 | RFU | L10……L6………L0 | R1 ¦ R0 | S1 ¦ S0 | RFU | H7…………H0 | T5…………T0
Field name | Rate |  | Payload Length | RFU | S |  | HCS | Tail
0
3
Replace figure 27f with the following
Figure 27f: OFDM PHR component
doc.: IEEE 15-10-0445-00-004g