IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Resolution with CID 75 |
| Date Submitted | [12th July, 2010] |
| Source | [Jaeseung Son, Sridhar Rajagopal, Samsung Electronics] | E-mail:[js1007.son@samsung.com] |
| Re: |  |
| Abstract | Adding subclause 5.5.1.4.2 Coexistence with CSK |
| Purpose | [TG 7 received about PHY header related comments in LB. This document is the response about PHY header comments] |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

5.5.1.4.2 Co-existence of PHY I, PHY II with PHY III

PHY I and PHY III also occupy different spectral regions in the modulation domain spectrum, with different data rates and different optical rate support, providing co-existence. However, the optical clock frequencies used for PHY II and PHY III overlap, causing significant overlap in the frequency domain spectrum. In addition, not all devices may support multiple optical frequency bands needed for PHY III. Hence, all PHY III devices use a PHY II device for device discovery to support co-existence. The details of the co-existence mechanism for PHY III are provided in 6.8.

[Delete sub clause title in 6.8.1, implying 6.8.1 becomes 6.8 to be consistent with 6.7 and 6.6. We decided to use the PHY I, II, III terminology throughout the document]

[Add normative text at the end of text Section 6.8, line 47, page 54]

PHY III devices shall utilize PHY II devices for device discovery. After all devices in the network are discovered and if all of them support PHY III when their capabilities are exchanged, the coordinator can decide to switch to PHY III mode of operation. In addition, all PHY III devices should match the operating optical frequency bands for communication so that transmission on two optical frequency bands do not fall within one optical filter band of the receiver.