## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Data rates in licensed bands]
Date Submitted: [July 2010]
Source: [Roberto Aiello, John Buffington] Company [Itron]
Address [San Diego, CA. Liberty Lake, WA USA]
Voice:[], FAX:], E-Mail:[aiello@ieee.org, john.buffington@itron.com]
Abstract: [This presentation proposes data rates and modulation parameters for licensed bands in 802.15.4g]
Purpose: [For information]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary
SUN industry data rate requirements
Licensed bands of interest
Proposed data rates and modulation parameters

## Slide 3: Licensed spectrum (low data rate)
450-470 MHz
  FCC part 22/90

## Slide 4: Data rate requirements
Example OpenSG AMI-Net requirements (*)
  Worst case meter read transaction between meter and data access point
  Up to 2,400 bytes delivered in <5 seconds with >98% reliability
Minimum required data rate (no overhead)
  2,400 bytes/ 5 sec = 3.8 kbps
(*) SG Network System Requirements Specification v4.0

## Slide 5: Data rates with overhead
5 kbps too tight
10 kbps marginal
20kbps probably minimum reasonable

## Slide 6: Proposed data rates
Modulation similar to:
  470-510 MHz (China)
  863-870 MHz (Europe)
  950 MHz (Japan)