## Slide 1
Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Bit Order Comment Resolution]
Date Submitted: [ “13 July, 2010”]
Source: [Daniel Popa], Company [Itron, Inc], Address [76 Avenue Pierre Brossolette, 92240 Malakoff, France], E-Mail:[daniel.popa@itron.com]
[J.L.Taylor], Company [DTC (UK)], Address [UK], E-Mail:[larry.taylor@discretetime.com]
Re: [LB51 Comment Resolution]
Abstract: [This contribution proposes a resolution to bit order representation for the 4g amendment]
Purpose: [LB#51 Comment Resolution]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Bit Order Comment Group
Related Comments
Popa / Taylor
781, 783, 789, 815, 871, 889, 915, 938, 951, 952, 954, 1059-1063

## Slide 3: Additional Changes
Additional changes might be required, as a function of the work-in-progress on comment resolution
These changes will be only related to eventual reorganization of the structure of PHY components

## Slide 4: Text Changes to Draft
General comment
  Section 6.3.x introduces the Preamble, SHR and PHR structures and describes each of them for each PHY variant
  6.3.1 refers to 6.3.4a for the preamble for OFDM
  6.3.2 declares exceptions for the SFD for SUN PHYs. It describes the SFD for MR-FSK and MR-O-QPSK but says nothing about the SFD for OFDM
  6.3.3 describes the PHY header for MR-FSK and MR-O-QPSK but not for OFDM
Would it not be easier to read and more consistent with the complete text to treat each PHY separately and define the SHR and PHR just for one PHY in each part of the document?
i.e. have 6.12a.x define the SHR and PHR for MR-FSK, 6.12b.x define the SHR and PHR for MR-O-QPSK and 6.12c.x define the SHR and PHR for OFDM

## Slide 5: How it will be ?
General Description of a 4g PPDU;
defines bit order rules for PPDU global components: SHR, PHR and PSDU.
SHR & PHR
Description
for MR-FSK
SHR & PHR
Description
for MR-O-QPSK
SHR & PHR
Description
for OFDM
Section 6.3
Add a dedicated subsection
(Section 6.12a.1) to describe mapping
between the bit string and fields of the
MR-FSK (SHR + PHR) components
Add a dedicated subsection (Section 6.12c.1)
to describe mapping between the bit string
and fields of the OFDM (SHR + PHR)
components
Add a dedicated subsection
(Section 6.12b.1) to describe mapping
between the bit string and fields of the
MR-O-QPSK (SHR + PHR) components

## Slide 6: If not, and we have to keep the complex logic of the existing draft 6.3
The text change to 6.3 has been defined
In section 6.3.2a change
  The Packet Control field is 5 bits in length and is shown in Figure 27a.
  to
  The Packet Control field occupies the first 5 bits of the PHR as shown in Figure 27a.
Identify the Packet Control field in the replacement PHR diagram as in the following slides
Question – is it useful to retain the naming of the 5 bits as a field instead of just defining the meaning of each group of bits?

## Slide 7: Change to 6.2.3b
Change
  The Packet Control field of the MR-O-QPSK PHY is five bits in length and is shown in Figure 27b
  To
  The Packet Control field occupies the first 5 bits of the PHR as shown in Figure 27b
  Identify the Packet Control field in the replacement PHR diagram in the following slides
Question – is it useful to retain the naming of the 5 bits as a field instead of just defining the meaning of each group of bits?

## Slide 8: Text change to 6.3.3
Change
    The Frame Length field is 7 bits in length and specifies the total number of octets contained in the PSDU (i.e., PHY payload). For the MR-FSK, OFDM, and MR-O-QPSK PHYs, the Frame Length field is 11 bits in length. The Frame Length field is a value between 0 and aMaxPHYPacketSize (see 6.4). For the MR-FSK PHY, the most-significant bit (leftmost) shall be transmitted first.
  To
    The Frame Length field is 7 bits in length and specifies the total number of octets contained in the PSDU (i.e., PHY payload). For the MR-FSK, OFDM, and MR-O-QPSK PHYs, the Frame Length field is 11 bits in length as shown in figures 27a, 27b and 27f respectively. The Frame Length field is a value between 0 and aMaxPHYPacketSize (see 6.4).

## Slide 9: Text changes to 6.3.3a
Change
  The Mode Switch Parameter Entry subfield is 2 bits in length…
  To
  The Mode Switch Parameter Entry sub-field is an unsigned 2-bit integer…(refer to table defining the values)
  The Modulation Scheme bits indicate the modulation scheme (see 6.1.2.5a)
  To
  If phyCurrentPage = 7 Modulation Scheme is an unsigned 2-bit integer identifying the modulation scheme as in Table 3b, otherwise it is not used.

## Slide 10: Text changes to 6.3.4a.3
Change
  The PHY header fields include:
  — An unsigned 5-bit integer Rate field which specifies the data rate of the payload frame (insert reference to definition of rate values – couldn’t find this)
  — One reserved bit after the Rate field
  — An 11-bit unsigned integer Frame Length field which specifies the number of octets in the payload
  — Two reserved bits after the Frame Length field
  — A 2-bit Scrambler seed field (insert reference to where the scrambler seed is defined – couldn’t find this)
  — One reserved bit after the Scrambler field
  — An 8-bit Header Check Sequence (HCS) CRC taken over the data fields only (insert reference to where the bit correspondence for the HCS is defined – I couldn’t find this)
  — Six tail bits, each set to zero, for Viterbi decoder flushing

## Slide 11: Changes to 6.12c.4.1
Delete the following text after Table 75q as it is redundant with 6.3 and now updated:
  Each bit in the (SHR,PHR) shall be processed in octet-wise order, beginning with the Preamble field and ending with the last octet of the PHR. Within each octet, the LSB, b0, is processed first and the MSB, b7, is processed last.

## Slide 12: Text Change Suggestion - Update the 3rd paragraph of 6.3 to say:
Slide 12
Slide 12
  Delete “When the transmission order differs from this convention, it is described in the appropriate sub-clause” at the end of the 1st paragraph of 6.3
  Change 3rd paragraph in 6.3 as follows
    “In general, a PPDU packet consists of the following basic components:
      A synchronization header (SHR), which allows….
      A PHY header (PHR), which contains..
      A variable length payload (PSDU), which carries…
  Insert after the last bullet of the 3rd paragraph of 6.3
    For SUN PHYs (MR-FSK, MR-O-QPSK and OFDM) the SHR, PHR and PSDU components are treated as bit strings of length n, numbered b0 on the left and bn-1 on the right. When transmitted, they are processed b0 first to bn-1 last without regard to their content or structure as shown in Figure xx.
    (Note that since the PHR defines the PSDU length in octets, the PSDU bits are numbered b0 to b8*Frame Length-1 )
Bit order processing at transmitter/receiver
Octet string index | 0 |  |  |  |  |  |  |  | 1 |  |  |  |  | 
Bit string index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
 | Component name |  |  |  |  |  |  |  |  |  |  |  |  | 
Figure xx: Example of bit order processing for a 4g PHY component; the number of octets {m = (k+1)} forming a PHY component is not necessarily an integer value.
Note: Changes are in bold italics
“In general..” is added since the
MSF PPDU has no PSDU
 | K |  |  |  |  |  |  | 
 | 8(k+1)-8 | 8(k+1)-7 | 8(k+1)-6 | 8(k+1)-5 | 8(k+1)-4 | 8(k+1)-3 | 8(k+1)-2 | 8(k+1)-1
 | Component name (cont’d) |  |  |  |  |  |  | 

## Slide 13: Mapping between bit string and PHR fields: 4g MR-FSK PHY All multi-bit fields are unsigned integers and shall be processed MSB first
Slide 13
Slide 13
MS = Mode Switching
RFU = Reserved for further use
FCS = FCS length
DW = Data Whitening
Bit string index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Bit Mapping | MS=0 | R1 | R0 | FCS | DW | L10 | L9 | L8 | L7 | L6 | L5 | L4 | L3 | L2 | L1 | L0
Field Name |  | RFU |  |  |  | Payload Length |  |  |  |  |  |  |  |  |  | 
 | Packet Control |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Delete 1st sentence of 6.3.2a as it is already defined in figure 26a
Replace figure 27a with the following
Figure 27a: MR-FSK PHR component

## Slide 14: Mapping between bit string and MSF fields 4g MR-FSK PHY All multi-bit fields are unsigned integers and shall be processed MSB first
Slide 14
Slide 14
MS = Mode Switching
MSPE = mode Switch Parameter Entry
FEC = new mode FEC field
Page = 0 if Channel Page =7 or 1 if Channel Page=8
Mod – Modulation Scheme
Md = Mode
B = BCH
PC = Parity Check
Bit string index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Bit Mapping | MS=1 | M1 | M0 | FEC | Page | Mod1 | Mod0 | Md3 | Md2 | Md1 | Md0 | B3 | B2 | B1 | B0 | PC
Field Name |  | MSPE |  |  | New Mode |  |  |  |  |  |  | Mode Switch FEC |  |  |  | 
Replace figure 27c with the following
Figure 27c: MR-FSK Mode Switching Frame PHR component

## Slide 15
Slide 15
Slide 15
PC = Parity Check
RM = Rate Mode
RFU = Reserved for further use
Mapping between bit string and PHR fields
4g MR-O-QPSK PHY
All multi-bit fields are unsigned integers and shall be processed MSB first
Bit string index | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Bit Mapping | P1 | P0 | RM1 | RM0 | RFU | L10 | L9 | L8 | L7 | L6 | L5 | L4 | L3 | L2 | L1 | L0
Field Name | PC |  | RM |  |  | Payload Length |  |  |  |  |  |  |  |  |  | 
 | Packet Control |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Delete 1st sentence in 6.3.2b
Replace figure 27b with the following
Figure 27b: MR-O-QPSK PHR component

## Slide 16
Slide 16
Slide 16
RFU = Reserved for further use
S = Scrambler
HCS = Header Check Sequence
Mapping between bit string and PHR fields
4g OFDM PHY
All multi-bit fields are unsigned integers and shall be processed MSB first
Bit string index | 0 - 4 | 5 | 6 - 16 | 17 - 18 | 19 - 20 | 21 | 22 - 29 | 30 – 35
 | R4 ……..R0 | RFU | L10……L6………L0 | R1 ¦ R0 | S1 ¦ S0 | RFU | H7…………H0 | T5…………T0
Field name | Rate |  | Payload Length | RFU | S |  | HCS | Tail
Replace figure 27f with the following
Figure 27f: OFDM PHR component

## Slide 17: Resolutions
# | Comment | Proposed Resolution
781 | The section on PPDU format requires further clarification, e.g. that the reserved bits shall be set to 0 on transmit and ignored on receipt, also the packet formats need to be consistent with the behavior detailed in sub-clause 6.12, etc. | Accept in principle - resolution as in Document 15-10-0558-01-0004g
783 | Lines 47-48. LSB should be transmitted or received first for all 802.15.4 PHYs | Withdrawn
789 | The second phrase, which states on the transmission order for the multi-octet fields of the PPDU structure, creates confusion with respect to the first phrase. | Accept in principle - resolution as in Document 15-10-0558-01-0004g
815 | There is not sufficient and crystal clear information about the (over-the-air) transmission order for the bytes and/or bits from PHR and Mode Switching Fields. This is clarified for Preamble and SFD but not for the aforementioned PPDU fields. | Accept in principle - resolution as in Document 15-10-0558-01-0004g

## Slide 18: Resolutions
# | Comment | Proposed Resolution
871 | There is no crystal clear information on the (over-the-air) transmission order for the bits from the Packet Control Field. | Accept in principle - resolution as in Document 15-10-0558-01-0004g
889 | It is not necessary to say that the LSB is transmitted first and that the MSB is transmitted last. This is stated in the opening paragraph of 6.3. | Reject. Current text is unfortunately ambiguous. Replacement text and figures in Document 15-10-0558-01-0004g provide corrections
915 | Lines 3-4. For the Frame Length field, the LSB should be transmitted first. | Withdrawn
938 | This isn't really a field, this is an alternate format for the PPDU. | Accept in principle - resolution as in Document 15-10-0558-01-0004g
951 | "For the MR-FSK PHY, the most-significant bit (leftmost) shall be transmitted first" Why reverse the transmission order for the length field? | Reject. Current text is unfortunately ambiguous. Replacement text and figures in Document 15-10-0558-01-0004g provide corrections

## Slide 19: Resolutions
# | Comment | Proposed Resolution
952 | "For the MR-FSK PHY, the most-significant bit (leftmost) shall be transmitted first" | Reject. Current text is unfortunately ambiguous. Replacement text and figures in Document 15-10-0558-01-0004g provide corrections
954 | Inverting the bit transmission order for the subfield "Payload Length" of the PHR adds useless design burden. | Reject. Current text is unfortunately ambiguous. Replacement text and figures in Document 15-10-0558-01-0004g provide corrections
1059-1063 | It should be clarified that the rate field and frame length field are transmitted LSB first. | Reject. Current text is unfortunately ambiguous. Replacement text and figures in Document 15-10-0558-01-0004g provide corrections