IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Yet Another Frame Proposal |
| Date Submitted | 12 July 2010 |
| Source | Jonathan Simon Dust Networks 30695 Huntwood Ave Hayward, CA 94544 | Voice: 510-400-2936 Fax: E-mail: jsimon@dustnetworks.com |
| Re: | [Overhead reduction] |
| Abstract | [Describes a frame type that could be used generically to represent a wide variety of frame options] |
| Purpose | [To propose an approach to be included in the next draft] |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

Proposal:

The desired set of options for fields across all optional modes is:

| Octets: 1/2 | 0/1 | 0/2 | 0/1/2/8 | 0/2 | 0/1/2/8 | 0/5/6/10/14 | variable | variable | 0/2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Frame Control | Seq # | Dest PAN | Dest Addr | Src pan | Src Addr | Aux Sec | IE’s | Payload | FCS |

We define a new frame type using one of the currently reserved types (e.g. 110). The frame control is self-describing, and contains 1 or 2 octets.  If addressing fields are required, sequence number is enabled, IE’s are used, or the version changes, the FC field expands to 2 octets, otherwise it is 1 octet.  The frame control indicates which fields are present in the remainder of the header and their size.

| Bit: 0-2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11-12 | 13 | 14-15 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Frame Type | Security enabled | Frame pending | Ack requested | Addressing fields | Aux sec header | Seq # | Version | IEs | Src mode | PAN ID | Dst mode |
| 110 | 0 = off 1 = on and no FCS | 0 = no 1 = yes | 0 = no 1 = yes | 0 = none 1 = some, set in next octet | 0 = none, and frame counter must be reconstructed if security is on 1- carried inline | 0 = none 1 = 1B (none if 1 octet FC) | 0 (version is 0 if 1 octet FC) | 0 = none 1 = present | 00 = none 01 = 1B 10 = 2B 11 = 8B | 0 = none 1 = 2B | 00 = none 01 = 1B 10 = 2B 11 = 8B |