IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Some Proposed Changes to IEEE P802.15.6/D01 MAC and Security Subclauses |
| Date Submitted | September 6, 2010 |
| Source | Jin-Meng Ho Texas Instruments Inc. 2500 TI Blvd Dallas, TX, USA 214-480-1994 jinmengho@ti.com |
| Re: | LB# 55 comment resolution |
| Abstract | This submission shows how the proposed resolutions to some MAC and security related comments, especially those described in doc. IEEE 802.15-10-0676-00-0006 and doc. IEEE 802.15-10-0677-00-0006, would look like if they were incorporated into doc. IEEE 802.15.6/D01. It incorporates the proposed security related changes as reflected in doc. IEEE 802.15-10-0678-00-0006. |
| Purpose | To facilitate resolution of LB#55 MAC and security comments and revision of IEEE P802.15.6/D01 MAC and security subclauses |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

Contents

1. Overview	1

1.1 General	1

1.2 Scope	1

1.3 Purpose	2

1.4 Need for the Project	2

2. Normative references	3

3. Definitions	4

4. Abbreviations and acronyms	9

5. General framework elements	12

5.1 General	12

5.2 Network topology	12

5.3 Reference model	12

5.4 Time base	13

5.5 State diagram	14

5.6 Security paradigm	16

6. MAC frame formats	18

6.1 Conventions	18

6.2 General format	19

6.3 Management type frames	28

6.4 Control type frames	52

6.5 Data type frames	55

6.6 MAC / PHY Capability fields	55

6.7 Information elements (IEs)	58

7. MAC functions	70

7.1 General	70

7.2 Frame processing	70

7.3 Access classification and division	77

7.4 BAN creation and connection setup	80

7.5 Random access (connectionless contention-based access)	81

7.6 Improvised and unscheduled access (connectionless contention-free access)	86

7.7 Scheduled access and variants (connection-oriented contention-free access)	90

7.8 MICS band communication	94

7.9 Two-hop star topology extension	98

7.10 Clock synchronization and guardtime provisioning	110

7.11 Power management	113

7.12 Coexistence and interference mitigation	115

7.13 MAC / PHY capability handling/interaction and Application Specific IE usage	120

7.14 MAC sublayer parameters	121

8. Security services	125

8.1 Master keys	125

8.2 Temporal keys	137

8.3 Message security	139

8.4 Optional cipher functions	147

9. Narrowband (NB) PHY specification	148

9.1 Data rate-dependent parameters	149

9.2 PLCP preamble	151

9.3 PLCP Header	153

9.4 PSDU	156

9.5 General Requirements	162

9.6 PHY layer timing	163

9.7 Transmitter Specifications	164

9.8 Receiver Specifications	167

10. Ultra wideband (UWB) PHY specification	171

10.1 Modes of operation	171

10.2 Rules for use of modes and options	171

10.3 Definitions of FFDs (coordinators) and RFDs (devices)	172

10.4 UWB PHY Frame Format	172

10.5 PSDU construction	173

10.6 PHR construction	176

10.7 SHR Preamble	178

10.8 UWB symbol structure	179

10.9 Data Rates	179

10.10 PSDU timing parameters	180

10.11 UWB Modulations	182

10.12 Operating frequency bands	189

10.13 Clock accuracy and central frequency alignment	189

10.14 Transmit spectrum mask	189

10.15 Pulse Shape Waveform	190

10.16 Hybrid type II ARQ mechanism	195

10.17 FM-UWB PHY	197

10.18 Clear Channel Assessment	197

11. Human Body Communications (HBC) PHY specification	197

11.1 General	197

11.2 EFC packet structure	197

11.3 EFC Transmitter	197

11.4 PHY Preamble	197

11.5 Start Frame Delimiter (SFD)	197

11.6 PHY Header	197

11.7 S2P and FS-spreader	197

11.8 Rate Indicator and Pilot Signal	197

11.9 Transmitter Specifications	197

11.10 Receiver Specifications	197

Annex A (informative) Bibliography	197

Annex B (informative)	197

B.1 Appendix B (informative) Soft detection	197

B.2 Appendix B (informative) Shortened BCH (31,19) Code	197

Draft Standard for Information Technology - Telecommunications and Information Exchange Between Systems - Local and Metropolitan Area Networks - Specific Requirements - Part 15.6: Wireless Medium Access Control (MAC) and Physical Layer (PHY) Specifications for Wireless Personal Area Networks (WPANs) used in or around a body

IMPORTANT NOTICE: This standard is not intended to ensure safety, security, health, or environmental protection in all circumstances. Implementers of the standard are responsible for determining appropriate safety, security, environmental, and health practices or regulatory requirements.

This IEEE document is made available for use subject to important notices and legal disclaimers. 
These notices and disclaimers appear in all publications containing this document and may 
be found under the heading “Important Notice” or “Important Notices and Disclaimers 
Concerning IEEE Documents.” They can also be obtained on request from IEEE or viewed at http://standards.ieee.org/IPR/disclaimers.html.

Overview

General

This document defines a standard for Body Area Network (BAN) used in or around a body.

It is designed to serve advanced medical and entertainment options enabled by this standard. It will allow medical equipment manufacturers and consumer electronics manufacturers to have small, power-efficient, inexpensive solutions to be implemented for a wide range of devices.

This standard specifies a medium access control (MAC) layer 802.15 in support of several physical layers (PHYs).

Scope

This is a standard for short range, wireless communication in the vicinity of, or inside, a human body (but not limited to humans). It uses existing ISM bands as well as frequency bands approved by national medical and/or regulatory authorities. Support for quality of service, extremely low power, and data rates up to 10 Mbps is required while simultaneously complying with strict non-interference guidelines where needed. This standard considers effects on portable antennas due to the presence of a person (varying with male, female, skinny, heavy, etc.), radiation pattern shaping to minimize specific absorption rate (SAR) into the body, and changes in characteristics as a result of the user motions.

Purpose

The purpose is to provide an international standard for a short range (i.e. about human body range), low power and highly reliable wireless communication for use in close proximity to, or inside, a human body. Data rates, typically up to 10Mbps, can be offered to satisfy an evolutionary set of entertainment and healthcare services. Current Personal Area Networks (PAN)s do not meet the medical (proximity to human tissue) and relevant communication regulations for some application environments. They also do not support the combination of reliability, Quality of Service (QoS), low power, data rate and noninterference required to broadly address the breadth of body area network applications.

Need for the Project

There is a need for a standard optimized for ultra-low power devices and operation on, in or around the human body to serve a variety of applications including medical and personal entertainment. Examples of the applications served by the proposed standard are: Electroencephalogram (EEG), Electrocardiogram (ECG), Electromyography (EMG), vital signals monitoring (temperature (wearable thermometer), respiratory, wearable heart rate monitor, wearable pulse oximeter, wearable blood pressure monitor, oxygen, pH value , wearable glucose sensor, implanted glucose sensor, cardiac arrhythmia), wireless capsule endoscope (gastrointestinal), wireless capsule for drug delivery, deep brain stimulator, cortical stimulator (visual neuro-stimulator, audio neuro stimulator, Parkinson’s disease, etc…), remote control of medical devices such as pacemaker, actuators, insulin pump, hearing aid (wearable and implanted), retina implants, disability assistance, such as muscle tension sensing and stimulation, wearable weighing scale, fall detection, aiding sport training. This will include body-centric solutions for future wearable computers. In a similar vein, the same technology can provide effective solutions for personal entertainment as well. The existence of a body area network standard will provide opportunities to expand these product features, better healthcare and wellbeing for the users. It will therefore result in economic opportunity for technology component suppliers and equipment manufacturers.

Normative references

The following standards contain provisions which, through references in this text, constitute provisions of this standard. At the time of publication, the editions indicated were valid. All standards are subject to revision, and parties to agreements based on this standard are encouraged to investigate the possibility of applying the most recent editions of the standards listed below.

IEEE Std 802-2001, IEEE Standard for Local and Metropolitan Area Networks: Overview and Architecture.

IEEE Std 1363-2000, IEEE Standard Specifications for Public-Key Cryptography.

FIPS Pub 197, Advanced Encryption Standard (AES), November 2001.

FIPS Pub 186-3, Digital Signature Standard (DSS), June 2009.

NIST Special Publication 800-38B, Recommendation for Block Cipher Modes of Operation: The CMAC Mode for Authentication, May 2005.

NIST Special Publication 800-38C, Recommendation for Block Cipher Modes of Operation: The CCM Mode for Authentication and Confidentiality, July 2007.

NIST Special Publication 800-90, Recommendation for Random Number Generation Using Deterministic Random Bit Generators, March 2007.

ISO/IEC Standard　18033-3, Information technology – Security techniques – Encryption algorithms – Part 3: Block ciphers, July 2005.

ISO/IEC Standard 10116, Information technology – Security techniques – Modes of operation for an n-bit block cipher, February 2006.

ISO/IEC Standard 19772, Information technology – Security techniques – Authenticated encryption, February 2009.

ISO/IEC 10646, Universal Multiple-Octet Coded Character Set (UCS), December 2003. Amendment 1, November 2005. Amendment 2, July 2006. Amendment 3, February 2008.

IETF RFC 4086, Randomness Requirements for Security, June 2005.

Definitions

For the purposes of this document, the following terms and definitions apply. The IEEE Standards Dictionary: Glossary of Terms & Definitions should be referenced for terms not defined in this clause.

abbreviated address	A one-octet identifier (ID) selected as an address for a node, hub, or body area network (BAN) in frame exchanges.

active state	 An internal power management state that is ready for frame reception and transmission.

active superframe	 A superframe in which frame transmission typically occurs within the body area network (BAN) of the hub announcing such a superframe.

allocation	 One or more time intervals that a node or a hub obtains using an access method for initiating one or more frame transactions. An allocation comprises one or more allocation intervals. Reference to allocation of a node means that the node is the sender or recipient in the allocation.

allocation interval	 A continuous time interval in an allocation, comprising one or more consecutive allocation slots. Reference to allocation interval of a node means that the node is the sender or recipient in the allocation interval.

allocation slot	 A time unit used to designate the lengths of medium access related time intervals, such as beacon period and allocation interval.

association	 A term synonymous to security association in absence of the qualifier “security”.

beacon	 A frame transmitted by a hub to facilitate network management, such as the coordination of medium access and power management of the nodes in the body area network (BAN) of the hub, and to facilitate clock synchronization therein.

beacon period	 A repetitive time interval to which medium access is referenced and in which a beacon is transmitted when appropriate, comprising the same number of time units (allocation slots) of equal duration.

bilink	 A communications link for transfer of management and data traffic from a hub to a node or/and vice versa.

bilink allocation	 An allocation with allocation interval(s) in which a hub or a node initiates one or more frame transactions to transmit management and data traffic to a node or a hub, respectively, and the recipient returns acknowledgment if required, with the provision that the node initiates frame transaction(s) only after receiving a poll from the hub.

bilink allocation / delay	 A bilink allocation in which the scheduled start of a bilink allocation interval is subject to delay.

connected node	 A node that has a connection with a hub.

connection	 A relationship between a node and a hub in a body area network (BAN), substantiated by a Connected_NID assigned to the node by the hub and by a wakeup arrangement between them, and optionally by one or more scheduled allocations between them.

contended allocation	 A non-reoccurring time interval, within a random access phase (RAP) or a contention access phase (CAP), that a node obtains using random access for initiating a frame transaction. A contended allocation is an uplink allocation, suitable for “unpredictable” uplink traffic (for example, due to data rate variations and/or channel impairments).

contention access	 An access method, based on carrier sense multiple access with collision avoidance (CSMA/CA) or slotted Aloha access but not both, by which a node obtains a time interval in a contention access phase (CAP) for initiating one or more frame transactions. As an access method, contention access is synonymous with random access.

contention access phase	 A time span set aside by a hub and announced via a preceding non-beacon frame for contention access to the medium by the nodes in the body area network (BAN) of the hub.

delayed-polling access	 A variant of scheduled-polling access, by which the scheduled start of frame transactions is subject to delay.

downlink	 A communications link for transfer of management and data traffic from a hub to a node.

downlink allocation	 An allocation with allocation interval(s) in which a hub initiates one or more frame transactions to transmit management and data traffic to a node and the node returns acknowledgment if required.

entity authentication	 Corroboration of the identity of the node or the hub in a security association procedure.

exclusive access phase	 A time span set aside by a hub in a beacon period for transfer of the traffic of the highest user priority (for emergency or medical event report).

frame	 An uninterrupted sequence of octets delivered by the medium access control (MAC) sublayer to the physical (PHY) layer, or vice versa, within a node or a hub.

frame transaction	 The exchange of one or more functionally related frames between a node and a hub, without interruption by other frames to facilitate frame transmission and reception as well as frame acknowledgment if required. An example frame transaction consists of a frame transmission followed by an acknowledgment return.

hub	 An entity that possesses a node’s functionality and coordinates the medium access and power management of the nodes in its body area network (BAN).

hub identifier	 An abbreviated address of a hub.

implant	An entity that is placed inside a human body for medical purposes.

improvised access	 An access method, based on improvised polling or posting by a hub, by which a hub grants to a node or itself a polled or posted allocation, typically outside scheduled downlink and uplink allocations, for initiating one or more frame transactions by the node or hub, respectively.

inactive state	 An internal power management state that is not ready for frame reception and transmission.

inactive superframe	 A superframe in which no frame transmission occurs within the body area network (BAN) of the hub announcing such a superframe.

information element	An optional part, with variable but self-identifiable length, of some frames.

master key (MK)	 A secret bit string activated or established between a node and a hub in a security association procedure and used to create a pairwise temporal key (PTK) shared between them.

medical implant event	 A term referenced in regulatory documents governing the use of the medical device radio communication (MedRadio) service band, which includes the medical implant communications service (MICS) band.

message authentication	 Corroboration of the origin of a message in a message transfer.

multi-periodic (m-periodic) allocation     A scheduled allocation that has allocation intervals reoccurring in every mth beacon period (superframe) with m being an integer larger than one. An m-periodic allocation is an uplink allocation, a downlink allocation, or a bilink allocation, suitable for low duty cycle periodic or quasi-periodic traffic.

node	 An entity that contains a medium access control (MAC) sublayer, a physical (PHY) layer, and a node management entity (NME) and that provides message security services in accordance with this standard. Unless otherwise noted, reference to nodes refers to nodes that are not acting as hubs.

node identifier (NID)	 An abbreviated address of a single node or of a logical group of nodes.

non-secure frame	 A term that is interchangeable with unsecured frame.

nonce	number used once

one-periodic (1-periodic) allocation	      A scheduled allocation that has allocation intervals reoccurring in every beacon period (superframe). A 1-periodic allocation is an uplink allocation, a downlink allocation, or a bilink allocation, suitable for high duty cycle periodic or quasi-periodic traffic.

pairwise temporal key (PTK)	 A secret bit string shared between a node and a hub and used to secure frames transferred between them.

pairwise temporal key (PTK) creation     A procedure used to create a PTK between a node and a hub based on a master key shared between them, and to confirm possession of a shared MK between the node and the hub.

poll	 A control type frame or its variant sent by the hub to grant an immediate polled allocation to the addressed node or to inform the node of an intended future poll or post.

polled allocation	 A non-reoccurring time interval, typically outside scheduled downlink and uplink allocations, that a hub grants to a node using polling access for initiating one or more frame transactions by the node. A polled allocation is an uplink allocation, suitable for “ordinary”, “unexpected”, or “extra” uplink traffic (for example, due to data rate variations and/or channel impairments).

polling access	 An access method, based on impromptu or scheduled polling by a hub, by which a hub grants to a node a polled allocation, typically outside scheduled downlink and uplink allocations, for initiating one or more frame transactions by the node.

post	 A management or data type frame sent by a hub to a node within its body area network (BAN). A post starts a posted allocation.

posted allocation	 A non-reoccurring time interval that a hub grants to itself using posting access for initiating a frame transaction. A posted allocation is a downlink allocation, suitable for “unexpected” or “extra” downlink traffic (for example, due to network management needs, data rate variations, and/or channel impairments).

posting access	 An access method, based on impromptu or scheduled posting by a hub, by which a hub grants to itself a posted allocation, typically outside scheduled uplink allocations, for initiating one or more frame transactions by the hub.

random access	 An access method, based on carrier sense multiple access with collision avoidance (CSMA/CA) or slotted Aloha access but not both, by which a node obtains a time interval in a random access phase (RAP) for initiating one or more frame transactions.

random access phase	 A time span set aside by a hub and announced via a beacon frame for random access to the medium by the nodes in the body area network (BAN) of the hub.

scheduled access	 An access method, based on advance reservation and scheduling, by which a node and a hub obtain one or more scheduled reoccurring time intervals for initiating frame transactions.

scheduled allocation	 One or more scheduled reoccurring time intervals that a node or a hub obtains using scheduled access for initiating frame transactions. A scheduled allocation is an uplink allocation, a downlink allocation, or a bilink allocation, suitable for high or low duty cycle periodic or quasi-periodic traffic.

scheduled-polling access	 A combination of scheduled access and polling access, by which a node and a hub obtain one or more scheduled reoccurring time intervals and impromptu non-reoccurring time intervals within the scheduled time intervals, for initiating frame transactions on uplink and/or downlink.

secure frame	 A term that is interchangeable with secured frame.

secured communication	 Exchange of secured frames.

secured frame	 A frame that is secured with authenticity, integrity, confidentiality if required, and replay protection.

security association	 A procedure used to identify a node and a hub to each other and establish a new master key shared between them or activate an existing master key pre-shared between them.

sleep state	 A term synonymous to inactive state in this standard.

star network	A logical network partition comprising a hub and zero or more nodes whose medium access and power management are coordinated by the hub.

superframe	 A term that is interchangeable with beacon period used especially when no beacons are transmitted.

type-I polled allocation	 A polled allocation the length of which is specified in terms of the duration of time granted for transmission.

type-II polled allocation	 A polled allocation the length of which is specified in terms of the number of frames granted for transmission.

unconnected node	 A node that does not have a connection with a hub in a body area network (BAN).

unsecured communication	 Exchange of unsecured frames.

unsecured frame	 A frame that is not secured with authenticity, integrity, confidentiality, or replay protection.

uplink	 A communications link for transfer of management and data traffic from a node to a hub.

uplink allocation	 An allocation with allocation interval(s) in which a node initiates one or more frame transactions to transmit management and data traffic to a hub and the hub returns acknowledgment if required.

Abbreviations and acronyms

AES	advanced encryption standard

ARQ	automatic repeat request

B-Ack	block acknowledgment

BAN	body area network

BCH Code	Bose, Ray-Chaudhuri, Hocquenghem Code

CAP	contention access phase

CBC	cipher block chaining

CCA	clear channel assessment

CCM	counter mode for message encryption and cipher block chaining (CBC) mode for message authentication

CMAC	(block) cipher-based message authentication code algorithm

CP	contention probability (for Aloha access)

CRC	cyclic redundancy check

CSMA/CA	carrier sense multiple access with collision avoidance

CW	contention window (for carrier sense multiple access with collision avoidance)

D8PSK	differential 8-phase-shift keying

DBPSK	differential binary phase-shift keying

DQPSK	differential qadrature phase-shift keying

EAP	exclusive access phase

EIRP	equivalent isotropically radiated power

EUI	extended unique identifer

EVM	error vector magnitude

FCS	frame check sequence

FM-UWB	frequency modulation ultra-wide band

G-Ack	group acknowledgment

GFSK	gaussian frequency-shift keying

GT	guardtime

GTK	group temporal key

HCS	header check sequence

HID	hub identifier

HME	hub management entity

I-Ack	immediate acknowledgment

IE	information element

IR-UWB	impulse radio ultra-wide band

ISM	industrial scientific medical

KCK	key confirmation key

KMAC	key message authentication code

L-Ack	late acknowledgment (acknowledgment later)

LFSR	linear feedback shift register

MAC	media access control

MIC	message integrity code

MICS	medical implant communications service

MIFS	minimum inter-frame space

MK	master key

MSDU	media access control service data unit

N-Ack	no acknowledgment

NID	node identifier

NME	node management entity

PHY	physical layer

PLCP	physical layer convergence protocol

PN	pseudo-random

PPDU	physical layer protocol data unit

PSDU	physical layer service data unit

PTK	pairwise temporal key

RAP	random access phase

RX	receive or reception

SAP	service access point

SAR	specific absorption rate

SIFS	short inter-frame spacing

SRRC	square-root raised cosine

TK	temporal key

TX	transmit or transmission

UP	user priority

UWB	ultra wide band

General framework elements

General

This clause provides the basic framework of nodes and hubs. The framework serves as a prerequisite to supporting the functions of nodes and hubs and their interactions specified later in detail. It covers the following aspects— the network topology used for medium access, the reference model used for functional partitioning, the time base used for access scheduling, the state diagram used for frame exchange, and the security paradigm used for message protection.

Network topology

All nodes and hubs shall be organized into logical sets, referred to as body area networks (BANs) in this specification, and coordinated by their respective hubs for medium access and power management as illustrated in Figure 1. There shall be one and only one hub in a BAN, whereas the number of nodes in a BAN may range from zero to mMaxBANSize. In a one-hop star BAN, frame exchanges may occur directly only between nodes and the hub of the BAN. In a two-hop extended star BAN, the hub and a node may optionally exchange frames via a relay-capable node.

— Network topology

Access coordination at the MAC sublayer between BANs is not specified in this standard. Optional mechanisms for coexistence and interference mitigating between adjacent or overlapping BANs are provided. Nodes referenced in this standard are in the context of a given BAN, unless noted otherwise.

Reference model

All nodes and hubs shall be internally partitioned into a physical (PHY) layer and a medium access control (MAC) sublayer, in accordance with the ISO/OSI-IEEE 802 reference model, as shown in Figure 2. Direct communications between a node and a hub shall transpire at the PHY layer and MAC sublayer as specified in this standard; the PHY and MAC sublayer of a node or a hub shall use only one operating channel at any given time. Message security service shall occur at the MAC sublayer, and security key generations may take place inside and/or outside the MAC sublayer.

— Reference model

Within a node or a hub, the MAC provides its service to the MAC client through the MAC service access point (SAP) located immediately above the MAC sublayer, while the PHY provides its service to the MAC through the PHY SAP located between them. On transmission, the MAC client passes MAC service data units (MSDUs) to the MAC sublayer via the MAC SAP, and the MAC sublayer passes MAC frames (also known as MAC protocol data units or MPDUs) to the PHY layer via the PHY SAP. On reception, the PHY layer passes MAC frames to the MAC sublayer via the PHY SAP, and the MAC sublayer passes MSDUs to the MAC client via the MAC SAP. Both MAC SAP and PHY SAP are not exposed and their specifications are beyond the scope of this specification.

There may be a logical node management entity (NME) or hub management entity (HME) that exchanges network management information with the PHY and MAC as well as with other layers. The HME is a superset of the NME in terms of the management functionality they each support. However, the presence of the NME or HME and the partitioning between the NME or HME and the MAC or the PHY is not mandated, nor is the behavior of the NME or HME specified, in this standard.

Time base

All nodes and hubs shall establish a time reference base as shown in Figure 3, if their medium access is to be scheduled in time, where the time axis is divided into beacon periods (superframes) of equal length and each beacon period is composed of allocation slots of equal length and numbered from 0, 1, ..., s, where s ≤ 255. An allocation interval may be referenced in terms of the numbered allocation slots comprising it, and a point of time may be referenced in terms of the numbered allocation slot preceding or following it as appropriate.

— Time reference base

If time reference is needed for access scheduling in its BAN, the hub shall choose the boundaries of beacon periods (superframes) and hence of the allocation slots therein. In beacon mode operation for which beacons are transmitted, the hub shall communicate such boundaries by transmitting beacons at the start or other specified locations of beacon periods (superframes), and optionally timed frames (T-Poll frames) containing their transmit time relative to the start time of current beacon period (superframe). In non-beacon mode operation for which beacons are not transmitted but time reference is needed, the hub shall communicate such boundaries by transmitting timed frames (T-Poll frames) also containing their transmit time relative to the start time of current superframe.

A node requiring a time reference in the BAN shall derive and recalibrate the boundaries of beacon periods (superframes) and allocation slots from reception of beacons or/and timed frames (T-Poll frames).

A frame transmission may span more than one allocation slot, starting or ending not necessarily on an allocation slot boundary.

State diagram

All nodes and hubs shall go through certain stages, i.e., states, at the MAC level before they exchange user (MAC client) data, as shown in Figure 4, where frames permitted or required to exchange between a node and a hub at each state are also indicated. State classification and transition are defined with respect to a pair of a node and a hub, but is often referenced in the name of the node only. Broadcast or multicast frames, such as beacons, are frame exchanges between a hub and a group of nodes but not between a hub and a node; their transmissions are not dictated by the pairwise state diagram specified in this subclause.

(a) Secured communication

(b) Unsecured communication

— Access state diagram

Secured communication

A node and a hub shall follow the MAC state diagram Figure 4(a) for secured communication if either of them requires secured frame exchanges with the other.

Orphan state

At this state, the node does not have any relationship with the hub for secured communication. It is the state that the node initially enters in relation with the hub. The node and the hub shall not transmit any frames to each other —other than Security Association and control unsecured frames. The node may exchange Security Association frames with the hub to establish a security association, i.e., to activate a pre-shared master key (MK) or generate a new MK, and to authenticate with each other if so required, thereby transitioning to next state, Associated state. However, if the node and the hub fail to activate or establish a shared MK, they shall not advance to Associated state.

Associated state

At this state, the node is associated, i.e., holds a shared master key, with the hub for Pairwise Temporal Key (PTK) creation. The node and the hub shall not transmit any frames to each other —other than Security Disassociation and PTK unsecured frames, as well as control unsecured frames. The node may exchange PTK frames with the hub to establish a secured relationship, i.e., to confirm possession of a shared MK and to create a PTK, thereby transitioning to next state, Secured state. However, if the node and the hub fail to create a PTK, they shall not advance to Secured state. To repeal a security association and hence the current MK, either the node or the hub may send a Disassociation frame to the other, thus moving back to Orphan state.

Secured state

At this state, the node is secured, i.e., holds a PTK, with the hub for message security, i.e., for secured frame exchanges. The node and the hub shall not transmit any frames to each other—other than Disassociation, Connection Request, and Connection Assignment secured frames, as well as control secured or unsecured frames depending on whether authentication of control type frames was selected during their association. The node may exchange Connection Request and Connection Assignment frames with the hub to establish a connection, thereby transitioning to next and final state, Connected state. However, if the node and the hub fail to establish a connection, they shall not advance to Connected state.

Connected state

At this state, the node is connected, i.e., holds an assigned Connected_NID, a wakeup arrangement, and optionally one or more scheduled allocations with the hub for abbreviated node addressing, desired wakeup, and optionally scheduled access. The node and the hub may transmit any secured frames to each other—other than Security Association secured frames, but shall not transmit any unsecured frames to each other—other than control unsecured frames if authentication of control type frames was not selected during their association. To repeal the Connected_NID, the wakeup arrangement, and the scheduled allocations of the node, either the node or the hub may send a Disconnection frame to the other, thereby moving back to Secured state.

Unsecured communication

A node and a hub follow the MAC state diagram Figure 4 (b) for unsecured communication if neither of them requires secured frame exchanges with the other.

Orphan state

At this state, the node does not have any relationship with the hub for unsecured communication. It is the state that the node initially enters in relation with the hub. The node and the hub shall not transmit any frames to each other—other than Connection Request, Connection Assignment, and control unsecured frames. The node may exchange Connection Request and Connection Assignment frames with the hub to establish a connection, thereby transitioning to next and final state, Connected state. However, if the node and the hub fail to establish a connection, they shall not advance to Connected state.

Connected state

At this state, the node is connected, i.e., holds an assigned Connected_NID, a wakeup arrangement, and optionally one or more scheduled allocations with the hub for abbreviated node addressing, desired wakeup, and optionally scheduled access. The node and the hub may transmit any unsecured frames to each other—other than Security Association, Disassociation, and PTK frames, but shall not transmit secured frames to each other. To repeal the Connected_NID, the wakeup arrangement, and the scheduled allocations of the node, either the node or the hub may send a Disconnection frame to the other, thereby moving back to Orphan state.

To change to secured communications between them, the node and the hub shall disconnect from each other, thus moving back to Orphan state and then following the state diagram Figure 4(a) for secured communication.

Security paradigm

All nodes and hubs shall be offered three security levels in this standard:

Level 0 – unsecured communication. At this level, messages are transmitted in unsecured frames, which provide no measures for message authenticity and integrity validation, confidentiality and privacy protection, and replay defense.

Level 1 – authentication but not encryption. At this level, messages are transmitted in secured authenticated but not encrypted frames, which provide measures for message authenticity and integrity validation and replay defense but not confidentiality and privacy protection.

Level 2 – authentication and encryption. At this level, messages are transmitted in secured authenticated and encrypted frames, which provide measures for message authenticity and integrity validation, confidentiality and privacy protection, and replay defense.

During association, a node and a hub shall jointly select a security level suitable for their subsequent secured frame exchanges, and whether to require authentication of control type frames, based on their respective security requirements and certain information specific to each other.

For unicast secured communication, the node and the hub shall activate a pre-shared master key (MK) or establish a new MK via an unauthenticated or authenticated association, and shall create a pairwise temporal key (PTK) via a PTK creation procedure. For multicast secured communication, the hub shall distribute a group temporal key (GTK) to the corresponding multicast group in a unicast manner.

The node and the hub shall follow the security structures shown in Figure 5 to perform security key generations and provide message security services. A “session” indicated in this figure refers to a time span in which a temporal key remains valid. The length of the “session” is determined by the security policy governing data transfers between the two communicating parties. It is further limited by the technical restrictions on the reuse of the same temporal key over successive messages (i.e., MAC frames in this specification).

— Security hierarchy

MAC frame formats

Conventions

A MAC frame is an ordered sequence of fields delivered to or from the physical layer service access point (PHY SAP). Each figure in Clause 6 depicts the fields contained in a MAC frame, or a part thereof, from left to right in the transmit order, with fields that are optional or selectively absent drawn in dash where possible. The figure also indicates the number of octets contained in each field and the corresponding octets transmit order, on top of the field, as illustrated in Figure 6.

— Example of fields aligned with octet boundaries

Unless otherwise noted, an atomic field, i.e., a field that is not in turn comprised of other fields, denotes a numerical value encoded in unsigned binary. If such a field contains F octets (F > 1), octet 0 is the octet containing the least-significant bits of that field and is the first octet transmitted of the field, whereas octet F-1 is the octet containing the most-significant bits of that field and is the last octet transmitted of the field. The octet order is indicated as “L-R”, i.e., from left to right, above a multi-octet non-atomic field.

In a field containing an EUI-48, the three octets specifying the organizationally unique identifier (OUI) contain the most-significant bits of the field, and the other three octets specifying the organization’s selected extension identifier contain the most-significant bits of the field.

In a figure that depicts certain fields not aligned with octet boundaries, the number of bits and the corresponding bit order of encoding are shown instead for each field in the figure, as illustrated in Figure 7. Bits are ordered continually across the fields that are not aligned with octet boundaries, from left to right, starting from bit 0, i.e., the least-significant bit of the bits comprising these fields. Bit numbering restarts from 0 in fields located on octet boundaries.

— Example of fields not aligned with octet boundaries

Each field is defined, or set, based on the perspective of the node or the hub that is sending the frame containing that field, referred to as the sender. It is parsed based on its definition by the hub or the node intended to receive the frame containing it, referred to as the recipient or the intended recipient.

Reserved fields are set to 0 on transmission and ignored on reception. If some values in a field are reserved, the field is not set to any of those reserved values on transmission. Unless otherwise noted, fields that are set to reserved values or defined based on other fields that are set to reserved values are ignored on reception.

MAC constants are referenced through parameters as listed 7.14.  These parameters are denoted with a preceding “m” if they are PHY independent or with a preceding “p” if they are PHY dependent.

General format

A MAC frame consists of a fixed-length MAC header, a variable-length MAC frame body, and a fixed-length FCS field as shown in Figure 8. The MAC frame body has an octet length L_FB such that 0 ≤ L_FB ≤ pMaxFrameBodyLength, and is present only if it has a nonzero length.

— MAC frame format

MAC header

The MAC header is formatted as shown in Figure 9.

— MAC header format

Frame control

The Frame control is formatted as shown in Figure 10.

— Frame control format

Protocol Version

The Protocol Version field is set to 0 for this revision of the standard. All other values are reserved. This field is invariant in size and place across all revisions of this standard.

Acknowledgment (Ack) Policy

The Ack Policy field is set according to Table 1 to indicate the acknowledgement requirement of the current frame.

— Acknowledgement (ACK) policy field encoding

| Field value b2 b1 | Acknowledgment requirement |
| --- | --- |
| 00 | No acknowledgment (N-Ack) or group acknowledgment (G-Ack) |
| 01 | Immediate acknowledgment (I-Ack) |
| 11 | Block acknowledgment later (L-Ack) |
| 10 | Block acknowledgment (B-Ack) |

The group acknowledgment (G-Ack) value is applicable to frames sent to a hub and of frame type set to data and frame subtype set to mG-AckDataSubtype.

Security Level

The Security Level field is set according to Table 2 such that it indicates the security level of the current frame.

— Security level field encoding

| Field value b4 b3 | Security level of current frame |
| --- | --- |
| 00 | Level 0 – frame not secured |
| 01 | Level 1 – frame authenticated but not encrypted |
| 10 | Level 2 – frame authenticated and encrypted |
| 11 | Reserved |

TK Index

The TK Index field is set as follows to indicate the pairwise temporal key (PTK) or group temporal key (GTK) being used to secure the current frame:

In frames secured by a PTK, it is set to the value of the PTK Index field in the PTK frames that were exchanged in creating the PTK.

In frames secured by a GTK, it is set to the value of the GTK Index field in the GTK frame that was exchanged in distributing the GTK.

The TK Index field is reserved in unsecured frames.

Relay

The Relay field is set to 1 in frames sent to or from a relaying node in a two-hop extended star network. It is reserved in all other frames.

EAP Indicator / First Frame On Time

The EAP Indicator field / First Frame on Time is set as follows:

In beacon frames, it is used as an EAP Indicator field, which is set to 1 if exclusive access phase 1 (EAP 1) in the current (with beacon shifting not enabled) or next (with beacon shifting enabled) beacon period has a nonzero length, or is set to 0 otherwise.

In unicast frames sent by a hub to a node, it is used as a First Frame On Time field, which is set to 1 if this is the first frame sent by the hub to the node at the start of every allocation interval of an allocation assigned to the node, or is set to 0 otherwise.

In all other frames, it is reserved.

Frame Subtype

The Frame Subtype field is set to indicate the subtype of the current frame of a given type according to Table 3.  The name of the frame subtype of a frame is used as the name of the frame throughout clauses 3-8.

Frame Type

The Frame Type field is set to indicate the type of the current frame according to Table 3.

— Frame Type and Frame Subtype field encoding

| Frame Type value b5 b4 | Frame Type name | Frame Subtype value b3 b2 b1 b0 | Frame Subtype name |
| --- | --- | --- | --- |
| 00 | Management | 0000 | Beacon |
| 00 | Management | 0001 | Reserved |
| 00 | Management | 0010 | Security Association |
| 00 | Management | 0011 | Security Disassociation |
| 00 | Management | 0100 | PTK |
| 00 | Management | 0101 | GTK |
| 00 | Management | 0110-0111 | Reserved |
| 00 | Management | 1000 | Connection Request |
| 00 | Management | 1001 | Connection Assignment |
| 00 | Management | 1010 | Multinode Connection Assignment |
| 00 | Management | 1011 | Disconnection |
| 00 | Management | 1100-1110 | Reserved |
| 00 | Management | 1111 | Command |
| 01 | Control | 0000 | I-Ack |
| 01 | Control | 0001 | B-Ack |
| 01 | Control | 0010-0011 | Reserved |
| 01 | Control | 0100 | I-Ack+Poll |
| 01 | Control | 0101 | B-Ack+Poll |
| 01 | Control | 0110 | Poll |
| 01 | Control | 0111 | T-Poll |
| 01 | Control | 1000-1101 | Reserved |
| 01 | Control | 1110 | Reserved |
| 01 | Control | 1111 | B2 |
| 10 | Data | 0111 | Emergency |
| 10 | Data | 0000-0110 1000-1111 | User defined data subtype |
| 11 | Reserved | 0000-1111 | Reserved |

More Data

The More Data field is set as follows:

In frames sent by a node to a hub,

it is set to 0 if the node has no pending frame transactions to initiate with the hub, or

it is set to 1 if the node has one or more pending frame transactions to initiate with the hub.

In unicast management and data type frames sent by a hub to a node,

it is set to 0 if the hub is not to send a post or poll to the node after the current frame transaction, or

it is set to 1 if the hub is to send a post or poll to the node after the end of the current frame transaction.

In I-Ack and B-Ack frames sent by a hub to a node,

  - it is set to 0 if the hub is not announcing a time to send a post or poll to the node through the Sequence Number / Poll-Post Window and Fragment Number / Coexistence / Next fields of the current frame, or

  - it is set to 1 if the hub is announcing a time to send a post or poll to the node thorugh the Sequence Number / Poll-Post Window and Fragment Number / Coexistence / Next fields of the current frame.

In I-Ack+Poll, B-Ack+Poll, Poll, and T-Poll frames sent by a hub to a node,

it is set to 0 if the hub grants to the node through this frame a polled allocation starting pSIFS after the end of the current frame, with the end or size of the polled allocation indicated in the Sequence Number / Poll-Post Window field of the current frame, or

it is set to 1 if the hub grants to the node through this frame no polled allocation but is to send another poll or a post to the node at a future time as indicated in the Sequence Number / Poll-Post Window and Fragment Number / Coexistence / Next fields of the current frame.

In all other frames, it is reserved.

Retry / B2 / Poll Type

The Retry / B2 / Poll Type field is set as follows:

- In beacon frames, it is used as a B2 field, which is set to 1 if a B2 frame is to be transmitted in the current beacon period, or is set to 0 otherwise.

In non-beacon management or data frames that were transmitted previously and are being transmitted again, it is used as a Retry field, which is set to 1.

In I-Ack+Poll, B-Ack+Poll, Poll, and T-Poll frames sent by a hub to a node, if the More Data field is set to 0 indicating a polled allocation, it is used as a Poll Type field, which is set to 0 for a type-I polled allocation or 1 for a type-II polled allocation, in conjunction with the Poll-Post Window field encoding for these frames as defined in next subclause.

In all other frames, it is reserved.

Sequence Number / Poll-Post Window

The Sequence Number / Poll-Post Window field is set as follows:

- In beacon frames, it is used as a Sequence Number field, which is set as follows:

It is incremented by one, modulo 256, from its value applicable to the last beacon period (superframe), active or inactive.

It is also referred to as the sequence number of the current beacon period (superframe).

In non-beacon management type frames, it is used as a Sequence Number field, which is set to the sequence number of the current beacon period (superframe) as follows:

It is set to the sequence number of the beacon that is or was transmitted in the current beacon period.

It is set to the sequence number of the beacon that would otherwise have been or be transmitted in the current superframe if no beacon was or is to be transmitted in this superframe.

In I-Ack and B-Ack frames sent by a hub to a node, it is used as a Poll-Post Window field, which is set as follows:

If the More Data field of the current frame is set to 0, it is reserved.

If the More Data field of the current frame is set to 1, it is set to B such that the hub is to send a poll or post to the node at the start of the allocation slot numbered B, in a beacon period indicated in the Fragment Number / Coexistence / Next field of the current frame.

In I-Ack+Poll, B-Ack+Poll, Poll, and T-Poll frames sent by a hub to a node, it is used as a Poll-Post Window field, which is set as follows:

If the More Data field of the current frame is set to 0, indicating that the node is granted via this frame a polled allocation starting pSIFS after the end of this frame, it is set to A such that the polled allocation ends at the end of the allocation slot numbered A in the current beacon period (superframe) for a Type-I polled allocation, or is set to the maximum number of frames the polled node is granted to transmit in the polled allocation for a Type-II polled allocation. Whether the polled allocation is of type-I or type-II is indicated in the preceding Poll Type field.

If the More Data field of the current frame is set to 1, indicating that the node is granted via this frame no polled allocation but is to be sent another poll or a post, it is set to B such that the hub is to send next poll or post at the start of the allocation slot numbered B, in a beacon period indicated in the Fragment Number / Coexistence / Next field of the current frame.

In Wakeup frames locally broadcast by a hub in its body area network (BAN), it is used as a Poll-Post Window field, which is set as follows:

If the current frame is to keep only one node at active state for a duration of D, it is set to D in units of 20 milliseconds.

If the current frame is to bring multiple nodes to active state at the end of duration of D, it is set to D in units of 20 milliseconds.

In B2 frames, it is used as a Poll-Post Window field, which is set to C such that the current frame starts a contention access phase (CAP) ending at the end of the allocation slot numbered C in the current beacon period (superframe).

In data type frames, it is used as a Sequence Number field, which is set as follows:

It is incremented by one, modulo 256, from its value in the frame that was of the same frame subtype and addressed to the same recipient(s) and that contained the previous MSDU or part thereof.

It has the same value in frames containing fragments of the same MSDU.

In all other frames, it is reserved.

Fragment Control / Coexistence / Next

The Fragment Control / Coexistence / Next field is set as follows:

- In beacon frames, it is used as a Coexistence field, which is formatted as shown in Figure 11.

The Beacon Shifting field is set to 1 if beacon shifting is currently enabled, or is set to 0 otherwise.

The Channel Hopping field is set to 1 if channel hopping is currently enabled, or is set to 0 otherwise.

The Inactive Superframe Starting field is set to 1 if one or more inactive superframes are enabled (starting) at the end of the current beacon period (superframe), or is set to 0 otherwise.

The Active BAN Time Sharing field is set to 1 if active BAN time sharing with one or more body area networks (BANs) is currently enabled, or is set to 0 otherwise.

— Coexistence format for beacon frames

In non-beacon management type frames, it is used as a Fragment Control field, which is formatted as shown in Figure 12.

The Fragment Number field is set to 0 if the frame contains no frame payload, a frame payload not fragmented, or the first first fragment of a fragmented frame payload, and is incremented by one from its value in the frame containing the previous fragment of a frame payload if the frame contains a fragmented frame payload.

The Non-final Fragment field is set to 0 if the frame contains no frame payload, a frame payload not fragmented, or the final fragment of a fragmented frame payload, and is set to 1 if the frame contains a non-final fragment of a fragmented frame payload.

In data type frames, it is used as a Fragment Control field, which is formatted as shown in Figure 12.

The Fragment Number field is set to 0 if the frame contains no frame payload, an MSDU not fragmented, or the first first fragment of a fragmented MSDU, and is incremented by one from its value in the frame containing the previous fragment of an MSDU if the frame contains a fragmented MSDU.

The Non-final Fragment field is set to 0 if the frame contains no frame payload, an MSDU not fragmented, or the final fragment of a fragmented MSDU, and is set to 1 if the frame contains a non-final fragment of a fragmented MSDU.

— Fragment Control format for non-beacon management and data type frames

In I-Ack and B-Ack frames sent by a hub to a node,

if the More Data field of the current frame is set to 0, it is reserved;

if the More Data field of the current frame is set to 1, indicating that the hub is to send a post or poll to the node at the start of the allocation slot indicated in the Poll-Post Window field of the current frame, it is used as a Next field, which is set to N such that the allocation slot is the one located in the current beacon period if N = 0 or in the next Nth beacon period not counting the current beacon period if N > 0.

In I-Ack+Poll, B-Ack+Poll, Poll, and T-Poll frames sent by a hub to a node,

if the More Data field of the current frame is set to 0, indicating that the node is granted via this frame a polled allocation starting pSIFS after the end of this frame and ending at the end of the allocation slot indicated in the Sequence Number field of the current frame, it is reserved;

if the More Data field of the current frame is set to 1, indicating that the node is granted via this frame no polled allocation but is to be sent another poll or post at the start of the allocation slot indicated in the Poll-Post Window field of the current frame, it is used as a Next field, which is set to N such that the allocation slot is the one located in the current beacon period if N = 0 or in the next Nth beacon period not counting the current beacon period if N > 0.

- In B2 frames, it is used as a Coexistence field, which is formatted as shown in Figure 13. The BAN Prority field is set according to Table 4 to indicate the priority of the services provided to the BAN of this hub.  The higher the value of this field, the higher the priority of the BAN services.

— Coexistence format for B2 frames

— BAN Priority field encoding

| Field value in decimal | BAN services |
| --- | --- |
| 0 | Non-medical services |
| 1 | Mixed medical and non-medical services |
| 2 | General health services |
| 3 | Highest priority medical services |

In all other frames, it is reserved.

Recipient ID

The Recipient ID field is set to the abbreviated address (i.e., NID or HID) of the recipient of the current frame.

Sender ID

The Sender ID field is set to the abbreviated address (i.e., NID or HID) of the sender of the current frame.

BAN ID

The BAN ID field is set to the abbreviated address of the body area network (BAN) in which the current frame is transferred.

MAC frame body

The MAC frame body, when it has a nonzero length, is formatted as shown in Figure 14. The length of the MAC frame body L_FB must not exceed pMaxFrameBodyLength.

— MAC frame body format

The Security Sequence Number and Message Integrity Code (MIC) fields are not present in unsecured frames, as indicated by the Security Level field of the MAC header of the current frame.

Security Sequence Number

The Security Sequence Number field is set as follows for nonce construction and replay detection:

In frames secured with a new pairwise temporal key (PTK) or group temporal key (GTK), it is set to 1.

In frames secured with a used PTK, whether they are transmitted for the first time or they are retries, it is incremented by one from its value in the last transmitted frame secured with the same PTK.

In frames secured with a used GTK, whether they are transmitted for the first time or they are retries, it is incremented by one from its value in the last transmitted frame secured with the same GTK.

The value of the Security Sequence Number field increments in frames secured with the same PTK or GTK, rather than in frames of the same frame type or frame subtype. It increments even if the current frame transmission is a retransmission of an earlier transmission.

Frame Payload

The Frame Payload field is set as follows:

In management type frames, prior to encryption (if any) it is set to a sequence of fields to be communicated to the recipient(s), with the fields defined in 6.3.

In control type frames, it is set to a sequence of fields to be communicated to the recipient(s), with the fields defined in 6.4

In data type frames, prior to encryption (if any) it is set to a sequence of octets passed as an MSDU through the MAC SAP to the MAC, without altering the order of the sequence.

In data type frames with the Relay field in their MAC header set to 1, prior to encryption (if any) it is set to the relayed MAC frame that would otherwise be sent directly between a node and a hub without relay.

If a frame payload is fragmented and carried in multiple frames, the Frame Payload field is set to a fragment of the otherwise unfragmented frame payload.

The length of the Frame Payload field, denoted as L_FP in Figure 14, must be such that the length of the MAC frame body does not exceed pMaxFrameBodyLength. If the Frame Payload has a zero length, i.e., if a frame does not have a frame payload, then the frame does not have a MAC frame body if it is not secured, but still has a MAC frame body containing the Security Sequence Number and MIC fields if it is secured.

Message Integrity Code (MIC)

The MIC field is set to a message authentication code for preserving the authenticity and integrity of the MAC header and the MAC frame body of the current secured frame, as further specified in 8.3.1.5.

Frame Check Sequence (FCS)

The FCS field is formatted as shown in Figure 15, where a15 is the least-significant bit of the field, and a0 is the most-significant bit. The bits a15, a14, … , a0 are the binary coefficients of a CRC polynomial of degree 15 denoted as:

R(x) = a15x15 + a14x14 + … + a1x + a0

— FCS format

The CRC polynomial is calculated over a calculation field using the following CRC-16-CCITT standard generator polynomial of degree 16:

G(x) = x16 + x12 + x5 + 1

The calculation field is the transmitted MAC frame except the FCS field for this specification. It is mapped to a message polynomial M(x) of degree k-1, where k is the number of bits in the calculation field. The least-significant bit of the first octet presented to the PHY SAP is the coefficient of the xk-1 term, the next least-significant bit is the coefficient of the xk-2 term, and finally the most-significant bit of the last octet transmitted is the coefficient of the x0 term.

The CRC polynomial is the remainder R(x) resulting from the (modulo 2) division of [x16 × M(x)] by G(x):

R(x) = x16 × M(x) mod G(x)

Management type frames

A management type frame contains certain mandatory fixed-length fields and some optional variable length components referred to as information elements.

Beacon

A beacon frame contains a Frame Payload that is formatted as shown in Figure 16. It is locally broadcast by a hub in every beacon period.

— Frame Payload format for Beacon frames

Sender Address

The Sender Address field is set to the EUI-48 of the hub sending the current beacon.

Beacon Period Length

The Beacon Period Length field is set to the length of the current beacon period (superframe) in units of allocation slots. It is set to 0 to encode a value of 256 allocation slots.

Allocation slot numbering

If beacon shifting is not enabled, the allocation slots in a beacon period (superframe) are numbered 0, 1, …, starting from the allocation slot that starts at the beacon transmission time of the beacon period (superframe) consecutively to the allocation slot that ends at the end of the beacon period (superframe), as shown in Figure 17.

— Allocation slot ordering and numbering in beacon periods

Allocation slot numbering with beacon shifting

If beacon shifting is enabled, a beacon period must have 4N allocation slots in length, where N is an integer. The allocation slots in a beacon period are numbered 0, 1, …, 4N-1, starting from the allocation slot that starts at the beacon transmission time of the beacon period to the allocation slot that ends at the end of the beacon period and, if the beacon transmission time is not at the start of the beacon period, wrapping back to the allocation slot that starts at the start of the beacon period and finally to the allocation slot that ends at the beacon transmission time, as shown in Figure 18. A beacon period has four quarters, which are comprised of allocation slots 0 to N-1, N to 2N-1, 2N to 3N-1, and 3N to 4N-1, respectively. An allocation interval that does not cross a quarter boundary will not be fragmented regardless of which beacon shifting sequence is being used.

— Allocation slot ordering and numbering in beacon periods                                    with exemplary beacon shifting

Allocation Slot Length

The Allocation Slot Length field is set to L such that the length of an allocation slot is equal to pAllocationSlotMin + L × pAllocationSlotResolution.

RAP1 Start

The RAP1 Start field is present only if exclusive access phase 1 (EAP1) has a nonzero length as indicated by the EAP Indicator / First Frame on Time field of the MAC header of the current frame. When present, it is set to the number of the allocation slot that starts random access phase 1 (RAP1).

Both EAP1 (if of nonzero length) and RAP1 (if of nonzero length) occur in the current beacon period if beacon shifting is not enabled or in the next beacon period if beacon shifting is enabled. If EAP1 has a nonzero length, it immediately follows the preceding beacon, and is immediately followed by RAP1. If EAP1 has a zero length, RAP1 immediately follows the preceding beacon.

RAP1 Length

The RAP1 Length field is set to the length of random access phase 1 (RAP1), in units of allocation slots. The value of this field must not be smaller than the value of the Minimum RAP1 Length field in any Connection Assignment frame sent by the hub transmitting this beacon.

RAP2 Start

The RAP2 Start field is set to the number of the allocation slot that starts random access phase 2 (RAP2). If exclusive access phase 2 (EAP2) has a nonzero length, it immediately precedes RAP2. The start time of EAP2 is encoded in Connection Assignment frames defined in 6.3.7

Both EAP2 (if of nonzero length) and RAP2 (if of nonzero length) occur in the current beacon period if beacon shifting is not enabled or in the next beacon period if beacon shifting is enabled.

RAP2 Length

The RAP2 Length field is set to the length of random access phase 2 (RAP2), in units of allocation slots.

MAC Capability

The MAC Capability is as defined in 6.6.1.

PHY Capability

The PHY Capability is as defined in 6.6.2.

Beacon Shifting Sequence

The Beacon Shifting Sequence is present only if beacon shifting is currently enabled as encoded according to Figure 11. When present, it is formatted as shown in Figure 19 to indicate the beacon transmission time in the current beacon period.

— Beacon Shifting Sequence format

Beacon Shifting Sequence Index

The Beacon Shifting Sequence Index field is set according to Table 5 to the index m of the PN sequence PNm(n) governing the beacon transmission time pattern.

— Beacon Shifting Sequence field encoding

| Beacon Shifting Sequence Index m in decimal value | Beacon Shifting Sequence as function of Beacon Shifting Sequence Phase n = 0, 1, 2, …, 15 | Beacon Shifting Sequence pattern (“…” denotes pattern repeat) |
| --- | --- | --- |
| 0 | PN0(n) = n mod 2 | PN0(n) = 0, 1, 0, 1, … |
| 1 | PN1(n) = 2×PN0(n) | PN1(n) = 0, 2, 0, 2, … |
| 2 | PN2(n) = n mod 4 | PN2(n) = 0, 1, 2, 3, … |
| 3 | PN3(n) = [PN0(n) + PN2 (n)]/2 mod 2 + [PN0(n) + PN1(n) + PN2 (n)] mod 4 | PN3(n) = 0, 1, 3, 2, … |
| 4 | PN4(n) = [PN0(n) + PN1(n) + PN2(n)]/2 | PN4(n) = 0, 2, 1, 3, … |
| 5 | PN5(n) = {PN2(n) + [PN0(n) + PN2(n)]/2} mod 4 | PN5(n) = 0, 2, 3, 1, … |
| 6 | PN6(n) = PN1(n)+{[ PN0(n)+ PN2(n)]/2 mod 2} | PN6(n) = 0, 3, 1, 2, … |
| 7 | PN7(n) = [PN1(n) + PN2(n)] mod 4 | PN7(n) = 0, 3, 2, 1, … |
| 8-15 | Reserved | Reserved |

Beacon Shifting Sequence Phase

The Beacon Shifting Sequence Phase field is incremented by one, modulo 16, from its value applicable to the last beacon period (superframe), active or inactive.

Channel Hopping State

The Channel Hopping State field is present only if channel hopping is currently enabled as encoded according to Figure 16. When present, it is set to the current state of a 16-bit maximum-length linear feedback shift register (LFSR) used to generate the channel hopping sequence by the hub sending this beacon, as further specified in Figure 90.

Next Channel Hop

The Next Channel Hop field is present only if channel hopping is currently enabled as encoded according to Figure 16. When present, it is set to the sequence number of the beacon period (superframe) in which the hub sending the current beacon is to hop to another channel according to its channel hopping sequence. Channel hopping is independent of inactive duration as defined in 6.3.1.13.

Inactive Duration

The Inactive Duration field is present only if inactive superframes are enabled (starting) at the end of the current beacon period (superframe). When present, it is set to the number of inactive superframes before the occurrence of next active superframe; it is set to 0 to encode a value of 256 inactive superframes.

Security Association

A Security Association frame contains a Frame Payload that is formatted as shown in Figure 20. It is exchanged between a node and a hub during the execution of a security association protocol to activate a pre-shared MK or generate a new shared MK.

— Frame Payload format for Security Association frames

Recipient Address

The Recipient Address field is set to the EUI-48 of the recipient of the current frame.

Sender Address

The Sending Address field is set to the EUI-48 of the sender of the current frame.

Security Suite Selector

The Security Suite Selector is formatted as shown in Figure 21.

— Security Suite Selector format

Security Association Protocol

The Security Association Protocol field is set according to Table 6 to select a desired security association protocol.

— Security Association Protocol field encoding

| Field value in decimal | Security Association protocol |
| --- | --- |
| 0 | Master key pre-shared association |
| 1 | Unauthenticated association |
| 2 | Public key hidden association |
| 3 | Password authenticated association |
| 4 | Display authenticated association |
| 5-7 | Reserved |

Security Level

The Security Level field is set to the security level required by this sender according to Table 7.

— Security Level field encoding

| Field value in decimal | Security level required |
| --- | --- |
| 0 | Level 0 – unsecured communication |
| 1 | Level 1 – authentication but not encryption |
| 2 | Level 2 – authentication and encryption |
| 3 | Reserved |

Control Frame Authentication

The Control Frame Authentication field is set to 1 if control type frames sent from or to this sender must be authenticated but not encrypted when they are required to have security level 1 or 2. It is set to 0 if control type frames sent from or to this sender must be neither authenticated nor encrypted even when they are otherwise required to have security level 1 or 2.

Cipher Function

The Cipher Function field is set according to Table 8 to indicate the underlying cipher function selected by this sender for performing security services as specified in Clause 8.

— Cipher Function field encoding

| Field value in decimal | Cipher function |
| --- | --- |
| 0 | AES-128 forward cipher function |
| 1 | Camellia-128 forward cipher function |
| 2-15 | Reserved |

Association Control

The Association Control is formatted as shown in Figure 22.

— Association Control format

Association Sequence Number

The Association Sequence Number field is set to the number (i.e., position) of the current Security Association frame in the execution of the selected security association protocol. In particular, it is set to 1 in the first Security Association frame of the protocol, 2 in the second Security Association frame, etc. The first Security Association frame is the Security Association frame transmitted or retransmitted by the node initializing the security association, the second Security Association frame is the next Security Association frame transmitted or retransmitted by the responding hub, and the like.

Association Status

The Association Status field in the second Security Association frame of a security association protocol (procedure) is set according to Table 9 to indicate the status of the current security association procedure.  It is reserved in other Security Association frames.

— Association Status field encoding

| Field value in decimal | Association status |
| --- | --- |
| 0 | Joining the security association procedure |
| 1 | Aborting the security association procedure with a different security suite selector |
| 2 | Aborting the security association procedure due to lack of needed security credential (no master key pre-shared with the initiator of the security association procedure for master key preshared association; no public key of the initiator of the security association procedure for public key hidden association; no password shared with the initiator of the security association procedure for password authenticated association) |
| 3 | Aborting the security association procedure due to temporary lack of resources |
| 4 | Aborting the security association procedure due to policy restrictions |
| 5-15 | Reserved |

Security Association Data

The Security Association Data field is specific to the selected security association protocol.

For master key pre-shared association, the Security Association Data field is not present.

For unauthenticated association, public key hidden association, password authenticated association, and display authenticated association, the Security Association Data field is formatted as shown in Figure 23.

— Security Association Data format for security association protocols 1-4

Sender Nonce

The Sender Nonce field is set to a statistically unique number per sender and per security association procedure, except otherwise indicated:

- For unauthenticated association, public key hidden association, and password authenticated association,

in the first Security Association frame of the security association procedure, the field is set afresh to an integer randomly drawn with a uniform distribution over the interval (0, 2^128);

in the second Security Association frame of the procedure, the field is set afresh to an integer randomly drawn with a uniform distributio over the interval (0, 2^128) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise.

in the third Security Association frame, the field is set to its value contained in the second Security Association frame of the procedure;

in the fourth Security Association frame, the field is set to its value contained in the first Security Association frame of the procedure.

For display authenticated association,

in the first Security Association frame of the current security association procedure, the field is set to 0;

in the second Security Association frame of the procedure, the field is set afresh to an integer randomly drawn with a uniform distributio over the interval (0, 2^128) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise.

in the third Security Association frame, the field is set afresh to an integer randomly drawn with a uniform distribution over the interval (0, 2^128).

Sender PKx

The Sender PKx field is set to the X-coordinate of the sender’s elliptic curve public key, except otherwise indicated:

- For unauthenticated association,

in the first Security Association frame of the current security association procedure, the field is set to the X-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY);

in the second Security Association frame of the procedure, the field is set to the X-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise;

in the third Security Association frame, the field is set to its value contained in the second Security Association frame of the procedure;

in the fourth Security Association frame, the field is set to its value contained in the first Security Association frame of the procedure.

For public key hidden association,

in the first and fourth Security Association frames of the current security association procedure, the field is set to 0;

in the second Security Association frame, the field is set to the X-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise;

in the third Security Association frame, the field is set to its value contained in the second Security Association frame of the procedure.

For password authenticated association,

in the first and fourth Security Association frames of the current security association procedure, the field is set to the X-coordinate of the sender’s password-scrambled elliptic curve public key PK' = (PK'x, PK'Y);

in the second Security Association frame, the field is set to the X-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise;

in the third Security Association frame, the field is set to its value contained in the second Security Association frame of the procedure.

For display authenticated association,

in the first Security Association frame of the current security association procedure, the field is set to 0;

in the second Security Association frame, the field is set to the X-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise;

in the third Security Association frame, the field is set to the X-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY).

Sender PKY

The Sender PKY field is set to the Y-coordinate of the sender’s elliptic curve public key, except otherwise indicated:

- For unauthenticated association,

in the first Security Association frame of the current security association procedure, the field is set to the Y-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY);

in the second Security Association frame of the procedure, the field is set to the Y-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise;

in the third Security Association frame, the field is set to its value contained in the second Security Association frame of the procedure;

in the fourth Security Association frame, the field is set to its value contained in the first Security Association frame of the procedure.

For public key hidden association,

in the first and fourth Security Association frames of the current security association procedure, the field is set to 0;

in the second Security Association frame, the field is set to the Y-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise;

in the third Security Association frame, the field is set to its value contained in the second Security Association frame of the procedure.

For password authenticated association,

in the first and fourth Security Association frames of the current security association procedure, the field is set to the Y-coordinate of the sender’s password-scrambled elliptic curve public key PK' = (PK'x, PK'Y);

in the second Security Association frame, the field is set to the Y-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise;

in the third Security Association frame, the field is set to its value contained in the second Security Association frame of the procedure.

For display authenticated association,

in the first Security Association frame of the current security association procedure, the field is set to 0;

in the second Security Association frame, the field is set to the Y-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY) if the sender of the frame is to join the security association procedure, or is set to 0 otherwise;

in the third Security Association frame, the field is set to the Y-coordinate of the sender’s elliptic curve public key PK = (PKx, PKY).

MK_KMAC

The MK_KMAC field is set to a key message authentication code (KMAC) for certain fields of the frame payloads of the Security Association frames of the current security association procedure, except otherwise indicated:

- For unauthenticated association,

in the first and second Security Association frames of the current security association procedure, the field is set to 0;

in the third Security Association frame, the field is set to a KMAC for certain fields of the frame payloads of the first and second Security Association frames of the procedure if the sender of the frame is to join the security association procedure, or is set to 0 otherwise;

in the fourth Security Association frame, the field is set to a KMAC for certain fields of the frame payloads of the second and fourth Security Association frames.

For public key hidden association,

in the first and second Security Association frames of the current security association procedure, the field is set to 0;

in the third Security Association frame, the field is set to a KMAC for certain fields of the frame payloads of the first and second Security Association frames of the procedure if the sender of the frame is to join the security association procedure, or it is set to 0 otherwise;

in the fourth Security Association frame, the field is set to a KMAC for certain fields of the frame payloads of the second and fourth Security Association frames.

For password authenticated association,

in the first and Security Association frames of the current security association procedure, the field is set to 0;

in the third Security Association frame, the field is set to a KMAC for certain fields of the frame payloads of the first and second Security Association frames of the procedure if the sender of the frame is to join the security association procedure, or it is set to 0 otherwise;

in the fourth Security Association frame, the field is set to a KMAC for certain fields of the frame payloads of the second and fourth Security Association frames.

For display authenticated association,

in the first Security Association frame of the current security association procedure, the field is set to an initial witness equal to a KMAC for certain fields of the frame payload of the third Security Association frame of the procedure;

in the second and third Security Association frames, the field is set to 0.

Security Disassociation

A Security Disassociation frame contains a Frame Payload that is formatted as shown in Figure 24. It is transmitted by either an associated node or a hub to repeal an existing security association, i.e., the shared master key (MK).

— Frame Payload format for Security Disassociation frames

Recipient Address

The Recipient Address field is set to the EUI-48 of the recipient of the current frame.

Sender Address

The Sending Address field is set to the EUI-48 of the sender of the current frame.

DA_KMAC

The DA_KMAC field is set to a key message authentication code (KMAC) for the fields of the frame payload of this Security Disassociation frame.

Pairwise temporal key (PTK)

A PTK frame contains a Frame Payload that is formatted as shown in Figure 25. It is exchanged between a node and the hub with which the node is associated to create a PTK based on a shared master key (MK).

— Frame Payload format for PTK frames

Recipient Address

The Recipient Address field is set to the EUI-48 of the recipient of the current frame.

Sender Address

The Sending Address field is set to the EUI-48 of the sender of the current frame.

PTK Control

The PTK Control is formatted as shown in Figure 26.

— PTK Control format

Message Number

The Message Number field is set to the number (i.e., position) of the current PTK frame in the current PTK creation procedure. In particular, it is set to 1 in the first PTK frame of the procedure, 2 in the second PTK frame, and 3 in the third. The first PTK frame is the PTK frame transmitted or retransmitted by the node or hub initializing the procedure, the second PTK frame is the PTK frame transmitted or retransmitted by the responding hub or node, and the third PTK frame is the PTK frame transmitted or retransmitted by the initiating node or hub again. The other values of the field are reserved.

PTK Index

The PTK Index field in the first PTK frame transmitted or retransmitted by the node or hub initiating the PTK creation procedure is set as follows to identify the PTK being created:

If no PTK was previously created with the responding node, it is set to 0.

Otherwise, it is set to the modulo-2 sum of 1 and its value used in successfully creating the last PTK between the sender and the recipient.

The PTK Index field in the second and third PTK frames of the PTK creation procedure is set to its value contained in the first PTK frame of the procedure.

PTK Creation Status

The PTK Creation Status field in the second PTK frame of a security association protocol is set according to Table 9 to indicate the status of the current PTK creation procedure.  It is reserved in other PTK frames.

— PTK Creation Status field encoding

| Field value in decimal | PTK creation status |
| --- | --- |
| 0 | Joining the PTK creation procedure |
| 1 | Reserved |
| 2 | Aborting the PTK creation procedure due to lack of shared master key |
| 3 | Aborting the PTK creation procedure due to temporary lack of resources |
| 4 | Aborting the PTK creation procedure due to policy restrictions |
| 5-15 | Reserved |

Sender Nonce

The Sender Nonce field is set to a statistically unique number per sender and per PTK creation procedure:

In the first PTK frame of the current PTK creation procedure, it is set afresh to an integer randomly drawn with a uniform distribution over the interval (0, 2^128).

In the second PTK frame of the procedure, it is set afresh to an integer randomly drawn with a uniform distribution over the interval (0, 2^128) if the sender of the frame is to join the PTK creation procedure, or is set to 0 otherwise.

In the third PTK frame of the procedure, it is set to its value contained in the first PTK frame.

PTK_KMAC

The PTK_KMAC field is set to a key message authentication code (KMAC) for certain fields of the frame payloads of the PTK frames of the current PTK creation procedure, except otherwise indicated:

In the first PTK frame of the current PTK creation procedure, it is set to 0.

In the second PTK frame, it is set to a KMAC for certain fields of the frame payloads of the first and second PTK frames of the procedure if the sender of this frame is to join the PTK creation procedure, or it is set to 0 otherwise.

In the third PTK frame, it is set to a KMAC for certain fields of the frame payloads of the second and third PTK frames.

The PTK Index field takes on a value of either 0 or 1.

Group Temporal Key (GTK)

A GTK frame contains a Frame Payload that is formatted as shown in Figure 27. It is transmitted by a hub to distribute a GTK to a secured node for securing multicast traffic.

— Frame Payload format for GTK frames

Recipient Address

The Recipient Address field is set to the EUI-48 of the recipient of the current frame.

Sender Address

The Sending Address field is set to the EUI-48 of the sender of the current frame.

GTK NID

The GTK NID field is set according to Table 16 to the broadcast or multicast NID that is to appear in the NID field of the MAC header of the frames secured by the GTK distributed in the current frame.

GTK Control

The GTK Control is formatted as shown in Figure 28.

— GTK Control format

The GTK Index field is set as follows to identify the GTK being distributed:

If no GTK was previously distributed by this hub for the GTK NID indicated in the current frame, it is set to 0.

Otherwise, it is set to the modulo-2 sum of 1 and its value used in successfully distributing the last GTK by this hub for the indicated GTK NID.

The GTK Index field takes on a value of either 0 or 1.

GTK SSN

The GTK SSN field is set to the security sequence number of the last frame secured with the GTK distributed in the current frame and addressed to the GTK NID indicated in the current frame.

GTK

The GTK field is set to the bit string representing the GTK being distributed in the current frame.

Connection Request

A Connection Request frame contains a Frame Payload that is formatted as shown in Figure 29. It is transmitted by a node to request creation or modification of a connection with a hub, in particular, a Connected_NID, a wakeup arrangement, and optionally a scheduled allocation.

— Frame Payload format for Connection Request frames

Recipient Address

The Recipient Address field is set to the EUI-48 of the recipient of the current frame.

Sender Address

The Sending Address field is set to the EUI-48 of the sender of the current frame.

MAC Capability

The MAC Capability is as defined in 6.6.1.

PHY Capability

The PHY Capability is as defined in 6.6.2.

Connection Change Indicator

The Connection Change Indicator is formatted as shown in Figure 30. It indicates certain fields that follow in the current frame have been changed in value since their last exchange between the sender and the recipient.

— Connection Change Indicator format

Wakeup Phase Change

The Wakeup Phase Change field is set to 1 if the value of the Wakeup Phase field has been changed, or is set to 0 otherwise.

Wakeup Period Change

The Wakeup Period Change field is set to 1 if the value of the Wakeup Period field has been changed, or is set to 0 otherwise.

Uplink Request/Assignment IE Change

The Uplink Request/Assignment IE Change field is set to 1 if the value of the Uplink Request IE or Uplink Assignment IE has been changed, or is set to 0 otherwise.

Downlink Request/Assignment IE Change

The Downlink Request/Assignment IE Change field is set to 1 if the value of the Downlink Request IE or Downlink Assignment IE has been changed, or is set to 0 otherwise.

Bilink Request/Assignment IE Change

The Bilink Request/Assignment IE Change field is set to 1 if the value of the Bilink Request IE or Bilink Assignment IE has been changed, or is set to 0 otherwise.

Delayed Bilink Request/Assignment IE Change

The Delayed Bilink Request/Assignment IE Change field is set to 1 if the value of the Delayed Bilink Request IE or Delayed Bilink Assignment IE has been changed, or is set to 0 otherwise.

Channel Order IE Change

The Channel Order IE Change field in Connection Request frames is reserved.

The Channel Order IE Change field in Connection Assignment frames is set to 1 if the value of the Nibble Encoded Channel Order IE or Octet Encoded Channel Order IE has been changed, or is set to 0 otherwise.

Wakeup Phase

The Wakeup Phase field is set to the sequence number of the next beacon period (superframe) in which the node is willing to wake up for frame reception and transmission, with the sequence number of a beacon period (superframe) treated as incremented by one modulo 216, instead of modulo 28, from that of the previous beacon period (superframe).  With a length of two octets, this field allows a node’s next wakeup to be scheduled up to 65536 beacon periods (superframes) away from the current one.

Wakeup Period

The Wakeup Period field is set to the length, in units of beacon periods (superframes), between the start of successive wakeups of this node, and is effective from the next wakeup indicated in the preceding Wakeup Phase field. It is set to 0 to encode a value of 65536 beacon periods. The beacon periods (superframes) in which the node will wakeup for frame reception and transmission as defined by this field and the preceding one are referred to as the node’s wakeup beacon periods (superframes).  With a length of two octets, this field allows a node’s wakeup period to be up to 65536 beacon periods (superframes).

The value of this field determines whether the IEs in this frame and the responding Connection Assignment frame denote 1-periodic or m-periodic allocations:

If Wakeup Period = 1, these IEs denote 1-periodic allocations.

If Wakeup Period ≠ 1, these IEs denote m-periodic allocations.

Uplink request IE

The Uplink Request IE is as defined in 6.7.1.3

Downlink Request IE

The Downlink Request IE is as defined in 6.7.3.

Bilink Request IE

The Bilink Request IE is as defined in 6.7.4.

Delayed Bilink Request IE

The Delayed Bilink Request IE is as defined in 6.7.5.

Group Connection IE

The Group Connection IE is as defined in 6.7.6

Connection Assignment

A Connection Assignment frame contains a Frame Payload that is formatted as shown in Figure 31. It is transmitted by a hub to respond to a connection request or to initiate or change a connection assignment.

— Frame Payload format for Connection Assignment frames

Recipient Address

The Recipient Address field is set to the EUI-48 of the recipient of the current frame.

Sender Address

The Sending Address field is set to the EUI-48 of the sender of the current frame.

Status Code

The Status Code field is set to the status of the connection assignment encoded according to Table 11.

— Status Code field encoding

| Field value in decimal | Status |
| --- | --- |
| 0 | Connection request accepted |
| 1 | Connection request rejected – invalid or unsupported frame format |
| 2 | Connection request rejected – no reason |
| 3 | Connection request rejected – no more channel bandwidth for a new connection |
| 4 | Connection request rejected – no more Connected_NID for a new connection |
| 5 | Connection request rejected – no more internal resources for a new connection |
| 6-10 | Reserved |
| 11 | Connection assignment modified |
| 12-255 | Reserved |

Minimum RAP1 Length

The Minimum RAP1 Length field is set to the least length guaranteed for random access phase 1 (RAP1), in units of allocation slots, with RAP1 starting immediately after EAP1.

EAP2 Start

The EAP2 Start field is set to the number of the allocation slot that starts exclusive access phase 2 (EAP2). EAP 2 ends at the start time of random access phase 2 (RAP2) defined in the beacon.

MAC Capability

The MAC Capability is as defined in 6.6.1.

PHY Capability

The PHY Capability is as defined in 6.6.2.

NID

The NID field is set to an NID that is uniquely assigned or reassigned to the addressed node within the body area network (BAN) according to Table 16.

Connection Change Indicator

The Connection Change Indicator is as defined in 6.3.6.6

Wakeup Phase

The Wakeup Phase field is as defined in 6.3.6.7 . The field in this frame supersedes the field previously exchanged between the sender and the recipient.

Wakeup Period

The Wakeup Period field is as defined in 6.3.6.8. The field in this frame supersedes the field previously exchanged between the sender and the recipient.

Slotted Superframe IE

The Slotted Superframe IE is as defined in 6.7.1.

Uplink Assignment IE

The Uplink Assignment IE is as defined in 6.7.7.

Downlink Assignment IE

The Downlink Assignment IE is as defined in 6.7.8.

Bilink Assignment IE

The Bilink Assignment IE is as defined in 6.7.9.

Delayed Bilink Assignment IE

The Delayed Bilink Assignment IE is as defined in 6.7.10.

Group Connection IE

The Group Connection IE is as defined in 6.7.6

Channel Order IE

The Channel Order IE is either a Nibble Encoded Channel Order IE or an Octet Encoded Channel Order IE as defined in 6.7.12 and 6.7.13, respectively.

Channel Hopping IE

The Channel Hopping IE is as defined in 6.7.14.

Multinode Connection Assignment

A Multinode Connection Assignment frame contains a Frame Payload that is formatted as shown in Figure 32. It is optionally locally broadcast by a hub to respond to connection requests from multiple nodes or to change earlier connection assignments to multiple nodes.

— Frame Payload format for Multinode Connection Assignment frames

All the fields are as defined in 6.3.7 for Connection Assignment frames, except the Node Connection Assignment IE which is defined as in 6.7.11.

Disconnection

A Disconnection frame contains a Frame Payload that is formatted as shown in Figure 33. It is transmitted by a hub to repeal the connection with a node or by a node to repeal the connection with a hub.

(a) Sent by a node

(b) Sent by a hub

— Frame Payload format for Disconnection frames

Recipient Address

The Recipient Address field is set to the EUI-48 of the recipient of the current frame.

Sender Address

The Sending Address field is set to the EUI-48 of the sender of the current frame.

New Hub Address

The New Hub Address field in Disconnection frames sent by a node is set as follows:

If the node is not newly connected with another hub, it is null, i.e., not present.

Otherwise, it is set to the EUI-48 of the hub with which the node is newly connected.

The ith New hub Address field in Disconnection frames sent by a hub is set as follows:

If the hub does not have a suggested ith preferred new hub for the addressed node, it is null, i.e., not present.

Otherwise, it is set to the EUI-48 of the suggested ith preferred new hub for the addressed node.

Command

A Command frame contains a Frame Payload that is formatted as shown in Figure 34. It is optionally transmitted by a hub or node.

— Frame Payload format for Command frames

Recipient Address

The Recipient Address field is set to the EUI-48 of the recipient of the current frame.

Sender Address

The Sending Address field is set to the EUI-48 of the sender of the current frame.

Command ID

The Command ID field is set according to Table 12 such that it identifies the specific command of the current frame.

— Command ID field encoding

| Field value in decimal | Command name |
| --- | --- |
| 0 | Command – Active Temporal Coexistence Request |
| 1 | Command – Active Temporal Coexistence Response |
| 2 | Command – Battery Level Indication |
| 3 | Command – Battery Level Inquiry |
| 4-255 | Reserved |

Command Data

The Command Data field is specific to the command conveyed in the current frame.

Command – Active Temporal Coexistence Request

The Command Data field is formatted as shown in Figure 35 for a Command – Active Temporal Coexistence Request frame, which is optionally transmitted by a hub to another hub to convey certain active temporal coexistence information.

— Command Data format for Command – Active Temporal Coexistence Request frames

BAN Priority

The BAN Priority field is as defined in 6.2.1.1.12 f) and Table 4.

Active Temporal Coexistence Mode

The Active Temporal Coexistence Mode field is set according to Table 13 such that it indicates an active coexistence mode.

— Active Temporal Coexistence mode field encoding

| Field value in decimal | Active Temporal coexistence mode |
| --- | --- |
| 0 | Active BAN time sharing |
| 1 | Offset BAN synchronization |
| 2 | BAN inquiry |
| 3 | Reserved |

Allocation Percentage

The Allocation Percentage field is set to P such that this hub is to use an aggregate allocation of up to 1/2×P% of the total time on its operating channel for its body area network (BAN).

Command – Active Temporal Coexistence Response

The Command Data field is formatted as shown in Figure 36 for a Command – Active Temporal Coexistence Response frame, which is optionally transmitted by a hub in response to another hub to provide certain active temporal coexistence information.

— Command Data format for Command – Active Temporal Coexistence Response frames

Active Temporal Coexistence Status

The Active Temporal Coexistence Status field is set to 1 if the last active coexistence request from the recipient of this frame is accepted, or is set to 0 otherwise.

Active Temporal Coexistence Mode

The Active Temporal Coexistence Mode field is set to its value in the last Command – Active Temporal Coexistence Request frame received from the recipient of this frame.

Allocation Percentage

The Allocation Percentage field is as defined in 6.3.11.5.3.

Command – Battery Level Indication

The Command Data field is formatted as shown in Figure 37 for a Command – Battery Level Indication frame, which is optionally transmitted by a node unsolicited or in response to a command – battery level inquiry.

—Command Data format for Command – Battery Level indication frames

Battery Power Remaining

The Battery Power Remaining field is set to p, 0 ≤ p ≤ 100, if the battery power remaining at this sender is p%. It is set to 255 if the battery power remaining is unknown.

Battery Time Remaining

The Battery Time Remaining field is set to t, 0 ≤ t ≤ 253, if the battery time remaining at this sender assuming current medium access and data processing activities is t minutes. It is set to 254 if the battery time remaining is equal to or more than 254 minutes. It is set to 255 if the battery time remaining is unknown.

Command – Battery Level Inquiry

The Command Data field is not present in a Command – Battery Level Inquiry frame, which is optionally transmitted by a hub to make an inquiry about the battery level of the addressed node.

Control type frames

A control type frame contains no frame payload or a frame payload of variable length.

Immediate Acknowledgement (I-Ack)

An I-Ack frame contains no Frame Payload. It is transmitted by a node or a hub to acknowledge receipt of the preceding frame.

Block Acknowledgement (B-ACK)

A B-Ack frame selectively contains a Frame Payload that is formatted as shown in Figure 38. It is transmitted by a node or a hub to acknowledge the reception status of certain preceding data type frames each containing a whole MSDU.

— Frame Payload format for B-ACK frames

Oldest Frame Expected

The Oldest Frame Expected field is set to the sequence number of the oldest frame that is of the same frame subtype as the frame preceding the current B-Ack frame and that is still expected to be, but not yet, received.

Next Block Size

The Next Block Size field is set to the maximum number of data type frames permitted in the next block transmission from the acknowledged node or hub to the acknowledging hub or node, where the next block transmission is a transmission of data type frames whose reception status will be provided in next B-Ack frame and whose frame subtype is the same as that of the data type frame preceding the current B-Ack frame. The length of the frame preceding the current B-Ack frame was used to estimate the value of this field.

Frame Status Bitmap

The Frame Status Bitmap field is set as follows to indicate the reception status of the frames that are of the same frame subtype as the frame preceding the current B-Ack frame and that are subsequent in sequence to the frame indicated in the Oldest Frame Expected field:

The field comprises (N/8( octets, where N is the number of these frames and (f( is the least integer that is not smaller than f.

The least-significant bit of these octets denotes the oldest of these frames, i.e., the frame that is immediately subsequent in sequence to the frame indicated in the Oldest Frame Expected field.

Each successive bit denotes a successive frame, i.e., a frame with a successive sequence number, of the same frame subtype.

A bit is set to 1 if the corresponding frame is received, or is set to 0 otherwise.

Immediate Acknowledgement + Poll (I-Ack+Poll)

An I-Ack+Poll frame contains no Frame Payload. It is transmitted by a hub to acknowledge receipt of the preceding frame and to send a poll to the addressed node. The I-Ack+Poll frame is equivalent in function to an I-Ack frame followed by a Poll frame.

Block Acknowledgement +Poll (B-ACK+Poll)

A B-Ack+Poll frame selectively contains a Frame Payload that is formatted as defined in 6.4.2. It is transmitted by a hub to acknowledge the reception status of certain preceding data type frames and to send a poll to the addressed node. The B-Ack+Poll frame is equivalent in function to a B-Ack frame followed by a Poll frame.

Poll

A Poll frame contains no Frame Payload. It is transmitted by a hub to grant to the addressed node an immediate polled allocation that starts pSIFS after the end of the frame or to inform the node of a future poll or post.

Timed-Poll (T-Poll)

A T-Poll frame contains a Frame Payload that is formatted as shown in Figure 39. Except stated otherwise, it is transmitted by a hub to grant to the addressed node an immediate polled allocation that starts pSIFS after the end of the frame or to inform the node of a future poll or post, while providing the hub’s current time for the node’s clock synchronization. The T-Poll frame is equivalent in function to a Poll frame expanded by a frame payload containing a transmit timestamp for superframe boundary synchronization and optionally a relay link quality for relay selection.

— Frame Payload format for T-Poll frames

Current Superframe Number

The Current Superframe Number field is set to the sequence number of the current superframe (beacon period) as follows:

It is set to the sequence number of the beacon that is or was transmitted in the current beacon period.

It is set to the sequence number of the beacon that would otherwise have been or be transmitted in the current superframe if no beacon was or is to be transmitted in this superframe.

Current Allocation Slot Number

The Current Allocation Slot Number field is set to S such that the hub starts sending this frame during the allocation slot numbered S.

Current Slot Offset

The Current Slot Offset field is set to O in units of four microseconds such that the hub starts sending this frame at O after the start of the allocation slot indicated in the preceding field.

B2 Frame

A B2 frame contains a Frame Payload that is formatted as shown in Figure 40. It is broadcast by a hub to announce a contention access phase (CAP) and provide group acknowledgment and coexistence information.

— Frame Payload format for B2 frames

Earliest Next B2

The Earliest Next B2 field is set to E such that the earliest next B2 time occurs not earlier than the end of the allocation slot numbered E in the next beacon period (superframe).

NID

One or more NID fields are optionally present.  When present, each NID field is set to the NID of a node from which this hub received a frame requiring group acknowledgment since the last transmitted B2 frame.

Data type frames

A data type frame contains a full, a fragmented, or no MSDU.

A data type frame of Emergency subtype, i.e., an Emergency frame, is transmitted to indicate an emergency or medical event report.

A data type frame of a user-defined data subtype is transmitted such that all data type frames of the same data subtype contain MSDUs of the same application, or a group of MSDUs of the same attributes.

MAC / PHY Capability fields

A MAC Capability field and a PHY Capability field are included in beacons and some other management type frames. A hub and a node typically have different functional requirements for the capability of supporting a given function as listed in these fields, especially in the MAC Capability field. Indication of being capable of supporting a function implies being willing to enable and perform the function as well.

MAC Capability

The MAC Capability is formatted as shown in Figure 41.

— MAC Capability format

CSMA/CA

The CSMA/CA field is set to 1 if the sender supports CSMA/CA in random access phase 1 (RAP1), random access phase 2 (RAP2), and contention access phase (CAP), or is set to 0 otherwise.

Slotted Aloha Access

The Slotted Aloha Access field is set to 1 if the sender supports slotted Aloha access in exclusive access phase 1 (EAP1), random access phase 1 (RAP1), exclusive access phase 2 (EAP2), random access phase 2 (RAP2), and contention access phase (CAP), or is set to 0 otherwise.

Type-I Polling Access

The Type-I Polling Access field is set to 1 if the sender supports Type-I polled allocations, or is set to 0 otherwise.

Type-II Polling Access

The Type-II Polling Access field is set to 1 if the sender supports Type-II polled allocations, or is set to 0 otherwise.

Scheduled Access

The Scheduled Access field is set to 1 if the sender supports scheduled allocations, or is set to 0 otherwise. The sender supports scheduled-polling access if and only if it supports both scheduled allocations and Type-I or Type-II polled allocations.

Delayed-Polling Access

The Delayed-Polling Access field is set to 1 if the sender supports scheduled allocations that are subject to delay and Type-I or Type-II polled allocations, or is set to 0 otherwise.

G-Ack

The G-Ack field is set to 1 if the sender supports group acknowledgment, or is set to 0 otherwise.

L-Ack / B-Ack

The L-Ack / B-Ack field is set to 1 if the sender supports both L-Ack and B-Ack acknowledgment, or is set to 0 otherwise.

Group Connection

The Group Connection field is set to 1 if the sender supports group connection, or is set to 0 otherwise.

Multinode Connection Assignment

The Multinode Connection Assignment field is set to 1 if the sender supports multimode connection assignment, or is set to 0 otherwise.

Relaying Node

The Relaying Node field is set to 1 if the sender supports the functionality required of a relaying node in a two-hop extended star body area network (BAN), or is set to 0 otherwise.

Relayed Hub/Node

The Relayed Hub/Node field is set to 1 if the sender supports the functionality required of a relayed hub or node in a two-hop extended star body area network (BAN), or is set to 0 otherwise.

Always Active

The Always Active field is set to 1 if the sender will be always in active state (abbreviated as always active) ready to receive and transmit frames, or is set to 0 otherwise.

Command Frames

The Command Frames field is set to 1 if the sender supports the processing and functionality of Command frames, or is set to 0 otherwise.

PHY Capability

The PHY Capability is formatted as shown in Figure 42.

— PHY Capability format

Low Power Wakeup Radio

The Low Power Wakeup Radio field is set to 1 if the sender supports a low power wakeup radio, or is set to 0 otherwise.

Hybrid ARQ

The Hybrid ARQ field is set to 1 if the sender supports hybrid ARQ, or is set to 0 otherwise. Hybrid ARQ affects both MAC and PHY.

Data Rate

One or more Data Rate fields are defined. A Data Rate field is set to 1 if the sender supports the corresponding optional information data rate for both transmission and reception in the operating frequency band according to Table 14, or is set to 0 otherwise. Table 14 is specified based on 9.1.

— Data rate field representation

| Frequency band (MHz) | Data Rate 1 (kb/s) | Data Rate 2 (kb/s) | Data Rate 3 (kb/s) | Data Rate 4 (kb/s) | Data Rate 5 (kb/s) |
| --- | --- | --- | --- | --- | --- |
| 402-405 | 455.4 | Reserved | Reserved | Reserved | Reserved |
| 420-450 | 187.5 | Reserved | Reserved | Reserved | Reserved |
| 863-870 | 607.1 | Reserved | Reserved | Reserved | Reserved |
| 902-928 | 728.6 | Reserved | Reserved | Reserved | Reserved |
| 950-956 | 607.1 | Reserved | Reserved | Reserved | Reserved |
| 2360-2400 | Reserved | Reserved | Reserved | Reserved | Reserved |
| 2400-2483.5 | Reserved | Reserved | Reserved | Reserved | Reserved |
| UWB | Reserved | Reserved | Reserved | Reserved | Reserved |

Information elements (IEs)

An IE is formatted as shown in Figure 43. It is optionally contained in certain management type frames.

— IE format - general

The Element ID field is set to the value that identifies the information element according to Table 15.

The Length field is set to the length, in octets, of the IE-specific Information field that follows.

The Information field is set based on the Element ID as defined below.

— Information elements

| Element ID in decimal value | IE name | Description |
| --- | --- | --- |
| 0 | Slotted Superframe IE | Specifies superframe (beacon period) and allocation slot lengths |
| 1 | Uplink Request IE | Specifies time-based requirements by a node for scheduled uplink allocation(s) |
| 2 | Downlink Request IE | Specifies time-based requirements by a node for scheduled downlink allocation(s) |
| 3 | Bilink Request IE | Specifies time-based requirements by a node for scheduled bilink allocation(s) |
| 4 | Delayed Bilink Request IE | Specifies time-based requirements by a node for scheduled bilink allocation(s) that are subject to delay |
| 5 | Group Connection IE | Indicates a group connection request and the corresponding number of nodes included in the request |
| 6 | Uplink Assignment IE | Specifies scheduled uplink allocation(s) assigned to a node |
| 7 | Downlink Assignment IE | Specifies scheduled downlink allocation(s) assigned to a node |
| 8 | Bilink Assignment IE | Specifies scheduled bilink allocation(s) assigned to a node |
| 9 | Delayed Bilink Assignment IE | Specifies scheduled bilink allocation(s) assigned to a node that are subject to delay |
| 10 | Node Connection Assignment IE | Specifies connection assignment to a node within a multimode connection assignment |
| 11 | Nibble Encoded Channel Order IE | Specifies a list of 4-bit encoded channels in an operating band containing no more than 15 channels in the order of their selection by a hub |
| 12 | Octet Encoded Channel Order IE | Specifies a list of 8-bit encoded channels in an operating band containing more than 15 channels in the order of their selection by a hub |
| 13 | Channel Hopping IE | Specifies current channel dwell length and phase if channel hopping is enabled |
| 14-244 | Reserved | Reserved |
| 255 | Application Specific IE | Provides user-defined application-specific information |

Slotted Superframe IE

A Slotted Superframe IE is formatted as shown in Figure 44.  It is optionally contained in Connection Assignment frames to foretell some information on the superframe (beacon period) structure that is contained in beacons which are not being transmitted frequently or at all.

— Slotted Superframe IE format

Superframe Length

The Superframe Length field is as defined in 6.3.1.2 for the Beacon Period Length field.

Allocation Slot Length

The Allocation Slot Length field is as defined in 6.3.1.3.

Beacon Shifting Sequence

The Beacon Shifting Sequence field is present only if beacon shifting is enabled.  When present, it is as defined in 6.3.1.10.

Uplink Request IE

An Uplink Request IE is formatted as shown in Figure 45. It is optionally contained in Connection Request frames to request, using time-based requirements, for creation or modification of one or more scheduled uplink allocations.

— Uplink Request, Downlink Request, or Bilink Request IE format

One or more Allocation Request fields are present. Each Allocation Request is formatted as shown in Figure 46 to describe the time-based requirements of an allocation for servicing the data belonging to a given user priority.

— Allocation Request format

Allocation ID

The Allocation ID identifies an allocation requested by the node. It is comprised of the Frame Subtype and User Priority fields as defined below.

Frame Subtype

The Frame Subtype field is set to the frame subtype of the data type frames to be transferred in this requested allocation.

User Priority

The User Priority field is set to the user priority of the frame payloads to be transferred in this requested allocation according to 7.2.3.

Maximum Gap

The Maximum Gap field is set to the largest length, in units of allocation slots, of the gap between any two adjacent allocation intervals of this requested allocation in the same beacon period (superframe) or across beacon periods (superframes), if the Wakeup Period field in the current frame has a value of 1. It is reserved otherwise.

Minimum Gap

The Minimum Gap field is set to the smallest length, in units of allocation slots, of the gap between any two adjacent allocation intervals of this requested allocation in the same beacon period (superframe) or across beacon periods (superframes).

Minimum Length

The Minimum Length field is set to the smallest length, in units of allocation slots, of any of the allocation intervals of this requested allocation.

Allocation Length

The Allocation Length field is set to the overall length, in units of allocation slots, of the allocation intervals of this requested allocation in each wakeup beacon period (superframe) of this node.

Scaling Down Factor

The Scaling Down Factor field is set to D such that (1 – D/8)×Allocation Length is the least overall length of the allocation intervals this node is willing to accept for this requested allocation in each of its wakeup beacon periods (superframes).

Scaling Up Factor

The Scaling Up Factor field is set to U such that (1 + U/4) × Allocation Length is the most overall length of the allocation intervals this node is willing to accept for this requested allocation in each of its wakeup beacon periods (superframes).

Downlink Request IE

A Downlink Request IE is formatted as shown in Figure 45 in conjunction with Figure 46. It is optionally contained in Connection Request frames to request, using time-based requirements, for creation or modification of one or more scheduled downlink allocations.

Bilink Request IE

A Bilink Request IE is formatted as shown in Figure 45 in conjunction with Figure 46. It is optionally contained in Connection Request frames to request, using time-based requirements, for creation or modification of one or more scheduled bilink allocations.

Delayed Bilink Request IE

A Delayed Bilink Request IE is formatted as shown in Figure 47. It is optionally contained in Connection Request frames to request, using time-based requirements, for creation or modification of one or more scheduled bilink allocations that are subject to delay.

— Delayed Bilink Request IE format

One or more Delayed Allocation Request fields are present. Each Delayed Allocation Request is formatted as shown in Figure 48 to describe the time-based requirements of an allocation for servicing the data belonging to a given user priority.

— Delayed Allocation Request format

Allocation ID

The Allocation ID is as defined in Figure 1.

Frame Subtype

The Frame Subtype field is as defined in 6.7.2.1.1.

User Priority

The User Priority field is as defined in 6.7.2.1.2.

Maximum Gap

The Maximum Gap field is as defined in 6.7.2.2.

Minimum Gap

The Minimum Gap field is as defined in 6.7.2.3

Minimum Length

The Minimum Length field is as defined in 6.7.2.4

Allocation Length

The Allocation Length field is as defined in 6.7.2.5

Scaling Down Factor

The Scaling Down Factor field is as defined in 6.7.2.6.

Scaling Up Factor

The Scaling Up Factor field is as defined in 6.7.2.7

Maximum Delay

The Maximum Delay field is set to D, in units of allocation slots, such that this node is willing to wait for a transmission addressed to it till D from the scheduled start of the allocation interval specified through the preceding four fields.

Group Connection IE

A Group Connection IE is formatted as shown in Figure 49. It is optionally contained in Connection Request or Connection Assignment frames to indicate that the current connection request or assignment is made aggregately for a specified number of nodes with preinstalled group identification.

— Group Connection IE format

Group Size

The Group Size field is set to the number of nodes represented by the current Connection Request or Connection Assignment frame.

Group ID

The Group ID field is set to the group identification (ID) preinstalled for the group comprising this sender and the represented nodes.

Uplink Assignment IE

An Uplink Assignment IE is formatted as shown in Figure 50. It is optionally contained in Connection Assignment frames to assign or reassign one or more scheduled uplink allocations to the addressed node.

— Uplink Assignment, Downlink Assignment, or Bilink Assignment IE format

One or more Allocation Assignment fields are present. Each Allocation Assignment is formatted as shown in Figure 51 to specify an allocation interval of an assigned allocation for the data belonging to a given user priority. One or more Allocation Assignment fields are included in this IE to specify an allocation. Still more Allocation Assignment fields are included in the IE to specify additional allocations.

—Allocation Assignment format

Allocation ID

The Allocation ID identifies the allocation being assigned or reassigned to the node. It is set to the Allocation ID used to identify the allocation requested earlier by the node.

Frame Subtype

The Frame Subtype field is set to the frame subtype of the data type frames to be transferred in this assigned allocation.

User Priority

The User Priority field is set to the user priority of the frame payloads to be transferred in this assigned allocation.

Interval Start

The Interval Start field is set to the number of the allocation slot that starts an allocation interval of this assigned allocation.

Interval End

The Interval End field is set to the number of the allocation slot that ends the allocation interval whose start time is specified in the preceding field.

Downlink Assignment IE

A Downlink Assignment IE is formatted as shown in Figure 50 in conjunction with Figure 51. It is optionally contained in Connection Assignment frames to assign one or more scheduled downlink allocations to the addressed node.

Bilink Assignment IE

A Bilink Assignment IE is formatted as shown in Figure 50 in conjunction with Figure 51. It is optionally contained in Connection Assignment frames to assign one or more scheduled Bilink allocations to the addressed node.

Delayed Bilink Assignment IE

A Delayed Bilink Assignment IE is formatted as shown in Figure 52. It is optionally contained in Connection Assignment frames to assign or reassign one or more scheduled bilink allocations that are subject to delay to the addressed node.

— Delayed Bilink Assignment IE format

One or more Delayed Allocation Assignment fields are present. Each Delayed Allocation Assignment is formatted as shown in Figure 53 to specify an allocation interval of an assigned allocation for the data belonging to a given user priority and a corresponding maximum delay. One or more Delayed Allocation Assignment fields are included in this IE to specify an allocation. Still more Allocation Assignment fields are included in the IE to specify additional allocations.

— Delayed Allocation Assignment format

Allocation ID

The Allocation ID identifies the allocation being assigned or reassigned to the node. It is set to the Allocation ID used to identify the allocation requested earlier by the node.

Frame Subtype

The Frame Subtype field is set to the frame subtype of the data type frames to be transferred in this assigned allocation.

User Priority

The User Priority field is set to the user priority of the frame payloads to be transferred in this assigned allocation.

Interval Start

The Interval Start field is set to the number of the allocation slot that starts an allocation interval of this assigned allocation.

Interval End

The Interval End field is set to the number of the allocation slot that ends the allocation interval whose start time is specified in the preceding field.

Maximum Delay

The Maximum Delay field is set to D, in units of allocation slots, such that this node is required to wait for a transmission addressed to it till D from the scheduled start of the allocation interval specified in the preceding two fields.

Node Connection Assignment IE

A Node Connection Assignment IE is formatted as shown in Figure 54. It is optionally contained in Multinode Connection Assignment frames to assign or reassign one or more scheduled allocations to the identified node.

— Node Connection Assignment IE format

All the fields after the Length field pertain to the same node and are as defined in 6.3.7 for Connection Assignment frames, except the Node Address field which is set to the EUI-48 of the node.

Nibble Encoded Channel Order IE

A Nibble Encoded Channel Order IE is formatted as shown in Figure 55. It is optionally contained in Connection Assignment frames to indicate some or all channels in the operating band that has no more than 15 operating channels and the order in which those channels are to be selected as operating channels.

— Nibbled Encoded Channel Order IE and Octet Encoded Channel Order IE format

The Channel Ordered List field is set as follows:

The four least-significant bits are set to the channel number of the channel which will be the first candidate to each instance of channel selection.

Each successive four bits are set to the channel number of the channel which will be the next candidate to the instance of channel selection.

If the list conveys an odd number of channels, four bits with a binary value of 1111 are padded as the most-significant bits to the field.

Octet Encoded Channel Order IE

An Octet Encoded Channel Order IE is formatted as shown in Figure 55. It is optionally contained in Connection Assignment frames to indicate some or all channels in the operating band that has more than 15 operating channels and the order in which those channels are to be selected as operating channels.

The Channel Ordered List field is set as follows:

The eight least-significant bits are set to the channel number of the channel which will be the first candidate to each instance of channel selection.

Each successive eight bits are set to the channel number of the channel which will be the next candidate to the instance of channel selection.

Channel Hopping IE

A Channel Hopping IE is formatted as shown in Figure 56. It is optionally contained in Connection Assignment frames to enable channel hopping.

— Channel Hopping IE format

Channel Dwell Length

The Channel Dwell Length field is set to the length of the time, in units of beacon periods (superframes), over which the hub sending the current frame is to dwell at any chosen operating channel before hopping to another one. It is set to 0 to encode a value of 256 beacon periods (superframes).

Channel Dwell Phase

The Channel Dwell Phase field is set to H if the hub sending the current frame is to hop to another channel according to its channel hopping sequence at the end of the next Hth beacon period (superframe) not counting the current beacon period (superframe) if H > 0 or at the end of the current beacon period (superframe) if H = 0.

Application Specific IE

An Application Specific IE is formatted as shown in Figure 57. It is optionally contained in some management type frames to convey application-specific information.

— Application Specific IE format

OUI-24

The OUI-24 field is set to the 24-bit Organizationally Unique Identifier (OUI) assigned by the IEEE Registration Authority to the vendor or manufacturer that defines this IE.

Application Specific Data

The Application Specific Data field is set by the owner (“assignee” in IEEE terms) of the OUI.

MAC functions

General

This clause specifies MAC sublayer functionality. It starts with the ground rules for preparing frame transmission and performing frame reception in 7.2. The next subclause 7.3 is an access umbrella encompassing the access modes and structures provided in this standard for medium access. With these overall preparations, medium access starts in earnest in 7.4 with the creation of a body area network (BAN) by a hub and the unconnected exchange (“connection setup”) between unconnected nodes and the hub. The following three subclauses 7.5, 7.6, and 7.7 specify the operation of a variety of selectable access schemes for obtaining allocation intervals of preferred attributes. Additional access steps are given in 7.8 for communication in the tightly regulated medical implant communications service (MICS) band. Two-hop access extension of star BAN topology is optionally made available in 7.9.

Supplemental MAC functions follow in the remaining subclauses. Clock synchronization and guardtime provisioning are addressed in 7.10. Power management is expounded in 7.11. Coexistence support and interference mitigation are optionally offered in Figure 88. MAC / PHY optional capability handling and Application Specific IE usage are elucidated in 7.13.  MAC sublayer parameters are listed in 7.14.

Frame processing

This subclause provides fundamental rules on preparing MAC frames for transmission and processing them on reception.

Abbreviated addressing

A hub shall select a one-octet body area network identifier (BAN ID) from an integer between 0x00 and 0xFF, inclusive, as its BAN’s abbreviated address contained in the MAC header of all frames sent from or to the hub. The hub should select a BAN ID that is currently not being used by neighbor BANs.

A hub shall select or reselect a one-octet hub identifier (HID) from an integer in the Connected_NID subset as specified in Table 16 as its abbreviated address contained in the MAC header of all frames sent from or to the hub. The hub shall not reselect an HID equal to a Connect_NID that is currently being used for a node connected with it. The hub should select an HID that is currently not being used by neighbor hubs.

A one-octet node identifier (NID) selected in accordance with Table 16 shall be used as a node’s abbreviated address contained in the MAC header of all frames sent (unicast) from or to the node, or shall be used as a group of nodes’ common abbreviated address contained in the MAC header of all frames sent (multicast or broadcast) to the nodes by a hub.

— NID selection

| NID value in hex | NID subtotal | NID notation | NID usage |
| --- | --- | --- | --- |
| 0x00 | 1 | Unconnected_Broadcast_NID | For broadcast to unconnected nodes |
| 0x01 | 1 | Unconnected_NID | For unicast from/to unconnected nodes in a BAN |
| 0x02-0xF5 | 244 | Connected_NID | For unicast from/to connected nodes in a BAN |
| 0xF6 | 1 | Reserved | Reserved |
| 0xF7- 0xFD | 7 | Multicast_NID | For multicast to connected nodes in a BAN |
| 0xFE | 1 | Local_Broadcast_NID | For broadcast to all nodes in a BAN |
| 0xFF | 1 | Broadcast_NID | For broadcast to all nodes in all BANs |

An unconnected node without an assigned Connected_NID shall choose the Unconnected_NID as its NID in its first (management type) frame, and retries thereof, sent to a hub before being connected with the hub.

Upon receiving the first frame from an unconnected node, a hub shall assign as the node’s NID a Connected_NID that is not being used for itself or another node in its BAN, and shall use that Connected_NID as the Recipient ID of the MAC header in its I-Ack and all subsequent frames sent to the node.

The unconnected node shall be ready to receive frames from the hub, without regard to the Recipient ID field of the MAC header, before finding its assigned Connected_NID. The node shall use as its NID in all subsequent exchanges with the hub the Connected_NID of the Recipient ID field in the MAC header of the last management type frame received with the frame payload containing a Recipient Address field set to its EUI-48. The node may retry its first frame after failing to receive the expected first management type frame from the hub.

If the node receives a frame from the hub with the Recipient ID in the MAC header set to its current Connected_NID but with the Recipient Address in the frame payload not set to its EUI-48, the node shall consider itself to have disconnected with the hub and lost its Connected_NID accordingly. It may employ the above procedure again to obtain its Connected_NID.

Full addressing

A separate EUI-48 shall be used to uniquely identify a sender or a recipient when desired. In particular, the EUI-48 of a hub sending a beacon is included in the MAC frame payload of the beacon. The EUI-48es of both the sender and the recipient of other management type frames are included in the MAC frame payload of those frames.

Exceptionally, an unconnected node may set to 0 the Recipient Address field of the first management type frame it sends to a hub, if the node has not yet known the EUI-48 of the hub.

A recipient shall check the Recipient Address and Sender Address fields of the MAC frame payload of a received management type frame to determine if the frame was indeed addressed to it from an expected sender, taking the aforementioned exception into account.

Priority mapping

User priority values, when referenced in prioritizing medium access of data and management type frames, shall be determined based on the designation of frame payloads (traffic) contained in the frames according to Table 17.

— User priority mapping

| Priority | User Priority | Traffic designation | Frame type |
| --- | --- | --- | --- |
| Lowest | 0 | Background (BK) | Data |
|  | 1 | Best effort (BE) | Data |
|  | 2 | Excellent effort (EE) | Data |
|  | 3 | Controlled load (CL) | Data |
|  | 4 | Video (VI) | Data |
|  | 5 | Voice (VO) | Data |
|  | 6 | Medical data or network control | Data or management |
| Highest | 7 | Emergency or medical event report | Data |

Frame reception

A node shall receive a frame if the following conditions are met:

The Recipient ID field of the MAC header of the frame is set to its own NID, any applicable multicast_NID, the Local_Broadcast_NID, or the Broadcast_NID.

The Sender ID field of the MAC header of the frame is set to the HID of the desired hub with which to exchange frames.

The BAN ID field of the MAC header of the frame is set to an expected value.

The Protocol Version of the MAC header of the frame is set to a value it supports.

The FCS of the frame is valid, i.e., equal to the FCS value it calculates over the applicable fields received.

A hub shall receive a frame if the following conditions are met:

The Recipient ID field of the MAC header of the frame is set to its own HID.

The Sender ID field of the MAC header of the frame is set to the NID of an expected sender or the Unconnected_NID.

The BAN ID field of the MAC header of the frame is set to an expected value.

The Protocol Version of the MAC header of the frame is set to a value it supports.

The FCS of the frame is valid.

The node or the hub shall ignore a received frame, aside from performing applicable acknowledgment, whose MAC frame payload has a Sender Address field that is not set to the EUI-48 of the expected sender or whose MAC frame payload has a Recipient Address field that is not set to its own EUI-48.

The node or the hub shall ignore a received frame, aside from performing applicable acknowledgment, that is detected to be a duplicate, as described in 7.2.10

Frame transfer

A sender shall transmit MAC service data units (MSDUs) contained in data type frames of the same frame subtype and addressed to the same recipient(s) in the octet order in which they arrived at the local MAC service access point (SAP).

When fragmenting an MSDU, the sender shall extract the first fragment, the second fragment, and so on, in sequential octet order. The sender shall transmit the first fragment, then the second fragment, and so on, accordingly.

A sender may transmit an MSDU earlier than another MSDU, even if the former arrived at the local MAC SAP later than the latter, so long as the two MSDUs are contained in data type frames not of the same frame subtype or not addressed to the same recipient(s).

A recipient shall release to the MAC client MSDUs that were transmitted by the same sender and contained in data type frames of the same frame subtype in the octet order in which they were received.

Frame retry

A node or a hub may retry a frame, i.e., may transmit a frame that was previously transmitted but not necessarily received, to the same recipient(s), as appropriate, taking into consideration such factors as delay requirements, fairness policies, channel conditions, and medium availability.

Frame timeout

A node or a hub shall treat an expected frame, such as an I-Ack or B-Ack frame, as not received, if at the end of the expected frame, it has not received such a frame nor is in the process of receiving a frame.  It shall estimate the end of the expected frame by assuming that such an expected frame was of the shortest length possible for the frame and was transmitted at the lowest data rate mandated for the frequency band containing the operating channel.

Frame separation

If a sender – a node or a hub – is to send a frame pSIFS or pMIFS after (the end of) the previous frame, it shall ensure that the start of the frame occurs between pSIFS and pSIFS+pExtraIFS or between pMIFS and pMIFS+pExtraIFS, respectively, after the end of the previous frame, where the start of a frame and the end of a frame are specified according to the specification for the underlying physical layer (PHY).  If the previous frame is an expected frame not received, its end time is estimated according to 7.2.7.

If a recipient – a node or a hub – is to receive a frame pSIFS or pMIFS after (the end of) the previous frame, it shall be ready to receive a frame no later than pSIFS or pMIFS, respectively, after the end of the previous frame, and shall not exit receive state earlier than the end of the frame estimated according to 7.2.7 with the assumption that the time interval between the end of the previous frame and the start of the expected frame is pSIFS+pExtraIFS or pMIFS+pExtraIE, respectively.

Frame acknowledgement

A sender shall set the Ack Policy field of the MAC header of a frame to be transmitted according to Table 18. A recipient shall acknowledge a received frame if the criteria in 7.2.4 for qualifying a frame as received are met and if required by the acknowledgment policy set in the frame as further described below.

— Acknowledgement (ACK) Policy field setting

| Frame Type name | Frame Subtype name | Ack Policy field |
| --- | --- | --- |
| Management | Beacon | N-Ack |
| Management | Security Association | I-Ack |
| Management | Security Disassociation | I-Ack |
| Management | PTK | I-Ack |
| Management | GTK | I-Ack |
| Management | Connection Request | I-Ack |
| Management | Connection Assignment | I-Ack |
| Management | Multinode Connection Assignment | N-Ack |
| Management | Disconnection | I-Ack |
| Management | Command | I-Ack |
| Control | I-Ack | N-Ack |
| Control | B-Ack | N-Ack |
| Control | I-Ack+Poll | N-Ack |
| Control | B-Ack+Poll | N-Ack |
| Control | Poll | N-Ack |
| Control | T-Poll | N-Ack |
| Control | B2 | N-Ack |
| Data | Data subtype set to mG-AckDataSubtype | G-Ack |
| Data | User defined data subtype other than mG-AckDataSubtype | N-Ack, I-Ack, L-Ack, or B-Ack |

No Acknowledgment (N-Ack)

A sender may send a frame with the Ack Policy field set to N-Ack to require no acknowledgment at all, as permitted by Table 18.

A recipient shall not acknowledge a received frame containing an Ack Policy field set to N-Ack, either immediately or later.

The sender may retry a data type frame with the Ack Policy field set to N-Ack, as appropriate.

Group Acknowledgment (G-Ack)

A node, but not a hub, may send to a hub a frame with the Ack Policy field set to G-Ack if the following two conditions are satisfied:

The frame is a data type frame with the frame subtype set to mG-AckDataSubtype.

The hub supports G-Ack as indicated in its MAC Capability field.

A hub shall acknowledge data type frames with the Ack Policy field set to G-Ack and the Frame Subtype field set to mG-AckDataSubtype that were received since its last B2 transmission by including the NIDs of the nodes from which those frames were received in the frame payload of the next B2 frame. The hub should send such a B2 frame as soon as permitted.

The node may retry the frame requiring G-Ack upon failing to receive the expected B2 frame or the expected acknowledgment in the next received B2 frame.

An example for group acknowledgment (G-Ack) is shown in Figure 58.

— Group Acknowledgement (G-ACK)

Immediate Acknowledgment (I-Ack)

A sender may send a frame with the Ack Policy field set to I-Ack to require an immediate acknowledgment.

A recipient shall acknowledge a received frame with the Ack Policy field set to I-Ack by sending an I-Ack frame back pSIFS after the end of the received frame.

Examples for immediate acknowledgment are shown in Figure 59.

— Immediate Acknowledgement (I-Ack) illustration

Block Acknowledgment Later (L-Ack) and Block Acknowledgment (B-Ack)

A source—a node or a hub—may send a frame with the Ack Policy field set to B-Ack if the following two conditions are satisfied:

The frame contains a whole MSDU.

The recipient supports L-Ack / B-Ack as indicated in the latter’s MAC Capability field.

The recipient shall acknowledge a received frame with the Ack Policy field set to B-Ack by sending a B-Ack frame back pSIFS after the end of the received frame. The B-Ack frame shall contain a frame payload as defined in 6.4.2 unless the following two conditions are both true:

No older frames of the same frame subtype as the last received frame are still expected to be received.

Only one frame in the next block transmission is allowed.

A block transmission starts from the first frame sent after the last B-Ack frame received and ends with the last frame sent before receiving next B-Ack frame.

The source node may send a frame with the Ack Policy field set to L-Ack if the following conditions are all satisfied:

The frame contains a whole MSDU.

It has sent a frame of the same frame subtype with the Ack Policy field set to B-Ack and received a B-Ack frame acknowledging that frame and containing a frame payload.

That B-Ack frame was the last B-Ack frame received from the recipient.

The source shall not transmit more frames in a block transmission than allowed as specified in the last B-Ack frame received. These frames should not be longer than the final frame sent in the previous block transmission. The source shall end a block transmission with a frame with the Ack Policy field set to B-Ack.

The source shall separate the frames in a block transmission within an allocation interval by pMIFS or pSIFS, depending on whether it is setting the block transmission as a burst mode transmission defined at the PHY layer.

The source shall send frames in a block transmission in the order of increasing sequence number values, which are not necessarily consecutive if the block transmission contains retransmitted frames, considering that sequence number wraparound is also increasing the sequence number value. The source shall not retransmit frames that are older than the frame indicated in the Oldest Frame Expected field of the last B-Ack frame received. It should retransmit frames that were not received as indicated in the Frame Status Bitmap field of that B-Ack frame, starting with the oldest frame expected or the next oldest frame still buffered.  The source may discard frames if permitted by the application generating those frames, due to buffer constraints or aging considerations.

The source, once starting a block transmission, shall not transmit frames of another frame type or subtype until it has finished the block transmission.  Subject to this restriction, a block transmission may span more than one allocation interval or beacon period (superframe).

The recipient shall not acknowledge immediately a received frame with the Ack Policy field set to L-Ack. Rather, it shall indicate the reception status of the frames newer than the oldest frame still expected through the B-Ack frame it returns at the end of the current block transmission.

The source may retransmit in an appropriate time the last frame which had the Ack Policy field set to B-Ack after failing to receive the expected B-Ack frame.

The recipient may implement a timeout that enables it to stop waiting for missing old frames if appropriate, hence allowing new MSDUs to be released to the MAC client and some B-Ack buffer resources to be freed without receiving those missing frames.

Examples for late acknowledgment (L-Ack) and block acknowledgment (B-Ack) are shown in Figure 60.

— Late Acknowledgement (L-ACK) and block acknowledgement (B-Ack) illustration

Duplicate detection

A received frame shall be treated by the recipient as a duplicate of the last management or data type frame received if the Retry bit in its MAC header is set to 1 and the two frames have identical values in the following fields of their MAC header: Recipient ID, Sender ID, BAN ID, Protocol Version, Security Level, Frame Type, Frame Subtype, Sequence Number, and Fragment Number.

Fragmentation and reassembly

A sender may fragment only MAC service data units (MSDUs) to be transferred in data type frames with the Ack Policy field set to N-Ack, G-Ack, or I-Ack.

The sender shall not fragment any MSDU to more than mMaxFragmentCount fragments. All fragments, except the last one, of the same MSDU shall have the same length. The sender shall not alter the length of the fragments of an MSDU, by refragmentation or recombination, in retransmitting them.

The sender shall complete the transmission of a fragmented MSDU before transmitting another MSDU or a fragment thereof, regardless of whether the MSDUs are contained in data type frames with the same or different frame subtypes. The sender shall not transmit any other fragments of an MSDU after discarding one fragment of the MSDU.

A recipient shall completely reassemble an MSDU in the correct order before delivery to the MAC client. The recipient shall discard any MSDU with missing fragments.

Access classification and division

To provide or support time referenced allocations in its body area network (BAN), a hub shall establish a time base as specified in 5.4 which divides the time axis into beacon periods (superframes) regardless of whether it is to transmit beacons. In such cases, the hub shall transmit a beacon in each beacon period, except in inactive superframes, unless prohibited by regulations such as imposed in the MICS band. The hub may shift (rotate) its beacon transmission time, as specified in 7.12.1, from one offset from the start of current beacon period to another offset from the start of next beacon period, thereby shifting the time reference for all scheduled allocations, to prevent large-scale repeated transmission collisions between its BAN and neighbor BANs.

In cases where a hub is not to provide or support time referenced allocations in its BAN, it may operate without establishing a time base nor superframe boundaries and hence without transmitting beacons at all.

Equivalently, a hub shall operate in beacon mode transmitting a beacon in every beacon period other than in inactive superframes to enable time referenced allocations, unless regulations as applicable in the MICS band disallow beacon transmission. In the latter case, a hub shall operate in non-beacon mode transmitting no beacons, with superframe and allocation slot boundaries established if access to the medium in its BAN involves time referencing, or without superframe or allocation slot boundaries if access to the medium in its BAN involves no time referencing.

In summary, a hub shall operate in one of the following three access modes:

beacon mode with beacon period (superframe) boundaries;

non-beacon mode with superframe boundaries;

non-beacon mode without superframe boundaries.

Beacon mode with beacon period (superframe) boundaries

In this mode, a hub shall divide each active beacon period into applicable access phases as illustrated in Figure 61 where a beacon (B) is also shown. The hub may announce some superframes (beacon periods) as inactive superframes where it transmits no beacons and provides no access phases, if there are no allocation intervals scheduled in those superframes.

— Layout of access phases in a beacon period (superframe) for beacon mode

The hub shall place the access phases – exclusive access phase 1 (EAP1), random access phase 1 (RAP1), type-I/II access phase, exclusive access phase 2 (EAP2), random access phase 2 (RAP2), type-I/II access phase, and contention access phase – in the order stated and shown above. The hub may set to 0 the length of any of these access phases, but shall not have RAP1 shorter than the guaranteed minimum length communicated in Connection Assignment frames sent to nodes that are still connected with it. To provide a non-zero length CAP, the hub shall transmit a preceding B2 frame.

A type-I/II access phase is either a type-I or type-II access phase as described below, but not both. The two type-I/II access phases may be both of type-I, both of type-II, or one of type-I and the other of type-II. If one is of type-I and the other is of type-II, either one may appear before the other.

Type-I access phase

The hub may schedule uplink allocation intervals, downlink allocation intervals, and bilink allocation intervals anywhere in a type-I access phase. It may improvise type-I and type-II polled allocation intervals as well as posted allocation intervals anywhere outside the scheduled allocation intervals in the type-I access phase. It may also provide type-I and type-II polled allocation intervals within scheduled bilink allocation intervals in a type-I access phase.

As defined in 6.2.1.1.10 and 6.2.1.1.11,

a type-I polled allocation is conveyed in terms of its time duration (the maximum time the polled node may use for its frame transactions in the allocation);

a type-II polled allocation is conveyed in terms of a frame count (the maximum number of frames the polled node may transmit in the allocation).

These allocation intervals along with the corresponding access methods by which they are obtained are illustrated in Figure 62.

— Allocation intervals and access methods permitted in a type-1 access phase

Type-II access phase

The hub may schedule bilink allocation intervals and delayed bilink allocation intervals anywhere in a type-II access phase, except that it shall not schedule any bilink allocation intervals after delayed bilink allocation intervals in the same type-II access phase. It may improvise type-II, but not type-I, polled allocation intervals as well as posted allocation intervals anywhere outside the scheduled bilink allocation intervals and delayed bilink allocation intervals in the type-II access phase. It may also provide type-II, but not type-I, polled allocation intervals within scheduled bilink allocation intervals and delayed bilink allocation intervals. These allocation intervals along with the corresponding access methods by which they are obtained are illustrated in Figure 63.

— Allocation intervals and access methods permitted in a type-II access phase

Non-beacon mode with superframe boundaries

In this mode, a hub may have only a type-I or type-II access phase as described in 7.3.1 in any superframe (beacon period), but not both or any other access phases, as illustrated in Figure 64.

— Layout of access phases in a superframe (beacon period) for non-beacon mode

Non-beacon mode without superframe boundaries

In this mode, a hub may provide only unscheduled type-II polled allocations, as illustrated in Figure 65.

— Allocation intervals and access methods permitted for non-beacon mode     without superframe boundaries

BAN creation and connection setup

A hub shall choose an operating channel to start a body area network (BAN), taking into account policy regulations, channel conditions, application requirements, coexistence considerations, etc. The hub shall choose a new channel when required by regulations as applicable in the medical implant communications service (MICS) band. The hub may hop to new channels periodically, as specified in Figure 90, to effect frequency diversity and interference mitigation.

The hub shall choose and enable an applicable access mode as described in 7.3 to support desired access methods.

If the hub selected non-beacon mode without superframe boundaries, it shall transmit Poll frames each addressed to Unconnected_Broadcast_NID and providing an immediate type-II polled allocation to enable unconnected nodes’ connection or reconnection with it.

If the hub selected non-beacon mode with superframe boundaries, it shall transmit T-Poll frames each addressed to Unconnected_Broadcast_NID and providing an immediate type-I or type-II polled allocation to enable unconnected nodes’ connection or reconnection with it.

If the hub selected beacon mode with superframe boundaries, it may transmit T-Poll frames each addressed to Unconnected_Broadcast_NID and providing an immediate type-I or type-II polled allocation to facilitate unconnected nodes’ connection or reconnection with it.

An unconnected polled allocation is a type-I or type-II polled allocation granted by a hub via a Poll or T-Poll frame addressed to Unconnected_Broadcast_NID, and an unconnected node is a node without a scheduled uplink allocation, a scheduled bilink allocation, or a delayed bilink allocation, in the BAN identified in the MAC header of those Poll or T-Poll frames.

An unconnected node may send at most a management type frame to the hub in an unconnected polled allocation with contention probability P = 1/2. If the node does not receive an expected acknowledgment, it may retry it in another unconnected polled allocation with contention probability P = max(1/8, (1/2) / ((R+1)/2(), where R counts the retries of the frame, i.e., R equals 1 for the first retry of the frame, 2 for the second retry, and so on. The function (x( is defined to be the least integer not smaller than x. With contention probability P, the node shall transmit if z ≤ P, where z is a value the node has newly drawn at random from the interval [0, 1].

The hub shall not provide unconnected polled allocations with time duration shorter than the appropriate guard time plus pUnconnectedPolledAllocationMin, which is the time required for sending the longest management type frame containing no information elements (IEs) and returning an immediate acknowledgment at a mandatory data rate, plus pSIFS.

The unconnected node may disregard the indicated time duration of a type-I polled allocation in sending a management type frame containing no IEs, before receiving a Connection Assignment frame with a Slotted Superframe IE providing the necessary time information for determining such time duration. The unconnected node may later send another management type frame of the same frame subtype, such as Connection Request, with updated information (e.g., on wakeup phase, wakeup period, and Uplink Request IEs), after finding the beacon period (superframe) and allocation slot lengths.

After the hub receives and acknowledges the first management type frame sent from an unconnected node, it should provide polled allocations specifically addressed (unicast) to this node to facilitate the transmission of the unconnected node. The unconnected node should stay in active state until it does not need polled or posted allocations that are not announced in advance.

Figure 66 illustrates how to instantiate or obtain unconnected and unicast polled allocations for or by an unconnected node.

— Unconnected and unicast polled allocations for unconnected nodes

The node may also use CSMA/CA or slotted Aloha access as described in 7.5, if capable, to transmit its frames before and after its connection with the hub.

The hub may locally broadcast a Multinode Connection Assignment frame granting scheduled allocations to multiple nodes that are capable of handling multimode connection assignment as indicated in their last exchanged MAC Capability field.

Random access (connectionless contention-based access)

In exclusive access phase 1(EAP1), random access phase 1 (RAP1), exclusive access phase 2(EAP2), random access phase 2 (RAP2), and contention access phase (CAP), as depicted in 7.3, allocations may only be contended allocations, which are non-reoccurring time intervals valid per instance of access. The access method for obtaining the contended allocations shall be

CSMA/CA as specified in 7.5.1 if pRandomAccess is set to CSMA/CA, or

slotted Aloha access as specified in 7.5.2 if pRandomAccess is set to Slotted Aloha.

A hub or a node may obtain contended allocations in EAP1 and EAP2, if it needs to send data type frames of the highest user priority (i.e., containing an emergency or medical event report) as defined in Table 17. The hub may obtain such a contended allocation pSIFS after the start of EAP1 or EAP2 without actually performing the CSMA/CA or slotted Aloha access procedure. Only nodes may obtain contended allocations in RAP1, RAP2, and CAP, to send management or data type frames.

To send data type frames of the highest user priority based on CSMA/CA, a hub or a node may treat the combined EAP1 and RAP1 as a single EAP1, and the combined EAP2 and RAP2 as a single EAP2, so as to allow continual invocation of CSMA/CA and improve channel utilization. To send data type frames of the highest user priority based on slotted Aloha access, a hub or node may treat RAP1 as another EAP1 but not a continuation of EAP1, and RAP2 as another EAP2 but not a continuation of EAP2, due to the time slotted attribute of slotted Aloha access.

Prioritized access for traffic of differing user priorities (UPs) shall be attained through the predefined relationships in Table 17 and Table 19 between contention window (CW) bounds CWmax and CWmin and UP for CSMA/CA and between contention probability (CP) thresholds CPmax and CPmin and UP for slotted Aloha access.

— Contention window bounds for CSMA/CA and contention probability thresholds  for slotted Aloha access

| User Priority | CSMA/CA | Slotted Aloha access |
| --- | --- | --- |
|  | CWmin | CWmax | CPmax | CPmin |
| 0 | 16 | 64 | 1/8 | 1/16 |
| 1 | 16 | 32 | 1/8 | 3/32 |
| 2 | 8 | 32 | 1/4 | 3/32 |
| 3 | 8 | 16 | 1/4 | 1/8 |
| 4 | 4 | 16 | 3/8 | 1/8 |
| 5 | 4 | 8 | 3/8 | 3/16 |
| 6 | 2 | 8 | 1/2 | 3/16 |
| 7 | 1 | 4 | 1 | 1/4 |

CSMA/CA

To employ CSMA/CA, a node shall maintain a backoff counter and contention window to determine when it obtains a new contended allocation as described in 7.5.1.1, and shall initialize the backoff counter to 0.

Starting a contended allocation

To obtain a new contended allocation, a node shall set its backoff counter to a sample of an integer random variable uniformly distributed over the interval [1, CW], when its backoff counter has a value of 0 and the node has at least one frame of user priority UP to transmit or retransmit, where CW is a contention window chosen as follows.

- If the node did not obtain any contended allocation previously, it shall set the CW to CWmin[UP].

- If the node succeeded, i.e., if the node received an expected acknowledgment, I-Ack or B-Ack frame, to its last frame transmission, in the last contended allocation it had obtained, it shall set the CW to CWmin[UP] as well.

- If the node transmitted a frame requiring no acknowledgment or group acknowledgment at the end of its last contended allocation, it shall keep the CW unchanged.

- If the node failed, i.e., if the node did not receive an expected acknowledgment to its last frame transmission, in the last contended allocation it had obtained,

it shall keep the CW unchanged if this was the mth time the node had failed consecutively, where m is an odd number;

it shall double the CW if this was the nth time the node had failed consecutively, where n is an even number.

If doubling the CW would have the new CW exceed CWmax[UP], the node shall set the CW to CWmax[UP].

The node shall lock the backoff counter when any of the following events occurs:

- The backoff counter is reset upon decrementing to 0.

The channel is busy. If the channel is busy because the node detected a frame transmission, the channel remains busy until at least the end of the frame transmission without the node having to re-sense the channel.

The current time is outside any RAP or CAP if UP does not have the highest value (i.e., not for an emergency or medical event report) according to Table 17, or is outside any EAP, RAP, or CAP if UP has the highest value (i.e., for an emergency or medical event report).

The current time is at the start of a CSMA slot within an EAP, RAP, or CAP, but the time between the end of the slot and the end of the EAP, RAP, or CAP is not long enough for completing a frame transaction and setting aside a nominal guardtime mGT_Nominal.

The node shall unlock the backoff counter when both of the following conditions are met:

- The channel has been idle for pSIFS within an RAP or CAP if UP does not have the highest value (i.e., not for an emergency or medical event report) according to Table 17, or within an EAP, RAP, or CAP if UP has the highest value (i.e., for an emergency or medical event report).

The time duration between the current time plus a CSMA slot and the end of the EAP, RAP, or CAP is long enough for completing a frame transaction plus a nominal guardtime mGT_Nominal.

Upon unlocking its backoff counter, the node shall decrement its backoff counter by one for each idle CSMA slot that follows, as shown in Figure 67. In particular, the node shall treat a CSMA slot to be idle if it determines that the channel has been idle between the start of the CSMA slot and pCCATime later, decrementing the backoff counter effectively pCCATime after the start of the CSMA slot, so that the node will transmit a frame to the transport medium (i.e., air) at the end of the CSMA slot in case its backoff counter reaches 0, as further described below. Each CSMA slot shall have a fixed duration of pCSMASlotLength.

— CSMA slot structure

If the backoff counter reaches zero in the current CSMA slot, the node shall have obtained a contended allocation that starts at the end of the current CSMA slot with a maximum length of mCSMADurationLimit. Figure 68 illustrates how to start and use contended allocations based on CSMA/CA.

— CSMA/CA Illustration

Using a contended allocation

A node may transmit a frame for which it obtained the contended allocation at the start of the allocation. The recipient shall transmit an acknowledgment frame, I-Ack or B-Ack, when required, pSIFS after the end of the previous frame.

To resume its transmission following a received acknowledgment frame, the node may transmit a new frame or retransmit an old frame, with an UP not lower than the UP used to obtain the current contended allocation, pSIFS after the end of the acknowledgment frame. The node shall end its transmission in the allocation such that the last transmission in the allocation completes at least the nominal guardtime GTn = mGT_Nominal earlier than the end of the allocation or of the current EAP, RAP, or CAP, whichever is earlier.

Modifying a contended allocation

The node shall not modify a contended allocation to a different location without performing another instance of CSMA/CA.

Aborting a contended allocation

A node may relinquish the remaining allocation interval of a contended allocation by indicating that it has no more data to transmit in the frame being transmitted and then by transmitting no more frames in the interval.

A node shall treat a contended allocation to have been aborted after failing to receive the expected acknowledgment frame in the allocation.

A node may start a new contended allocation procedure as specified in 7.5.1 to obtain another contended allocation.

Ending a contended allocation

A node may at any time end a contended allocation by not following with another frame transmission in the allocation.

Slotted Aloha access

To employ slotted Aloha access, a node shall maintain a contention probability to determine if it obtains a new contended allocation in an Aloha slot as described in 7.5.2.1.

Starting a contended allocation

To obtain a new contended allocation for the transmission or retransmission of a frame of user priority UP, a node shall set its contention probability (CP) as follows.

- If the node did not obtain any contended allocation previously, it shall set the CP to CPmax[UP].

- If the node succeeded, i.e., if the node received an expected acknowledgment, I-Ack or B-Ack frame, to its last frame transmission, in the last contended allocation it had obtained, it shall set the CP to CPmax[UP] as well.

- If the node transmitted a frame requiring no acknowledgment or group acknowledgment at the end of its last contended allocation, it shall keep the CP unchanged.

- If the node failed, i.e., if the node did not receive an expected acknowledgment to its last frame transmission, in the last contended allocation it had obtained,

it shall keep the CP unchanged if this was the mth time the node had failed consecutively, where m is an odd number;

it shall halve the CP if this was the nth time the node had failed consecutively, where n is an even number.

If halving the CP would make the new CP smaller than CPmin[UP], the node shall set the CP to CPmin[UP].

With the CP set to CP as stated above, the node shall have obtained a contended allocation in the current Aloha slot if z ≤ CP, where z is a value the node has newly drawn at random from the interval [0, 1]. Each Aloha slot shall be of equal length predetermined to be pAlohaSlotLength as shown in Figure 69.

— Aloha slot structure

An Aloha slot available to the node for contention shall start at the beginning of an RAP or CAP if UP does not have the highest value (i.e., not for an emergency or medical event report) according to Table 17, or after the start of an EAP, RAP, or CAP if UP has the highest value (i.e., for an emergency or medical event report). Successive Aloha slots may be available to the node for contention if they are fully located within the EAP, RAP, or CAP. Figure 70 illustrates how to start and use contended allocations based on slotted Aloha access.

— Slotted Aloha access illustration

Using a contended allocation

A node may transmit a frame for which it obtained the contended allocation in the allocation. The recipient shall transmit an acknowledgment frame, I-Ack or B-Ack, when required, pSIFS after the end of the previous frame.

To resume its transmission following a received acknowledgment frame, the node may transmit a new frame or retransmit an old frame, with an UP not lower than the UP used to obtain the current contended allocation, pSIFS after the end of the acknowledgment frame. The node shall end its transmission in the allocation such that the last transmission in the allocation completes at least the nominal guardtime GTn = mGT_Nominal earlier than the end of the current EAP, RAP, or CAP.

Modifying a contended allocation

The node shall not modify a contended allocation obtained in an Aloha slot to a different Aloha slot without performing another instance of slotted Aloha access.

Aborting a contended allocation

A node may relinquish the remaining allocation interval of a polled allocation by indicating that it has no more data to transmit in the frame being transmitted and then by transmitting no more frames in the interval, or by requesting an immediate or block acknowledgment in case of a type-II polled allocation.

A node may continue its transmission within a contended allocation, without aborting the allocation, after failing to receive the expected acknowledgment frame in the allocation.

A node may start a new contended allocation procedure as specified in 7.5.1.1 to obtain another contended allocation in a different Aloha slot.

Ending a contended allocation

A node may at any time end a contended allocation by not following with another frame transmission in the allocation.

Improvised and unscheduled access (connectionless contention-free access)

Unscheduled access

A hub may employ unscheduled polling and posting access to send polls or posts at any time to grant  polled or posted allocations either in beacon mode or non-beacon mode as characterized in 7.3, so long as the addressed nodes indicated that they will always be in active state through their last transmitted MAC Capability field (i.e., with Always Active bit set to 1). A node that has so indicated shall constantly be in active state ready to receive unscheduled polls or posts.

Improvised access

A hub may employ improvised polling and posting access to send polls or posts without pre-announcement or at previously announced times according to Table 20 and as described below to grant polled or posted allocations, either in beacon mode or non-beacon mode as also noted in 7.3, for on-demand contention-free frame exchanges outside the scheduled uplink allocations within its body area network (BAN). A polled or posted allocation contains an explicit or implicit time interval that does not reoccur subsequently without the hub invoking another instance of improvised access.

— Frames and fields sent by a hub enabling polls and posts

| For unscheduled poll/post | For immediate poll/post | For future poll/post |
| --- | --- | --- |
| I-Ack or B-Ack frame, with More Data = 0, Sequence Number / Poll-Post Window = Reserved (0), Fragment Control / Coexistence / Next = Reserved (0): A poll or post is not scheduled with the current frame transmission, but may be sent if the addressed node is always active as indicated in its MAC Capability field. | Non-beacon management or data type frame, with More Data = 1: A poll or post is intended to start after the end of the current frame transaction (which includes an I-Ack or B-Ack frame if expected). | I-Ack or B-Ack frame, with More Data = 1, Poll-Post Window = B, Next = N: A poll or post is intended to be sent at the start of allocation slot B located in the current beacon period (superframe) if N = 0 or in the next Nth beacon period (superframe) if N > 0. |
|  |  | I-Ack+Poll, B-Ack+Poll, Poll, or T-Poll frame, with More Data = 1, Poll-Post Window = B, Next = N: No polled allocation follows this frame, but another poll or a post is intended to be sent at the start of allocation slot B located in the current beacon period (superframe) if N = 0 or in the next Nth beacon period (superframe) if N > 0. |
| Type-I polled allocation (Poll Type = 0) | Type-II polled allocation (Poll Type = 1) |
| I-Ack+Poll, B-Ack+Poll, Poll, or T-Poll frame, with More Data = 0, Poll-Post Window = A, Fragment Number / Coexistence / Next = Reserved: |
| A polled allocation is intended to start pSIFS after the end of the current frame, and to end at the end of allocation slot A located in the current beacon period (superframe). | A polled allocation is intended to start pSIFS after the end of the current frame, and to end after the polled node has sent A frames or requested an I-Ack or B-Ack frame, whichever is earlier. |

Polling access

A hub may send polls and grant type-I or type-II polled allocations to a node only if both of them support polling access of the corresponding type as indicated in their last exchanged MAC Capability field (i.e., with Type-I or Type-II Polling Access bit set to 1). A hub may send polls addressed to Unconnected_Broadcast_NID and granting type-I or type-II polled allocations any time outside beacons and scheduled allocations, as described in 7.4 for unconnected exchange, without regard to the polling access settings in the MAC Capability indicated by the nodes in its body area network (BAN).

Starting a polled allocation

To obtain a polled allocation for initiating another frame transaction, a node shall set the More Data field to 1 in the frame it is transmitting. The node, if not always active as indicated in its MAC Capability field, should also set the Ack Policy field to I-Ack or B-Ack in some management or data type frames being transmitted. This enables the hub to send the node an immediate or future poll at an announced time through an I-Ack+Poll or B-Ack+Poll frame as described in Table 20.

To grant a polled allocation to a node, a hub shall send to the node a Poll or T-Poll frame when appropriate or an I-Ack+Poll or B-Ack+Poll frame when required to return an acknowledgment according to Table 20 with the Ack Policy field set to 0. To grant no immediate polled allocation but to inform of an intended future poll or post, a hub shall send one of these frames also according to Table 20. The hub should send a Poll or T-Poll frame at the time indicated in a frame previously sent to the node. The hub may send to a node a Poll or T-Poll frame at a time not indicated earlier to the node if the node has also indicated to be always active in its last transmitted MAC Capability field (i.e., with Always Active bit set to 1).

Figure 71 illustrates instances of polls and polled allocations.

— Example polls and polled allocations

Using a polled allocation

A node that has indicated support for polling access shall receive Poll and T-Poll frames at times that have been announced in frames previously sent to it by the hub, as described in Table 20. A node that has indicated to be always active shall be ready to receive Poll and T-Poll frames at any time. The node shall also receive I-Ack+Poll and B-Ack+Poll frames at times expected for acknowledgment arrivals. The node shall initiate a frame transaction at the start of a polled allocation granted to it through a preceding Poll, T-Poll, I-Ack+Poll, or B-Ack+Poll frame, as also illustrated in Figure 71.  The node may send a data frame without a frame payload in that frame transaction.

A hub shall transmit an acknowledgment frame I-Ack or B-Ack when required, or I-Ack+Poll or B-Ack+Poll for another polled allocation, pSIFS after the end of the previous frame in a polled allocation.

In a type-I polled allocation granted to a connected node, the node may start another frame transaction, for retransmitting old frames or /and transmitting new frames, pSIFS after the end of the expected acknowledgment frame regardless of whether it received the acknowledgment frame. The node shall ensure that the frame transactions, including acknowledgment frames if required, in a polled allocation stay within the polled allocation interval, taking the appropriate guardtime into account.

In a type-II polled allocation granted to a connected node, the node shall not transmit more frames than granted for transmission via the preceding Poll frame or its variant, nor the node shall transmit any more frames after transmitting a frame requiring return of an I-Ack or B-Ack frame. The hub shall ensure in granting a type-II polled allocation that the frame transaction, including the acknowledgment frame if required, stays within the intended polled allocation interval, taking the appropriate guardtime into account.

Modifying a polled allocation

A hub may modify a polled allocation of a node by sending the node another poll through an I-Ack+Poll or B-Ack+Poll frame within the polled allocation that expands the allocation interval, effectively granting a new polled allocation in place of the existing one.

Aborting a polled allocation

A node may relinquish the remaining allocation interval of a polled allocation by indicating that it has no more data to transmit in the frame being transmitted and then by transmitting no more frames in the interval, or by requesting an immediate or block acknowledgment in case of a type-II polled allocation.

A hub shall not reclaim a polled allocation on the basis that it has not received any frame in the allocation, unless the node has explicitly relinquished the allocation as described above.

Ending a polled allocation

A node may at any time decline future type-I or type-II polled allocations to it by sending a modified Connection Request frame that contains a MAC Capability indicating no capability for the polling access of the corresponding type.

A hub may at any time decline future polled allocations to all the nodes connected with it by indicating no poll support in the MAC Capability of its subsequent beacons.

Posting access

A hub may send posts to a node while granting posted allocations outside the scheduled uplink allocations of the node, so long as it has informed the node of the pending posts through previously transmitted frames or if the node has indicated to be always active in its last transmitted MAC Capability field (i.e., with Always Active bit set to 1).

Starting a posted allocation

To obtain a posted allocation for receiving a post, a node that is not always active as indicated in its MAC Capability field and does not have a scheduled downlink allocation shall send at least one management or data type frame with the Ack Policy field set to I-Ack or B-Ack in each of its wakeup beacon periods (superframes). This enables the hub to inform the node, through an I-Ack or B-Ack frame as described in Table 20, of a specific time for sending the node a future post containing essential network management information or a critical user message.

To send an immediate post to a node, a hub shall set the More Data field to 1 in the non-beacon management or data type frame it is transmitting, as described in Table 20.  To send a future post to a node not always active, a hub shall send to the node an I-Ack or B-Ack frame when required to return an acknowledgment, as also described in Table 20.

Figure 72 illustrates instances of posts and posted allocations.

— Example posts and posted allocations

Using a posted allocation

A hub shall initiate frame transactions at the start of its posted allocations that have been announced in earlier frames as described in Table 20. The hub may send a data frame without a frame payload in that frame transaction.

A node shall receive posts and participate in the frame transactions in its posted allocations that have been indicated to it earlier through other frames. A node that has indicated to be always active shall be ready to receive posts at any time.

The node shall transmit an acknowledgment frame I-Ack or B-Ack when required, pSIFS after the end of the previous frame in a posted allocation. If the hub has announced in the current frame that it has another immediate post, it may initiate another frame transaction, for retransmitting old frames or/and transmitting new frames, pSIFS after the end of the expected acknowledgment frame regardless of whether it received the acknowledgment frame. The hub shall ensure that the frame transaction, including the acknowledgment frame if required, in a posted allocation stays within the intended posted allocation interval, taking the appropriate guardtime into account.

Modifying a posted allocation

A hub shall not modify a posted allocation once it initializes a frame transaction in the allocation, as a posted allocation is just long enough for a frame transaction. A hub may grant itself another posted allocation for initializing another frame transaction after informing the target node of the time of the new allocation through the current frame, or without pre-announcement if the target node is always active.

Aborting a posted allocation

A hub shall not abort a posted allocation once it initializes a frame transaction in the allocation.

Ending a posted allocation

A node shall not end a pending posted allocation nor potential future posted allocations, as it needs to receive all the posts—which might carry essential network management information or critical user messages—from the hub with which it is connected.

A hub should not end a pending posted allocation once it has announced it through a frame.

Scheduled access and variants (connection-oriented contention-free access)

As outlined in 7.3, a node and a hub may employ scheduled access to obtain scheduled uplink allocations and scheduled downlink allocations, scheduled-polling access to obtain scheduled bilink allocations and polled allocations therein, and delayed polling access to obtain delayed bilink allocations and polled allocations therein. Scheduled uplink allocations, scheduled downlink allocations, scheduled bilink allocations, and delayed bilink allocation, collectively referred to as scheduled allocations, may be 1-periodic or m-periodic allocations, except that a node shall not have both 1-periodic and m-periodic allocations in the same body area network (BAN).

To have a 1-periodic uplink or downlink allocation, which has one or more allocation intervals spanning the same allocation slots in every beacon period (superframe), the node shall wake up in every beacon period, i.e., the node shall treat all beacon periods as its wakeup beacon periods, as illustrated in Figure 73(a).

To have an m-periodic allocation, which has one or more allocation intervals spanning the same allocation slots in every m > 1 beacon periods (superframes), the node shall wakeup in the beacon periods containing those allocation intervals, i.e., the node shall treat those beacon periods as its wakeup beacon periods, as illustrated in Figure 73(b).

(a) Example 1-periodic allocation

(b) Example m-periodic allocation

— Scheduled uplink, downlink, bilink, and delayed bilink allocations

Starting scheduled allocations

To obtain one or more new scheduled allocations, a node shall send a Connection Request frame to the hub when permitted to do so, setting the Wakeup Period field in the frame to 1 for 1-periodic allocations and to m > 1 for m-periodic allocations. The node shall include in the frame

an Uplink Request IE if scheduled uplink allocations are needed;

a Downlink Request IE if scheduled downlink allocations are needed;

a Bilink Request IE if scheduled bilink allocations are needed;

a Delayed Bilink Request IE if delayed bilink allocations (i.e., scheduled bilink allocations that are subject to delay) are needed;

a Group Connection IE if the current connection request is made aggregately for a group of nodes.

In these IEs, the Minimum Length and Allocation Length fields, when present, shall have nonzero values.

To grant scheduled allocations, requested by the node or initiated by itself, the hub shall send a Connection Assignment frame to the node, including

an Uplink Assignment IE if scheduled uplink allocations are granted;

a Downlink Assignment IE if scheduled downlink allocations are granted;

a Bilink Assignment IE if scheduled bilink allocations are granted;

a Delayed Bilink Assignment IE if delayed bilink allocations are granted;

a Group Connection IE if the current connection assignment is made aggregately for a group of nodes.

In these IEs, the Interval Start and Interval End fields shall have nonzero values.

The hub may grant scheduled bilink allocations in lieu of delayed bilink allocations requested by the node, but not vice versa.

Using scheduled allocations

Upon receiving the Connection Assignment frame granting it scheduled uplink allocation intervals, the node may start initiating frame transactions with the hub therein, as illustrated in Figure 74. The hub shall be ready to receive the frames transmitted by the node and acknowledge them when appropriate during these allocation intervals.

Upon successfully sending the Connection Assignment frame granting the node scheduled downlink allocation intervals, the hub may start initiating frame transactions with the node therein, as also illustrated in Figure 74. The node shall be ready to receive the frames transmitted by the hub and acknowledge them when appropriate during these allocation intervals.

Upon successfully sending the Connection Assignment frame granting the node scheduled bilink allocation intervals, the hub may start initiating frame transactions with the node, or the hub may start sending to the node a poll granting an immediate polled allocation for the node to initiate one or more frame transactions therein, in these allocation intervals, as illustrated in Figure 75. The poll should be a Poll frame if it is sent at the start of the scheduled bilink allocation or if the hub does not need to provide a time reference update to the node, or should be a T-Poll frame otherwise. The node shall not initiate a frame transaction, until it receives a Poll or T-Poll frame, in a bilink allocation interval. The recipient, the node or the hub, shall be ready to receive the frames transmitted by the sender and return appropriate frames during the allocation intervals.

Upon successfully sending the Connection Assignment frame granting the node delayed bilink allocation intervals, the hub may start initiating frame transactions with the node, or the hub may start sending to the node a poll granting an immediate polled allocation for the node to initiate one or more frame transactions therein, in these allocation intervals, as illustrated in Figure 76. The poll should be a Poll frame if it is sent at the start of the scheduled bilink allocation or if the hub does not need to provide a time reference update to the node, or should be a T-Poll frame otherwise. The hub may delay its first frame transmission to the node up to the maximum delay from the start of the delayed bilink allocation interval as specified in the connection assignment. If the hub fails to send a frame to the node within the maximum delay, the hub shall not send a frame to the node in the interval. The node shall not initiate a frame transaction, until it receives a Poll or T-Poll frame, in a delayed bilink allocation interval. The recipient, the node or the hub, shall be ready to receive the frames transmitted by the sender and return appropriate 
frames during the allocation intervals. If the node fails to receive a frame addressed to it within the maximum delay of the start of the interval from the hub, it may be in sleep state in the remaining interval.

The node or the hub shall transmit next frame pSIFS after the end of the current frame. The node or the hub may initiate another frame transaction in the remaining scheduled uplink or downlink allocation interval, respectively, pSIFS after the end of the expected acknowledgment frame regardless of whether it received the acknowledgment frame. In the remaining scheduled bilink allocation interval, after the end of the preceding frame transactions initiated by the hub or after the end of the preceding polled allocation interval, the hub may initiate more frame transactions with the node, or the hub may send to the node another poll granting another immediate polled allocation for the node to initiate one or more frame transactions therein.

The node and the hub shall ensure that the frame transactions, including acknowledgment frames if required, stay within their scheduled uplink or downlink allocation intervals, respectively, taking the appropriate guardtime into account. The hub shall ensure that the frame transactions, including acknowledgment frames if required, stay within the scheduled bilink allocation intervals, also accounting for the appropriate guardtime. The hub shall ensure that the frame transactions, including acknowledgment frames if required, stay within the delayed bilink allocation intervals or till the maximum delay applicable to the next delayed bilink allocation interval that follows immediately, also accounting for the appropriate guardtime.

In a type-I polled allocation interval, the node shall ensure that the frame transactions, including acknowledgment frames if required, stay within the polled allocation intervals. In a type-II polled allocation interval, the node shall not transmit more frames than granted for transmission therein or after it has requested an I-Ack or B-Ack frame for acknowledgment.

In a scheduled uplink allocation interval, the node may through its current data type frame indicate no more data for transmission in the remaining interval. In a scheduled downlink allocation interval, a scheduled bilink allocation interval, or a delayed bilink allocation interval, the hub may send a data type frame indicating no more data with or without frame payload to indicate no more transmissions in the remaining interval; the node may enter sleep state accordingly in the remaining interval.

— Example scheduled allocation intervals – Frame transactions in scheduled uplink allocation interval and scheduled downlink allocation interval

Example scheduled allocation intervals – Frame transactions in scheduled bilink allocation intervals

— Example scheduled allocation intervals – Frame transactions in delayed bilink allocation intervals

Modifying scheduled allocations

A node may modify existing scheduled allocations by sending another Connection Request frame specifying the new requirements. The hub shall treat this request as a new one, except that it shall set the Connection Change Indicator field in its responding Connection Assignment frame with reference to the last Connection Assignment frame it sent to the node. In particular, if the hub rejects the modifications but maintains the existing allocations, it shall respond with a Connection Assignment frame with the Connection Change Indicator field set to 0 and the other fields kept to the respective values contained in the last Connection Assignment frame sent to the node.

A hub may, but should not where possible, modify scheduled allocations of a node on its own by sending the node an unsolicited Connection Assignment frame specifying the new assignments to those allocations, setting the Connection Change Indicator field in the frame with reference to the last Connection Assignment frame it sent to the same node.

Aborting scheduled allocations

A node may relinquish the remainder of a scheduled uplink allocation interval by indicating that it has no more data to transmit in the frame being transmitted and then by transmitting no more frames in the interval.

A hub shall not reclaim a scheduled uplink allocation interval on the basis that it has not received any frame in that specific allocation interval, unless the node has explicitly relinquished the allocation interval as described above.

A node or a hub shall treat an existing scheduled allocation to have been aborted after failing to receive any frame in the last mScheduledAllocationAborted allocation intervals of the allocation. Subsequently, the hub may reclaim the aborted scheduled allocations.

A node or a hub shall transmit at least one frame requiring an immediate return of a frame, such as an I-Ack or B-Ack frame, or a poll if applicable, in every allocation interval of a scheduled allocation so as to reduce the chance of experiencing an abortion of the scheduled allocation.

A node and a hub may start a new scheduled allocation procedure as specified in Figure 73 to reinstate their lost scheduled allocations or obtain their replacements.

A node or a hub shall treat their connection to have been aborted after all the scheduled allocations of the node with the hub have been aborted.

Ending scheduled allocations

A node may at any time end scheduled allocations by sending a modified Connection Request frame that contains Allocation Request fields with the Allocation ID fields identifying those allocations and with the corresponding Minimum Length and Allocation Length fields both set to 0.

A hub may, but should not where possible, at any time end any scheduled allocations of a node by sending the node a modified Connection Assignment frame that contains Allocation Assignment fields with the Allocation ID fields identifying those allocations and the Interval Start and Interval End fields set to 0.

A node or a hub shall not send a frame in an already ended scheduled allocation.

A node or a hub may send a Disconnection frame to end their connection, i.e., to void the node’s Connected_NID, wakeup arrangement, and scheduled allocations with the hub.

MICS band communication

In the medical implant communications service (MICS) band, a hub shall operate in non-beacon mode with or without superframe boundaries as specified in 7.3. The hub may choose a new channel only when required by, and in compliance with, applicable regulations and considerations. An implant shall communicate as a node with a hub. The hub and the node may perform a mutual discovery procedure described below immediately before their frame exchanges.

Unconnected mutual discovery

A hub may facilitate mutual discovery with unconnected nodes and connection with them as follows.

As illustrated in Figure 77, every pMICSUnconnectedPollPeriod or shorter the hub shall transmit a group of up to pMICSUnconnectedPolls unconnected T-Poll frames separated by pMICSUnconnectedPollSeparation. The hub shall listen for a frame arrival after each transmission and before the next transmission of such an unconnected T-Poll frame. An unconnected T-Poll frame is a T-Poll frame addressed to Unconnected_Broadcast_NID as defined in Table 16 and providing an unconnected polled allocation as specified in 7.4.

An unconnected node in need of a connection may discover a hub as follows.

The unconnected node should cyclically tune to each MICS band channel for pMICSUnconnectedPollRxTime, until it receives an unconnected T-Poll frame and hence discovers a hub. Once it starts receiving a frame, it should stay on the receive mode until it receives the whole frame.  The unconnected node should not further change the channel unless recommended otherwise.

— Unconnected mutual discovery and frame exchange in MICS band

The pMICSUnconnectedPollPeriod parameter value is obtained as a result of an overall consideration of connection latency, power consumption, channel utilization efficiency, interference, and other factors. The parameter pMICSUnconnectedPolls has a value designed to provide enough unconnected T-Poll frames so that a node can receive one of them within a cycle of tuning to each of the MICS band channels. The parameter pMICSUnconnectedPollSeparation has a value such that the hub can detect a frame sent by a node following its last unconnected T-Poll frame before it would otherwise send the next unconnected T-Poll frame. The parameter pMICSUnconnectedPollRxTime has a value to ensure with a certain margin that a node can receive one of the two adjacent unconnected T-Poll frames once it tunes to the transmit channel.

Now that the hub and the unconnected node are on the same channel, they are in a position to follow the connection setup procedure specified in 7.4 to exchange management type frames necessary for a connection, including a wakeup arrangement and scheduled allocations as appropriate. The hub should provide the node with an ordered list of channels it intends to choose in decreasing likelihood when required to choose a new channel. The hub should subsequently select a new channel, when required by and in compliance with the regulations, in the order indicated in the list. The hub may update nodes with a new channel order list in view of changes in the channel conditions such as interference levels or/and based on other considerations.

Connected mutual discovery

A hub may facilitate mutual discovery with connected nodes immediately prior to frame exchanges with them, based on any or a combination of the following discovery procedures.

Unicast poll aided discovery

As illustrated in Figure 78, prior to more frame exchanges with a connected node, the hub shall transmit a group of up to pMICSPolls Poll frames separated by pMICSPollSeparation, each addressed to the node and providing an immediate polled allocation. The hub shall listen for a frame arrival after each transmission and before the next transmission of such a Poll.

The connected node shall be in active mode in anticipation of pending frame exchanges with the hub by scheduling or other means, accounting for the appropriate guardtime. It should tune to the channel in which it last received a frame with a valid FCS from the hub for pMICSPollSeparation + pMICSPollRxTime to receive a Poll frame.  If it does not receive a Poll frame, it should change to another channel.  After dwelling on the current channel for pMICSPollRxTime, it should switch to yet another channel in accordance with the channel order last provided by the hub, until it receives a Poll frame addressed to it. The node should not further change the channel unless recommended otherwise.

— Unicast poll aided connected discovery and frame exchange in MICS band

Now that the hub and the unconnected node are on the same channel, they are in a position to exchange more frames with each other using appropriate access methods as specified in 7.6 and 7.7 in view of 7.3.

While cycling through the MICS band channels for mutual discovery with the hub, upon receiving a Poll frame sent by the hub but not addressed to them on a channel, nodes should skip that channel from their subsequent channel cycling for the duration of the polled allocation granted via the Poll frame.

Multicast poll aided discovery

As illustrated in Figure 79, prior to more frame exchanges with a group of connected nodes, the hub shall transmit a group of up to pMICSMcastPolls Poll frames forming a lockup phase and separated by pMICSMcastPollSeparation, each addressed to the Multicast_NID of the group and providing no immediate polled allocation but announcing a future poll starting at the intended beginning of the first individual communication phase with a node of the group. In particular, the time of the future poll is encoded according to Table 20.

The hub shall transmit a poll addressed to a node of the group at the indicated future poll time and providing an immediate polled allocation, thus starting the individual phase for the node as also illustrated in Figure 79.

The connected nodes of the group should be in active mode in anticipation of pending frame exchanges with the hub by scheduling or other means, accounting for the appropriate guardtime. Each of them should tune to the channel in which it last received a frame with a valid FCS from the hub. After dwelling on the current channel for pMICSMCastPollRxTime, each should switch to another channel in accordance with the channel order last provided by the hub, until it receives a Poll frame addressed to the Multicast_NID of its group. It should not further change the channel unless recommended otherwise. It may enter sleep state until the start of the first individual phase as announced in the received Poll frame, when it should be in active state to receive a unicast Poll frame.

— Multicast poll aided connected discovery and frame exchange in MICS band

Now that the hub and the connected nodes of the group are on the same channel, they are in a position to exchange more frames with each other using appropriate access methods as specified in 7.6 and 7.7 in view of 7.3.

Medical implant event report

When not transmitting, a hub should stay on receive mode in the channel selected according to its channel order list communicated to the nodes connected with it.

A node connected with a hub may transmit frames reporting a medical implant event in its next scheduled bilink allocation interval, if available, following a Poll or T-Poll frame granting an immediate polled allocation to it by the hub, using the a connected mutual discovery procedure as specified in 7.8.2

The node may also transmit such frames anytime as illustrated in Figure 80. Before discovering the hub’s operating channel, the node should send Emergency frames without a frame payload to reduce the transmission times of the frames which will not be received by the hub. In particular, the node should transmit an Emergency frame with no frame payload and with the Ack Policy field set to I-Ack, in the first channel of the channel order list last communicated to it by the hub. It should retry the frame for up to pMICSNodeEmergencyRetries times on this channel upon failing to receiving an expected acknowledgment. If it still receives no acknowledgment, it should similarly send and retry the frame in the next MICS channel on the channel order list, and again in another channel, until it receives an expected I-Ack frame or pauses its transmission.  The node shall space one data frame and the next as if an I-Ack frame were received in between.

After receiving an I-Ack frame, it should proceed to transmit the Emergency frames (with incremental sequence numbers) containing frame payloads generated from the medical implant event. The node shall set to 1 the More Data field in the MAC header of these Emergency frames except the last one, and shall set to 0 the More Data field in the MAC header of that last frame to indicate the end of the medical event report transfer.

On receiving an Emergency frame with More Data field set to 1 from the node, the hub should not initiate its own frame transactions with this node or another one until it has received all Emergency frames as indicated by the More Data field value.

— Medical implant event report outside scheduled allocations in MICS band

After retrying a frame for up to pMICSHubMaxRetries without receiving an expected response, the hub should enter the receive mode to receive possible Emergency frames.

Two-hop star topology extension

A node and a hub may use a two-hop extension to exchange frames through another node that is connected and capable of direct communication with both of them, as illustrated in Figure 81, turning the terminal and intermediate nodes into the relayed and relaying nodes, respectively, and the hub into the target hub of the relayed node.

Either the relayed node or the target hub may initiate a two-hop extension at times determined fit by the initiator, regardless of whether they have been never, or are no longer, in direct communication with each other.

The relaying node may also exchange its own frames with the hub directly just as in a one-hop star network.

— Two-hop extended star network topology

Exchanging frames for a two-hop extension

The relayed node and the target hub may exchange unicast management or data, but not control, type frames through the relaying node by frame encapsulation as illustrated in Figure 82 and described below.  The relayed node, the relaying node, and the target hub shall not apply frame encapsulation to control type frames, such as I-Ack frames.

(a) Transmission of management or data type frames from relayed node through relaying node to target hub

(b) Transmission of management or data type frames from target hub through relaying node to relayed node (except Connection Assignment frames)

(c) Transmission of Connection Assignment frames from target hub to relaying node and relayed node

— Management or data type frame exchanges on a two-hop extension

The relayed node and the target hub shall follow the state diagram specified in 5.5 for a one-hop star network in exchanging encapsulated frames through the relaying node, as if they were in direct communication, applying the appropriate security level for both transmission and reception of the encapsulated frames.

The relaying node and the target hub shall follow the state diagram specified in 5.5 for a one-hop star network in exchanging frames, encapsulated or not, as if the relaying node were a non-relaying node, applying the appropriate security level for both transmission and reception of the frames.

The relayed node and the relaying node shall follow the state diagram specified in 5.5 for a one-hop star network in exchanging frames, encapsulated or not, as if the relaying node were a hub, applying the appropriate security level for both transmission and reception of the frames, with the followings exceptions:  To exchange frames for a two-hop extension, they shall not be connected with each other in the way a node and a hub would be in a one-hop star network, i.e., they shall not exchange with each other Connection Request and Connection Assignment frames not encapsulating another frame.

Frame transmission from relayed node through relaying node to target hub

To send a management or data type frame, designated as an encapsulated “X” frame, through the relaying node to the target hub as shown in Figure 82(a), the relayed node shall send to the relaying node an encapsulating “X” frame, wherein

the Recipient ID is set to the NID of the relaying node;

the Relay field of the MAC header is set to 1;

the other fields of the MAC header are set as if the relaying node were a hub and the relayed node were sending the encapsulated “X” frame to that hub without frame encapsulation in a one-hop star network, e.g., the Frame Type and Frame Subtype fileds are set to the corresponding values of their counterparts in the encapsulated “X” frame;

the frame payload is set to the encapsulated “X” frame, which is formatted as if the relayed node were sending the encapsulated “X” frame directly to the target hub for the first time in a one-hop star network, with the Recipient ID field of the MAC header set to 0 if the relayed node does not yet know the NID of the target hub.

Upon receiving an encapsulating “X” frame, i.e., a management or data type frame with the Relay field of the MAC header set to 1, the relaying node shall process the frame according to 7.2 specified for a one-hop star network with the following additional considerations:

The Sender ID of the MAC header is set to the NID of the relayed node.

The frame is not a duplicate of another frame with the Relay field of the MAC header set to 0 even if it would be otherwise treated as a duplicate according to 7.2.10 specified for a one-hop star network.

The frame payload, after appropriate security is applied, is an encapsulated “X” frame.

The Relay field of the MAC header of the required I-Ack frame is set to 1 if relay is feasible, or is set to 0 otherwise.

If relay is feasible, i.e., if the relaying node is capable of providing relay between the relayed node and the target hub and if the target hub is capable of being a relayed hub as indicated in its MAC Capability field, the relaying node shall send to the target hub an encapsulating “X” frame, wherein

the Relay field of the MAC header is set to 1;

the other fields of the MAC header are set as if the relaying node were sending the encapsulated “X” frame to the hub without frame encapsulation in a one-hop star network;

the frame payload is set to the encapsulated “X” frame to be next relayed to the target hub.

Upon receiving an encapsulating “X” frame, i.e., a management or data type frame with the Relay field of the MAC header set to 1, the target hub shall process the frame according to 7.2 specified for a one-hop star network with the following additional considerations:

The frame is not a duplicate of another frame with the Relay field of the MAC header set to 0 even if it would be otherwise treated as a duplicate according to 7.2.10 specified for a one-hop star network.

The frame payload, after appropriate security is applied, is an encapsulated “X” frame.

The Relay field of the MAC header of the required I-Ack frame is set to 1 if it is capable of being a relayed hub as announced in its MAC Capability field, or is set to 0 otherwise.

Frame transmission from target hub through relaying node to relayed node

To send a management or data type frame, designated as an encapsulated “Y” frame, through the relaying node to the relayed node as shown in Figure 82(b), the target hub shall send to the relaying node an encapsulating “Y” frame, wherein

the Relay field of the MAC header is set to 1;

the other fields of the MAC header are set as if the target hub were sending the encapsulated “Y” frame to the relaying node without frame encapsulation in a one-hop star network;

the frame payload is set to the encapsulated “Y” frame, which is formatted as if the target hub were sending the encapsulated “Y” frame directly to the relayed node for the first time in a one-hop star network.

Upon receiving an encapsulating “Y” frame, i.e., a management or data type frame with the Relay field of the MAC header set to 1, the relaying node shall process the frame according to 7.2 specified for a one-hop star network with the following additional considerations:

The frame is not a duplicate of another frame with the Relay field of the MAC header set to 0 even if it would be otherwise treated as a duplicate according to 7.2.10 specified for a one-hop star network.

The frame payload, after appropriate security is applied, is an encapsulated “Y” frame.

The Relay field of the MAC header of the required I-Ack frame is set to 1 if relay is feasible or is set to 0 otherwise.

If relay is feasible, i.e., if the relaying node is capable of providing relay between the target hub and the relayed node, the relaying node shall send to the relayed node an encapsulating “Y” frame, wherein

the Recipient ID field of the MAC header is set to the NID of the relayed node, i.e., the Recipient ID of the MAC header of the encapsulated “Y” frame;

the Sender ID field of the MAC header is set to the NID of the relaying node;

the Relay field of the MAC header is set to 1;

the other fields of the MAC header are set as if the relaying node were a hub and sending the encapsulated “Y” frame to the relayed node without frame encapsulation in a one-hop star network;

the frame payload is set to the encapsulated “Y” frame to be next relayed to the relayed node.

Upon receiving an encapsulating “Y” frame, i.e., a management or data type frame with the Relay field of the MAC header set to 1, the relayed node shall process the frame according to 7.2 specified for a one-hop star network with the following additional considerations:

The Sender ID field of the MAC header is set to the NID of the relaying node.

The frame is not a duplicate of another frame with the Relay field of the MAC header set to 0 even if it would be otherwise treated as a duplicate according to 7.2.10 specified for a one-hop star network.

The frame payload, after appropriate security is applied, is an encapsulated “Y” frame.

The Relay field of the MAC header of the required I-Ack frame is set to 1 if it is capable of being a relayed node as announced in its MAC Capability field, or is set to 0 otherwise.

Connection assignment from target hub to relaying node and relayed node

To specify connection assignment for a two-hop extension involving a relaying node and a relayed node as shown in Figure 82(c), the target hub shall send two encapsulated Connection Assignment frames 1 and 2 in two encapsulating Connection Assignment frames 1 and 2 to the relayed node and the relaying node, respectively, as further described below.

Connection assignment from target hub through relaying node to relayed node

To send encapsulated Connection Assignment frame 1 through the relaying (capable) node to the relayed node as shown in the upper diagram of Figure 82(c), the target hub and the relaying node shall follow the frame transmission procedure for “Y” Connection Assignment frame = Connection Assignment frame 1 as described in Figure 82(b) and 7.9.1.2, with the following modifications made to the frame payload of encapsulated Connection Assignment frame 1:

the MAC Capability and PHY Capability fields are set to those for the relaying node;

the Connection Change Indicator field is set such that it accounts for all the included IEs defining both hops;

after each Uplink Assignment, Downlink Assignment, or Bilink Assignment IE defining the assignment of scheduled allocations applicable between the target hub and the relaying node for the two-hop extension, another Uplink Assignment, Downlink Assignment, or Bilink Assignment IE is inserted defining the assignment of scheduled allocations applicable between the relaying node and the relayed node for the corresponding two-hop extension, with the relaying node considered as a hub for link direction referencing purposes.

Connection assignment from target hub to relaying node

To send encapsulated Connection Assignment frame 2 to the relaying (capable) node as shown in the lower diagram of Figure 82(c), the target hub shall send to the relaying node encapsulating Connection Assignment frame 2, wherein

the Relay field of the MAC header is set to 1;

the other fields of the MAC header are set as if the target hub were sending encapsulating Connection Assignment frame 2 to the relaying node without frame encapsulation in a one-hop star network;

the frame payload is set to encapsulated Connection Assignment frame 2, which is formatted as if the target hub were sending the frame directly to the relaying node for the first time in a one-hop star network, with some modifications to support the two-hop extension.

In particular, encapsulated Connection Assignment 2 is formatted with the following modifications:

In the MAC header, the Sender ID field is set to the NID of the relayed node to indicate that the connection assignment is for a two-hop extension to the relayed node.

In the frame payload,

the MAC Capability and PHY Capability fields are set to those for the relayed node if they are known to the target hub, or are set to zero otherwise;

the Connection Change Indicator field is set such that it accounts for all the included IEs defining both hops;

after each Uplink Assignment, Downlink Assignment, or Bilink Assignment IE defining the assignment of scheduled allocations applicable between the target hub and the relaying node for the two-hop extension, another Uplink Assignment, Downlink Assignment, or Bilink Assignment IE is inserted defining the assignment of scheduled allocations applicable between the relaying node and the relayed node for the corresponding two-hop extension, with the relaying node considered as a hub for link direction referencing purposes.

Upon receiving encapsulating Connection Assignment frame 2 as defined in the above, the relaying node shall process the frame according to 7.2 specified for a one-hop star network, taking into account the above modifications.

The relaying node shall not send to the relayed node another encapsulating Connection Assignment frame with the frame payload set to encapsulated Connection Assignment frame 2, after it has already sent to the relayed node an encapsulating Connection Assignment frame with the frame payload set to encapsulated Connection Assignment frame 1.

Control type frame transmission without frame encapsulation

The target hub may send a control type frame to the relaying node so long as a hub may send the frame to a node in a one-hop star network, with the modification that in the MAC header the Relay field is set to 1 or 0 depending on whether relay is involved and feasible.

The relaying node may send a control type frame to the target hub so long as a node may send the frame to a hub in a one-hop star network, with the modification that in the MAC header the Relay field is set to 1 or 0 depending on whether relay is involved and feasible.

The relaying node may send a control type frame to the relayed node so long as a hub may send the frame to a node in a one-hop star network, with the modification that in the MAC header

the Relay field is set to 1 or 0 depending on whether relay is involved and feasible;

the Recipient ID field is set to the NID of the relayed node;

the Sender ID field is set to the NID of the relaying node.

Upon receiving a control type frame, the recipient shall process the frame according to 7.2 specified for a one-hop star network with the additional considerations as noted above in defining the frame.

Selecting a relaying node for a two-hop extension

Either the relayed node or the target hub may select their relaying node through prearrangement.

The relayed node may also select node B as its relaying node if it recently received acknowledgment frames sent from node B to the target hub.  The relayed node may receive such acknowledgment frames based on the frame reception rules specified in 7.2.4, with appropriate exceptions given to the values of the Recipient ID and Sender ID fields of the MAC header of the frames.

The relayed node may alternatively select node C as its relaying node if it recently received T-Poll frames locally broadcast by node C.  The relayed node shall not select more than one node as its relaying node at any given time.

In selecting the relaying node, the relayed node should take into account the quality of the links between itself and the relaying node and between the relaying node and the target hub.

A relaying node in emergency, i.e., with pending Emergency frames to send, may recognize whether the relayed nodes to which it is providing relay are in emergency through receipt of Emergency frames from them.  Such a relaying node may continue or discontinue its relay service to relayed nodes that are not in emergency and to which it is providing relay, by taking into account such factors as quality of service, level of traffic load, and availability of power.  The relayed nodes relaying through a relaying node in emergency may attempt to relay through an alternative relaying capable node not in emergency to reduce the load on the relaying node.  A relaying node in emergency may accept or decline to provide relay to nodes newly requesting for relay, depending on whether the requesting nodes are in emergency, the number of relayed nodes that are in emergency and to which it is providing relay, etc.

Using broadcast T-Polls for a two-hop extension

To facilitate a two-hop extension for relayed nodes, a relaying node may obtain a scheduled uplink allocation in accordance with 7.7 to be used as described below and illustrated in Figure 83, setting the user priority of the allocation request to that for controlled load as defined in Table 17.

— Scheduled uplink allocation                                                                                          for relaying node to send broadcast T-Polls and relay frames

In the scheduled uplink allocation, the relaying node shall locally broadcast T-Poll frames formatted as if it were sending them as a hub, with the modifications that in the MAC header

the Relay field is set to 1;

the Recipient ID field is set to Local_Broadcast_NID

the Sender ID field is set to the NID of the relaying node.

Via such a T-Poll frame, the relaying node may provide either no or an immediate (shared) polled allocation within the scheduled uplink allocation, facilitating the selection of a relaying node and the synchronization with the target hub by potential relayed nodes, as well as offering the latter a frame transmission opportunity for frame relay to the target hub.

In the scheduled uplink allocation, the relaying node may also send to the hub or relayed nodes frames it has received from relayed nodes or the hub for further transmission to the hub or relayed nodes, respectively.

A relayed node that does not directly receive beacons from the target hub should indirectly synchronize with the hub through reception of T-Poll frames sent by a relaying node in the same body area network (BAN).

A relayed node may send at most a frame to the relaying node in a shared polled allocation, initially with contention probability P = 1/2.  If the relayed node does not receive an expected acknowledgment from the relaying node, it may retry it in the shared polled allocation conveyed by another such T-Poll frame locally broadcast by the relaying node, with contention probability P = max(1/8, (1/2) / ((R+1)/2(), where R counts the retries of the frame, i.e., R equals 1 for the first retry of the frame, 2 for the second retry, and so on. The function (x( is defined to be the least integer not smaller than x. With contention probability P, the relayed node shall transmit if z ≤ P, where z is a value the relayed node has newly drawn at random from the interval [0, 1].

A relayed node may also send its frames to the relaying node in contended allocations it obtains according to 7.5 in a random access phase (RAP) or contention access phase (CAP) provided by the target hub, provided it knows their locations such as through previously received beacons and its clock drift relative to the hub since its last direct synchronization with the hub is still within the appropriate guard time.

A relayed node shall not send a frame in a polled or contended allocation if the frame transmission and the expected acknowledgment plus pSIFS would not be located within the allocation.  A relaying node should not provide an immediate shared polled allocation that is not adequately long.

A node willing to serve as a relaying node as announced in its MAC capability field should be ready to receive frames from relayed nodes during the RAPs and CAPs when it is not transmitting.

A relayed node should send only management type or control type frames in shared polled allocations or contended allocations.  To transmit data type frames, it should obtain scheduled allocations for its two-hop extension.

Using improvised access for a two-hop extension

The target hub and the relaying node may obtain improvised polled and posted allocations according to 7.6.2, as if they were a hub and a node, respectively, in a one-hop star network, to exchange data or management type frames originated from or destined to the relayed node.

The relaying node and the relayed node may obtain improvised polled and posted allocations in the scheduled uplink allocations applicable between the target hub and the relaying node according to 7.6.2, as if they were a hub and a node, respectively, in a one-hop star network, to exchange data or management type frames originated from or destined to the target hub.

Starting scheduled allocations for a two-hop extension

Either the relayed node or the target hub may initiate scheduled allocations for a two-hop extension as illustrated in Figure 84, which also shows equivalent one-hop scheduled allocations, regardless of whether the latter have been obtained.

— Equivalent one-hop and two-hop scheduled allocations

Allocation request for a two-hop extension

To obtain scheduled allocations for a two-hop extension, the relayed node shall send an encapsulated Connection Request frame through the relaying node to the target hub, as illustrated in Figure 82(a) and specified in 7.9.1.1.

In this frame, the relayed node shall include an Uplink Request IE, a Downlink Request IE, or/and a Bilink Request IE specifying equivalent scheduled allocation(s) applicable between the relayed node and the target hub in a one-hop star network, setting the Allocation ID field of each Allocation Request field of these IEs to the Allocation ID value identifying the corresponding one-hop scheduled allocation if it currently holds the latter.

Allocation assignment for a two-hop extension

To grant scheduled allocations for a two-hop extension, requested by the relayed node or initiated by itself, the target hub shall send an encapsulated Connection Assignment frame to the relaying node, which shall subsequently send the frame upon some modifications to the relayed node, as illustrated in Figure 82(c) and specified in 7.9.1.3.

In this frame, the target hub shall include appropriate Uplink Assignment IEs, Downlink Assignment IEs, or/and Bilink Assignment IEs specifying the two-hop scheduled allocations with the following matches to the corresponding one-hop scheduled allocations:

Each allocation applicable between the target hub and the relaying node for the two-hop extension has the same allocation direction (i.e., uplink for uplink, downlink for downlink, and bilink for bilink), and approximately the same total allocation length, as the equivalent allocation applicable between the target hub and the relayed node in a one-hop star network.

Each allocation applicable between the relaying node and the relayed node for the two-hop extension has a bilink allocation direction and more total allocation length than the equivalent allocation applicable between the target hub and the relayed node in a one-hop star network, with the additional allocation length provided for T-Poll frame transmissions by the relaying hub.

The target hub should take into account the overall latency that results from a two-hop extension in specifying the two-hop scheduled allocation intervals.

Using scheduled allocations for a two-hop extension

Upon successful transmission of the encapsulating Connection Assignment frame from the target hub to the relaying node, the target hub and the relaying node shall use their scheduled allocations conveyed in the encapsulated Connection Assignment frame according to 7.7.2, as if they were a hub and a node, respectively, in a one-hop star network, to exchange data, and occasionally management, type frames originated from or destined to the relayed node.

Upon successful transmission of the encapsulating Connection Assignment frame from the relaying node to the relayed node, the relaying node and relayed node shall use their scheduled bilink allocations conveyed in the encapsulated Connection Assignment frame according to 7.7.2, as if they were a hub and a node, respectively, in a one-hop star network, to exchange data type frames originated from or destined to the target hub.  The relaying node should send one or more T-Poll frames to the relayed node in each allocation interval of the bilink allocations, and the relayed node should perform its clock synchronization based on received T-Poll frames.

Modifying scheduled allocations for a two-hop extension

The relayed node and the target hub may modify their two-hop scheduled allocations via another exchange of Connection Request or/and Connection Assignment frames according to 7.7.3, as if they were a node and a hub in a one-hop star network, with additional considerations based on the modified definition in 7.9.1.3 of the Connection Assignment frames for a two-hop extension.

Aborting scheduled allocations for a two-hop extension

The target hub and the relaying node shall abort their two-hop scheduled allocations according to 7.7.4, as if they were a hub and a node in a one-hop star network.  Subsequently, the hub may reclaim the aborted scheduled allocations.

Once the relaying node aborts its two-hop scheduled allocations applicable with the target hub, it shall abort its two-hop scheduled allocations applicable with the relayed node as well.

The relaying node and the relayed node shall abort their two-hop scheduled allocations according to 7.7.4, as if they were a hub and a node, respectively, in a one-hop star network.

The target hub, the relaying node, and the relayed node shall respectively transmit at least one frame requiring an immediate return of a frame in every allocation interval of their two-hop scheduled allocations allowing for such a transmission, so as to reduce the chance of experiencing an abortion of their two-hop scheduled allocations, as also specified in 7.7.4 for one-hop star network.

Ending scheduled allocations for a two-hop extension

The relayed node or the target hub may initiate to end their two-hop scheduled allocations at any time the initiator determines fit, in exchange for or without regaining equivalent one-hop scheduled allocations.

The relaying node may end the two-hop scheduled allocations applicable between a relayed node and the target hub by setting to 0 the Relay field of the MAC header of a required I-Ack frame in response to a frame received from the relayed node or the target hub, when it determines that its relay between them is no longer feasible.  The relaying may, and should, keep the two-hop scheduled allocations, if any, applicable between another relayed node and the target hub, so long as its relay between them is feasible and desirable.

A relayed node, a relaying node, or a target hub shall not send a frame in an already ended scheduled allocation.

In exchange for equivalent one-hop scheduled allocations

To request for replacing the two-hop scheduled allocations with equivalent one-hop scheduled allocations, the relayed node shall send a Connection Request frame directly to the target hub as in a one-hop star network, where the frame specifies the one-hop scheduled allocations using the Allocation IDs for the two-hop scheduled allocations.   The relayed node should send the frame in a scheduled allocation applicable between itself and the relaying node.

To replace the two-hop scheduled allocations with equivalent one-hop scheduled allocations, in response to a request from the relayed node as described in the above or to its own decision, the target hub shall send to

the relaying node an encapsulated Connection Assignment frame formated to end the two-hop scheduled allocations as described in 7.7.5, and

the relayed node directly a Connection Assignment frame formated to specify the granted one-hop scheduled allocations in a one-hop star network.

The target hub should send the encapsulated Connection Assignment frame to the relaying node in a scheduled allocation applicable between itself and the relaying node.  The target hub should send the Connection Assignment frame directly to the relayed node in a scheduled allocation currently or previously applicable between the relaying node and the relayed node.

Without regaining equivalent one-hop scheduled allocations

To request for ending the two-hop scheduled allocations without regaining equivalent one-hop scheduled allocations, the relayed node shall send a Connection Request frame directly to the target hub as in a one-hop star network, where the frame is formatted to end the equivalent one-hop allocations as described in 7.7.5.  The relayed node should send the frame in a scheduled allocation applicable between itself and the relaying node.

To end the two-hop scheduled allocations without regaining equivalent one-hop scheduled allocations, in response to a request from the relayed node as described in the above or to its own decision, the target hub shall send to the relaying node an encapsulated Connection Assignment frame formatted to end the two-hop scheduled allocations as described in 7.7.5; the relaying node shall subsequently send to the relayed node the encapsulated Connection Assignment frame with the modifications as specified in 7.9.1.3.

The target hub should send the encapsulated Connection Assignment frame to the relaying node in a scheduled allocation applicable between itself and the relaying node.  The relaying node should send the Connection Assignment frame to the relayed node in a scheduled allocation applicable between the relaying node and the relayed node.

Clock synchronization and guardtime provisioning

A node or a hub shall maintain a clock with a minimum resolution of mClockResolution and with a minimum accuracy of mClockAccuracy to time its frame transmission and reception.

A node or a hub shall time its transmission and reception in any of its allocation intervals according to its local clock, setting aside appropriate guardtimes as specified below and illustrated in Figure 85 and Figure 86:

The hub shall commence its beacon transmission at the nominal start of the beacon transmission.

The hub shall commence its transmission in a downlink allocation interval at the nominal start of the interval, and the hub shall end its transmission in the interval early enough such that the last transmission in the interval completes at least a guardtime of GTn prior to the nominal end of the interval.

The hub shall commence its reception in an uplink allocation interval at least GTn prior to the nominal start of the interval.

If a node’s last synchronization to the hub was less than SIn ago at the nominal start of its next uplink allocation interval, the node shall commence its transmission in the interval at that nominal start time, and the node shall end its transmission in the interval early enough such that the last transmission in the interval completes at least a guardtime of GTn prior to the nominal end of the interval.

If a node’s last synchronization to the hub was less than SIn ago at the nominal start of the next beacon transmission, the node shall commence its reception of the beacon at least GTn prior to that nominal start time.

If a node’s last synchronization to the hub was less than SIn ago at the nominal start of its next scheduled downlink or bilink allocation interval, the node shall commence its reception in the interval at least GTn prior to that nominal start time.

If a node’s last synchronization to the hub was SIn + SIa ago at the nominal start of its next scheduled uplink allocation interval, the node shall commence its transmission in the interval a guardtime of GTa later than that nominal start time, and the node shall end its transmission in the interval early enough such that the last transmission in the interval completes at least a guardtime of GTn + GTa prior to the nominal end of the interval.

If a node’s last synchronization to the hub was SIn + SIa ago at the nominal start of its next scheduled downlink or bilink allocation interval, the node shall commence its reception in the interval at least GTn + GTa earlier than that nominal start time.

(a) Nominal guardtime

(b) Additional guardtime and nominal guardtime

— Example of guardtimes

A node shall synchronize to its hub through the beacons, T-Poll frames, or the first frames (on-time frames) in scheduled allocation intervals received from the hub. In particular, the node shall advance or delay its clock by a total amount of

D = TS – TL, if TS > TL

or

D = TL – TS, if TS < TL

respectively, where TS is the time when a beacon, a T-Poll frame, or a frame with the “First Frame / On Time” bit in its MAC header set to 1 was scheduled to start on the transport medium (i.e., air), and TL is the time when the frame was received according to the local clock.

The various guardtime components shall be determined as follows:

mGT_Nominal = GTn = GT0 + 2×Dn, Dn = SIn×mClockAccuracy

GT0 = pSIFS + pSynchResolution + mTxResolution

mTxResolution = mClockResolution

GTa = 2 × Da, Da = SIa × mClockAccuracy

The parameter GTn = mGT_Nominal has a predefined value as listed in Table 23, and designates the guardtime nominally observed by a node or a hub. The parameter GT0 comprises the RX-TX or TX-RX turnaround time pSIFS, the synchronization error pSynchResolution, and the transmission timing error mTxResolution, which are all of fixed values that are independent of clock drifts and listed in Table 23 as well. Thus the value of GT0 is also predefined. Given the values of GTn and GT0, the parameter Dn represents the nominally allowed clock drift of a node or hub relative to an ideal (nominal) clock. With the minimum clock accuracy of mClockAccuracy also given in Table 23, Dn and SIn are predetermined too for all nodes and hubs. Dn delimits a nominal synchronization interval SIn over which the clock drift of any node is accounted for in the nominal guardtime GTn.

The parameter SIa denotes the synchronization interval that has accrued in addition to SIn since last synchronization. The corresponding additional clock drift Da is a function of SIn and accounts for the required additional guardtime GTa. The values of Da and SIa are specific to the node and time of concern.

For scheduled access and its variants as specified in 7.7, a node may attain a desired GTa through the setting of the Scaling Up Factor field of the Allocation Request fields contained in its latest Connection Reqeust frame.

An illustration of clock drift and guardtime provisioning is given in Figure 86.

— Clock drifts and guard times

Power management

A node not indicating to be always in active state, referred to as a node in short in this subclause, may hibernate across a number of beacon periods (superframes), and may sleep over some time intervals even in its wakeup beacon periods (superframes), as clarified below.

Hibernation—macroscopic power management

To hibernate—without receiving or transmitting any traffic—in some beacon periods, the node shall set the Wakeup Period field in its last Connection Request frame to an integer larger than 1, while setting the Wakeup Phase field in the frame to a value specifying its intended next wakeup beacon period.

To wakeup—for receiving or/and transmitting frames—in every beacon period, the node shall set the Wakeup Period field in its last Connection Request frame to 1, while setting the Wakeup Phase field in the frame to a value identifying the next beacon period.

The intended recipient hub of the Connection Request frame should honor the values of the received Wakeup Period and, to a less extend, Wakeup Period fields whenever possible, but may set them to different values if need be, in its responding Connection Assignment frame. The hub may later modify these values by sending to the node another Connection Assignment frame if warranted by new conditions.

If the hub sets the Wakeup Period field in its responding frame to an integer larger than 1, it may grant only m-periodic allocations to the node, with the allocation intervals being in the node’s wakeup beacon periods, in accordance with the node’s last connection request whenever possible, but shall not grant to the node any 1-periodic allocations.

If the hub sets the Wakeup Period field in its responding frame to 1, it may grant only 1-periodic allocations to the node, with the allocation intervals being in every beacon period, in accordance with the node’s last connection request whenever possible, but shall not grant to the node any m-periodic allocations.

If the Wakeup Period value in the Connection Assignment frame last received from the hub is larger than 1, the node shall wake up in each of its wakeup beacon periods based on the latest Wakeup Period and Wakeup Phase values provided in that frame by the hub, to transmit or/and receive frames in the granted m-periodic allocation intervals, and to receive the beacon if needed.

If the Wakeup Period value in the Connection Assignment frame last received from the hub is 1, the node shall wake up in every beacon period, to transmit or/and receive frames in the granted 1-periodic allocation intervals, and to receive the beacon if appropriate.

Figure 87 illustrates macroscopic power management across beacon periods.

— Macroscopic power management

Sleep—microscopic power management

A node shall wake up to receive a beacon from a hub when it needs a beacon reception to synchronize with the hub or to obtain certain information contained in a beacon.

A node shall wake up to receive and transmit frames in its scheduled allocations in its wakeup beacon periods, as illustrated in Figure 88.

In addition, the node shall stay active participating in frame transactions in its expected posted allocations, as illustrated in Figure 88. The hub should arrange to have the posted allocations of a node to occur in the node’s wakeup beacon periods, if possible. If the node did not receive a frame at the announced time for a pending post, it should stay in receive mode until the hub could have finished a frame transaction for the post and retransmitted a frame pSIFS later, as also illustrated in Figure 88, unless it needs to make a turnaround to transmit mode.

If the node has indicated its support for polls through its MAC Capability field of its last Connection Request frame, it shall also stay active in such times as to receive announced polls and initiate frame transactions in its polled allocations, as further illustrated in Figure 88. The hub should arrange to have the polled allocations of a node to occur in the node’s wakeup beacon periods, if possible.

Outside the time intervals noted in the above, the node may sleep—without receiving or transmitting any traffic.

Figure 88 illustrates microscopic power management in a wakeup beacon period.

— Microscopic power management

Coexistence and interference mitigation

A hub may employ one or more of the optional mechanisms described in 7.12.1 for coexistence and/or interference mitigation between its body area network (BANs) and neighbor BANs.

Beacon shifting

A hub may transmit its beacons at different time offsets relative to the start of the beacon periods by including a Beacon Shifting Sequence field in its beacons as defined in 6.3.1.10. A hub should choose a beacon shifting sequence that is not being used by its neighbor hubs to mitigate potential repeated beacon collisions and scheduled allocation conflicts between overlapping or adjacent BANs operating on the same channel.

As shown in Figure 89, the hub shall transmit a beacon out of its physical layer (PHY) at a time t = PNm(n)×BP/4 relative to the start of beacon period n. Here, m = 4 is the beacon shifting sequence index that the hub has chosen for its BAN, BP is the length of its beacon period, and n is the phase of the chosen sequence (n = 0, 1, … ) for this beacon period.

— Beacon shifting illustration

As defined in 6.3.1.2, the allocation slots in a beacon period shift around with the beacon transmit time. The access phases – exclusive access phase 1 (EAP1), random access phase 1 (RAP 1), exclusive access phase 2 (EAP2), random access phase 2 (RAP2), and contention access phase (CAP) – shown in Figure 61 are referenced to numbered allocation slots and shift around with the beacon in the beacon period accordingly. The RAP1 and RAP2 related fields contained in the beacon of the current beacon period now refer to the EAP1, RAP1, EAP2, and RAP2 in the next beacon period.  A node does not know nor use these access phases in the beacon period in which it received its first beacon indicating beacon shifting is enabled, but it may use Type I and Type II access phases through polls or posts.

The hub shall ensure in choosing these access phases and the beacon shifting sequence that beacon shift does not result in a split of any of the aforementioned access phases into two parts.

Scheduled allocation intervals are also referenced to numbered allocation slots and shift around with the beacon transmit time accordingly in the beacon period as shown in Figure 90. A scheduled allocation interval in a beacon period may be split into two portions as a result of shifting around the beacon period, but the aggregate length remains the same.

(a) 1-priodic allocation

(b) m-periodic allocation

— Beacon and scheduled allocation interval shifting

Channel hopping

A hub may enable channel hopping only if its physical layer (PHY) is a narrow band (NB) PHY not operating in the medical implant communications service (MICS) band.  In such cases, the hub may change its operating channel periodically by including the Channel Hopping State and Next Channel Hop fields in its beacons as defined in 6.3.1.11 and 6.3.1.12, respectively. A hub should choose a channel hopping sequence that is not being used by its neighbor hubs.

The hub shall hop to another channel after dwelling on the current channel for a fixed number of beacon periods as communicated to the nodes connected with the hub through Connection Assignment frames. To hop to a new channel, the hub shall start switching to the new channel at pChannelSwitchTime prior to the start of the beacon period that begins with the new channel, neither sending nor receiving frames during the channel switch.  A node should not send a frame during this transition.

A hub shall generate a channel hopping sequence based on the maximum-length Galois linear feedback shift register (LFSR) defined in Figure 91and by the following generator polynomial

x16 + x14 + x13 + x11 + 1

The state of the LFSR at stage k is given by

Yk = 20 × rk,0 + 21 × rk,1 + … + 215 × rk,15

Yk represents the binary value read from the bits rk,0, rk,1, …, rk,15 of the individual registers at stage k, with rk,0 being the least-significant bit and rk,15 being the most-significant bit.

— 16-bit Galois LFSR for channel hopping sequence generation

Given the current state Yk of the LFSR, the hub shall generate the next state Yk+1 of the LFSR, i.e., the state of the LFSR at the next stage, stage k+1. Accordingly, the hub shall generate the channel number Ck+1 of the next channel from the channel number Ck of the current channel and the next state Yk+1 of the LFSR as follows:

Zk+1 = Yk+1 mod Nreduced

Ck+1 = (Ck + Zk+1 + Nsep) mod Nch

In the above, the notation mod denotes modular operation. Nch = pChannelsTotal is the number of total channels in the operating frequency band as listed in Table 24. Nsep = pChannelSeparation is the minimum number of channels separated between two consecutive hops as illustrated in Figure 92. Nreduced is the number of channels available for each hop on account of the channel separation constraint Nsep, and is given by:

Nreduced = Nch – 2Nsep + 1

The channels are numbered from 0 through Nch – 1. Given the current channel number Ck, the next channel number Ck+1 will be such that |Ck+1 – Ck| ≥ Nsep. All channels are selected with equal probability, as also shown in Figure 92.

— Channel separation in consecutive hops

The hub shall set the initial state Y0 of its LFSR to the 16 least-significant bits of its EUI-48, with r0,0 corresponding to the least-significant bit. The hub shall select the channel number C0 of its initial channel as follows:

C0 = Y0 mod Nch

To remain connected with a hub, a node shall hop to the same channel as the hub.

Active BAN time sharing

A hub may listen for beacon and B2 frames sent by other hubs over different channels in a given operating frequency band to collect certain coexistence information.  Based on such collected information the hub may then select an operating channel.

The hub may send to another hub that is using the same operating channel and enabled for active BAN time sharing a Command – Active Temporal Coexistence Request frame to request for inter-BAN time sharing.  Upon acknowledging receipt of the frame, the latter hub should respond to the former hub with a Command – Active Temporal Coexistence Response frame to indicate its plan on their inter-BAN time sharing.

The former hub shall set the MAC header of the frame to be sent to the latter hub as if it were an unconnected node sending the frame to the recipient hub in the latter’s body area network (BAN).   The latter hub shall set the MAC header of the frame to be sent to the former hub to the MAC header of the frame, with the same frame type and frame subtype, received from the former hub and then shall swap the Recipient ID and Sender ID fields.  Only the aforementioned two frames and I-Ack frames may be unicast by one hub to another hub.

Code division

A hub may treat as an operating channel a logical channel as defined in Clause 10 based on spread spectrum code division in a frequency band for the ultra wide  band (UWB) physical layer (PHY), and may choose such a channel for its BAN creation and maintenance as described in 7.4.  The coexistence and interference mechanisms specified in 7.12 that are applicable to an operating channel in a given frequency band apply to an operating channel defined through a logical channel in a frequency band for the UWB PHY, unless otherwise stated.

Allocation reduction

A hub may reduce or remove the allocations to the services of its body area network (BAN) when other coexistence mechanisms are not applicable or adequate, as specified in Table 21.

— Allocation reduction for load control

| BAN services | BAN priority | Allocation reduction |
| --- | --- | --- |
| Non-medical services | Lowest | 100% |
| Mixed medical and non-medical services | Second lowest | 20% |
| General health services | Second highest | 10% |
| Highest priority medical services | Highest | 0% |

Applicability guideline

A hub may employ one or more coexistence and interference mitigation mechanisms applicable for the operating frequency bands as highlighted in Table 22.  In selecting the mechanisms, the hub should consider the relative mobility of its body area network (BAN) over short-term durations (minutes to hours) relative to other BANs in the vicinity.  To a lesser extent, the hub should also consider the traffic volume of its own BAN and the adjacent BANs.

Three mobility levels, designated as static (S), semi-dynamic (S), and dynamic (D), are referenced in the table, which also uses the following legend:  LBT – listen before talk, LDC – low duty cycle, and DAA – detect and avoid.  Some examples of mobility levels are given as follows:

Static (S) – a single BAN in a residential environment or a hospital with a single patient node and a fixed bedside hub;

Semi-dynamic (SD) – slowly moving ambulatory patients in an elder care facility requiring infrequent and/or event-based low-rate data transfers;

Dynamic (D) – fast moving ambulatory patients in a hospital with a large number of BANS collecting continuous data traffic from many sensor nodes.

— Recommended coexistence mechanisms

| Coexistence mechanism | 10-50 MHz HBC/EFC | MICS band | 868 MHz band | 902-928 MHz band | 2.4 GHz ISM band | UWB band |
| --- | --- | --- | --- | --- | --- | --- |
| Regulatory rules | None if low power, non-spread spectrum power levels | LBT based channel selection and communi-cation session occupancy | LBT based channel selection and communi-cation session occupancy | None if low power, non-spread spectrum power levels | None if low power, non-spread spectrum power levels | LDC or DAA for 3.1 to 4.8 GHz | Different regulations for bands in 6 -10.6 GHz |
| Beacon shifting | Not applicable | Not applicable given LBT restrictions | SD, D | SD, D | SD, D | D | D |
| Channel hopping | Not applicable | D | SD, D | SD, D | SD, D | Not applicable | Not applicable |
| Scan for channel selection | S, SD, D | S, SD | S, SD | S, SD | S, SD | S, SD | S, SD |
| Active BAN time sharing | S, SD, D | None | S | S | S, SD | S, SD | S, SD |
| Allocation reduction | Not applicable | Not applicable – only medical traffic on this PHY by regulations | S, SD, D Load control for non-medical traffic | S, SD, D Load control for non-medical traffic | S, SD, D Load control for non-medical traffic | S, SD, D Load control for non-medical traffic | S, SD, D Load control for non-medical traffic |

MAC / PHY capability handling/interaction and Application Specific IE usage

MAC / PHY optional capability support

A node or a hub shall be ready to carry out a function that it has indicated to be capable of supporting in its last transmitted MAC Capability or PHY Capability field. A node or a hub shall not initiate or execute a function that its communication partner has indicated to be incapable of supporting through the last MAC Capability or PHY Capability field sent by the partner.

To transmit beacons, a hub shall use a mandatory data rate for the underlying PHY. To transmit Poll and T-Poll frames addressed to Unconnected_Broadcast_NID or Local_Broadcast-NID, a hub shall use the lowest data rate in the operating frequency band mandated for the underlying PHY.

MAC / PHY interaction for hybrid ARQ

A node and a hub may employ type-II hybrid automatic repeat request (ARQ) in transmitting and receiving a frame as specified in 10.16 for the UWB PHY if pHybridARQ is set to TRUE.

The sender shall send the frame with the Ack Policy field of the MAC header set to I-Ack. Unless the sender receives an expected I-Ack frame or aborts the current frame retransmission at the physical (PHY) layer, it shall transmit a frame containing alternately either the parity bits of the MAC frame constructed at the physical layer (PHY) per the hybrid HARQ scheme or the MAC frame itself, pSIFS after the estimated end of the expected I-Ack frame.

The recipient shall receive and acknowledge the frame according to 7.2.4 and 7.2.7.3.  It shall not send any frame when it is otherwise required to send a negative acknowledgment (NACK) per the hybrid ARQ operation described in 10.16.  Upon not receiving an expected I-Ack frame, the sender shall treat an NACK to have been received as far as thehybrid ARQ operation is concerned.  Note that NACK for negative acknowledgment is different from N-Ack for no acknowledgment defined as an acknowledgment policy in Table 1.

The sender shall ensure that in invoking a type-II hybrid ARQ operation for a frame transmission, the transmissions of the frame containing a MAC frame or the parity bits thereof, the expected I-Ack frames, and the appropriate guardtime are all within an allocation interval it has obtained.

Application Specific IE usage

A hub may include one or more Application Specific IEs at the end of its beacon.

A node may include one or more Application Specific IEs at the end of its Connection Request frame. A hub may also include one or more Application Specific IEs at the end of its Connection Assignment frame.

A recipient shall ignore unrecognized Application Specific IEs.

MAC sublayer parameters

Table 23 provides the values for the MAC sublayer parameters.

— MAC sublayer parameters

| Parameter | Value |
| --- | --- |
| mCSMADurationLimit | 2 × Allocation Slot Length |
| mClockAccuracy | 20 ppm |
| mClockResolution | 10 (s |
| mG-AckDataSubtype | 1111 (binary) |
| mGT_Nominal | GT0 + 2×Dn, GT0 = pSIFS + pSynchResolution + mClockResolution, Dn = SI×mClockAccuracy, SI = 8 × Beacon Period (Superframe) Length |
| mMaxChannelChangeTime | 256 beacon periods |
| mMaxFragmentCount | 8 |
| mMaxBANSize | 64 |

Table 24 and Table 25 provide the values of the PHY dependent parameters used by the MAC sublayer.

— PHY-dependent MAC sublayer parameters pertaining to narrowband PHY

| Parameter | Value |
| --- | --- |
| pAllocationSlotMin | 1 ms |
| pAllocationSlotResolution | 1 ms |
| pCCATime | 63 / Symbol Rate (See Table 27 to Table 33 for Symbol Rates) |
| pChannelSeparation | 2 |
| pChannelsTotal | See Table 43 |
| pCSMASlotLength | pCCATime + 20 (s |
| pExtraIFS | 5 (s |
| pHybridARQ | FALSE |
| pMaxFrameBodyLength | 255 octets |
| pMICSAckTxTime | pMICSPreambleTxTime + pMICSPLCPHeaderTxTime + (7+2) × 8 / 75.9 ms = 1594 (s |
| pMICSChannelsTotal | 10 |
| pMICSChannelSwitchTime | 100 (s |
| pMICSHubMaxRetries | 10 |
| pMICSMcastPollRxTime | pMICSMcastPollSeparation + pMICSPreambleTxTime = 2094 (s |
| pMICSMcastPolls | (pMICSChannelsTotal × (pMICSMcastPollRxTime + pMICSChannelSwitchTime ) / pMICSMcastPollSeparation( = 14 |
| pMICSMcastPollSeparation | pMICSPollTxTime + pMIFS = 1614 (s |
| pMICSNodeEmergencyRetries | 2 |
| pMICSPollRxTime | pMICSPollSeparation + pMICSPreambleTxTime = 2819 (s |
| pMICSPollSeparation | pMICSPollTxTime + 2×pSIFS + pMICSPreambleTxTime + pMICSPLCPHeaderTxTime = 2339 (s |
| pMICSPollTxTime | pMICSAckTxTime = 1594 (s |
| pMICSPreambleTxTime | 90 / 187.5 ms = 480 (s |
| pMICSPLCPHeaderTxTime | 31 / 187.5 ms = 165 (s |
| pMICSUnconnectedPollPeriod | > pMICSUnconnectedPollSeparation×pMICSUnconnectedPolls) = 35880 (s |
| pMICSUnconnectedPollRxTime | pMICSUnconnectedPollSeparation + pMICSPreambleTxTime = 3240 (s |
| pMICSUnconnectedPolls | (pMICSChannelsTotal × (pMICSUnconnectedPollRxTime + pMICSChannelSwitchTime ) / pMICSUnconnectedPollSeparation( = 13 |
| pMICSUnconnectedPollSeparation | pMICSUnconnectedPollTxTime + 2×pSIFS + pMICSPreambleTxTime + pMICSPLCPHeaderTxTime = 2760 (s |
| pMICSUnconnectedPollTxTime | pMICSPreambleTxTime + pMICSPLCPHeaderTxTime + (7+4+2) × 8 / 75.9 ms = 2015 (s |
| pMIFS | 20 (s |
| pRandomAccess | CSMA/CA |
| pSynchResolution | 1 / Symbol Rate (See Table 27 - Table 33 for Symbol Rates) for NB |
| pSIFS | 50 (s |
| pUnconnectedPolledAllocationMin | ≥ transmit time of a PHY frame with a MAC frame of 7+112+2 octets transmitted at the lowest mandatory data rate of the operating frequency band, plus pSIFS, plus transmit time of a PHY frame with a MAC frame of 7+2 octets transmitted at the lowest mandatory data rate of the operating frequency band |

— PHY-dependent MAC sublayer parameters pertaining to UWB PHY

| Parameter | Value |
| --- | --- |
| pAllocationSlotMin | 1 ms |
| pAllocationSlotResolution | 16 (s |
| pAlohaSlotLength | (800 (s + pSIFS) × 1.1 |
| pCSMASlotLength | pCCATime + 20 (s |
| pExtraIFS | 5 (s |
| pHybridARQ | TRUE |
| pMaxFrameBodyLength | 255 octets |
| pRandomAccess | CSMA/CA or Slotted Aloha |
| pSynchResolution | 1 / Symbol Rate (See Table 55, Table 56 and Table 64 for Symbol Rates) |
| pSIFS | 50 (s |
| pUnconnectedPolledAllocationMin | ≥ transmit time of a PHY frame with a MAC frame of 7+112+2 octets transmitted at the lowest mandatory data rate of the operating frequency band, plus pSIFS, plus transmit time of a PHY frame with a MAC frame of 7+2 octets transmitted at the lowest mandatory data rate of the operating frequency band |

Security services

This clause expounds on the elements of the security hierarchy introduced in Figure 5.  Security in this standard starts with a negotiation of the desired security suite between the two communicating parties, a node and a hub. The security selection in turn sets off a security association between the two parties for activating a pre-shared or generating a new shared master key (MK). Several security association protocols suitable for a variety of use cases are provided in 8.1, which finishes off with security disassociation for legitimately repealing a shared master key between the two parties. Pairwise temporal key (PTK) creation and group temporal key (GTK) distribution are then described in 8.2.

Treated in 8.3 is message security at the MAC level, i.e., message authentication and encryption, based on the Advanced Encryption Standard (AES) forward cipher function for 128-bit keys operating on counter mode and cipher block chaining (CBC) mode, respectively. As part of message security, replay protection is also considered in this subclause.

Support for mandatory and optional cipher functions is clarified in 8.4.

Master keys

The security association protocols specified in 8.1.2, 8.1.3, 8.1.4, and 8.1.5 shall be based on the Diffie-Hellman key exchange employing the elliptic curve public key cryptography. The elliptic curve, characterized by the following equation

y2 ( x3 + ax + b (mod p), with a, b ( GF (p), 4a3 + 27b2 ≠ 0

where GF(p) is a prime finite field, shall have the following values for its coefficients and domain parameters, as specified for Curve P-256 in FIPS Pub186-3, with p (an odd prime), r (order of base point G), and a (a coefficient) given in decimal form, and coefficient b and base point G = (Gx, Gy) given in hex:

p = 2256 – 2224 + 2256 + 296 – 1

= 115792089210356248762697446949407573530086143415290314195533631308867097853951

r = 115792089210356248762697446949407573529996955224135760342422259061068512044369

a = p - 3

b = 5ac635d8 aa3a93e7 b3ebbd55 769886bc 651d06b0 cc53b0f63bce3c3e 27d2604b

Gx = 6b17d1f2 e12c4247 f8bce6e5 63a440f2 77037d81 2deb33a0f4a13945 d898c296

Gy = 4fe342e2 fe1a7f9b 8ee7eb4a 7c0f9e16 2bce3357 6b315ececbb64068 37bf51f5

The private keys (also called secret keys) SKA and SKB of the elliptic curve public key cryptography for the two communicating parties, a node (party A) and a hub (party B), respectively, shall be each statically unique 256-bit integers chosen independently and at random from the range [1, r-1]. The corresponding 256-bit public keys PKA and PKB shall be computed as follows:

PKA = SKA × G, PKB = SKB × G

where × denotes scalar multiplication of the base point G = (Gx, Gy) by an integer as described in A.9.2 of IEEE Std P1363-2000. A received public key, denoted by a pair of X-coordinate and Y-coordinate values, shall be treated valid only if it is a non-infinity point on the elliptic curve defined in the above, i.e., that its X and Y coordinates satisfy the elliptic curve equation given above.

In the security association and disassociation procedures, except that for master key pre-shared association, that are specified in this subclause, the cipher-based message authentication code (CMAC) algorithm as specified in the NIST Special Publication 800-38B, with the AES forward cipher function under a 128-bit key as specified in FIPS Pub 197, is used to compute key message authentication codes (KMAC) and the desired shared master key. Specifically, the functional notation CMAC(K, M, L) represents the L-bit output of the CMAC applied under key K to message M based on the AES forward cipher function.

Moreover, the bit string truncation functions LMB_n(S) and RMB_n(S) designate the n leftmost and the n rightmost bits of the bit string S, respectively. The sign || denotes concatenation of bit strings that are converted according to FIPS Pub 180-2 from certain fields of the frames of concern.

Master key (MK) pre-shared association

A node and a hub shall each have a secret pre-shared MK prior to running the MK pre-shared association protocol to activate their pre-shared MK as their shared MK for their PTK creation, with the benefit of keeping third parties not possessing the secret MK from launching impersonation attacks via the PTK creation procedure.

The node, but not the hub, may initiate a security association procedure to run the MK pre-shared association protocol, by sending to the hub the first Security Association frame of the procedure.

Upon receiving the first Security Association frame, the hub shall send to the node the second Security Association frame, joining or aborting the security association procedure.

If the node receives the second Security Association frame indicating the hub is aborting the security association procedure, it shall abort the current security association procedure.  It may initiate a new security association procedure if the hub aborted the procedure with a different security suite selector.  It may later initiate a new security association procedure if the hub aborted the procedure due to temporary lack of resources.

Upon successfully sending the second Security Association frame indicating it is joing the security association procedure, the hub shall activate the pre-shared MK as its shared MK with the node, treating the node’s true identity unauthenticated but the security association procedure completed. Upon receiving the second Security Association frame indicating the hub is joing the security association procedure, the node shall also activate the pre-shared MK as its shared MK with the hub, treating the hub’s true identity unauthenticated but the security association procedure completed as well. The node shall proceed to the PTK creation procedure to create a PTK with the hub, meanwhile performing mutual authentication of each other based on the claimed pre-shared MK.

The MK pre-shared association procedure is illustrated in Figure 93.

— MK pre-shared association procedure

Unauthenticated association

A node and a hub shall each require no authentication credentials such as a shared secret or human intervention prior to running the unauthenticated association protocol to generate their shared MK for their PTK creation, without the benefit of keeping third parties from launching impersonation attacks.

The node, but not the hub, may initiate a security association procedure to run the unauthenticated association protocol, by sending to the hub the first Security Association frame of the procedure.

Upon receiving the first Security Association frame, the hub shall send to the node the second Security Association frame, joining or aborting the security association procedure.

If the node receives the second Security Association frame indicating the hub is aborting the security association procedure, it shall abort the current security association procedure.  It may initiate a new security association procedure if the hub aborted the procedure with a different security suite selector.  It may later initiate a new security association procedure if the hub aborted the procedure due to temporary lack of resources.

The hub shall abort the security association procedure if the node’s public key (PKAX, PKAY) contained in the first Security Association frame is not a valid public key.  Otherwise, upon successfully sending the second Security Association frame indicating it is joing the security association procedure, the hub shall send to the node the third Security Association frame, setting the MK_KMAC field of the Security Association Data thereof to MK_KMAC_3 as calculated in Eq. (20).

The node shall abort the security association procedure if the hub’s public key (PKBX, PKBY) contained in the second Security Association frame is not a valid public key.  Otherwise, upon receiving the third Security Association frame with the MK_KMAC equal to MK_KMAC_3, the node shall send to the hub the fourth Security Association frame, setting the MK_KMAC field of the Security Association Data thereof to MK_KMAC_4 as calculated in Eq. (21).

Upon successfully sending the fourth Security Association frame, the node shall compute the shared MK as given in Eq. (22), treating the hub’s true identity unauthenticated but the association procedure completed. Upon receiving the fourth Security Association frame with the MK_KMAC equal to MK_KMAC_4, the hub shall also compute the shared MK, treating the node’s true identity unauthenticated but the association procedure completed as well.

The node and the hub shall each compute DHKey and extract Temp_1 as follows:

DHKey = X(SKA×PKB) = X(SKB×PKA) = X(SKA×SKB×G)

Temp_1 = RMB_128(DHKey)

The node and the hub shall each derive MK_KMAC_3 and MK_KMAC_4 as follows:

MK_KMAC_3 = CMAC(Temp_1, Address_A || Address_B || Nonce_A || Nonce_B || Security_Suite_Selector, 64)

MK_KMAC_4 = CMAC(Temp_1, Address_B || Address_A || Nonce_B || Nonce_A || Security_Suite_Selector, 64)

After the aforementioned verifications have passed, the node and the hub shall each derive their shared MK as follows:

MK = CMAC(Temp_2, Nonce_A || Nonce_B, 128), where Temp_2 = LMB_128(DHKey)

In the above, X(P) = X(PX, PY) = PX = X-coordinate of P, which is computed from SKA×PKB at the node and from SKB×PKA at the hub, respectively.

SKA is the node’s 256-bit private key (an integer) kept secret by the node.

SKB is the hub’s 256-bit private key (an integer) kept secret by the hub.

PKA is the node’s 256-bit public key (a pair of X and Y coordinates) transmitted by the node.

PKB is the hub’s 256-bit public key (a pair of X and Y coordinates) transmitted by the hub.

Address_A is the Sender Address field of the frame payload of the first Security Association frame.

Address_B is the Recipient Address field of the frame payload of the first Security Association frame.

Nonce_A is the Sender Nonce field of the frame payload of the first Security Association frame.

Nonce_B is the Sender Nonce field of the frame payload of the second Security Association frame.

Security_Suite_Selector is the Security Suite Selector field of the frame payload of the first Security Association frame.

The unauthenticated association procedure is illustrated in Figure 94.

— Unauthenticated association procedure

Public key hidden association

A node and a hub shall have a secured, secret transfer of the node’s public key to the hub, typically through an out-of-band channel, prior to running the public key hidden association protocol to generate their shared MK for their PTK creation, with the benefit of keeping third parties from launching impersonation attacks.

The node, but not the hub, may initiate a security association procedure to run the public key hidden association protocol, by sending to the hub the first Security Association frame of the procedure.

Upon receiving the first Security Association frame, the hub shall send to the node the second Security Association frame, joining or aborting the security association procedure.

If the node receives the second Security Association frame indicating the hub is aborting the security association procedure, it shall abort the current security association procedure.  It may initiate a new security association procedure if the hub aborted the procedure with a different security suite selector.  It may later initiate a new security association procedure if the hub aborted the procedure due to temporary lack of resources.

The hub shall abort the security association procedure if the node’s public key (PKAX, PKAY) transferred through an out-of-band channel is not a valid public key.  Otherwise, upon successfully sending the second Security Association frame indicating it is joing the security association procedure, the hub shall send to the node the third Security Association frame, setting the MK_KMAC field of the Security Association Data thereof to MK_KMAC_3 as calculated in (25).

The node shall abort the security association procedure if the hub’s public key (PKBX, PKBY) contained in the second Security Association frame is not a valid public key.  Otherwise, upon receiving the third Security Association frame with the MK_KMAC equal to MK_KMAC_3, the node shall send to the hub the fourth Security Association frame, setting the MK_KMAC field of the Security Association Data thereof to MK_KMAC_4 as calculated in (26).

Upon successfully sending the fourth Security Association frame, the node shall compute the shared MK as given in (27), treating the hub’s true identity authenticated and the association procedure completed. Upon receiving the fourth Security Association frame with the MK_KMAC equal to MK_KMAC_4, the hub shall also compute the shared MK, treating the node’s true identity authenticated and the association procedure completed as well.

The node and the hub shall each compute DHKey and extract Temp_1 as follows:

DHKey = X(SKA×PKB) = X(SKB×PKA) = X(SKA×SKB×G)

Temp_1 = RMB_128(DHKey)

The node and the hub shall each derive MK_KMAC_3 and MK_KMAC_4 as follows:

MK_KMAC_3 = CMAC(Temp_1, Address_A || Address_B || Nonce_A || Nonce_B || Security_Suite_Selector, 64)

MK_KMAC_4 = CMAC(Temp_1, Address_B || Address_A || Nonce_B || Nonce_A || Security_Suite_Selector, 64)

After the aforementioned verifications have passed, the node and the hub shall each derive their shared MK as follows:

MK = CMAC(Temp_2, Nonce_A || Nonce_B, 128), where Temp_2 = LMB_128(DHKey)

In the above, X(P) = X(PX,PY) = PX = X-coordinate of P, which is computed from SKA×PKB at the node and from SKB×PKA at the hub, respectively.

SKA is the node’s 256-bit private key (an integer) kept secret by the node.

SKB is the hub’s 256-bit private key (an integer) kept secret by the hub.

PKA is the node’s 256-bit public key (a pair of X and Y coordinates) transferred only to the hub by a secure out-of-band channel.

PKB is the hub’s 256-bit public key (a pair of X and Y coordinates) transmitted by the hub.

Address_A is the Sender Address field of the frame payload of the first Security Association frame.

Address_B is the Recipient Address field of the frame payload of the first Security Association frame.

Nonce_A is the Sender Nonce field of the frame payload of the first Security Association frame.

Nonce_B is the Sender Nonce field of the frame payload of the second Security Association frame.

Security_Suite_Selector is the Security Suite Selector field of the frame payload of the first Security Association frame.

The public key hidden association procedure is also illustrated in Figure 94 as well.

Password authenticated association

A node and a hub shall each have a secret shared password prior to running the password authenticated association protocol to generate their shared MK for their PTK creation, with the benefit of keeping third parties not possessing the secret password from launching impersonation attacks.

The node, but not the hub, may initiate a security association procedure to run the password authenticated association protocol, by sending to the hub the first Security Association frame of the procedure.

Upon receiving the first Security Association frame, the hub shall send to the node the second Security Association frame, joining or aborting the security association procedure.

If the node receives the second Security Association frame indicating the hub is aborting the security association procedure, it shall abort the current security association procedure.  It may initiate a new security if the hub aborted the procedure with a different security suite selector.  It may later initiate a new security association procedure if the hub aborted the procedure due to temporary lack of resources.

The hub shall abort the security association procedure if the node’s password-scrambled public key (PK'AX, PK'AY) contained in the first Security Association frame is not a valid public key.  Otherwise, upon successfully sending the second Security Association frame indicating it is joing the security association procedure, the hub shall send to the node the third Security Association frame, setting the MK_KMAC field of the Security Association Data thereof to MK_KMAC_3 as calculated in Eq. (33).

The node shall abort the security association procedure if the hub’s public key (PKBX, PKBY) contained in the second Security Association frame is not a valid public key.  Otherwise, upon receiving the third Security Association frame with the MK_KMAC equal to MK_KMAC_3, the node shall send to the hub the fourth Security Association frame, setting the MK_KMAC field of the Security Association Data thereof to MK_KMAC_4 as calculated in Eq. (34).

Upon successfully sending the fourth Security Association frame, the node shall compute the shared MK as given in Eq. (35), treating the hub’s true identity authenticated and the association procedure as completed. Upon receiving the fourth Security Association frame with the MK_KMAC equal to MK_KMAC_4, the hub shall also compute the shared MK, treating the node’s true identity authenticated and the association procedure completed as well.

The node shall compute its password-scrambled public key PK'A = (PK'AX, PK'AY) from its public or private key and the password shared with the hub as follows:

PK'A = PKA – (MX + 1)×Q(PW) = SKA×G – (MX + 1)×Q(PW)

Q(PW) = (QX = PW+MX, QY = even positive integer)

The hub shall recover the node’s public key from the received password-scrambled public key PK'A = (PK'AX, PK'AY) for the subsequent DHKey computation as follows:

PKA = PK'A + (MX + 1)×Q(PW), Q(PW) = (QX = PW+MX, QY = even positive integer)

The parameters involved in these equations are defined as follows:

PW is a positive integer converted according to IEEE Std P1363-2000 from the UTE-16BE representation of the shared password by treating the leftmost octet as the octet containing the most-significant bits.

MX is the smallest nonnegative integer such that QX = PW+MX is the X-coordinate of a point on the elliptic curve defined earlier.

Q(PW) is the point on the elliptic curve with X-coordinate = QX and Y-coordinate = QY of an even positive integer.

The node shall choose a private key SKA such that the X-coordinate of PKA is not equal to the X-coordinate of (MX + 1) × Q(PW).

The node and the hub shall each compute DHKey and extract Temp_1 as follows:

DHKey = X(SKA×PKB) = X(SKB×PKA) = X(SKA×SKB×G)

Temp_1 = RMB_128(DHKey)

The node and the hub shall each derive MK_KMAC_3 and MK_KMAC_4 as follows:

MK_KMAC_3 = CMAC(Temp_1, Address_A || Address_B || Nonce_A || Nonce_B || Security_Suite_Selector, 64)

MK_KMAC_4 = CMAC(Temp_1, Address_B || Address_A || Nonce_B || Nonce_A || Security_Suite_Selector, 64)

After the aforementioned verifications have passed, the node and the hub shall each derive their shared MK as follows:

MK = CMAC(Temp_2, Nonce_A || Nonce_B, 128), where Temp_2 = LMB_128(DHKey)

In the above, X(P) = X(PX,PY) = PX = X-coordinate of P, which is computed from SKB×PKA at the hub and from SKA×PKB at the node, respectively.

SKA is the node’s 256-bit private key (an integer) kept secret by the node.

SKB is the hub’s 256-bit private key (an integer) kept secret by the hub.

PKA is the node’s 256-bit public key (a pair of X and Y coordinates) kept secret by the node.

PKB is the hub’s 256-bit public key (a pair of X and Y coordinates) transmitted by the hub.

Address_A is the Sender Address field of the frame payload of the first Security Association frame.

Address_B is the Recipient Address field of the frame payload of the first Security Association frame.

Nonce_A is the Sender Nonce field of the frame payload of the first Security Association frame.

Nonce_B is the Sender Nonce field of the frame payload of the second Security Association frame.

Security_Suite_Selector is the Security Suite Selector field of the frame payload of the first Security Association frame.

The password authenticated association procedure is illustrated in Figure 95.

— Password authenticated association procedure

Display authenticated association

A node and a hub shall each have a display of a 5-digit decimal number prior to running the display authenticated association protocol to generate their shared MK for their PTK creation, with the benefit of keeping third parties from launching man-in-the middle attacks.

The node, but not the hub, may initiate a security association procedure to run the display authenticated association protocol, by sending to the hub the first Security Association frame of the procedure.

Upon receiving the first Security Association frame, the hub shall send to the node the second Security Association frame of the procedure, joining or aborting the security association procedure.

If the node receives the second Security Association frame indicating the hub is aborting the security association procedure, it shall abort the current security association procedure.  It may initiate a new security association procedure if the hub aborted the procedure with a different security suite selector.  It may later initiate a new security association procedure if the hub aborted the procedure due to temporary lack of resources.

The hub shall abort the security association procedure if the node’s public key (PKAX, PKAY) contained in the first Security Association frame is not a valid public key.  Otherwise, upon successfully sending the second Security Association frame indicating it is joing the security association procedure, the hub shall send to the node the third Security Association frame, setting the MK_KMAC field of the Security Association Data thereof to MK_KMAC_3 as calculated in (38).

The node shall abort the security association procedure if the hub’s public key (PKBX, PKBY) contained in the second Security Association frame is not a valid public key.  Otherwise, upon receiving the third Security Association frame with the MK_KMAC equal to MK_KMAC_3, the node shall send to the hub the fourth Security Association frame, setting the MK_KMAC field of the Security Association Data thereof to MK_KMAC_4 as also calculated (39).

Upon successfully sending the fourth Security Association frame, the node shall display a 5-digit decimal number Display_A as derived in (41). Upon receiving the fourth Security Association frame with the MK_KMAC equal to MK_KMAC_4, the hub shall display a 5-digit decimal number Display_B as also derived in (41).  After the node and the hub have been verified to display the same 5-digit number, they shall each be informed through their respective user interfaces that their mutual authentication has succeeded. Otherwise, they shall each be informed that their mutual authentication has failed.

Upon determining that their mutual authentication has succeeded, the node and the hub shall each compute the shared MK as given in Eq. (42), treating their association procedure completed.

The node and the hub shall each compute DHKey and extract Temp_1 as follows:

DHKey = X(SKA×PKB) = X(SKB×PKA) = X(SKA×SKB×G)

Temp_1 = RMB_128(DHKey)

The node and the hub shall each derive MK_KMAC_3 and MK_KMAC_4 as follows:

MK_KMAC_3 = CMAC(Temp_1, Address_A || Address_B || Nonce_A || Nonce_B || Security_Suite_Selector, 64)

MK_KMAC_4 = CMAC(Temp_1, Address_B || Address_A || Nonce_B || Nonce_A || Security_Suite_Selector, 64)

The node and the hub shall also compute Display_A and Display_B, respectively, as follows:

D = CMAC(Nonce_B, Nonce_A ||Temp_1, 16)

Display_A = BS2DI(D), Display_B = BS2DI(D)

After the aforementioned verifications have passed, the node and the hub shall each derive their shared MK as follows:

MK = CMAC(Temp_2, Nonce_A || Nonce_B, 128) , where Temp_2 = LMB_128(DHKey)

In the above, X(P) = X(PX,PY) = PX = X-coordinate of P, which is computed from SKA×PKB at the node and from SKB×PKA at the hub, respectively. BS2DI(BS) converts the bit string BS, based on IEEE Std P1363-2000, to a positive decimal integer by treating the leftmost bit of the string as the most-significant bit of the integer.

SKA is the node’s 256-bit private key (an integer) kept secret by the node.

SKB is the hub’s 256-bit private key (an integer) kept secret by the hub.

PKA is the node’s 256-bit public key (a pair of X and Y coordinates) transmitted by the node.

PKB is the hub’s 256-bit public key (a pair of X and Y coordinates) transmitted by the hub.

Address_A is the Sender Address field of the frame payload of the third Security Association frame.

Address_B is the Recipient Address field of the frame payload of the third Security Association frame.

Nonce_A is the Sender Nonce field of the frame payload of the third Security Association frame.

Nonce_B is the Sender Nonce field of the frame payload of the second Security Association frame.

Security_Suite_Selector is the Security Suite Selector field of the frame payload of the first Security Association frame.

The display authenticated association procedure is illustrated in Figure 96.

— Display authenticated association procedure

Disassociation

Either the node or the hub may initiate a security disassociation procedure to nullify an existing security association and hence the shared MK and PTK with a hub or a node, by unilaterally sending a Security Disassociation frame, setting the DA_KMAC field of the frame payload depicted in Figure 24 to DA_KMAC as calculated in Eq. (43).

Upon successfully sending the Security Disassociation frame, the sender shall erase the MK and the corresponding PTK materials from its internal storage.  Upon receiving a Security Disassociation frame with the DA_KMAC equal to DA_KMAC, the recipient shall also erase the MK and the corresponding PTK materials from its internal storage.

The node and the hub shall compute DA_KMAC as follows:

DA_KMAC = CMAC(MK, Address_A || Address_B, 64)

The input fields to the computation above are defined as follows:

MK is the shared MK to be repealed.

Address_A is the Sender Address field of the frame payload of the Security Disassociation frame.

Address_B is the Recipient Address field of the frame payload of the Security Disassociation frame.

The security disassociation procedure is illustrated in Figure 97.

— Security Disassociation procedure

Temporal keys

In the PTK creation procedure specified in this subclause, the cipher-based message authentication code (CMAC) algorithm as specified in the NIST Special Publication 800-38B, with the AES forward cipher function under a 128-bit key as specified in FIPS Pub 197, is used to compute key message authentication codes (KMAC). Specifically, the functional notation CMAC(K, M, L) represents the L-bit output of the CMAC applied under key K to message M based on the AES forward cipher function.

Moreover, the bit string truncation functions LMB_n(S) and RMB_n(S) designate the n leftmost and the n rightmost bits of the bit string S, respectively. The sign || denotes concatenation of bit strings that are converted according to FIPS Pub 180-2 from certain fields of the frames of concern.

PTK creation

A node and a hub shall have a 128-bit secret shared master key (MK) resulting from a successful run of a security association protocol as provided in 8.1 prior to running a pairwise temporal key (PTK) creation procedure to generate a PTK for exchanging secured frames with each other.

Either the node or the hub may initiate a PTK creation procedure, by sending to the hub or the node the first PTK frame of the procedure.  Whichever sends the first PTK frame is referred to as the iniator, and the other is referred to as the responder.

Upon receiving the first PTK frame, the responder shall send to the initiator the second PTK frame, joining or aborting the PTK creation procedure, and setting the PTK_KMAC field of the frame payload depicted in Figure 25 to PTK_KMAC_2 as calculated in Eq. (47) if joining.

If the initiator receives the second PTK frame indicating the responder is aborting the PTK creation procedure, it shall abort the current PTK creation procedure.  It may later initiate a new PTK creation procedure if the responder aborted the procedure due to temporary lack of resources.

Upon receiving the second PTK creation frame, the initiator shall send to the responder the third PTK frame, setting the PTK_KMAC field of the frame payload to PTK_KMAC_3 as also calculated in Eq. (47). The initiator shall send this PTK frame only after it has verified that the PTK_KMAC contained in the second PTK frame is equal to PTK_KMAC_2.

Upon successfully sending the third PTK frame, the initiator shall compute a new PTK as given below, treating the responder’s true identity authenticated and the PTK creation procedure completed. Upon receiving the third PTK frame with the PTK_KMAC equal to PTK_KMAC_3, the responder shall also compute the new PTK, treating the initiator’s true identity authenticated and the PTK creation procedure completed as well.

After the respective appropriate verifications have passed, the initiator and the responder shall each derive the PTK, KCK, PTK_KMAC_2, and PTK_KMAC_3 as follows:

PTK = CMAC(MK, Address_I || Address_R || Nonce_I || Nonce_R || PTK_Index, 128)

KCK = CMAC(MK, Address_R || Address_I || Nonce_R || Nonce_I || PTK_Index, 128)

P = CMAC(KCK, Address_I || Address_R || Nonce_R || Nonce_I || PTK_Index, 128)

PTK_KMAC_2 = LMB_64(P), PTK_KMAC_3 = RMB_64(P)

The fields that form the message of CMAC correspond to the fields in the PTK frames of the current PTK creation procedure and are converted to bit strings according to FIPS Pub 180-2:

Address_I is the Sender Address field of the frame payload of the first PTK frame.

Address_R is the Recipient Address field of the frame payload of the first PTK frame.

Nonce_I is the Sender Nonce field of the frame payload of the first PTK frame.

Nonce_R is the Sender Nonce field of the frame payload of the second PTK frame.

PTK_Index is the PTK Index field of the frame payload of the first PTK frame.

The PTK creation procedure is illustrated in Figure 98.

— PTK creation procedure

GTK distribution

A node and a hub shall have a pairwise temporal key (PTK) prior to running a group temporal key (GTK) distribution procedure to transport a GTK to the node for multicasting secured frames to the node and others.

The hub, but not the node, may send a GTK to the node, by sending to the node a GTK frame containing the GTK and secured with the PTK being used between the hub and the node.

Message security

A hub shall transmit a beacon, if appropriate, as an unsecured frame or as a secured frame authenticated, but not encrypted, by a group temporal key (GTK) distributed to the nodes that are secured with it. Nodes that do not have a secured relationship with the hub may receive and process the beacon without validating the message integrity code (MIC) included therein.

At their Secured or Connected State, a node and a hub shall exchange and process only secured frames at a security level negotiated during their last association, with the following additional considerations:

GTK frames shall always be secured, both authenticated and encrypted.

Poll and T-Poll frames shall never be authenticated or encrypted.

Control type frames other than Poll and T-Poll frames

shall be neither authenticated nor encrypted if the hub and the node have agreed to applying no control type frame authentication;

shall be authenticated but not encrypted if the hub and the node have agreed to applying control type frame authentication.

A recipient shall ignore a received frame with an unexpected security level, other than performing acknowledgment if needed. A recipient shall also ignore a received secured frame with an invalid MIC, i.e., the MIC value calculated from the received frame as described in 8.3.1.5 is not the same as the MIC field contained in the received frame, except again for returning an acknowledgment.

Frame authentication, encryption, and decryption

Frames shall be transmitted as secured or unsecured frames according to Figure 4 and Table 26, wherein SL and CFA denote the Security Level field and the Control Frame Authentication field, respectively, of the Security Suite Selector field contained in the last Association frame exchanged between the sender and the recipient.  A node or a hub shall ignore received frames secured or unsecured unexpectedly, except for returning an acknowledgment if required by the acknowledgment policy and for taking an appropriate defensive measure against potential security violations.

— Conditions for transmitting unsecured and secured frames

| Frame name | Frame (message) security |
| --- | --- |
| Beacon | unsecured or authenticated with a distributed GTK, at sender’s discretion |
| Security Association | unsecured at Orphan state for secured communication; not sent otherwise |
| Security Disassociation | unsecured at Associated state; authenticated but not encrypted at Secured or Connected state if SL = 1; authenticated and encrypted at Secured or Connected state if SL = 2; not sent otherwise |
| PTK | unsecured at Associated state; authenticated but not encrypted at Secured or Connected state if SL = 1; authenticated and encrypted at Secured or Connected state if SL = 2; not sent otherwise |
| GTK | authenticated but not encrypted at Secured or Connected state if SL = 1; authenticated and encrypted at Secured or Connected state if SL = 2; not sent otherwise |
| Connection Request, Connection Assignment | unsecured at Orphan state for unsecured communication; authenticated but not encrypted at Secured or Connected state if SL = 1; authenticated and encrypted at Secured or Connected state if SL = 2; not sent otherwise |
| Multinode Connection Assignment | unsecured always |
| Disconnection | unsecured at Connected state for unsecured communication; authenticated but not encrypted at Connected state if SL = 1; authenticated and encrypted at Connected state if SL = 2; not sent otherwise |
| Command exchanged within same BAN | unsecured at Connected state for unsecured communication; authenticated but not encrypted at Connected state if SL = 1; authenticated and encrypted at Connected state if SL = 2; not sent otherwise |
| Command exchanged between BANs | unsecured always |
| I-Ack, B-Ack, I-Ack+Poll, B-Ack+Poll | unsecured at Orphan or Associated state; unsecured at Secured state if CFA = 0; unsecured at Connected state for unsecured communication or if CFA = 0 for secured communication; authenticated but not encrypted at Secured or Connected state if SL = 1 or 2 and CFA = 1; not sent otherwise |
| Poll and T-Poll addressed to Connected_NID |  |
| Poll and T-Poll not addressed to Connected_NID | unsecured always |
| B2 | unsecured or authenticated with a distributed GTK, at sender’s discretion |
| Emergency, User defined data subtype | unsecured at Connected state for unsecured communication; authenticated but not encrypted at Connected state if SL = 1; authenticated and encrypted at Connected state if SL = 2; not sent otherwise |

Secured frames shall be authenticated, and encrypted/decrypted when required, based on AES-128 CCM, i.e., the CCM mode as specified in the NIST Special Publication 800-38C, with the AES forward cipher function for 128-bit keys as specified in FIPS Pub 197 applied as the underlying block cipher algorithm.

Prior to exchanging secured unicast frames, the two communicating parties, a node and a hub, shall have a pairwise temporal key (PTK) for use as the AES key applied to the unicast frames. They may have an additional PTK before the current PTK is retired. Prior to multicast secured frames to a group, the hub shall have distributed a group temporal key (GTK) to the nodes of the group for use as the AES key applied to the multicast frames.

A temporal key, PTK or GTK, shall be retired no later than when the Security Sequence Number field of the last frame secured by the key has reached the maximum value supported by the field. It may be retired earlier as needed.

The length of what is referred to as the Message Authentication Code (MAC) for message (frame) authentication in NIST Special Publication 800-38C but as the Message Integrity Code (MIC) in this standard—to be distinguished from another accustomed standing of the term MAC for medium access control—shall be four octets. That is, in the NIST Special Publication 800-38C, t = 4. Also, q = 2 shall be chosen as the octet length of the binary representation of the octet length of the frame payload.

The bit order of each input block to the CCM invocation and AES encryption shall be formatted as illustrated in Figure 99.  It is the concatenation of the bits of the ordered octets of the constituent fields of the block, where the octet order of each constituent field is defined below, and the bits of each octet are ordered such that the most-significant bit (msb) is the first bit of the octet while the least-significant bit (lsb) is the last bit of the octet. The first octet or the first bit of a given component is shown on the left, and the last octet or the last bit is shown on the right, in the context of the component. The bit notations input0, …, input127 correspond to those used for AES input block formation specified in FIPS Pub 197.

— Bit order for AES input blocks

Nonce formation

The Nonce as a required input field to each instance of CCM frame authentication and encryption/decryption is a 13-octet field that is formatted as shown in Figure 100.

Here, the octets of the MAC header and Security Number fields are each ordered from left to right in accordance with their transmit order as defined in 6.1 and 6.2.

— Nonce format

Initial block B0 construction

The block B0 as the first input block to the cipher block chaining (CBC) for frame authentication, i.e., MIC computation, is a 16-octet field that is formatted as shown in Figure 101.  Here, Q = L_FP is the octet length of the frame payload as defined in Figure 101 and is encoded with the octet containing the most-significant bits on the left and the octet containing the least-significant bits on the right.

Only this block is present if the current frame does not have a frame payload.

(a) Frame payload encrypted

(b) Frame payload not encrypted

— Initial block B B0 format

Payload blocks B1, …, Bm construction

The blocks B1, …, Bm as the subsequent input blocks to the CBC frame authentication, and also as the input blocks to the counter mode encryption/decryption, i.e., ciphertext computation and plain text recovery, if the frame payload is to be encrypted/decrypted, are each a 16-octet field that is formatted as shown in Figure 102.

Here, a =L_FP is the octet length of the frame payload as defined in Figure 14 and is encoded with the octet containing the most-significant bits on the left and the octet containing the least-significant bits on the right.  The Frame Payload field is ordered from left to right in consistency with it transmit order as defined in 6.1 and 6.2.

These blocks are constructed from the unencrypted or decrypted frame payload. The last block contains one or more padded zero octets on the right end if the frame payload is not an integral multiple of 16 octets.

None of these blocks is present if the current frame does not have a frame payload.

(a) Frame payload encrypted

(b) Frame payload not encrypted

— Payload blocks B1, …, Bm format

Counter blocks Ctr0, …, Ctrm formation

The block Ctr0 as the input block to the counter mode encryption of the CBC output for MIC computation, and each of the blocks Ctr1…, Ctrm as the input blocks to the counter mode encryption/decryption if the frame payload is to be encrypted/decrypted, is a 16-octet field that is formatted as shown in Figure 103.

Here, i = 0, …, m, respectively, and is encoded with the octet containing the most-significant bits on the left and the octet containing the least-significant bits on the right.

— Counter Blocks Ctr0, …, Ctrm format

MIC computation

The MIC field in an authenticated frame is calculated as shown in Figure 104 , where

MIC = LMB_n(M), M = AES(Ctr0) ( Xm

X0 = AES(B0), Xi = AES(Bi ( Xi-1), i = 1, …, m

Here, LMB_n(M) designates the n leftmost bits of the bit string M, the symbol ( denotes bitwise exclusive-OR, and AES(B) represents the output of the forward cipher function of the AES block cipher algorithm applied to block B under the AES key PTK or GTK used to secure the frame. The MIC is ordered for transmission from its first octet on the left to its last octet on the right, as also illustrated in Figure 104

The octet notations out0 , …, out15 correspond to those used for AES output block formation specified in FIPS Pub 197.

The blocks required for the MIC computation are constructed from the unencrypted version of the frame to be transmitted at the sender side, and from the decrypted version of the received frame at the recipient side if the frame is encrypted.

— MIC calculation and transmit order

Frame payload encryption

The encrypted frame payload in an encrypted frame is formatted as shown Figure 105, where

B'i = Bi ( AES(Ctri), i = 1, …, m-1

B'm = L_n(Bm) ( L_n(AES(Ctrm))

Here, the symbol ( denotes bitwise exclusive-OR, and L_n(B) designates the n leftmost octets of B. Moreover, AES(Ctri) represents the output of the forward cipher function of the AES block cipher algorithm applied to the counter block Ctri under the AES key PTK or GTK used to secure the frame. The encrypted frame payload has the same length as the unencrypted frame payload, so that n ≤ 16 is the number of octets in Bm excluding the zero padding octets if any.

Each encrypted block is ordered for transmission from its first octet on the left to its last octet on the right, as also illustrated in Figure 105. The octet notations out0, …, out15 correspond to those used for AES output block formation specified in FIPS Pub 197.

— Encrypted Frame Payload format for encrypted frames

Frame payload decryption

The frame payload in an encrypted frame is decrypted as shown in Figure 106, where

Bi = B'i ( AES(Ctri), i = 1, …, m-1

B–m = B'm ( L_n(AES(Ctrm))

The decrypted frame payload has the same length as the encrypted frame payload, so that n ≤ 16 is the number of octets in the last block B'm of the encrypted frame payload received. The last decrypted block B–m is padded with 16 – n zero octets at the right end to form the last block Bm as shown in Figure 101 (a) for MIC calculation over the received frame as described in 8.3.1.5.

Each decrypted block is ordered for MIC calculation, and delivery to the MAC client if the MIC is valid, from its first octet on the left to its last octet on the right, as also illustrated in Figure 106. Again the octet notations out0, …, out15 correspond to those used for AES output block formation specified in FIPS Pub 197.

— Decrypted Frame Payload format for encrypted frames

Replay protection

A recipient shall treat a received frame with a valid MIC value, i.e., with the MIC field contained in the received frame equal to the MIC value calculated from the received frame, as a replay of a previously received frame if the Security Sequence Number field of the current frame has a value equal to or smaller than

GTK_SSN if the current frame is secured by a group temporal key (GTK) that has not been used for any previously received frames with a valid MIC field, where GTK_SSN is the value of the GTK SSN field contained in the Group Temporal Key (GTK) frame through which the node received this GTK from the sender of the current frame;

SSN if the current frame is secured by a PTK or GTK that has been used for one or more previously received frames with a valid MIC field, where SSN is the value of the Security Sequence Number field found in the last received frame containing a valid MIC and secured by this PTK or GTK.

The recipient shall discard all detected replayed frames.  Appropriate precautions should be taken against excessive detected replays.

Optional cipher functions

For secured communications, all nodes and hubs shall support the forward cipher function of the Advanced Encryption Standard (AES). For secured broadcast and multicast transmissions, the sender shall use the forward cipher function of AES.

If a node and a hub both support a non-AES cipher function as listed in Table 8, in their secured unicast communications with each other, they may use it in place of the AES forward cipher function as specified in 8.1-8.3.

Narrowband (NB) PHY specification

This clause specifies a narrowband physical layer (PHY) option for IEEE 802.15.6. The PHY is responsible for the following tasks:

Activation and deactivation of the radio transceiver

CCA within the current channel

Data transmission and reception

This clause also provides a method for transforming a physical-layer service data unit (PSDU) into a physical-layer protocol data unit (PPDU). During the transmission, the PSDU shall be pre-appended with a physical-layer preamble and a physical-layer header in order to create the PPDU. At the receiver, the physical-layer preamble and physical-layer header serve as aids in the demodulation, decoding and delivery of the PSDU.

Figure 107 shows the format for the PPDU, which is composed of three main components: the PLCP preamble, the PLCP header and the PSDU. The components are listed in the order of transmission. The PLCP preamble is the first component of the PPDU (see 11.2). The purpose of the preamble is to aid the receiver in the timing synchronization and carrier-offset recovery

The PLCP header is the second main component of the PPDU (see 9.3). The purpose of this component is to convey the necessary information about the PHY and media access control (MAC) parameters to aid in the decoding of the PSDU at the receiver. The PLCP header can be further decomposed into a RATE field, a LENGTH field, a SCRAMBLER SEED, a BURST MODE field, reserved bits, a header check sequence (HCS), and spell out what acronym means first time in document BCH parity bits. The BCH parity bits are added in order to improve the robustness of the PLCP header. The PLCP header shall be transmitted using the given header data rate in the operating frequency band.

The PSDU is the last component of the PPDU (see 9.4). This component is formed by concatenating the MAC header with the MAC frame body and frame check sequence (FCS). The PSDU is then scrambled and optionally encoded by a BCH code. The PSDU shall be transmitted using any of the available data rates available in the operating frequency band.

— Standard PPDU structure

When transmitting the packet, the PLCP preamble is sent first, followed by the PLCP header and finally the PSDU. All multiple octet fields shall be transmitted with least significant octet first and each octet shall be transmitted with least significant bit (LSB) first.

A compliant device shall be able to support transmission and reception in one of the following frequency bands: 402 – 405 MHz, 420 – 450 MHz, 863 – 870 MHz, 902 – 928 MHz, 950 – 956 MHz, 2360 – 2400 MHz and 2400 – 2483.5 MHz.

Data rate-dependent parameters

The data-rate dependent parameters for each of the possible frequency bands of operation are provided in subsequent subclauses. This standard is intended to conform to established regulations in United States, Europe, Japan and Korea.

402 – 405 MHz

The modulations parameters for this band are defined in Table 27.

— Modulation parameters for PLCP Header and PSDU

| Packet Component | Modulation | Symbol Rate (ksps) | Code Rate (k/n) | Spreading Factor (S) | Pulse Shape | Information Data Rate (kbps) | Support |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PLCP Header | π/2-DBPSK | 187.5 | 19/31* | 2 | SRRC | 57.5 | Mandatory |
| PSDU | π/2-DBPSK | 187.5 | 51/63 | 2 | SRRC | 75.9 | Mandatory |
| PSDU | π/2-DBPSK | 187.5 | 51/63 | 1 | SRRC | 151.8 | Mandatory |
| PSDU | π/4-DQPSK | 187.5 | 51/63 | 1 | SRRC | 303.6 | Mandatory |
| PSDU | π/8-D8PSK | 187.5 | 51/63 | 1 | SRRC | 455.4 | Optional |
| * BCH (31, 19) code is a shortened code derived from a BCH (63, 51) code |

420 – 450 MHz

The modulations parameters for this band are defined in Table 27.

— Modulation parameters for PLCP Header and PSDU

| Packet Component | Modulation | Symbol Rate (ksps) | Code Rate (k/n) | Spreading Factor (S) | BT | Information Data Rate (kbps) | Support |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PLCP Header | GMSK | 187.5 | 19/31* | 2 | 0.5 | 57.5 | Mandatory |
| PSDU | GMSK | 187.5 | 51/63 | 2 | 0.5 | 75.9 | Mandatory |
| PSDU | GMSK | 187.5 | 51/63 | 1 | 0.5 | 151.8 | Mandatory |
| PSDU | GMSK | 187.5 | 1/1 | 1 | 0.5 | 187.5 | Optional |
| * BCH (31, 19) code is a shortened code derived from a BCH (63, 51) code |

863 – 870 MHz

The modulations parameters for this band are defined in Table 29.

— Modulation parameters for PLCP Header and PSDU

| Packet Component | Modulation | Symbol Rate (ksps) | Code Rate (k/n) | Spreading Factor (S) | Pulse Shape | Information Data Rate (kbps) | Support |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PLCP Header | π/2-DBPSK | 250 | 19/31* | 2 | SRRC | 76.6 | Mandatory |
| PSDU | π/2-DBPSK | 250 | 51/63 | 2 | SRRC | 101.2 | Mandatory |
| PSDU | π/2-DBPSK | 250 | 51/63 | 1 | SRRC | 202.4 | Mandatory |
| PSDU | π/4-DQPSK | 250 | 51/63 | 1 | SRRC | 404.8 | Mandatory |
| PSDU | π/8-D8PSK | 250 | 51/63 | 1 | SRRC | 607.1 | Optional |
| * BCH (31, 19) code is a shortened code derived from a BCH (63, 51) code |

902 – 928 MHz

The modulations parameters for this band are defined in Table 30.

— Modulation parameters for PLCP Header and PSDU

| Packet Component | Modulation | Symbol Rate (ksps) | Code Rate (k/n) | Spreading Factor (S) | Pulse Shape | Information Data Rate (kbps) | Support |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PLCP Header | π/2-DBPSK | 300 | 19/31* | 2 | SRRC | 91.9 | Mandatory |
| PSDU | π/2-DBPSK | 300 | 51/63 | 2 | SRRC | 121.4 | Mandatory |
| PSDU | π/2-DBPSK | 300 | 51/63 | 1 | SRRC | 242.9 | Mandatory |
| PSDU | π/4-DQPSK | 300 | 51/63 | 1 | SRRC | 485.7 | Mandatory |
| PSDU | π/8-D8PSK | 300 | 51/63 | 1 | SRRC | 728.6 | Optional |
| * BCH (31, 19) code is a shortened code derived from a BCH (63, 51) code |

950 – 956 MHz

The modulations parameters for this band are defined in Table 31.

— Modulation parameters for PLCP Header and PSDU

| Packet Component | Modulation | Symbol Rate (ksps) | Code Rate (k/n) | Spreading Factor (S) | Pulse Shape | Information Data Rate (kbps) | Support |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PLCP Header | π/2-DBPSK | 250 | 19/31* | 2 | SRRC | 76.6 | Mandatory |
| PSDU | π/2-DBPSK | 250 | 51/63 | 2 | SRRC | 101.2 | Mandatory |
| PSDU | π/2-DBPSK | 250 | 51/63 | 1 | SRRC | 202.4 | Mandatory |
| PSDU | π/4-DQPSK | 250 | 51/63 | 1 | SRRC | 404.8 | Mandatory |
| PSDU | π/8-D8PSK | 250 | 51/63 | 1 | SRRC | 607.1 | Optional |
| * BCH (31, 19) code is a shortened code derived from a BCH (63, 51) code |

2360 – 2400 MHz

The modulations parameters for this band are defined in Table 32.

— Modulation parameters for PLCP Header and PSDU

| Packet Component | Modulation | Symbol Rate (ksps) | Code Rate (k/n) | Spreading Factor (S) | Pulse Shape | Information Data Rate (kbps) | Support |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PLCP Header | π/2-DBPSK | 600 | 19/31* | 4 | SRRC | 91.9 | Mandatory |
| PSDU | π/2-DBPSK | 600 | 51/63 | 4 | SRRC | 121.4 | Mandatory |
| PSDU | π/2-DBPSK | 600 | 51/63 | 2 | SRRC | 242.9 | Mandatory |
| PSDU | π/2-DBPSK | 600 | 51/63 | 1 | SRRC | 485.7 | Mandatory |
| PSDU | π/4-DQPSK | 600 | 51/63 | 1 | SRRC | 971.4 | Mandatory |
| * BCH (31, 19) code is a shortened code derived from a BCH (63, 51) code |

2400 – 2483.5 MHz

The modulations parameters for this band are defined in Table 33.

— Modulation parameters for PLCP Header and PSDU

| Packet Component | Modulation | Symbol Rate (ksps) | Code Rate (k/n) | Spreading Factor (S) | Pulse Shape | Information Data Rate (kbps) | Support |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PLCP Header | π /2-DBPSK | 600 | 19/31* | 4 | SRRC | 91.9 | Mandatory |
| PSDU | π/2-DBPSK | 600 | 51/63 | 4 | SRRC | 121.4 | Mandatory |
| PSDU | π/2-DBPSK | 600 | 51/63 | 2 | SRRC | 242.9 | Mandatory |
| PSDU | π/2-DBPSK | 600 | 51/63 | 1 | SRRC | 485.7 | Mandatory |
| PSDU | π /4-DQPSK | 600 | 51/63 | 1 | SRRC | 971.4 | Mandatory |

PLCP preamble

A preamble shall be added prior to the PLCP header in order to aid the receiver in packet detection, timing synchronization and carrier-offset recovery. Two unique preambles are defined in order to mitigate false alarms due to networks operating on adjacent channels. The mapping between channel number and preamble is defined in 9.5.3. Each preamble is constructed by concatenating a length-63 m-sequence with a 010101010101101101101101101 extension sequence. The former sequence can be used to implement packet detection, coarse-timing synchronization and carrier-offset recovery, while the latter sequence can be used to implement fine-timing synchronization.

The two preamble sequences are defined in Table 34 and Table 35. The preambles shall be transmitted at the symbol rate for the desired band of operation and will be encoded using the same modulation parameters as defined for the PLCP Header in the preceding tables

— Preamble Sequence #1

| Bit | Bit Value | Bit | Bit Value | Bit | Bit Value | Bit | Bit Value |
| --- | --- | --- | --- | --- | --- | --- | --- |
| b0 | 0 | b23 | 0 | b46 | 1 | b69 | 0 |
| b1 | 1 | b24 | 0 | b47 | 0 | b70 | 1 |
| b2 | 0 | b25 | 1 | b48 | 0 | b71 | 0 |
| b3 | 1 | b26 | 1 | b49 | 0 | b72 | 1 |
| b4 | 0 | b27 | 1 | b50 | 0 | b73 | 0 |
| b5 | 1 | b28 | 0 | b51 | 1 | b74 | 1 |
| b6 | 1 | b29 | 0 | b52 | 0 | b75 | 1 |
| b7 | 0 | b30 | 0 | b53 | 0 | b76 | 0 |
| b8 | 0 | b31 | 1 | b54 | 0 | b77 | 1 |
| b9 | 1 | b32 | 0 | b55 | 0 | b78 | 1 |
| b10 | 1 | b33 | 1 | b56 | 0 | b79 | 0 |
| b11 | 0 | b34 | 1 | b57 | 1 | b80 | 1 |
| b12 | 1 | b35 | 1 | b58 | 1 | b81 | 1 |
| b13 | 1 | b36 | 1 | b59 | 1 | b82 | 0 |
| b14 | 1 | b37 | 0 | b60 | 1 | b83 | 1 |
| b15 | 0 | b38 | 0 | b61 | 1 | b84 | 1 |
| b16 | 1 | b39 | 1 | b62 | 1 | b85 | 0 |
| b17 | 1 | b40 | 0 | b63 | 0 | b86 | 1 |
| b18 | 0 | b41 | 1 | b64 | 1 | b87 | 1 |
| b19 | 1 | b42 | 0 | b65 | 0 | b88 | 0 |
| b20 | 0 | b43 | 0 | b66 | 1 | b89 | 1 |
| b21 | 0 | b44 | 0 | b67 | 0 |  |  |
| b22 | 1 | b45 | 1 | b68 | 1 |  |  |

— Preamble Sequence #2

| Bit | Bit Value | Bit | Bit Value | Bit | Bit Value | Bit | Bit Value |
| --- | --- | --- | --- | --- | --- | --- | --- |
| b0 | 0 | b23 | 1 | b46 | 1 | b69 | 0 |
| b1 | 1 | b24 | 0 | b47 | 1 | b70 | 1 |
| b2 | 1 | b25 | 0 | b48 | 0 | b71 | 0 |
| b3 | 0 | b26 | 1 | b49 | 0 | b72 | 1 |
| b4 | 1 | b27 | 0 | b50 | 0 | b73 | 0 |
| b5 | 0 | b28 | 0 | b51 | 1 | b74 | 1 |
| b6 | 0 | b29 | 1 | b52 | 1 | b75 | 1 |
| b7 | 0 | b30 | 1 | b53 | 1 | b76 | 0 |
| b8 | 1 | b31 | 1 | b54 | 0 | b77 | 1 |
| b9 | 0 | b32 | 1 | b55 | 1 | b78 | 1 |
| b10 | 0 | b33 | 0 | b56 | 0 | b79 | 0 |
| b11 | 0 | b34 | 0 | b57 | 1 | b80 | 1 |
| b12 | 0 | b35 | 0 | b58 | 1 | b81 | 1 |
| b13 | 1 | b36 | 0 | b59 | 1 | b82 | 0 |
| b14 | 0 | b37 | 0 | b60 | 1 | b83 | 1 |
| b15 | 1 | b38 | 1 | b61 | 1 | b84 | 1 |
| b16 | 1 | b39 | 1 | b62 | 1 | b85 | 0 |
| b17 | 0 | b40 | 0 | b63 | 0 | b86 | 1 |
| b18 | 0 | b41 | 1 | b64 | 1 | b87 | 1 |
| b19 | 1 | b42 | 1 | b65 | 0 | b88 | 0 |
| b20 | 0 | b43 | 1 | b66 | 1 | b89 | 1 |
| b21 | 1 | b44 | 0 | b67 | 0 |  |  |
| b22 | 0 | b45 | 0 | b68 | 1 |  |  |

PLCP Header

A PLCP header shall be added after the PLCP preamble to convey information about the PHY and MAC parameters that is needed at receiver in order to decode the PSDU. The PLCP header shall be constructed as shown in Figure 108:

- Based on the information provided by the MAC, form the PHY header according to 9.3.1.

Calculate the 4-bit HCS value over the PHY header using the CRC-4 ITU polynomial: , according to 9.3.2.

As shown in Figure 112 and according to 9.3.3, a BCH (31, 19) code, which is a shortened code derived from a BCH (63, 51) code, is applied to the concatenation of the PHY header (15 bits) and HCS (4 bits).

The encoded bits are spread using a repetition code according to 9.4.4, where , and then interleaved using a bit interleaver defined in 9.4.4. The spreading factor is determined by the frequency band of operation (see 9.1).

The resulting bit stream is then scrambled according to 9.4.5, where the seed of the scrambler is determined by the channel number, i.e., even channels are mapped to scrambler seed 0 and odd channels are mapped to scrambler seed 1.

Finally, the resulting scrambled bit steam is then mapped onto the appropriate constellation (see 9.4.6), which is determined by the data rate and frequency band of operation (see 9.1).

— Block diagram of PLCP header construction

— BCH encoding scheme for PLCP header construction

PHY Header

The PHY header contains information about the data rate of the MAC frame body, the length of the MAC frame body (which does not include the MAC header or the FCS) and information about the next packet – whether it is being sent in a burst mode.

The PHY header field shall be composed of 15 bits, numbered from 0 to 14 as illustrated in Figure 110. Bits 0-2 shall encode the RATE field, which conveys the information about the type of modulation, the symbol rate, frequency deviation or pulse shape, the coding rate, and the spreading factor used to transmit the PSDU. Bits 4-11 shall encode the LENGTH field, with the least-significant bit being transmitted first. Bit 13 shall encode whether or not the packet is being transmitted in the burst (streaming) mode. Bit 14 shall encode the scrambler seed. All other bits which are not defined in this Clause shall be understood to be reserved for future use and shall be set to 0.

— PHY Header bit assignment

Data Rate (RATE)

Depending on the data rate (RATE), bits R0–R2 shall be set according to the values in Table 36.

— Rate dependent parameters

|  | 402 – 405 MHz | 420 – 450 MHz | 863 – 870 MHz, 950 – 956 MHz | 902 – 928 MHz | 2360-2400 MHz 2400 – 2483.5 MHz |
| --- | --- | --- | --- | --- | --- |
| R0 – R2 | Data Rate (kbps) | Data Rate (kbps) | Data Rate (kbps) | Data Rate (kbps) | Data Rate (kbps) |
| 000 | 75.9 | 75.9 | 101.2 | 121.4 | 121.4 |
| 100 | 151.8 | 151.8 | 202.4 | 242.9 | 242.9 |
| 010 | 303.6 | 187.5 | 404.8 | 485.7 | 485.7 |
| 110 | 455.4 | Reserved | 607.1 | 728.6 | 971.4 |
| 001 | Reserved | Reserved | Reserved | Reserved | Reserved |
| 101 | Reserved | Reserved | Reserved | Reserved | Reserved |
| 011 | Reserved | Reserved | Reserved | Reserved | Reserved |
| 111 | Reserved | Reserved | Reserved | Reserved | Reserved |

PLCP Length Field (LENGTH)

The PLCP length field shall be an unsigned 8-bit integer that indicates the number of un-coded information octets in the MAC frame body (which does not include the MAC header or the FCS).

Burst Mode field (BM)

The MAC shall set the burst mode (BM) bit, as defined in Table 37, to indicate whether the next packet is part of a packet “burst”, i.e., burst mode transmission. In burst mode, the inter-frame spacing shall be equal to a pMIFS (see 9.6.4).

— Burst Mode field

| Burst Mode (BM) bit | Next Packet Status |
| --- | --- |
| 0 | Next packet is not part of burst |
| 1 | Next packet is part of burst |

Scrambler Seed Mode Field (SS)

The MAC shall set the scrambler seed bit (SS) according to the scrambler seed identifier value. This bit value corresponds to the seed value chosen for the data scrambler.

Header check sequence

The PHY header shall be protected with a 4-bit (CRC-4 ITU) header check sequence (HCS). The HCS shall be the ones complement of the remainder generated by the modulo-2 division of the PHY header by the polynomial: . The HCS bits shall be processed in the transmit order. A schematic of the processing order is shown in Figure 111. The registers shall be initialized to all ones.

— Block diagram of a CRC-4 implementation

BCH encoder for PLCP header

The PLCP header shall use a systematic BCH (31, 19, t = 2) code is a shortened code derived from a BCH (63, 51, t = 2) code, to improve the robustness of the PLCP header. A description of the BCH (63, 51, t = 2) code can be found in 9.4.1.2. The shortened bits are removed prior to transmission.

PSDU

The PSDU is the last major component of the PPDU and shall be constructed as shown in Figure 112.

- Form the PSDU by pre-pending the 7-octet MAC header to the MAC frame body and appending a 2-octet FCS to the result.

If the code rate (k/n) < 1, the PSDU is:

Divided into blocks of messages, where each message may contain shortened bits, according to 9.4.1.1;

The resulting messages are then encoded into codewords using a BCH (63, 51) encoder to achieve the desired code rate, according to 9.4.1;

Finally, the shortened bits are removed from each of the codewords.

Pad bits are then added in order to ensure alignment on a symbol boundary according to 9.4.3.

If the spreading factor is 2 or 4, the resulting un-coded or coded bits are spread using a repetition code, according to 9.4.4, and then interleaved using a bit interleaver defined in 9.4.5.

The resulting bit stream is then scrambled according to 9.4.5

Finally, the resulting scrambled bit stream is then mapped onto the appropriate constellation (see 9.4.6), which is determined by the data rate and frequency band of operation (see 9.1).

— Block diagram of PSDU construction

BCH Encoder for PSDU

A code rate of 51/63 shall be supported by a systematic BCH encoder. The information bits shall be encoded using BCH encoding process defined in 9.4.1.1. The definition for the systematic BCH encoder shall be defined in 9.4.1.2.

BCH Encoding Process

The scrambled PSDU shall be encoded using the following procedure:

- Compute the number of bits in the PSDU :

where  is the number of octets in the MAC header,  is the number of octets in the MAC frame body and  is the number of octets in the FCS.

Calculate the number of BCH codeword :

where  is the number of message bits for the selected BCH code.

Compute the number of shortening bits, , to be padded to the  data bits before encoding as follows:

The shortening bits shall be equally distributed over all  codewords with the first  codewords being shortened one bit more than the remaining codewords. Let

.

Thus, the first  codewords will have  shortened bits (message bits that are set to 0), while the remaining codewords will have  shortened bits. After encoding, the shortened bits shall be discard prior to transmission, i.e., the shortened bits are never transmitted on-air.

The BCH encoding process is illustrated in Figure 113 for a single codeword.

— BCH encoding process for a single codeword

BCH (63, 51) Encoder

The generator polynomial for a systematic BCH (63, 51, t = 2) code is given by:

.

The parity bits are determined by computing the remainder polynomial:

,

where  is the message polynomial:

,

and  and  are elements of .

The message polynomial  is created as follows:  is the first bit of the message and  is the last bit of the message, which maybe a shortened bit. The order of the parity bits is as follows:  is the first parity bit transmitted,  is the second parity bit transmitted, and  is the last parity bit transmitted.

Pad Bits

Pad bits shall be appended after the BCH encoder to ensure that the bit stream aligns on a symbol boundary. The number of pad bits, , that shall be inserted is a function of the number of PSDU bits , the number of codewords , the number of parity bits , and the modulation constellation size .

.

The pad bits shall be appended to scrambled and encoded PSDU and all of the appended pad bits shall be set to 0. In the case of un-coded transmission,  is set to 0.

Spreading

For a spreading factor of 2, each input bit is repeated two times (see illustration in Figure 114a). For a spreading factor of 4, each input bit is repeated four times (see illustration in Figure 114 b).

— Spreading scheme

Bit Interleaver

The output of the spreader shall be interleaved prior to modulation to provide robustness against error propagation. The exact structure of the bit interleaver depends on the number of un-coded or coded bits that will be transmitted on-air, which is given by:

,

where NCW is set to 0 in the case of un-coded transmission.

If , the bit interleaving operation is performed by first grouping the spread bits into blocks of 2S bits, where S is the spreading factor, and then using a block interleaver of size S(2 to permute the bits. Let the sequences  and, where, represent the input and output bits of the S(2 bit interleaver, respectively. The output of the S(2 bit interleaver is given by the following relationship:

.

If , the bit interleaving operation is performed by grouping the first 3S spread bits into a single block and then using a block interleaver of size S(3 to permute the bits within that single block. Let the sequences  and , where , represent the input and output bits of the S(3 bit interleaver, respectively. The output of the S(3 bit interleaver is given by the following relationship:

.

The remaining spread bits are then grouped into blocks of 2S bits and interleaved using the block interleaver of size S(2 shown in (19).

Data Scrambler

A side-stream scrambler with polynomial shall be used to whiten the PSDU. Figure 115 shows a typical implementation of the side-stream scrambler. The output of the scrambler is generated as:

where “(” denotes modulo-2 addition. Table 38 defines the initialization vector, xinit, for the side-stream scrambler as a function of the scrambler seed (SS) value.

— Block diagram of a side-stream scrambler

— Scrambler Seed Selection

| Scrambler Seed (SS) | Initialization Vector xinit = x[-1] x[-2] … x[-14] |
| --- | --- |
| 0 | 0 0 1 0 1 1 1 1 0 0 1 1 0 1 |
| 1 | 0 0 0 0 0 0 0 1 0 0 1 1 1 1 |

The MAC shall set the scrambler seed to 0 when the PHY is initialized and the scrambler seed shall be incremented, using a 1-bit rollover counter, for each frame sent by the PHY.

At the receiver, the side-stream de-scrambler shall be initialized with the same initialization vector, xinit, used by the transmitter. The initialization vector is determined from the scrambler seed value in the PHY header of the received frame.

Constellation Mapping

Gaussian Minimum Shift Keying (GMSK)

For the GMSK constellation, the un-coded or coded, potentially spread and interleaved binary bit stream b(n), n = 0,1,…, N-1 shall be mapped onto a corresponding frequency deviation Δf, which shall be the product of the symbol rate and a modulation index of 0.5. The relationship between the bit stream b(n) and the frequency deviation is given in Table 39 .

— GMSK symbol mapping

| b(n) | frequency deviation |
| --- | --- |
| 0 | – Δf |
| 1 | + Δf |

Differential Phase-Shift Keying (D-PSK)

For the D-PSK constellations, the coded potentially spread and interleaved bit stream shall be mapped onto one of three rotated and differentially-encoded constellations: /2-DBPSK, /4-DQPSK, or /8-D8PSK. The encoded information is carried in the phase transitions between symbols. For the PLCP preamble to PLCP header transition, the phase change is relative to the last symbol for the PLCP preamble. For the PLCP header to PSDU transition, the phase change is relative to the last symbol for the PLCP header.

The binary bit stream  shall be mapped onto a corresponding complex-values sequence  as follows:

.

whereand the relationship between the bit stream  and the phase change  is given in Table 40, Table 41, Table 42 for /2-DBPSK, /4-DQPSK, or /8-D8PSK, respectively.

— /2-DBPSK Mapping

| b(n) | k |
| --- | --- |
| 0 | π /2 |
| 1 | 3 π /2 |

— /4-D QPSK Mapping

| b(2n) | b(2n+1) | k |
| --- | --- | --- |
| 0 | 0 | π /4 |
| 0 | 1 | 3 π /4 |
| 1 | 0 | 7 π /4 |
| 1 | 1 | 5 π /4 |

— /8-D8PSK Mapping

| b(3n) | b(3n+1) | b(3n+2) | k |
| --- | --- | --- | --- |
| 0 | 0 | 0 | π /8 |
| 0 | 0 | 1 | 3 π /8 |
| 0 | 1 | 0 | 7 π /8 |
| 0 | 1 | 1 | 5 π /8 |
| 1 | 0 | 0 | 15 π /8 |
| 1 | 0 | 1 | 13 π /8 |
| 1 | 1 | 0 | 9 π /8 |
| 1 | 1 | 1 | 11 π /8 |

General Requirements

Operating Frequency Bands

A compliant device shall be able to support transmissions and reception in one of the following frequency bands:

- 402 – 405 MHz

- 420 – 450 MHz

- 863 – 870 MHz

- 902 – 928 MHz

- 950 – 956 MHz

- 2360 – 2400 MHz

- 2400 – 2483.5 MHz

Channel Numbering

The relationship between center frequency, fc, and channel number, nc, is shown in Table 43.

— Relationship between Center Frequency and Channel Number

| Frequency Band (MHz) | Relationship between fc and nc |
| --- | --- |
| 402 – 405 | fc = 402.15 + 0.30 ( nc (MHz), nc = 0, …, 9 |
| 420 – 450 | fc = 420.30 + 0.50 ( (MHz), nc = 0, …, 11 |
| 863 – 870 | fc = 863.20 + 0.40 ( (MHz), nc = 0, …, 13 |
| 902 – 928 | fc = 903.50 + 0.50 ( nc (MHz), nc = 0, …, 47 |
| 950 – 956 | fc = 951.10 + 0.40 ( nc (MHz), nc = 0, …, 11 |
| 2360 – 2400 | fc = 2362.00 + 1.00 ( nc (MHz), nc = 0, …, 37 |
| 2400 – 2483.5 | fc = 2402.00 + 1.00 ( nc (MHz), nc = 0, …, 78 |

The mapping functions and used in the 420 – 450 MHz and 863 – 870 MHz frequency bands, respectively, are defined as follows:

, and

.

Preamble sequence assignment

The relationship between channel number, nc, and preamble sequence used in the PLCP preamble is shown in. Table 44

— Relationship between Channel Number and Preamble

| Preamble Sequence | Relationship between preamble sequence and nc |
| --- | --- |
| 1 | rem(nc,2) = 0 |
| 2 | rem(nc,2) = 1 |

PHY layer timing

The values for the PHY layer timing parameters are defined in Table 45.

— Physical layer timing parameters

| PHY Parameter | Value |
| --- | --- |
| pSIFS | 50 μs |
| pMIFS | 20 μs |
| pEDTime | 8 preamble symbols |
| pCCATime | 63 preamble symbols |
| pChannelSwitchTime | 100 μs |

The values for pEDTime and pCCATime shall be those specified in Table 45 or the values specified by the local regulatory requirements, which is lower.

Inter-frame spacing

The inter-frame spacing parameters are given in Table 46.

— Inter-frame spacing parameters

| MAC Parameter | Value |
| --- | --- |
| SIFS | pSIFS |
| MIFS | pMIFS |

Receive-to-Transmit Turnaround Time

The RX-to-TX turnaround time shall not be greater than pSIFS. The turnaround is defined as time elapsed from when the last sample of the last received symbol is present on the air interface, to the time when first sample of the first transmitted symbol of the PLCP preamble for the next frame is present on the air interface.

Transmit-to-Receive Turnaround Time

The TX-to-RX turnaround time shall not be greater than pSIFS. The turnaround is defined as the time elapsed from when the last sample of the last transmitted symbol is present on the air interface until the time when the receiver is ready to begin the reception of first sample for the next PHY frame.

Time between Successive Transmissions

For burst mode transmissions, the inter-frame spacing between uninterrupted successive transmissions by a device shall be fixed to exactly pMIFS. The inter-frame spacing is defined as the time elapsed from when the last sample of the last transmitted symbol is present on the air interface, to the time when the first sample of the first transmitted symbol of the PLCP preamble for the following packet is present on the air interface.

Center Frequency Switch Time

The center frequency switch time is defined as the interval from when the PHY transmits or receives the last valid symbol on one center frequency until it is ready to transmit or receive the next symbol on a different center frequency. The center frequency switch time shall not exceed pChannelSwitchTime.

Transmitter Specifications

Transmit PSD Mask

The transmitted spectral mask shall be less than –X dBr (dB relative to the maximum spectral density of the signal, see Table 47) for , where fc is channel center frequency and fBW is the channel bandwidth and is a function of the frequency band of operation and is defined in Table 47.

— Channel bandwidth as a function of the frequency band of operation

| Frequency (MHz) | –X dBr | fBW |
| --- | --- | --- |
| 402 – 405 | –20 | 300 kHz |
| 420 – 450 | –20 | 320 kHz |
| 863 – 870 | –20 | 400 kHz |
| 902 – 928 | –20 | 500 kHz |
| 950 – 956 | –20 | 400 kHz |
| 2360 – 2400 | –20 | 1 MHz |
| 2400 – 2483.5 | –20 | 1 MHz |

The transmitted spectral density also shall comply with all regulations defined by local regulatory bodies.

Transmit Power

A transmitter shall be capable of transmitting at least –10 dBm EIRP in all frequency bands, except for 402 – 405 MHz, where a transmitter shall be capable of transmitting at most –16 dBm EIRP. Devices should transmit lower power when possible in order to reduce interference to other devices and systems.

The maximum transmit power is limited by local regulatory bodies.

Transmit power-on and power-down ramp

The transmit power-on ramp for 10% to 90% of maximum power shall be no greater than 5 symbols. The transmit power-on ramp is shown in Figure 116. The transmit power-down ramp for 90% to 10% maximum power shall be no greater than 5 symbols. The transmit power-down ramp is shown in Figure 117.

— Transmit power-on ramp

— Transmit power-down ramp

The transmit power ramps shall be constructed such that the emissions conform to the local spurious frequency regulations.

Transmit Center Frequency Tolerance

The transmitted center frequency tolerance shall be (20 ppm maximum.

Symbol Clock Frequency Tolerance

The symbol clock frequency tolerance shall be (20 ppm maximum.

Clock Synchronization

The transmit center frequencies and the symbol clock frequency shall be derived from the same reference oscillator.

Transmitter Constellation Error

The modulation accuracy of the transmitter is determined via an error-vector magnitude (EVM) measurement, which is calculated over N baud-spaced received complex values . A decision is made for each received complex value. The ideal position of the chosen symbol is represented by the vector. The error vector  is defined as the distance from the ideal position to the actual position of the received complex values, i.e., .

The EVM is defined as shown in the equation below:

,

where S is the magnitude of the vector to the ideal constellation point. A transmitter shall have EVM values less than or equal to those listed in Table 48 when measure for N = 1000 symbols. The EVM shall be measured on baseband I and Q samples after the received signal is passed through a reference receiver, which shall perform the following operations: matched SRRC filtering, carrier-frequency offset estimation and symbol timing recovery while making the measurements.

— Permissible EVM numbers as a function of constellation size

| Constellation | EVM Error |
| --- | --- |
| /2-DBPSK | 20.0 % |
| /4-DQPSK | 12.5 % |
| /8-D8PSK | 7.0 % |

Adjacent Channel Power Ratio

The Adjacent Channel Power Ratio (ACPR) is defined as the ratio of the total power in the adjacent channel to the total power in the wanted channel, where the measurement bandwidth in both cases is equal to the channel bandwidth as given in Table 49. The ACPR shall be measured at an output transmit power equal to the maximum possible power output of the device. For a compliant PHY, the corresponding ACPR shall be no greater than the values shown in Table 51

—ACPR as a function of the frequency band of operation

| Frequency (MHz) | ACPR (dB) |
| --- | --- |
| 402 – 405 | –26 |
| 420 – 450 | –26 |
| 863 – 870 | –26 |
| 902 – 928 | –26 |
| 950 – 956 | –26 |
| 2360 – 2400 | –26 |
| 2400 – 2483.5 | –26 |

Receiver Specifications

Receiver Sensitivity

For a packet error rate (PER) of less than 10% with a PSDU of 255 octets, the minimum receiver sensitivity numbers in AWGN for the highest data rate in each operating frequency band shall be the numbers listed in Table 50. The minimum input levels are measured at the antenna connector, where a noise figure of 10 dB (referenced at the antenna), an implementation loss of 6 dB, and antenna gain of 0 dBi for both the transmitter and receiver have been assumed.

— Receiver Sensitivity Numbers

| Frequency Band (MHz) | Information Data Rate (kbps) | Minimum Sensitivity (dBm) |
| --- | --- | --- |
| 402 – 405 | 75.9 | –98 |
|  | 151.8 | –95 |
|  | 303.6 | –92 |
|  | 455.4 | –86 |
| 420 – 450 | 75.9 | –93 |
|  | 151.8 | –90 |
|  | 187.5 | –87 |
| 863 – 870 950 – 956 | 101.2 | –97 |
|  | 202.4 | –94 |
|  | 404.8 | –90 |
|  | 607.1 | –85 |
| 902 – 928 | 121.4 | –96 |
|  | 242.9 | –93 |
|  | 485.7 | –89 |
|  | 728.6 | –84 |
| 2360 – 2400 2400 – 2483.5 | 121.4 | –95 |
|  | 242.9 | –93 |
|  | 485.7 | –90 |
|  | 971.4 | –86 |

Adjacent Channel Rejection

The Adjacent Channel Rejection (ACR) is defined as the ratio of the power of the interfering signal in the adjacent channel to the power of the wanted signal, when the desired signal's strength is set to 3 dB above the rate-dependent sensitivity, and the power of the interfering signal has been raised until a 10% PER is reached for a PSDU length of 255 octets. The interfering signal in the adjacent channel shall be a conformant PHY signal at the same information data rate, unsynchronized with the signal in the channel under test, and generated using a suitable test source. For a compliant PHY, the corresponding adjacent channel rejection shall be no less than the values given in Table 51

—ACR as a function of the frequency band of operation

| Frequency Band (MHz) | Information Data Rate (kbps) | ACR (dB) |
| --- | --- | --- |
| 402 – 405 | 75.9 | 17 |
|  | 151.8 | 14 |
|  | 303.6 | 10 |
|  | 455.4 | 5 |
| 420 – 450 | 75.9 | 12 |
|  | 151.8 | 9 |
|  | 187.5 | 6 |
| 863 – 870 950 – 956 | 101.2 | 17 |
|  | 202.4 | 14 |
|  | 404.8 | 10 |
|  | 607.1 | 5 |
| 902 – 928 | 121.4 | 16 |
|  | 242.9 | 14 |
|  | 485.7 | 10 |
|  | 728.6 | 5 |
| 2360 – 2400 2400 – 2483.5 | 121.4 | 17 |
|  | 242.9 | 15 |
|  | 485.7 | 13 |
|  | 971.4 | 9 |

Receiver Energy Detection

The receiver energy detection (ED) measurement is an estimate of the received signal power within the bandwidth of the channel. It is intended for use by a network/MAC layer as part of a channel selection algorithm. No attempt is made to identify or decode signals on the channel.

ED Threshold

The minimum ED value (0) shall indicate received power less than either

10 dB above the specified receiver sensitivity (see 9.8.1) OR

that which is prescribed by local regulatory requirements,

whichever is lower.

The range of received power spanned by the ED values shall be at least 40 dB. Within this range, the mapping from the received power in decibels to ED value shall be linear with an accuracy of ± 6 dB.

ED Measurement Time

The ED measurement time, to average over, shall be either

pEDTime (8 preamble symbol periods) OR

that which is prescribed by local regulatory requirements,

whichever is longer in duration.

Receiver Clear Channel Assessment

The PHY shall provide the capability to perform CCA according to at least one of the following three methods:

- CCA Mode 1: Energy above threshold. CCA shall report a busy medium upon detecting any energy above the ED threshold.

- CCA Mode 2: Carrier sense only. CCA shall report a busy medium only upon the detection of a signal compliant with this standard with the same modulation and characteristics of the PHY that is currently in use by the device. This signal may be above or below the ED threshold. The CCA detection time shall be equal to pCCATime.

- CCA Mode 3: Carrier sense with energy above threshold. CCA shall report a busy medium using a logical combination of

Detection of a signal with the modulation and characteristics of this standard and

Energy above the ED threshold, where the logical operator may be AND or OR

The CCA parameters are subject to the following criteria:

- The ED threshold shall correspond to a received signal power as prescribed in 9.8.4

The CCA detection time shall be equal to pCCATime (see Table 45) Any CCA procedures required by local regulatory requirements shall also be supported.

Ultra wideband (UWB) PHY specification

The ultra wideband (UWB) PHY specification is designed to provide robust performance for BANs. UWB transceivers allow low implementation complexity (critical for low power consumption). Moreover, the signal power levels are in the order of those used in the MICS band, for example, safety power levels for the human body and low interference to other devices.

The UWB PHY provides three levels of functionality:

- UWB PHY gives a frame exchange between the MAC and PHY under the control of the physical layer convergence procedure (PLCP) sub-layer. Moreover, the PLCP constructs the PHY layer protocol data unit (PPDU) by concatenating the preamble synchronization (SHR), physical layer header (PHR) and physical layer service data unit (PSDU), respectively.

The PLCP sub-layer converts the bits of information of PPDU into RF signals for the wireless media.

UWB PHY provides clear channel assessment (CCA) indication to the MAC in order to verify activity on the wireless media.

Modes of operation

In order to ensure interoperability, a mandatory mode is required. Therefore, a compliant UWB PHY shall support the following:

One mandatory FEC (see 10.5.3).

One mandatory preamble synchronization header (SHR) (see 10.7).

One mandatory data rate (see 10.9).

One mandatory modulation (see 10.11).

One mandatory channel in the low band and one mandatory channel in the high band (see 10.12).

One mandatory transmit spectrum mask (see 10.14).

One mandatory HARQ in the high QoS mode (see 10.16).

High QoS mode

Applications with high QoS mode shall employ the differentially coherent PHY and HARQ.

Rules for use of modes and options

The UWB band is divided into two band groups: low band and high band (see 10.12). A compliant UWB device shall transmit in at least one of the specified band groups. The low band and high band are allocated into operating frequency channels as shown in table 10. The implementer is free to select any frequency channel for implementation. However, a UWB device that implements the low band shall support channel 2. The rest low-band channels are optional. A UWB device that implements the high band shall support channel 7. The rest of high-band channels are optional.

There are two types of pulse shape waveforms supported:

- A concatenation or burst of short pulses.

- A long pulse waveform.

There is not a mandatory pulse shape. However, implementers can choose a pulse shape from a pool of pulse shape waveforms (see 10.15).

On the other hand, all beacon preambles are transmitted at the mandatory data rate during association. For synchronization, the preamble consists of repetitions of Kasami sequences of length 63. Such preamble can be used for non-coherent and differentially coherent transceivers.

A combination of on-off signaling (on-off modulation with 64-ary waveform coding) and differentially encoded binary/quaternary phase shift keying modulation schemes are used to support non-coherent and differently coherent transceivers. Different data rates are obtained by changing pulse waveform duration and modulation scheme (while maintaining the same data rate). On-off signaling is mandatory and DBPSK/DQPSK (differentially coherent modulation) is optional for the default mode. In the high QoS mode, DBPSK/DQPSK is mandatory and on-off signaling is optional.

FEC is mandatory for the transmission of PHR and PSDU, but optional during association (transmission of beacons). Moreover, FEC decoding is optional at the receiver for the PSDU as systematic encoding is employed. That is, a receiver simply would ignore parity bits.

Definitions of FFDs (coordinators) and RFDs (devices)

Full function devices (FFDs) shall implement IR-UWB PHY or shall implement IR-UWB PHY plus FM-UWB PHY.

Reduced function devices (RFDs) shall implement either IR-UWB PHY or FM-UWB PHY.

Only FFDs shall send beacon frame and to coordinate beacon-enabled networks.

Only FFDs shall form non-beacon enabled networks.

Priority of resources

Priority of resources is given around medical and non-medical applications.

Medical applications are given higher priority than non-medical applications in the form of two parameters:

- If bandwidth of BAN is scarce, medical applications shall give higher priority than non-medical applications.

- If medical receiver suffers degradation on sensitivity above 1 dB, the coordinator shall enforce non-medical devices to reduce their EIRP at transmitters.

UWB PHY Frame Format

The UWB PHY frame format or physical layer protocol data unit (PPDU) is formed by concatenating the preamble synchronization header (SHR), the physical layer header (PHR) and the physical layer service data unit (PSDU), respectively as illustrated in Figure 118.

— UWB PPDU structure

The PSDU contains the payload from the MAC via SAP, which is formatted for transmission over the wireless media (see 10.5).

The PHR contains information about the data rate of the PSDU, length of the payload, HARQ and scrambler seed. The PHR is protected with error detection parity bits CRC-4-ITU and parity bits of a FEC (shortened BCH code) appended at the end against channel errors (see 10.6.2).

The preamble SHR is formed of repetitions of Kasami sequences. The SHR is divided into two parts. The first part is intended for coarse timing synchronization while the second part is the start frame delimiter (SFD) for frame synchronization (see 10.7).

PSDU construction

The information bits of the PSDU are formatted for transmission. The PSDU construction process is illustrated in Figure 119.

— PSDU construction

MPDU

The MAC provides to the PHY with the MAC protocol data unit (MPDU) that consists of MAC header (7 octets), MAC payload (0-256 octets) and CRC-16-ITU (2 octets) parity bits as illustrated in Figure 120.

— MPDU structure

Scrambler

Data whitening applied using scrambling in order to minimize the DC bias on data if long strings of 1s or 0s are contained in the MPDU. An additive or synchronous scrambler with polynomial shall be employed. Figure 121 shows a typical implementation of the side-stream scrambler. The output of the scrambler is generated as:

where ( denotes modulo-2 addition.

Table 52 defines the initialization vector (sync-word), xinit, for the additive scrambler as a function of the scrambler seed (SS) value. The sync-words are placed in the data stream through equal intervals, i.e., each frame.

— Block diagram of a side-stream scrambler

— Scrambler Seed Selection

| Scrambler Word (S) | Initialization Vector xinit = x[-1] x[-2] … x[-14] |
| --- | --- |
| 0 | 0 0 1 0 1 1 1 1 0 0 1 1 0 1 |
| 1 | 0 0 0 0 0 0 0 1 0 0 1 1 1 1 |

The MAC shall set the scrambler word to 0 when the PHY is initialized and the scrambler word shall be incremented, using a 1-bit rollover counter, for each frame sent by the PHY.

At the receiver, the additive de-scrambler shall be initialized with the same initialization vector, xinit, used by the transmitter. The initialization vector is determined from the scrambler seed value in the PHY header of the received frame.

Systematic BCH(63,51) encoder

The generator polynomial for a systematic BCH (63, 51) code is given by:

.

The parity bits are determined by computing the remainder polynomial:

,

where is the message polynomial given by:

,

and  and  are elements of GF(2).

The message polynomial is created as follows: is the first bit of the message and  is the last bit of the message. The order of the parity bits is as follows:  is the first parity bit transmitted and  is the last parity bit transmitted.

— BCH (63,51) codeword

Pad bits

Pad bits sub-system shall append pad bits in order to ensure that its input bit stream aligns on a symbol boundary. The number of pad bits is given by

where  is the cardinality of the constellation of a given modulation scheme,  is the number of PSDU bits,

is the number of BCH codewords and the number of BCH parity bits.

All appended pad bits shall be set to 0. In the case of un-coded transmission,  is set to 0. Notice that the total number of bits to be transmitted on the air is given by

Bit interleaving

In order to protect against channel fading (quasi-static or dynamic) bit interleaving is applied prior to the mapping of modulation symbols. A binary labeling function that maps blocks of bits to signal constellation symbols is already defined by the non-coherent modulation. For DQPSK modulation, it is Gray encoding. Thus, this is a form of bit-interleaved coded modulation.

A simple algebraic interleaver that can be generated on-the-fly is defined as

(n) = nb Mod(NI)

where NI is the interleaver’s length, (n) denotes the new position to which index  is interleaved, Mod(NI) is modulo NI  arithmetic. The seeding parameter b satisfies 0 ≤ b < NI and b is a relative prime to NI to ensure one-to-one mapping. The interleaver’s length shall be set to NI = 64 and seeding parameter shall be set to b = 39.

Notice that in the last codeword, the interleaver is active only in the last remaining bits, Nrem = rem (Ntotal, NI).

PHR construction

The PHY header (PHR) contains information about the data rate, frame length, HARQ enable, and scrambler seed. The information in the PHR is used by the receiver in order to decode the PSDU. The PHR is protected by a combination of CRC-4-ITU error detection (4 parity bits) and shortened systematic BCH (31,19) FEC coding (12 parity bits). The concatenation of PHR, CRC-4-ITU parity bits and shortened BCH(31,19) parity bits forms the PHY header.

— PHR configuration

— PHR construction

PHR information

The PHR information is formed of 15 bits as illustrated in Table 53.

— PHR information structure

| Bit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | R0 | R1 | R2 | L0 | L1 | L2 | L3 | L4 | L5 | L6 | L7 | r | H0 | H1 | S |
|  | Data Rate | Frame length | a | HARQ | b |

a = Reserved. b = Scrambler word.

The description of the different fields of the PHR is as follows:

Data rate

Indication of data rates (R0, R1, R2) for the non-coherent, differentially coherent and FM-UWB PHYs are denoted in Table 55, Table 56 and Table 64 respectively.

Frame length

A variable frame length is indicated with eight bits (), i.e., from 0 to 255 octets or octets.

HARQ enable

The 13th bit H0=1 indicates HARQ enabled (see 10.16.3 for H1).

Scrambler word (sync-word)

The 15th bit indicates the sync-word for the bit scrambler as indicated in Table 52. This field shall be set up by the MAC.

PHR protection

CRC-4-ITU

The PLCP sub-layer shall append 4-bits from CRC-4 ITU error detection coding to the PHR information. The CRC-4-ITU shall be the 1’s complement of the remainder generated by the modulo-2 division of the PHR information by the polynomial:

Shortened BCH(31,19) encoder

The PLCP sub-layer shall append 12 parity bits from a shortened BCH(31,19) encoding (obtained from the BCH(63,51) encoder) to the PHR information and CRC-4-ITU parity bits. Thus, the same BCH encoder and decoder are used for the PSDU and PHR (see Appendix B.2).

SHR Preamble

The synchronization header (SHR) is formed by the preamble consisting of repetitions of Kasami sequences of length 63 in order to perform coarse timing acquisition and the start-of-frame delimiter (SFD) for frame synchronization. Such SHR field is detectable for both non-coherent and differentially coherent transceivers.

There are eight Kasami sequences defined in Table 54. Those can be used according to the band plan and the co-existence scheme used. Notice eight logical channels can be used per channel.

The preamble set shall be divided into two pools. Each pool has a set of 4 preambles. The first pool shall be used for odd number of channels. The second pool shall be used for even number of channels. The coordinator might scan all the logical channels and use the preamble with minimum received power level.

Coexistence of BANs and the interference mitigation can be achieved by virtue of the inherent duty cycling in the modulation and the preamble sequences with good correlation properties.

— Eight Kasami sequences of length 63

| C1 | 1 1 1 1 1 1 0 1 0 1 0 1 1 0 0 1 1 0 1 1 1 0 1 1 0 1 0 0 1 0 0 1 1 1 0 0 0 1 0 1 1 1 1 0 0 1 0 1 0 0 0 1 1 0 0 0 0 1 0 0 0 0 0 |
| --- | --- |
| C2 | 0 0 0 1 1 0 0 0 1 0 0 1 0 0 1 0 0 0 1 0 1 1 0 0 0 1 1 0 0 1 1 1 1 0 0 1 1 0 0 1 0 1 0 1 1 1 0 0 0 1 1 0 1 0 1 0 1 0 1 0 0 1 0 |
| C3 | 1 0 0 0 1 1 1 1 1 0 1 1 1 1 0 0 0 1 1 1 0 0 0 0 1 1 0 1 1 1 1 0 1 1 1 0 1 0 1 1 1 0 1 1 1 0 0 1 1 0 1 0 0 0 0 1 0 0 1 1 0 0 1 |
| C4 | 0 1 0 0 0 1 0 0 0 0 1 0 1 0 1 1 0 1 0 1 1 1 1 0 1 0 0 0 0 0 1 0 0 1 0 1 0 0 1 0 1 1 0 0 1 0 1 1 0 1 0 0 0 1 0 0 1 1 1 1 1 0 0 |
| C5 | 1 0 1 0 0 0 0 1 1 1 1 0 0 0 0 0 1 1 0 0 1 0 0 1 1 0 1 0 1 1 0 0 0 0 0 0 1 1 1 0 0 1 1 1 0 0 1 0 0 0 1 1 0 1 1 0 0 0 0 1 1 1 0 |
| C6 | 1 1 0 1 0 0 1 1 0 0 0 0 0 1 0 1 0 0 0 0 0 0 1 0 0 0 1 1 1 0 1 1 0 0 1 0 0 0 0 0 0 0 1 0 1 1 1 0 1 0 0 0 1 1 1 1 0 1 1 0 1 1 1 |
| C7 | 0 1 1 0 1 0 1 0 0 1 1 1 0 1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 0 0 0 0 1 0 1 1 0 1 1 1 0 0 0 0 0 0 0 0 1 1 0 1 0 0 1 1 1 1 0 1 0 1 1 |
| C8 | 0 0 1 1 0 1 1 0 1 1 0 0 1 1 1 0 1 0 0 1 0 1 0 1 0 0 0 1 0 1 0 1 0 1 1 1 1 1 0 0 1 0 0 1 0 1 1 1 1 1 1 1 1 1 0 1 1 0 0 0 1 0 1 |

Notice that Kasami sequences are binary and in Table 54, -1 was replaced by 0. Every Kasami sequence is indexed by for as illustrated in Table 54.

The preamble SHR consists of = 4 repetions of the symbol. Such symbol is obtained by a Kasami sequence of table 50 zero-padded by -1 zeros. The symbol  shall be computed as

where  and the operator indicates Kronecker product.

Figure 125 illustrates the construction of symbol .

— Construction of symbols from Kasami sequence

For transmission, every element of the Kasami sequence shall be transmitted with a waveform of duration = 8 ns. The chip time shall have duration of = 128 ns corresponding to L= 16 for zero-padding. Notice  can consist of one pulse waveform or a burst of short pulses (see Equations (88) and (90) and 10.15).

The preamble symbol shall use OOK modulation for the non-coherent PHY and shall use differentially encoded BPSK modulation for the differentially coherent PHY (see Equation (89) and 0). In case of FM-UWB PHY, there is not zero-padding, that is =1.

Start-of-frame delimiter

After the preamble, a start-of-frame delimiter (SFD) is transmitted for frame synchronization. The SFD is chosen to have low cross-correlation with the preamble such that the transition of correlation from preamble to SFD does not degrade the detection of the SFD.

UWB symbol structure

The UWB symbol structure supports on-off signaling and differentially encoded BPSK/QPSK. Each symbol time, consists of an integer number of basis waveform positions, each of duration. The symbol duration is divided into two intervals of duration  in order to enable on-off signaling. The duty cycle factor during transmission is given by the ratio when a pulse waveform is on () over the symbol time (when a pulse waveform is on and off during a symbol time), i.e., . The additional  or  waveform positions are used for time hopping in order to support multi-BANs for coexistence.

— UWB symbol structure

Data Rates

Data rates range from 0.5 Mbps up to 10 Mbps. The mandatory data rate (uncoded) shall be 0.4882 Mbps.

PSDU timing parameters

The PSDU timing and data rate parameters are given in Table 55, Table 56 and Table 64. Notice that in case of long pulse shape waveform option, the pulse repetition frequency (number of pulses transmitted in one second) or PRF coincides with the mean PRF (number of pulses transmitted in a symbol period divided by the symbol period), because a single pulse is transmitted per symbol duration. In case of short pulse shape option, the peak PRF is defined as the maximum rate at which a transmitter emits pulses. This definition is not applicable to the long pulse shape option.

— Data rates for non-coherent modulation

| R0,R1,R2 | PRF | Nw | Nhop | Tw | Tsym | Sym. rate | FEC | Bit rate | Ncpb | Nguard | P.PRF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | (MHZ) |  |  | nsec | nsec | (Msps) | rate | (Mbps) |  |  | (MHz) |
| 0 0 0 | 0.4882 | 32 | 16 | 64 | 2048 | 0.4882 | 0.81 | 0.3954 | 32 | 2 | 499.2 |
| 0 0 1 | 0.9765 | 32 | 16 | 32 | 1024 | 0.9765 | 0.81 | 0.791 | 16 | 4 | 499.2 |
| 0 1 0 | 1.9531 | 32 | 16 | 16 | 512 | 1.9531 | 0.81 | 1.582 | 8 | 8 | 499.2 |
| 0 1 1 | 3.9062 | 32 | 16 | 8 | 256 | 3.9062 | 0.81 | 3.164 | 4 | 10 | 499.2 |
| 1 0 0 | 7.8125 | 32 | 16 | 4 | 128 | 7.8125 | 0.81 | 6.3281 | 2 | 12 | 499.2 |
| 1 0 1 | 15.625 | 32 | 16 | 2 | 64 | 15.625 | 0.81 | 12.656 | 1 | 12 | 499.2 |
| 1 1 0 |  |  |  |  |  |  |  |  |  |  |  |
| 1 1 1 |  |  |  |  |  |  |  |  |  |  |  |

Data rates corresponding to (R0, R1, R2) = 1 1 0 and 1 1 1 are reserved.

— Data rates for the differentially coherent modulation

| R0, R1, R2 | PRF | Nw | Nhop | Tw | Spr | Tsym | Modul. | Sym. rate | FEC | Bit rate | Ncpb | Nguard | P.PRF |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | (MHZ) |  |  | ns |  | ns | Mode 2 | (Msps) | rate | (Mbps) |  |  | (MHz) |
| 0 0 0 | 0.4882 | 32 | 32 | 64 | 1 | 2048 | DBPSK | 0.4882 | 0.81 | 0.3954 | 32 | 2 | 499.2 |
| 0 0 1 | 0.9765 | 32 | 32 | 32 | 1 | 1024 | DBPSK | 0.9765 | 0.81 | 0.791 | 16 | 4 | 499.2 |
| 0 1 0 | 1.9531 | 32 | 32 | 16 | 1 | 512 | DBPSK | 1.9531 | 0.81 | 1.582 | 8 | 8 | 499.2 |
| 0 1 1 | 3.9062 | 32 | 32 | 8 | 1 | 256 | DBPSK | 3.9062 | 0.81 | 3.164 | 4 | 16 | 499.2 |
| 1 0 0 | 7.8125 | 32 | 32 | 4 | 1 | 128 | DBPSK | 7.8125 | 0.81 | 6.3281 | 2 | 20 | 499.2 |
| 1 0 1 | 15.625 | 32 | 32 | 4 | 1 | 128 | DQPSK | 7.8125 | 0.81 | 12.656 | 2 | 20 | 499.2 |
| 1 1 0 | 3.9062 | 32 | 32 | 8 | 7 | 1792 | DBPSK | 0.558 | 0.81 | 0.452 | 4 | 16 | 499.2 |
| 1 1 1 | 3.9062 | 32 | 32 | 8 | 7 | 1792 | DQPSK | 0.558 | 0.81 | 0.904 | 4 | 16 | 499.2 |

The description of the different parameters is as follows:

PRF parameter

In case of long pulse shape option, PRF indicates the number of pulses transmitted in one second. It is equal to the mean PRF (number of pulses transmitted in a symbol period divided by the symbol period) as one pulse is transmitted per symbol duration.

Pulse waveform position parameter

It indicates the number of possible pulse waveform positions within a symbol time:.

Hop parameter

It gives the number of pulse waveform positions that can contain an active waveform for time hopping ().

Pulse waveform duration parameter

It is the pulse waveform duration and computed as. In case of the long pulse shape option is 1. In case of short pulse option  is larger than 1. Notice is the pulse shape duration.

Spreading parameter

It is described in Table 56 and indicates the number of chips per symbol.

Symbol duration parameter

It is the PSDU symbol duration ().

Modulation mode 2 parameter

It indicates either differentially encoded BPSK or differentially encoded QPSK.

Symbol rate parameter

It is the number of information symbols transmitted per second and computed as.

FEC rate parameter

It is the channel coding rate, i.e., number of information bits divided by the number of coded bits.

Bit rate parameter

It gives the bit rate on the air and computed as  in case of non-coherent PHY and DBSPK modulation and  in case of DQPSK.

Number of pulses parameter

It indicates the number of pulses shapes. In case of the long pulse shape option is 1. In case of short pulse option  is larger than 1. Notice that short pulse duration is 2 ns.

Nguard parameter

It is employed for the time hopping generator and computed as.

Peak PRF parameter

It is defined as the maximum rate at which a transmitter emits short pulse waveforms. This definition is applicable for the short pulse shape option only and it is not applicable for the long pulse shape option.

UWB Modulations

Once the PLCP sub-layer has constructed the PPDU, i.e., PHR, SHR and PSDU, the PPDU information bits are transformed into RF signals for transmission. For that purpose, there are three possible modulation schemes. PPDU information bits shall be modulated by either: on-off signaling (see 10.11.3), differentially coherent modulation (see 10.11.4) or FM-UWB modulation (see 10.17).

Scrambling for a burst of pulse shapes

In order to avoid DC bias and spectral lines due to long strings of short pulses with the same polarity (especially in low data rates), spectral shaping through scrambling at chip level shall be used (chip scrambling).

A burst of short pulses shall employ the sequences indicated Table 57.

— Static scrambling sequences

| 1 | 1 |
| --- | --- |
| 2 | 1 0 |
| 4 | 1 0 1 1 |
| 8 | 1 1 0 1 0 1 0 0 |
| 16 | 1 0 0 0 0 1 0 1 0 1 0 0 1 1 0 1 |
| 32 | 1 0 0 0 1 1 1 1 1 0 0 0 1 1 0 1 0 0 1 0 0 0 0 1 0 1 0 1 1 1 0 1 |

Optional dynamic scrambling

Optionally, the implementer may use dynamic or time-varying scrambling in order to improve the spectrum flatness at the cost of extra complexity. In dynamic scrambling, the LFSR shall be clocked at the peak PRF of 499.2 MHz,  times during each burst period.

The time-varying scrambling sequence  shall be generated from a common LFSR. The polynomial of the LFSR shall be

.

Figure 127 shows a typical implementation of the LFSR. By the given polynomial, the corresponding scrambling sequence is generated as

where  denotes modulo-2 addition.

— Block diagram of scrambling sequence and time-hopping sequence generation

The LFSR shall be initialized upon the transmission of the first bit of the PHR. The LFSR shall not be reset after transmission of the PHR. The initial state of the LFSR shall be determined from the preamble code. The first 14 bits of the preamble code shall be loaded into the LFSR. Table 58 shows the initial state for the LFSR for each preamble code.

The LFSR shall be clocked at the peak PRF of 499.2 MHz,  times during each symbol period. The scrambling sequence for the mth symbol shall be  where.

— Initial state of LFSR for scrambling sequence and time-hopping sequence generation

| Preamble code number (see 10.7) | Initial state of LFSR |
| --- | --- |
| 0 | 1 1 1 1 1 1 0 1 0 1 0 1 1 0 |
| 1 | 0 0 0 1 1 0 0 0 1 0 01 0 0 |
| 2 | 1 0 0 0 1 1 1 1 1 0 1 1 1 1 |
| 3 | 0 1 0 0 0 1 0 0 0 0 1 0 1 0 |
| 4 | 1 0 1 0 0 0 0 1 1 1 1 0 0 0 |
| 5 | 1 1 0 1 0 0 1 1 0 0 0 0 0 1 |
| 6 | 0 1 1 0 1 0 1 0 0 1 1 1 0 1 |
| 7 | 0 0 1 1 0 1 1 0 1 1 0 0 1 1 |

Time hopping sequence

The time-hopping sequence value for the m-th symbol shall be calculated as follows:

- Generate an integer number  using the left-most k shift registers (see in Figure 127) as follows:

where . As shown Table 55 and Table 56, the number of hop burst  is always a power of two, and consequently k is always an integer.

Calculate the following relevant parameters (or use a look-up table):

,

where  and  can be pre-computed for each data rate.

The parameter  shall be computed as

where  is the maximum expected delay spread of channel.

Values of  are provided in Table 55 and Table 56 for =128 ns.

Finally generate the time-hopping sequence value for the m-th symbol as follows:

where .

Non-coherent Modulation

The non-coherent PHY uses on-off signaling (on-off modulation in combination with 64-ary waveform coding). Such modulation strategy assigns information bits from an alphabet of size with a coded-pulse sequence of length (half rate) from a code set alphabet of the same size.

— Non-coherent modulation/demodulation flow diagram

Symbol mapper at half rate

A data symbol contains 6 bits . The transmitting symbol is given by the mapping  as indicated in Table 59.

— Symbol mapper for 64-ary waveform-coding

| Data symbol decimal | Data symbol binary | Codeword | Data symbol decimal | Data symbol binary | Codeword |
| --- | --- | --- | --- | --- | --- |
| 0 | 000000 | 000000111111 | 32 | 100000 | 100110001011 |
| 1 | 000001 | 000011011011 | 33 | 100001 | 100101011010 |
| 2 | 000010 | 000011101101 | 34 | 100010 | 100100101110 |
| 3 | 000011 | 000111000111 | 35 | 100011 | 100011101010 |
| 4 | 000100 | 001001010111 | 36 | 100100 | 100001001111 |
| 5 | 000101 | 011001110100 | 37 | 100101 | 100001111100 |
| 6 | 000110 | 000111111000 | 38 | 100110 | 100100010111 |
| 7 | 000111 | 000011110110 | 39 | 100111 | 100010011101 |
| 8 | 001000 | 000110011110 | 40 | 101000 | 011011000101 |
| 9 | 001001 | 000110110011 | 41 | 101001 | 011011101000 |
| 10 | 001010 | 001100011011 | 42 | 101010 | 011101000110 |
| 11 | 001011 | 101010010011 | 43 | 101011 | 011101011000 |
| 12 | 001100 | 011001001011 | 44 | 101100 | 100001110011 |
| 13 | 001101 | 000101101011 | 45 | 101101 | 011110110000 |
| 14 | 001110 | 110100011001 | 46 | 101110 | 011101100001 |
| 15 | 001111 | 000101011101 | 47 | 101111 | 011110000011 |
| 16 | 010000 | 010001011110 | 48 | 110000 | 010001100111 |
| 17 | 010001 | 010101101100 | 49 | 110001 | 110010100110 |
| 18 | 010010 | 001111010001 | 50 | 110010 | 010010101011 |
| 19 | 010011 | 001111100100 | 51 | 110011 | 010010010111 |
| 20 | 010100 | 001011011100 | 52 | 110100 | 010100001111 |
| 21 | 010101 | 001111001010 | 53 | 110101 | 010100110101 |
| 22 | 010110 | 001110101001 | 54 | 110110 | 010010111100 |
| 23 | 010111 | 001011100011 | 55 | 110111 | 010011110001 |
| 24 | 011000 | 011110001100 | 56 | 111000 | 011000011101 |
| 25 | 011001 | 001010001111 | 57 | 111001 | 011000110011 |
| 26 | 011010 | 001001111001 | 58 | 111010 | 010111100010 |
| 27 | 011011 | 001001101110 | 59 | 111011 | 011011010010 |
| 28 | 011100 | 001010111010 | 60 | 111100 | 010100111010 |
| 29 | 011101 | 001100110110 | 61 | 111101 | 010101010011 |
| 30 | 011110 | 001010110101 | 62 | 111110 | 010111010100 |
| 31 | 011111 | 101100100101 | 63 | 111111 | 010111001001 |

Pulse shaping

After the symbol mapper and SHR insertion, the pulse shaping shall place a pulse waveform when an input bit is 1, according to the UWB symbol structure and absence of a pulse waveform when an input bit is 0. Thus, the transmitting signal is given by

where m is the -th transmitting symbol, is the symbol time,  is a time hopping sequence for the -th BAN and is the pulse waveform given by

The pulse waveform has duration, where in case of a long pulse shape waveform and is the pulse shape () duration. When, a burst of short pulses is transmitted. Notice that if =1 then shall be set to 0.

Detection

On-off signaling does not require defining a threshold for detection as in OOK detection. The implementer is recommended to employ soft-detection. Soft detection can be either the correlation of the received signal with every sequence in the codebook at time lag zero or minimum Euclidian distance detection (see Annex B.1).

Differentially coherent PSK modulation

The differentially coherent modulation uses differentially encoded BPSK/QPSK.

— Differentially coherent modulation/demodulation flow diagram

DBPSK/DQPSK

The PPDU information bits shall be differentially encoded such that the PSK transmitting symbols are given by

where represents the -th differentially encoded BPSK or QPSK symbol, and  Such symbol carries either one bit of information (differentially encoded BPSK) or two bits of information (differentially encoded QPSK). The mapping between information bits onto  is given in Table 60 and Table 61.

— Mapping of information bits onto  for DBSK

| 0 | 0 |
| --- | --- |
| 1 |  |

— Mapping of information bits onto  for DQPSK

| 1 | 1 |  |
| --- | --- | --- |
| 0 | 1 |  |
| 0 | 0 |  |
| 1 | 0 | 0 |

Pulse shaping

After the generation of DBPSK/DQPSK symbols, the pulse shaping shall place a pulse waveform according to the UWB symbol structure. Thus, the transmitting signal is given by

where is the -th transmitting symbol, is the symbol time, is a time hopping sequence for the -th BAN and is the pulse waveform given by

The pulse waveform has duration, where in case of a long pulse shape waveform and is the duration of the pulse shape. When a burst of short pulses with =2 ns is transmitted. Notice that if =1 then shall be set to 0.

Differentially encoded PSK modulation with spreading

In order to enhance interference rejection, two data rates use differentially encoded BPSK/QPSK with spreading. The differentially encoded symbols are given by

where is a Barker code of length  and

.

Operating frequency bands

The UWB band is divided into two band groups: low band and high band as shown in Table 62. A compliant UWB device shall transmit in at least one of the specified band groups.

The low band and high band are divided into operating frequency channels as shown in Table 62. A UWB device that implements the low band shall support channel 2. The remaining low-band channels are optional. A UWB device that implements the high band shall support channel 7. The remaining high-band channels are optional.

— UWB PHY allocation

| Band group | Channel number | Central frequency (MHz) | Bandwidth (MHz) | Channel attribute |
| --- | --- | --- | --- | --- |
| Low band | 1 | 3494.4 | 499.2 | Optional |
|  | 2 | 3993.6 | 499.2 | Mandatory |
|  | 3 | 4492.8 | 499.2 | Optional |
| High band | 4 | 6489.6 | 499.2 | Optional |
|  | 5 | 6988.8 | 499.2 | Optional |
|  | 6 | 7488.0 | 499.2 | Optional |
|  | 7 | 7987.2 | 499.2 | Mandatory |
|  | 8 | 8486.4 | 499.2 | Optional |
|  | 9 | 8985.6 | 499.2 | Optional |
|  | 10 | 9484.8 | 499.2 | Optional |
|  | 11 | 9984.0 | 499.2 | Optional |

Clock accuracy and central frequency alignment

A UWB transmitter shall have a clock accuracy of 20 ppm. That is a PRF accuracy of 20 ppm for the long pulse shape waveforms and peak PRF accuracy of 20 ppm for short pulse shape waveforms. Furthermore, the central frequencies of the band plan shall have an accuracy of 20 ppm.

Transmit spectrum mask

The transmit spectrum mask shall be given by

,

Notice that =2 ns. For example, the transmit spectrum mask for channel 7 (=7987.2 MHz) is shown in figure 126. The transmit spectrum mask shall be fulfilled by the non-coherent, differentially coherent and FM-UWB PHYs.

— Transmit spectrum mask for band 7

Pulse Shape Waveform

There is not a mandatory pulse shape. However, the pulse waveform duration and PRF are mandatory according to the timing parameters of Table 55 and Table 56 in case of long pulse shape option. In case of short pulse shape option, the pulse waveform duration and peak PRF are mandatory according to the timing parameters of Table 55 and Table 56. Notice pulse shape waveforms have to fulfill the transmit spectrum mask (see 10.14) and regulatory spectral mask where applicable.

Short pulse waveforms

A complaint short pulse shape waveform, shall be constrained by the absolute value of its cross-correlation with a reference pulse of at least 0.8 in the main lobe. Such cross-correlation is defined as

where and are the energies of and, respectively. The reference pulse (having the square root raised cosine spectrum) shall be given by

The roll-off factor shall be set to and shall be set to 2 ns. The implementer is free to choose the truncation of.

— PSD of centered at 4492.8 MHz and truncated to satisfying the transmit spectrum mask.

Chirp pulse waveform

A compliant chirp pulse waveform in baseband complex representation shall satisfy the following equation:

where is an arbitrary constant phase,  is a window function given by

is the pulse duration defined in Table 55 and Table 56.  and  are transition times bounded by  and  respectively.  is an arbitrary continuous monotonic non-negative function that satisfies  and , while  is an arbitrary continuous monotonic non-negative function that satisfies  and . An example of a compliant window function for  is shown in Figure 132.

— Example of a window function for = 32 ns and Tukey window  = 2 ns

The chirp’s instantaneous frequency, is defined as

.

where  is the constant chirping slope that corresponds with the ideal linear chirp and given by

The chirp’s frequency sweep shall be set to520 MHz.

Let be an arbitrary instantaneous frequency error function that shall be bounded by

An example of a compliant instantaneous frequency function for  is shown in Figure 133. Examples of the ideal linear chirp pulses’ spectra for different values of , using a Tukey window with  as  are shown in Figure 134.

— Example of an instantaneous frequency function for= 32 ns.

— PSD of chirp pulses centered at 4492.8 MHz fulfilling the transmit spectral mask.

Notice that in case of,  is the ideal linear up chirp in baseband complex representation by

Chaotic pulse waveform

Chaotic pulses are near constant envelope signals that are produced by the concatenation of four different triangular or sawtooth waveforms. The sum of these triangular or sawtooth waveforms feeds a voltage controlled oscillator (VCO). This is similar to frequency modulating a carrier signal with the concatenation of the triangular signals. The center frequency of the oscillator is directly proportional to the DC offset of the VCO.

— Chaos waveform generator using triangular waveform

The duration of the triangular pulses and the peak to peak amplitudes are chosen to achieve the 500 MHz bandwidth. The period of the four triangular pulses are chosen as 3, 19, 53 and 59 ns respectively. Amplitudes are chosen in the ratio of 0.5, 0.2, 0.8, 1 respectively. This summation results in a spectrum shape with 10 dB bandwidth of 500 MHz. The spectrum of the chaotic pulse waveform is shown in Figure 136.

— Power spectral density of chaotic pulses with 10db bandwidth of 500 MHz

Hybrid type II ARQ mechanism

This configuration is based on invertible codes. Assuming systematic codewords (codewords consist of information bits plus parity bits), a code is said invertible when a decoder can recover the information bits by an inversion process of parity bits.

Packets detected in error by a cyclic redundancy code (CRC) are not discarded, but rather stored for posterior use. This HARQ scheme requires storing a packet at the transmitter and receiver. Codewords are form by information bits and parity bits of the same length. Packets are created by information bits only or parity bits only. The mechanism of retransmission is alternate repetitions of packets with the information bits or packets with parity bits at the time. The retransmissions continue until the information bits are finally recovered either by inversion or decoding process or a maximum number of retransmission is reached.

Figure 137 shows the flow diagram of HARQ Type II with invertible codes. As HARQ requires the interaction of PHY and MAC, the part of the MAC mechanism for HARQ is described in 7.13.2. The part of the PHY mechanism is through FEC coding, decoding, FEC inversion and storage of a packet.

Error detection codes

The cyclic redundancy check code is based on the CRC-16-CCITT generator polynomial described in 6.2.3. In figure 133, such CRC encoding for parity bits is represented as. The CRC decoding is given by.

Invertible codes

In Figure 137, the FEC encoding for parity bits is represented as. The FEC decoding is given by and FEC inversion of parity bits to retrieve information bits  is represented as.

PHR iteration

When HARQ is enabled, the fields (H0, H1) in the PHR are set to (1, 0). Information bits () and its FEC parity bits () form two packets, which are stored at the transmitter. The transmitter starts in state 0 (table 11) and only sends. In case of successful reception, the MAC will send and ACK. Thus the transmitter flushes the stored,  and it starts a new transmission. In case of unsuccessful reception (NACK in Figure 137), Table 63 illustrates the algorithmic flow of HARQ.

— Flow of H0, H1 and Rx action in case of packet failure (NACK)

| State | H0 | H1 | Tx | Rx Action |
| --- | --- | --- | --- | --- |
| 0 | 1 | 0 | Send | If CRC fails go to 1 |
| 1 | 1 | 1 | Send | If CRC and FEC decoding fails go to 2 |
| 2 | 1 | 0 | Send | If CRC and FEC decoding fails go to 1 |

(H0=0, H1=0) HARQ is disabled. (H0=0, H1=1) is reserved.

— Flow diagram of HARQ Type II with invertible codes

FM-UWB PHY

FM-UWB is an optional PHY targeting low data rate medical BAN. FM-UWB exploits high modulation index analog FM to obtain an ultra-wide signal. Frequency modulation has the unique property that the RF bandwidth BRF is not only related to the bandwidth fm of the modulating signal, but also to the modulation index β that can be chosen freely. This yields either a bandwidth efficient narrow-band FM signal (β <1) or a ultra wideband signal ( β >> 1) that can occupy any required bandwidth.

FM-UWB constitutes an analog implementation of a spread-spectrum system. This constant-envelope approach, where peak power equals average power, yields a flat spectrum with steep spectral roll-off. After wideband FM demodulation (analog instantaneous de-spreading) in the receiver, the FM-UWB radio behaves like a narrowband FSK radio from a synchronization and detection point-of-view. FM-UWB technology combines low complexity with robustness against interference and multipath. The following subclauses present the FM-UWB system and its properties.

Data rates

— FM-UWB data rates

| R0,R1,R2 | Sym. rate | FEC | Bit rate |
| --- | --- | --- | --- |
|  | (ksps) | rate | (kbps) |
| 0 0 0 | 31.25 | 0.81 | 25.31 |
| 0 0 1 | 62.5 | 0.81 | 50.62 |
| 0 1 0 | 125 | 0.81 | 101.25 |
| 0 1 1 | 250 | 0.81 | 202.5 |

Data rates corresponding to 100, 101, 101, 111 are reserved.

System characteristics

FM-UWB radios shall satisfy the system characteristics defined in Table 64. Operation shall be according to the frequency band plan of Table 62 (see 10.12). Moreover, FM-UWB shall satisfy the transmit spectrum mask of 10.14.

Preamble

The preamble SHR shall be formed by the 2nd Kasami sequence defined in Table 54.

— FM-UWB system characteristics.

| Parameter | Value |
| --- | --- |
| RF center frequency | Channel 7 |
| RF bandwidth (3 dB) | 499.2 MHz |
| RF output power | -15 dBm |
| Subcarrier frequency | 1.0, 1.25, 1.50, 1.75 MHz |
| Subcarrier modulation | FSK,  = 1 |
| Raw bit rates | 31.25, 62.5, 125 and 250 kbps |
| Receiver sensitivity | <-85 dBm1 |
| TX, RX switching time | < 100 us |
| RX synchronization time | < 500 us |

at BER ≤ 10-6

Transmitter

Figure 138 provides a block diagram of the FM-UWB transmitter. The low modulation index of frequency shift keying (FSK) is followed by high modulation index of frequency modulation (FM), creating a constant-envelope UWB signal. The transmitter shall consist of a 1-2 MHz subcarrier oscillator generating a triangular signal that is FSK modulated by the transmit data. This subcarrier signal m(t) modulates the RF VCO (wideband frequency modulator), yielding a constant-envelope UWB signal with a flat power spectral density and steep spectral roll-off.

— FM-UWB transmitter block diagram

The FM-UWB signal  with amplitude  and carrier frequency is obtained by modulating the RF oscillator with the subcarrier  of frequency  such that

where M represents the triangular waveform of the subcarrier signal. An RF oscillator sensitivity of  [rad/V-s] yields a deviation equal to, resulting in a FM signal  that can be expressed mathematically as

Figure 139 illustrates the power spectral density (PSD) of an ideal FM-UWB signal. The signal shall be compliant with the relevant regulatory limits. The signal power is –15 dBm (112 mVpp into a 50 Ohm load). The subcarrier frequency is 1 MHz and the deviation is 250 MHz, yielding a modulation index of 250. The –10 dB bandwidth is 500 MHz.

The subcarrier signal m(t) shall modulate the RF oscillator that implements FM with high modulation index and yields a constant-envelope UWB signal with a flat PSD and steep spectral roll-off at its output.

The PSD of a wideband FM signal is determined by and has the shape of the probability density function (PDF) of the modulating signal m(t). The use of a triangular subcarrier waveform, which is characterized by a uniform PDF, results in a flat RF spectrum. From an implementation point of view the triangular waveform is straightforward to generate using either analog or digital circuit techniques.

— Frequency spectrum of FM-UWB signal at 7.5 GHz center frequency

Receiver architecture

It is recommended to demodulate the FM-UWB signal without frequency translation (no mixing). Figure 140 shows an example of a receiver block diagram. The low complexity receiver comprises a LNA, a wideband FM demodulator, and low-frequency subcarrier filtering, amplification and demodulation circuitry.

— FM-UWB receiver block design

The absence of carrier synchronization allows for fast synchronization. Due to the FM demodulation (instantaneous de-spreading) in the wideband FM demodulator, the system behaves like a narrowband FSK system where synchronization is limited by the bit synchronization time.

Clear Channel Assessment

The receiver may perform clear channel assessment (CCA) by using either the energy detection or preamble detection. However, slotted aloha shall be employed.

Human Body Communications (HBC) PHY specification

General

This is Electrostatic Field Communication (EFC) specification for HBC PHY. It covers the entire Physical Layer (PHY) protocol for Body Area Networks, such as packet structure, modulation, preamble/SFD, etc. This standard is intended to conform to established regulations in the United States, Europe, Japan and Korea.

EFC transmitter is implemented with only digital circuits and needs one electrode (instead of antenna), and EFC receiver can be implemented without any blocks related to RF carrier signals (mixer, VCO, ADC/DAC, etc.). These allows EFC device to have very low implementation complexity and low power consumption.

There are two bands of operation centered at 16MHz and 27MHz with the bandwidth of 4MHz. Both operating bands are for the United States, Japan, and Korea, and the operating band centered at 27MHz is for Europe. More information regarding the regulation conformation is given in [B1].

EFC packet structure

The EFC packet is composed of Preamble, SFD (Start Frame Delimiter), Header, and PHY Payload (PSDU). And PHY Payload is composed of MAC Header, MAC Frame Body, and FCS (Frame Check Sequence). The packet structure with PHY Header fields is shown in Figure 141. The description of each header field is given in Table 72 of 11.6.

— EFC Packet Structure

EFC Transmitter

EFC transmitter uses frequency selective digital transmission (FSDT) scheme; data is spread in frequency domain using frequency selective spread codes and transmitted in digital form. The dominant frequency where most of transmitting signal is distributed can be selected by using specific frequency selective spread code. The EFC transmitter is composed of following blocks as shown in Figure 142.

Preamble Generator

SFD/RI Generator

Header Generator

Serial-to-Parallel (S2P)

FS-Spreader [FS = Frequency Selective]

Pilot Generator

MUX

The generated Preamble, SFD/RI, Header, PSDU, and Pilot signals are sent to an electrode via a MUX. Since preamble and SFD are fixed data patterns, they are pre-generated and sent ahead of the packet header and payload. These different signals are transmitted in sequence via a MUX and the electrode. The frequency band for EFC is from 10 MHz to 50 MHz.

— EFC Transmitter Block Diagram

PHY Preamble

A preamble sequence is transmitted four times (PR1 to PR4) to ensure packet synchronization by the receiver (see Figure 143).

— Preamble Field

Each preamble sequence is created by spreading a 128-bit gold code sequence via Frequency Shift Code (FSC). FSC uses a repeated [0, 1] code and the spreading factor (SF) is decided by the number of time FSC is repeated. If the FSC used is [0, 1], the SF is 2, and if the FSC used is [0, 1, 0, 1], the SF is 4. For EFC packet preamble, a SF of 4 is used. In other words, [0, 1, 0, 1] is used for FSC operation. The operating clock frequency is fCK. Figure 144 show the preamble generation block diagram.

— Preamble Generation Block Diagram

Table 66 shows the Gold Code Generation Polynomials, and Table 67 shows the code set used for generating preamble sequence. Table 68 shows the FSC bit mapping used for preamble sequence generation.

— Gold Code Generation Polynomials for Preamble

|  | Polynomial 1 | Polynomial 2 |
| --- | --- | --- |
| Polynomial | x10 + x3 + 1 | x10 + x8 + x3 + x2 +1 |
| Initial value | [1:10] (0010010001) | [1:10] (0011111010) |

— Code Set for Preamble

| Bit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Code | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 |
| Bit | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 |
| Code | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 |
| Bit | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 |
| Code | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 |
| Bit | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 |
| Code | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| Bit | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 |
| Code | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 |
| Bit | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 |
| Code | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 |
| Bit | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 |
| Code | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 |
| Bit | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 |
| Code | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 |

— FSC Bit Mapping for Preamble (@16 MHz)

| 16MHz channel | 0 | [1, 0, 1, 0] |
| --- | --- | --- |
|  | 1 | [0, 1, 0, 1] |

The specified preamble sequence length was chosen since it provides the desired preamble detection performance even without any RF carrier signal related blocks (mixer, VCO, ADC/DAC, etc.). The preamble miss detection performance versus SNR is shown in Figure 145.

— Preamble Detection Performance

Data rate = 125kbps; 128 bit / 2 oversampling)

Start Frame Delimiter (SFD)

During packet reception, the receiver finds the start of the packet by detecting preamble sequence, and then it finds the starting point of the frame by detecting Start Frame Delimiter (SFD). Unlike preamble sequence, SFD sequence is sent only once. The SFD sequence is generated by applying FSC with SF of 4 to a 128-bit gold code sequence. Figure 146 shows the SFD signal generation block.

By using “time offset,” the SFD field can also indicate the transmitted packets data rate. With this “Rate Indicator” (RI), the receiver does not need to refer to the PHY header to detect the incoming packet’s data rate. This allows the header along with the payload be transmitted at the same high data rate increasing transmission efficiency. More about Rate Indicator is given in 11.8.

— SFD/RI Signal Generation Block Diagram

Table 69 shows the Gold Code Generation Polynomials, and Table 70 shows the code set used for generating SFD sequence. 0 shows the FSC bit mapping used for SFD sequence generation.

— Gold Code Generation Polynomials for SFD

|  | Polynomial 1 | Polynomial 2 |
| --- | --- | --- |
| Polynomial | x10 + x3 + 1 | x10 + x8 + x3 + x2 +1 |
| Initial Values | [1:10] (0101100000) | [1:10] (0000100010) |

— Code Set for SFD

| Bit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Code | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 |
| Bit | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 |
| Code | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 |
| Bit | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 |
| Code | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 |
| Bit | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 |
| Code | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 |
| Bit | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 |
| Code | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| Bit | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 |
| Code | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| Bit | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 |
| Code | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 |
| Bit | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 |
| Code | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 |

— FSC Bit Mapping for SFD @ 16Mhz

| 16MHz channel | 0 | [1, 0, 1, 0] |
| --- | --- | --- |
|  | 1 | [0, 1, 0, 1] |

PHY Header

When DRF mode (instead of RI) is used, the Header signal is generated as shown in Figure 147. If RI method is used, the header signal is generated by the block shown in Figure 148. Table 72 shows the description of each PHY header field.

— Header Generation Block Diagram

— PHY Header Field Description

| Bit Position | Field | Length (bit) | Values | Description |
| --- | --- | --- | --- | --- |
| 0 ~ 2 | Data Rate | 3 | 000: 125 Kbps 001: 250 Kbps 010: 500 Kbps 011: 1 Mbps 100: 2 Mbps 101: - 110: - 111: - | PSDU data rate (RI can also be used. See 11.8) |
| 3 ~ 4 | Pilot Info | 3 | 000: 0.125 ms (16 octets) 001: 0.25 ms (32 octets) 010: 0.5 ms (64 octets) 011: 1 ms (128 octets) 100: 2 ms (256 octets) 101: 4 ms (512 octets) 110: no insertion | Pilot Insertion Interval (11.8.2) |
| 6 ~ 7 | Sync | 2 | 00, 01: no sync 10: frame sync 11: Superframe sync | Frame Sync Information ( 11.8) |
| 8 | D | 1 | 0: normal mode 1: dedicated mode | Dedicated mode () |
| 9 ~ 11 | BAN ID | 3 | 000 ~ 111 | Current BAN ID |
| 12 ~ 15 | Reserved | 4 | - | - |
| 16 ~ 23 | MAC Frame Body Length | 8 | 0 ~ 255 | MAC Frame Body Length in Octets |
| 24 ~ 31 | CRC8 | 8 | - | CRC value of PHY Header |

Sync Field

This field is for synchronization between the master device and slave nodes. When this field is set to 1x, the internal timing information is updated with the value of registers as below.

- (frame sync): updated with the pre-set values of the slot and chip count registers. (used for every downlink frame that is sent in sync with the frame period)

(superframe sync): updated with the pre-set values of the frame, slot and chip count registers (used for Broadcast frames transmitted at a specified time in a superframe)

D Field

Dedicated mode allows 1:1 full bandwidth transmission between the master device and a particular slave device. D field indicates whether the current frame is transmitted in dedicated mode or not. Other slave devices, if any, stop any communication when this field is set to 1. Any new device attempting to join the BAN should wait until dedicated mode ends.

S2P and FS-spreader

S2P and FS-Spreader generates PHY Header (for RI method) and PSDU. FS-Spreader is composed of Orthogonal coding and FSC as shown in Figure 148.

— S2P and FS-Spreader Block Diagram

The data to be transmitted is created by mapping 4 bits (a symbol) from FIFO to a 16-bit chip. Table 73 shows the symbol-to-chip mapping. The 16-bit chip is then spread by applying FSC. The spreading factor of FSC used determines the final data rate. Table 74 shows the number of chips per bit for each possible spreading factor.

— Symbol-to-Chip Mapping

| Symbol | Data Bits | Chip | Symbol | Data Bits | Chip |
| --- | --- | --- | --- | --- | --- |
| 1 | 0000 | 1111 1111 1111 1111 | 9 | 1000 | 1111 1111 0000 0000 |
| 2 | 0001 | 1010 1010 1010 1010 | 10 | 1001 | 1010 1010 0101 0101 |
| 3 | 0010 | 1100 1100 1100 1100 | 11 | 1010 | 1100 1100 0011 0011 |
| 4 | 0011 | 1001 1001 1001 1001 | 12 | 1011 | 1001 1001 0110 0110 |
| 5 | 0100 | 1111 0000 1111 0000 | 13 | 1100 | 1111 0000 0000 1111 |
| 6 | 0101 | 1010 0101 1010 0101 | 14 | 1101 | 1010 0101 0101 1010 |
| 7 | 0110 | 1100 0011 1100 0011 | 15 | 1110 | 1100 0011 0011 1100 |
| 8 | 0111 | 1001 0110 1001 0110 | 16 | 1111 | 1001 0110 0110 1001 |

— S2P and FS-Spreader Spreading Results

|  | Chip Length | Spreading Factor | Spreading Sequence/Bit |
| --- | --- | --- | --- |
| 2Mbps | 16 | 4 | 16×4/4 ( 16 chip/bit |
| 1Mbps | 16 | 8 | 16×8/4 ( 32 chip/bit |
| 500kbps | 16 | 16 | 16×16/4 ( 64 chip/bit |
| 250kbps | 16 | 32 | 16×32/4 ( 128 chip/bit |
| 125kbps | 16 | 64 | 16×64/4 ( 256 chip/bit |

Rate Indicator and Pilot Signal

Rate Indicator using SFD

Besides the default traditional method using Data Rate Field (DRF) in PHY header, the SFD sequence can be used to indicate the data rate of the whole incoming packet, both header and payload. This concept is called “Rate Indicator” (RI).

With RI, as shown in Figure 149, the transmitter can introduce varying time offset when sending the SFD sequence to indicate a fixed set of information. By detecting this time offset, the receiver can figure out what particular information is being sent. With RI, the information delivered is the whole packet’s data rate.

— Rate Indicator using SFD

A total of 24 garbage bits (all 1’s) are introduced to allow time offset in addition to 128 bit Gold code for SFD. This sums to a total of 152 bits. FSC with SF of 4 is applied to give the final SFD field length of 608 bits.

SFD Length = (128-bit gold code + 24 bits for time offset) × 4 = 608 bits

RI can indicate seven (7) different data rates as shown in 0. RI allows both PHY header and PDSU to be transmitted at the same data rate which provides throughput efficiency, especially for high data rates. To use RI, devices should negotiate using upper protocol any time during a session after initial handshaking.

— SFD Time Offset and Data Rate Mapping for RI

| RI | Data Rate |
| --- | --- |
| Toffset1 | 125kbps |
| Toffset2 | 250kbps |
| Toffset3 | 500kbps |
| Toffset4 | 1Mbps |
| Toffset5 | 2Mbps |
| Toffset6 | Reserved |
| Toffset7 | Reserved |

Pilot Signal

To prevent loosing synchronization due to clock drift, “Pilot” sequence can be inserted in PSDU as shown in Figure 150. The same sequence used for SFD is used for pilot, and the pilot insertion interval is indicated in the “Pilot Info” field in PHY header. There are three pilot insertion intervals (Table 76).

— Pilot Insertion in PSDU

— Pilot Insertion Periods

| Pilot Info Field | Insertion Period |
| --- | --- |
| 000 | 16 octet |
| 001 | 32 octet |
| 010 | 64 octet |
| 011 | 128 octet |
| 100 | Reserved |
| 101 | Reserved |
| 110 | No pilot insertion |

Transmitter Specifications

Transmit Mask

A transmit spectrum mask shall be used to remove harmonics and possible interference in other bands, especially with 400MHz medical band. The transmit power spectrum shall be less than 0 dBr (dB relative to the maximum spectral density of the signal) for , -1 dBr for , -0.5 dBr/MHz for  as a function of the frequency, and -32 dBr for , where fc is channel center frequency and fBW is the channel bandwidth. The recommended transmit spectrum mask for fc=16MHz is shown in Figure 151 and the specification is given in Table 77.

— Transmit Spectrum Mask (for fc-16Mhz)

— Transmit Spectrum Mask Specification (for fc=16Mhz)

| Frequency (MHz) | Mask Specification |
| --- | --- |
|  | 0 dBr |
|  | -1 dBr |
|  | -0.5 dBr/MHz |
|  | -32 dBr |

Transmit Power

The transmit power of a transmitter should be considered with both the conduction and radiation conditions. The conduction power can be measured with earth-grounded spectrum analyzer (SA) equipment. The ground of the transmitter shares that of the SA. However, the radiation power measurement can be conducted in a radiation emission (RE) chamber room where the ground of the device is separated far apart from the SA. The capacitive coupling under this condition incurs very weak return path. Hence, the electric-field strength at the output of the transmitter is considerably decreased when compared to the conduction power measurement.

The conduction power shall be more than -12 dBm as the overall power in the frequency band. The radiation power shall be more than -39 dBm EIRP as the overall power in the frequency band. Devices shall limit their transmit power to mitigate against interference to other devices and systems, and to meet the regulatory policies.

Clock Frequency Tolerance

Pilot symbol enables stable operation instead of variable clock frequency tolerance. In the case of 64MHz clock, Table 78 shows allowed clock frequency tolerance values for 256 octet transmission according to variable data rates.

— Clock Frequency Tolerance Example

| Pilot Info Field | Insertion Period | (20 ppm | (40 ppm |
| --- | --- | --- | --- |
| 000 | 16 octet | - | 125 kbps |
| 001 | 32octet | 125 kbps | 250 kbps |
| 010 | 64 octet | 250 kbps | 500 kbps |
| 011 | 128 byte | 500 kbps | 1 Mbps |
| 100 | Reserved |  |  |
| 101 | Reserved |  |  |
| 110 | No pilot insertion | > 1 Mbps | > 2 Mbps |

(Variable Data Rates; 256-octet transmission)

Transmit Timing Requirements

The timing information of the transmit signal is shown in Figure 152. It has two timing requirements: duty cycle and rising/falling time. Table 79 and Figure 152 show these requirements under the condition of 15pF capacitive load.

— Transmit Timing Requirements

| Parameter | Conditions (CL=15pF) | Min | Max | Unit |
| --- | --- | --- | --- | --- |
| Output Duty Cycle | Ratio of twh over (twh+twl) | 48 | 52 | % |
| Rising/Falling Time | 10% to 90% of VDDTX | 2 | 4 | ns |

—Transmit Timing information

Receiver Specifications

Receiver Sensitivity

The minimum receiver sensitivity levels shall be the levels listed in Table 80. The levels are obtained for a packet error rate (PER) of less than 1 % with a payload of 128 octets. The measured device under the condition shows a noise figure of 10 dB and an implemented loss of 6 dB.

— Minimum Receiver Sensitivity Level

| Data Rate (kbps) | Minimum Receiver Sensitivity (dBm) |
| --- | --- |
| 125 | -112 |
| 250 | -106 |
| 500 | -100 |
| 1000 | -94 |
| 2000 | -88 |

# (informative)
Bibliography

IEEE 802.15.6 Regulation Subcommittee Report” (doc. IEEE P802.15-08-0034-12-0006).

IEEE Std 802.15.4a™ 2007

# (informative)

## Appendix B (informative) Soft detection

Assuming symbol and frame synchronization, let  be the quantized values of after analog to digital conversion (ADC), where  represents sufficient statistics after the RF front-end. Let  be defined as  such that.

Decision rule 1: Correlation of the received signal with every sequence at time lag zero

where .

## Appendix B (informative) Shortened BCH (31,19) Code

A shortened BCH (31, 19) encoder is implemented from the BCH (63, 51) encoder by the following process:

Take 19 information bits, then append 32 zero bits to have 51-bit message block. Then encode with BCH (63, 51) and remove 32 zero bits in the systematic portion of the codeword such that 31 encoded bits are transmitted. A reverse operation is applied in the decoder.

# Footnotes

SAR (Specific Absorption Rate) is measured in (W/kg) = (J/kg/s). SAR is regulated, with limits for local exposure (Head) of: in US: 1.6 W/kg in 1 gram and in EU: 2 W/kg in 10 gram. This limits the transmit power in US < 1.6 mW and in EU < 20 mW.

IEEE publications are available from the Institute of Electrical and Electronics Engineers, 445 Hoes Lane, P.O. Box 1331, Piscataway, NJ 08855-1331, USA (http://standards.ieee.org).

FIPS publications and NIST special publications are available from the National Institute of Standards and Technology, 100 Bureau Drive, Stop 8900, Gaithersburg, MD 20899-8900 (http://www.nist.gov).

ISO/IEC publications are available from the ISO Central Secretariat, Case Postale 56, 1 rue de Varembé, CH-1211, Genève 20, Switzerland/Suisse. ISO/IEC publications are also available in the United States from the Sales Department, American National Standards Institute, 11 West 42nd Street, 13th Floor, New York, NY 10036, USA.

IETF RFCs are available from the Internet Engineering Task Force at http:///www.ietf.org.

The IEEE Standards Dictionary: Glossary of Terms & Definitions is available at http://shop.ieee.org/.

This method is not approved by medical authorities in many countries, at the time of publication.

# Comments

Make sure there is a comma here.

Only 2 or three bit are required to define priority remaining 6 bits can be reserved

Only 2 or three bit are required to define priority remaining 6 bits can be reserved

Make sure there is a comma here.

# Text boxes

Sync

Reserved

CRC

Payload Length

Data Rate

Pilot Info

BAN ID

D

Preamble

SFD

PHY

Header

PHY Payload

MAC

Header

MAC Payload

FCS

]