## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolutions to MR-FSK Comments on CSM Channel Spacing]
Date Submitted: [13 September 2010]
Source: [Daniel Popa, Hartman Van Wyk, Roberto Aiello, John Buffington]
Company [ITRON],
Address [France],
E-Mail:[daniel.popa@itron.com, hartman.vanwyk@itron.com]
Re: [ 802.15.4g Comment Resolution for LB51.]
Abstract: []
Purpose: [LB51 Comment Resolution]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Comments ID:
728, 749, 750, 1160

## Slide 3
Comments ID: 749, 750
CID # 750: ECC REC 70-03 require channel spacing < 100 kHz for narrowband modulation and wideband modulation other
than FHSS and DSSS
Requested resolution: Change channel spacing to 100 kHz for the common signaling mode.
Response: The solution described in document 15-10-0771-02-004g slide 8 delivers a simple and efficient solution.
Proposed resolution: Reject.
CID #749: ECC REC 70-03 require channel spacing < 100 kHz for narrowband modulation and wideband modulation other than
FHSS and DSSS
D. Popa et al <Itron>

## Slide 4
Comments ID: 728, 1160
CID #728: The channel spacing for the mandatory data rate (50 kbps) in 915 MHz and 2.4 GHz bands should not be restricted to only 200 kHz.
Switching from the MR-FSK mandatory 50 kbps / 200 kHz channel spacing to MR-FSK 150 ,200 kbps / 400 kHz, as well as
when switching from the MR-FSK 50 kpbs / 200 kHz to MR-O-QPSK or OFDM adds useless design burden and might increase
the power consumption.
CID #1160: The channel spacing for the mandatory data rate (50 kbps) in 915 MHz and 2.4 GHz bands should not be
restricted to only 200 kHz. Switching from the MR-FSK mandatory 50 kbps / 200 kHz channel spacing to
MR-FSK 150 ,200 kbps / 400 kHz, as well as when switching from the MR-FSK 50 kpbs / 200 kHz to MR-O-QPSK
or OFDM adds useless design burden and might increase the power consumption.
Requested resolution: Add a new PIB attribute phyChannelSpacingCSM (integer value) that takes the following values:
phyChannelSpacingCSM = 0 indicates the mandatory mode for MR-FSK uses 200 kHz channel spacing;
phyChannelSpacingCSM = 1 indicates the mandatory mode for MR-FSK uses 400 kHz channel spacing.
Response: Adding a new PIB attribute will challenge the interoperability goal because devices might not share the same context. Instead, a more
simpler solution consists in aligning carrier frequencies for 200 kHz and 400 kHz channel and allowing CSM message exchanges only on those 200 kHz-spacing channels that align with the 400 kHz-spacing channels. This is additionally benefic for FHSS, as it decreases the convergence time for the synchronization of unsynchronized devices.
Proposed resolution: Accept in principle. See slide 8 of document 15-10-0771-02-004g for resolution.
D. Popa et al <Itron>

## Slide 5
902.2
902.4
902.6
902.8
903.0
903.2
903.4
903.6
903.8
902.4
902.8
903.2
903.6
200 kHz channel
numbers
0
1
2
3
4
5
6
7
8
D. Popa et al <Itron>
400 kHz channel
numbers
0
1
2
3
Channel plan for MR-FSK optional modes @ {150, 200} kbps & 400 kHz channel spacing
Channel plan for MR-FSK mandatory mode @ 50 kbps & 200 kHz channel spacing
MR-FSK channel plan for 915 MHz Band: MR-FSK PHYs
CSM uses the mandatory MR-FSK PHY mode @ 50 kbps and 200 kHz channel spacing

## Slide 6
Issue: It is inefficient for an MR-FSK FH system operating at optional modes to exchange information with an MR-FSK unassociated device using CSM, if the center frequencies of the channels they use to exchange messages do not coincide.
Solution: Require that the unassociated device exchanges CSM messages only on the odd 200 kHz channel number.
Note:
CSM is optional;
CSM needs only to demonstrate the capability of communicating using the PHY;
A PHY capable to communicate in every 200 kHz channel spacing can also communication only on odd channel number.
This resolution does not add any additional requirements to the existing PHY.

## Slide 7
902.2
902.4
902.6
902.8
903.0
903.2
903.4
903.6
903.8
902.4
902.8
903.2
903.6
200 kHz
channel
number
0
1
2
3
4
5
6
7
8
D. Popa et al <Itron>
200 kHz odd
channel numbers
400 kHz
channels
Example at 915 MHz

## Slide 8
Insert the following text
For a MR-FSK frequency hopping systems operating in the mandatory mode, the commands exchanged during FH acquisition process shall use the channels whose center frequencies coincide with the center frequencies used by the MR-FSK optional modes.
D. Popa et al <Itron>