## Slide 1
NOTE: Update all red fields replacing with your information; they are required. This is a manual update in appropriate
fields. All Blue fields are informational and are to be deleted. Black stays. After updating delete this box/paragraph.
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Introduction to IEEE 802.15 Positive Train Control Interest Group]
Date Submitted: [13 October, 2011]
Source: [Jon Adams] Company [Independent]
Address [12023 N 62nd St, Scottsdale AZ, 85254 USA]
Voice:[+1 415.683.0213], FAX: [Add FAX number], E-Mail:[jonadams@ieee.org]
Re: [If this is a proposed revision, cite the original document.]
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: [Overview of the PTC-IG, the goals, the IEEE process and schedule. ]
Purpose: [Intention of this document is to inform the newly formed PTC-IG of the goals and process.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
IEEE-802-15-11-0731-00-0ptc

## Slide 2: Inaugural Telecon STDS-802-15-PTC Interest Group
Jon Adams
Independent
Interim Chair
IEEE-802-15-11-0731-00-0ptc

## Slide 3: Agenda
Introductions
Roll Call - please email (either during or shortly after the meeting) your attendance to me: jonadams@ieee.org
Reminder of IEEE P&P and Patent Policy and call for Potentially Essential Patents. Please see http://grouper.ieee.org/groups/802/15/pub/Rules.html and http://standards.ieee.org/board/pat/pat-slideset.ppt before the call.
Efforts to pursue before November IEEE Atlanta meeting
  Reminder of dates for registration and hotel availability
  Scheduling of sessions at Atlanta
  Differences between amendments and new standards
  The IEEE 802 way: Project Authorization Requests (PAR), the Five Criteria (5C), the process for moving from Interest Group to Study Group to Task Group to ratified output
Review and comment on landing page
  http://www.ieee802.org/15/pub/IGptc.html
Any other business
IEEE-802-15-11-0731-00-0ptc

## Slide 4: Why Are We Here?
PTC has four primary components
  Equipment deployed on the locomotive/train
  Equipment deployed trackside
  Equipment deployed at a remotely located control center
  A bi-directional wireless data link that links all these elements. It is this component upon which the Interest Group shall focus.
IEEE-802-15-11-0731-00-0ptc

## Slide 5: Why IEEE 802?
Long (31 years and counting) and successful history of creating robust and well deployed wired and wireless standards
Formal, coordinated, consensus-based and open process
Participation is by individual contributor, not by company
Six face to face meetings per year to allow sufficient vetting and promote standard development
Voting rights maintained only through active participation
Broad international participation
IEEE-802-15-11-0731-00-0ptc

## Slide 6: Some of IEEE 802 Efforts
IEEE 802.1 Bridging (networking) and Network Management
IEEE 802.2 Link Layer Control
IEEE 802.3 Ethernet
IEEE 802.5 MAC layer for Token Ring
IEEE 802.11 a/b/g/n/… Wireless LAN (WLAN) & Mesh (Wi-Fi certification)
IEEE 802.15 Wireless PAN
IEEE 802.16 Broadband Wireless Access (WiMAX certification)
IEEE 802.17 Resilient packet ring
IEEE 802.18 Radio Regulatory TAG
IEEE 802.19 Coexistence TAG
IEEE 802.20 Mobile Broadband Wireless Access
IEEE 802.21 Media Independent Handoff
IEEE 802.22 Wireless Regional Area Network
IEEE 802.23 Emergency Services
IEEE-802-15-11-0731-00-0ptc

## Slide 7: Why 802.15?
IEEE 802.15 Wireless PAN Working Group
  IEEE 802.15.2 WIEEE 802.15 and 802.11 coexistence
  IEEE 802.15.4 (2006)
    Used by the ZigBee Alliance, ISA, Wireless HART, IETF (6LoWPAN), others
  IEEE 802.15.4g Smart Utility Network
    In-process effort to enable wireless connectivity for next generation of smart utility meters (electricity, gas, water, heat) with utilities
    Operates on licensed or license-free bands, wide variety of channel widths, bandwidths, data rates
    Ranges to 10’s of km
  IEEE 802.15.4k Low-Energy Critical Infrastructure Monitoring
    PHY amendment to 802.15.4 to facilitate point to multi-thousands of points communications for critical infrastructure monitoring devices (bridges, buildings, canals, etc.)
    Addresses application's user needs of minimal network infrastructure
    Enables the collection of scheduled and event data from a large number of non-mains powered end points that are widely dispersed, or are in challenging propagation environments
    To facilitate low energy operation necessary for multi-year battery life, amendment minimizes network maintenance traffic and device wake durations
    Ranges to 10’s of km
  IEEE 802.15.4m TV White Space Amendment
    Chartered to specify new PHY to add functionality to the existing standard 802.15.4-2006 MAC meeting TV white space regulatory requirements
    enables operation in the available TV white space
    supporta typical data rates in the 40 kbits per second to 2000 kbits per second range
    Designed for optimal and power efficient device command and control applications
IEEE-802-15-11-0731-00-0ptc

## Slide 8: Why IEEE 802.15?
PTC overview at July 2011 IEEE 802.11 WNG and 802.15 WNG sessions
  Entitled: PTC Radio and System Architecture (11-11-1032-00-0wng-positive-train-control-radio-and-system-architecture.ppt), Jia-Ru Li, Lilee Systems
802.15 voted to approve formation of an interest group to explore further
First step to explore alignment with 15.4k LECIM
IEEE-802-15-11-0731-00-0ptc

## Slide 9: Challenging Propagation Environment
In the US, PTC allocated 220 – 222 MHz band (λ = 1.36 m)
High speed mobility environment
  500 km/h locomotive to trackside (1000 km/h closing speed)
“Collector” atop locomotive
  Antenna on locomotive “roof”, 5m height above railtop
  Roof 15 – 25 m long, 2.5 m wide, potentially 2km of metal-roofed cars ahead or behind
Endpoints (Wayside Equipment)
  Fixed equipment along the track, antennas may only a few meters high or pole-mounted up to 8-10 m
Base Station
  Network-connected base stations
  Antennas may be on towers, buildings or other structures
Track environment – extreme in every direction
  Mountainous terrain, tunnels, open cuts, viaduct with sound walls
  All of above but with horizontal curvature and rain sheeting down walls
  Dead flat straight track, technically line-of-sight between collector/endpoint but very strong Rayleigh fading due to strong reflection from rail/ground surface
  Dense urban, non-line of sight, extreme multipath
Distributed Power Unit (DPU)
  Remote controlled locomotive(s) separated from the crewed lead locomotive, separation up to 3 km
IEEE-802-15-11-0731-00-0ptc

## Slide 10: PTC Aspects 1
Train-centric communications (locomotive/train is “center of universe”)
High reliability PHY link, fault-tolerant, error-correcting or at least error-detecting
Intention that data carried may be “vital” (life/safety critical)
Strong link layer security features (flexible encryption, unique identity)
Data rates relatively low, depending on function (9.6k to 100’s of kbps)
Data communication speeds may be asymmetric
Propagation generally non-line of sight or close to ground, fade environment often Rayleigh, exponents 2.6 (fixed to fixed) to 3.2 (fixed to mobile)
Range to 2x braking distance (3 - 15 km) in typical urban/suburban/rural environments
Equivalent Radiated Power (ERP) (depending on antenna height, channel #, region)
Operation in licensed US 220 – 222 MHz band (but not excluding others)
  Channel spacing 5 kHz, may be aggregated (by license)
  Can support separate uplink and downlink bands (base and mobile)
  Potential for adjacent/alternate channel interferers
  Frequency agility may be useful
IEEE-802-15-11-0731-00-0ptc

## Slide 11: PTC Aspects 2
Absolute need for high-speed node mobility
  Speeds up to 500km/h, closing speeds to 1000 km/h
Latencies determined by stopping distance, order of 1 second sufficient
Payloads from a few bytes for control/command to ability to transfer larger files with fragmentation for remote upgrade/maintenance
Selectable QoS or communications priority may be useful
Wayside devices likely extremely power constrained (battery, vibration, pressure, solar, other scavenging)
Current requirements up to 24 locomotives and 30 waysides on one base station, but concept scales to dozens of devices per km of track
Flexible enough to handle very rapidly changing network membership
Time slotted and contention access periods necessary
Slide 11
IEEE-802-15-11-0731-00-0ptc
Notes: doc.: IEEE 802.15-<doc#>
<month year>
        <author>, <company>
Page 11

## Slide 12: Other Potential Future Rail Environment Applications of 802.15 Standards
Track and track infrastructure
  Switch/turnout operation and position
  Block occupancy
  Damage to rails
  Right of Way fouling
  Perimeter monitoring
  Bridge, viaduct, tunnel, culvert, etc.
  Highway / Rail grade crossing
Rolling Stock Defects
  Defect detection (hot box, dragging equipment, high/wide, etc.)
Signals
  Signal indication
  Signal function
  Grade crossing signaling and warning equipment
Maintenance of Way Vehicle
  On/off rail status
  Position, direction, speed
  Positive control?
Maintenance workers
Rest-of-train car-to-car communication networks
  Hot box, brake line pressure, end of train marker, etc.
IEEE-802-15-11-0731-00-0ptc

## Slide 13: Standards Development Lifecycle
Idea or concept to be standardized, may be broad or specific
Need IEEE Sponsor
  in this case, it’s IEEE Computer Society and IEEE 802 Local and Metropolitan Area Network Standards Committee
IEEE-802-15-11-0731-00-0ptc

## Slide 14: Process (in shorthand)
Propose the idea (PTC proposal was done at the last IEEE 802 Plenary in both 802.11 and 802.15 WNG sessions)
Get recognized officially
  Interest Group (IEEE 802.15 PTC, formed under the 802.15 Working Group (WG)
    Interim Chair: Jon Adams, Independent
    Interim Vice Chair: Dr Mark Hartong
    Interim Secretary – any volunteers?
      Meeting minutes, attendance-keeping, etc.
  Study Group
    Develop Project Authorization Request and complete the “Five Criteria” document
    Get PAR done, approved by WG, and submitted to 802 Executive Committee
  Task Group
    Once TG is formed, group may “do work” and move along path of creating a draft standard
    Once draft standard is successfully balloted and approved by TG and WG, submit draft to 802 EC for approval
IEEE-802-15-11-0731-00-0ptc

## Slide 15: Next Steps for Participation
Register for the Atlanta Plenary 7-11 November
Hotel rooms are filling up
IEEE-802-15-11-0731-00-0ptc

## Slide 16
IEEE-802-15-11-0731-00-0ptc

## Slide 17: Next Meeting
7-Day requirement on notification of meetings
Have already reserved next Wednesday 19 October in case we want to move earlier in week
Weekly meetings until Atlanta
IEEE-802-15-11-0731-00-0ptc