## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [New MBAN Standard Study on Chinese Sub-GHZ Bands]
Date Submitted: [Nov. 5, 2011]
Source: [Liang Li, Lan Zhu, XiaoMing Peng, Xin Tao,ZhongLiang Deng] Company [Vinno, CESI, I2R, WuXi –WSN, BUPT]
Address [Room 402 Building D, Shangdi Xinxi Lu No.2 Pioneering Park, Haidian District, Beijing, China 100085]
Voice:[8610-82782373], FAX: [8610-82893004], E-Mail:[liangli@vinnotech.com]
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: Proposes that FCC MBANS rules can be met with minimal additional amendments for the 15.4 PHY and MAC layers.
Purpose: Discussion on TG4j
Notice: This document has been to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Challenges on Chinese Wireless Medical Monitoring Networking Applications
There are a quite emergent requirements to apply Wireless Sensor Networks (WSN) on hospital / clinic / home healthcare / clinic and more. Chinese Health Ministry, Medical instrument Companies and an amount of hospitals announce their great IOT application plots.
NO NATIONAL MBAN STANDARS. NO APPLICATION SPEC.

## Slide 3: Challenges on Chinese Wireless Medical Monitoring Networking Applications
National CWPAN Standard GB/T15629.15-2010 only defines the 2.4GHz and 780MHz band PHY and MAC for general WPAN applications
2.4GHZ band (2400-2483.50MHz) is one ISM band, which is occupied by all short-range wireless devices, such as Wi-Fi, Bluetooth to name a few.
More and more multiple WPAN products and application are on 780Mhz. MBAN application may be one of them.
Interference to Wireless Medical Networking applications may be serious on 2.4GHz, 780MHz bands

## Slide 4: Approved Frequency Bands for Medical Application
We confirmed the following frequency bands are approved for “wireless communication for medical data”
  Frequency Bands:
    174 --- 216MHz,
    402 --- 425MHz
    608 --- 630MHz
  Transmission Power Limitation ≤ 10mw(e.r.p),
  Frequency Offset limitation ≤ 100ppm
  “Tech Requirement for Mini Power (Short-Rang) Wireless Device” Doc: MIIT-423 (2005)

## Slide 5: Frequency Emission Limitation
Transmitter On (Max Power)
Transmitter Standby (Max Power)
Freq Band | Measurement Band | Limitation | Measurement Method
30MHz-1Ghz | 100KHz (3dB) | -36 dBm | e.r.p
Freq Band | Measurement Band | Limitation | Measurement Method
30MHz-1Ghz | 100KHz (3dB) | -36 dBm | e.r.p
>1GHz | 1Mhz (3dB) | -47 dBm | e.r.p

## Slide 6: CWPAN Setup MBAN SG
On June 22, 2011, CWPAN Standard group conference passed the motion to setup this study group and going to a Task group for National standard soon.
The major promoters are: Vinno, CESI, Chinese Medical IOT Office , Chinese Radio Management Office, Chinese Academic Institutes, Wuxi Sensing Institute and Huawei.
On Aug.1, 2011, Chinese Standard Committee approves to set the CWPAN-MBAN Study Group.
In 2012, the MBAN Study Group(SG)  MBAN Task Group (TG)

## Slide 7: Purposes for CWPAN MBAN Study Group
Build up the Wireless MBAN Standard Task Group in 2012
The major interesting area:
  Safely introduce Wireless Sensor Networking, which is based on GB/T15629.15-2010, to Medical/Health application
  Study the tech spec of WPAN/WSN on approved bands for medical/health application
  Study the possibility to set up reasonable procedures and conditions to adopt medical applications on 780 MHz band

## Slide 8: Extend 15.4 to Medical/Health Area: IEEE802.15.4J
There are the direct or potential interference and troubles as 15.4 Networking applied on hospitals, clinics, and family cares on regular 2.4GHz band.
The FCC has issued a Notice of Proposed Rule Making (NPRM) (FCC NPRM 09-57) to allocate the band 2360 to 2400 MHz for Medical Body Area Network (or MBAN) systems using body sensor devices.
IEEE802.15.4J is a spec to extend the operation of 15.4 into a band that is reserved for MBAN use.

## Slide 9: Proposal: Set up New IEEE802.15.4- Interesting/Study / Task Group
Introduce a New Chinese MBAN Std Chance to IEEE802.15
IEEE802.15 and CWPAN coop again to build the tech spec for a huge markets (WSN/IOT on Medical/Health Application)
  CWPAN-MBAN Proposals and proposed spec are studied
  Expect to amend IEEE802.15.4-2009/4J for New Chinese MBAN bands
Other necessary amendments on IEEE802.15.4-2009/2010 (PHY and MAC)

## Slide 10: Discussion on Std Development Criteria
BROAD MARKET POTENTIAL
  Over $10B Hospital/Clinic Environment Monitoring, Management, Family HealthCare and more
COMPATIBILITY
  IEEE802.15.4-2009
DISTINCT IDENTITY
  Working on Chinese MBAN and Coop to Chinese MBAN Standards
TECHNICAL FEASIBILITY
  ????
ECONOMIC FEASIBILITY
  Low cost

## Slide 11: Discussion: Other Issues around MBAN Standard
Are there other standards or projects with a similar scope?
  There are no Chinese MBAN standards
  Similar to IEEE802.15.4J, but on different bands.
  Different application areas to ones of IEEE802.15.6
Intellectual Property
  Based on IEEE-SA IP policy.
Extend to Other Standard Groups
  ???
Safely
  ???
Others
  ???