## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: LECIM DSSS PHY Merger Update
Date Submitted: November 6, 2011
Source: [Sourav Dey, David Howard, Shu Kato, Kyung Sup Kwak and M. Al Ameen, Xiang Wang, Shusaka Shimada] Company [On-Ramp Wireless, Tohuku University and Hitachi, Inha University and ETRI, WSNIRI and SIMIT, Yokogawa Co. and Toyko Institute of Technology]
Address []
Voice:[+1(858)592-6008], FAX: [+1(858)592-6009], E-Mail:[ sourav.dey@onrampwireless.com, david.a.howard@ieee.org, shukato@riec.tohoku.ac.jp, kskwak@inha.ac.kr, wilsonwangxiang@gmail.com, shusaku@ieee.org ]
Re: [LECIM Call For Proposals, DCN: 0147-02]
Abstract: [Response to LECIM Call For Proposals, DCN: 0147-02]
Purpose: [Update the LECIM group on the status of DSSS PHY merger.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Et.

## Slide 2: LECIM DSSS PHY Merger Update
11/7/2011

## Slide 3: LECIM DSSS PHY Proposals to Merge
DCN: 641, Tohuku University and Hitachi
DCN: 611, Inha University/ETRI
DCN: 591, WSNRI/SIMIT
DCN: 629, Yokogawa
DCN: 627, On-Ramp Wireless

## Slide 4: General Updates
Continuing conversation from Okinawa in weekly conference calls
Agreement on many features
Still exploring other features
“A work in progress”

## Slide 5: Bands and Channels
Agreement on making DSSS PHY inclusive to all bands that make sense around the world
Agreement to have different chip rates to fit in different channel bandwidths around the world

## Slide 6: Bands and Channels
2.4 GHz
  2400 MHz – 2483.5 MHz
  Channel center frequency
    f(k) = 2402 + 1.99*k; k= 0,…,40
  Chip rate = 1Mchip/s?
900 MHz
  900 MHz – x?
  Channel center frequency
    f(k) = 900 + 1.99*k; k= 0,…,36
    f(k) = 900 + (0.2*p)*k; k= 0,...,72 where p= 1 to 5
  Chip rate = 1Mchip/s?
423MHz (Japan)
  429.8125 MHz – 429.925 MHz
  Narrowband 8.5 KHz/channel
800 MHz (Korea)
  868 MHz – 870 MHz
  Channel center frequency
    f(k) = xxx + 640*k; k= 0,…,x
  Chip rate = 320Kchips/s?

## Slide 7: Bands and Channels
915MHz (Korea)
  902 MHz – 928 MHz
  Channel center frequency
    f(k) = 902 + 1280*k; k= 1-10
  Chip rate = 1280Mchips/s?
470MHz (China)
  470MHz – 510MHz
  Channel center frequency
    f(k) = 470.4+0.4*k; k= 0,…,98
  Chip rate = 100Kchips/s
780MHz (China)
  779MHz – 787MHz
  Channel center frequency
    780/782/784/786MHz
  Chip rate = 1Mchips/s

## Slide 8: DSSS Reference Modulator
PHY Header
Forward Error Correction
Interleaving
Modulation
SYNC Header
Direct Sequence Spreading

## Slide 9: PHY Header
Working on developing a short PHR
  Incorporates length of packet, dynamic spreading factor selection, etc.
  Format not decided, requires further exploration
Exploring the Option of no PHR
  Commissioned packet size and spreading factor could make PHR unnecessary

## Slide 10: Forward Error Correction
Agreement on Rate ½ Convolutional Code
  Octal Generators: (133,171), Constraint Length = 7, Free Distance = 10
Exploring Optional Tail-Biting Implementation
  Tail-Biting initialization preserves code rate reducing overhead
  Could be important for small LECIM packets sizes
  Small hit to performance at 10^-2 BER

## Slide 11: Interleaver
Agreement on need for interleaver
  Makes reception robust to bursty interference and channel events
Exploring required interleaver depth
  One option is 6*7= 42 bits (6 = traceback depth, 7 = constraint length)
  Interleaver delay is not important consideration in LECIM applications
Exploring potential interleaver implementations
  Bit-reversal addressing interleaver over the entire packet

## Slide 12: Modulation
Agreement on Differential BPSK
  Differential modulation allows the option of building a simple non-coherent rcvr
  Higher order modulation undoes processing gain by requiring much higher SNR
Exploring offset QPSK as another modulation technique
  Good for PA efficiency and reduced spectral leakage
  Note: Offset is over chips with modulator after spreading (not like diagram above)
  Tradeoff in going to a higher spreading factor may be worth it in some situations
  SIMIT will be presenting on this technique this week
Exploring optional higher order modulation with no spreading
  Useful to make a standard that is flexible to higher throughput applications as well

## Slide 13: Sync Header (SHR)
Exploring design of sync header (SHR)
  Need to decide what system specifications we are designing for, i.e. what BER? 10^-2? 10^-3?
  Need to decide length of preamble; 16 symbols is a good goal but needs more exploration
  Need to explore the length of the SFD, particularly for variable length packets
  Need to explore how to use the symbols of the SHR, e.g. channel estimation, synchronization, frame detection, modulation and coding scheme (MCS), etc.

## Slide 14: Direct Sequence Spreading
Agreement on the use of Gold Codes as PN sequences
  Large family of spreading codes, m = 25 --> 33,554,433 unique codes
  Good periodic cross-correlation and off-peak auto-correlation properties
  Exploring not resetting the PN sequence through the packet
Exploring the option of OVSF Codes cascaded with Gold Code
  Inha University will be presenting this week
Exploring the necessary timing accuracy of the MAC
  Need to have enough slack to account for propagation delay in frame structure
  Need to account for time offset between endpoint and collector
Notes: What sort of timing accuracy do we need MAC?

## Slide 15: Spreading Factors
Exploring the Range of Data Rates
  Dynamically assigned data rates; integer rates (MAC-SAP) could be good
  Pre-set commissioned data rates (MAC-SAP)
Exploring Range of Spreading Factors
  Powers of 2 vs. integer
  Exploring the use of no spreading is an optional mode
  Exploring broad range of spreading factors from ~SF16 to ~SF32k
Exploring Range of Chip Rates
  Powers of 2 vs. integer
  Agree on different chip rates for different spectrum allocations in different regulatory regimes
Explore interaction of MAC timeouts with lower data rates
  Can we go 15bps? 100 bps?
Will build a table of rates, spreading factors, and chip rates

## Slide 16: Conclusion
Broad agreement from all proposers on general features of DSSS PHY
Further exploration of certain optional techniques
More work to be done
  PHY Header
  SYNC Header
  Supported Spreading Factors
All support to move DSSS PHY as a part of the LECIM baseline