## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: KMP Transport Proposal
Date Submitted: January 16, 2012
Source: Robert Moskowitz, Verizon
Address 1000 Bent Creek Blvd, MechanicsBurg, PA, USA
Voice:+1 (248) 968-9809, e-mail: rgm@labs.htt-consult.com
Re: Key Managementn over 4e Multipurpose Frames
Abstract: Proposal for tg9 document structure and content
Purpose: To add Key Management capabilities to 15.4 and 15.7
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Key Management Support for 15.4 and 15.7
Robert Moskowitz
Jacksonville
January 16, 2012

## Slide 3
Abstract
To provide for a Key Management Protocol Transport for 802.15.4 and .7
  KMP agnostic
  Support: HIP, IKEv2, 802.1X, ...
Provide recommended functionality for KMPs
Use Information Elements
  From 15.4e for 15.4
  How for 15.7?

## Slide 4
Document Structure
Recommended Practice
  EVERYTHING is Recommended, nothing is REQUIRED
4 sections
  KMP Transport frame format and state machine
  15.4 support for KMP Transport
  15.7 support for KMP Transport
  KMP specific implementation guidelines

## Slide 5
KMP Transport Frames and State Machine
Fragmentation Support
  KMP packet size WILL exceed MPDU
  Forced fragment chaining for simplification
  Concurrent KMP sessions
Security Association content
  What keys? PTK, GTK, etc.
  Counters, lifetimes, etc.

## Slide 6
KMP Transport Frames and State Machine
Frame format
  MAC specific content
    ID
    Length
  Control Field – 1 byte
  KMP fragment

## Slide 7
KMP Transport Frames and State Machine
Control Field
  1 bit chaining flag (yes, last/onlyone)
  7 bit KMP ID/Chain count
    First packet provides KMP ID
      ID range 1-31
      HIP, IKEv2, SAE, 802.1X, etc.
    Chain Count
      Starts at 32 to disambiguate ID or count
      C=32 is 2nd fragment
      C=33 is 3rd fragment
      SHOULD provide for 8KB KMP payload

## Slide 8
KMP Transport Frames and State Machine
State Machine
  TBD!

## Slide 9
15.4 Specifics
Use 15.4e Information Elements
  In the multipurpose frame or command frame
  Use data payload IEs (not header IEs)
    Larger payload length
  Need IE type assignment
Use Forced ACK for chaining support
For pre-4e devices work with IETF on 6lowpan support

## Slide 10
15.7 Specifics
TBD!
  We need help on 15.7
  It looks workable, but details lacking

## Slide 11
KMP Guidelines
Each KMP SHOULD have a sub-section
General KMP description and use cases
  References to defining documents
Security Association(s) definitions