## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Global Overview of Existing Radio Communication Systems used for Positive Train Control]
Date Submitted: [18 January, 2012]
Source: [Ibrahim Muftic] Company [Parsons Brinckerhoff]
Address [303 2nd Street, Suite 700 N, San Francisco, CA 94107, USA]
Voice:[+1 415.218.2554], FAX: [Add FAX number], E-Mail:[muftici@pbworld.com]
Re: [If this is a proposed revision, cite the original document.]
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: [Existing Radio communication Systems used for PTC, Development, Standardization, ERTMS, ETCS, GSM-R]
Purpose: [For the PTC Study Group to use as an informative information as it moves forward.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Global Overview of Existing Radio Communication Systems for Positive Train Control Development and Standardization
Ibrahim Muftic
Parsons Brinckerhoff

## Slide 3: Key Terms
PTC - Positive Train Control
ERTMS – European Rail Traffic Management System
ETCS – European Train Control System
CTCS – Chinese Train Control System
GSM-R – Global System for Mobile – Railways
TETRA - Terrestrial Trunked Radio
CBTC – Communication Based Train Control

## Slide 4: Radio Communication Systems used for Positive Train Control
Open-standard, multi-vendor
  GSM-R for ETCS (ERTMS)
  IEEE 802.11 for CBTC (Monorail Las Vegas/4-mile route, low-speed trains)
Proprietary technologies, not standardized, single vendor solutions
  Radio based CBTC systems mainly for transit/metro systems
  Transrapid Maglev System
  Shinkansen (some backup information for train control)

## Slide 5
The US PTC systems based on propriatery, non standardized, single vendor radios
  ACSES (Advanced Civil Speed Enforcement System) – NEC (North East Corridor)
  CAS (Collision Avoidance System) – Alaska Railroad, PATH (Port Authority of NY & NJ)
  ETMS – BNSF (35 subdivisions)
  CBTM (Communications Based Train Management) – CSXT, South Carolina-Georgia
  ITCS – Amtrack, Michigen
  VTMS – UP (Wyomiong, State of Washington)
  OTC – South Carolina
  Train Sentinel – Ohio Central Railroad System
Radio Communication Systems used for Positive Train Control

## Slide 6: In Europe Before ERTMS
Train Control Systems
  Tens of different legacy train control systems, analog systems based on inductive loops and/or transponders
  Issues with interoperability, multiple on-board train control equipment on locomotives for international corridors, high maintenance costs, proprietary technologies
Radio Communication Systems
  Tens of different legacy radio communication systems, analog, 450 MHz, mostly semi/half duplex - voice only, obsolete systems, high maintenance costs, poor QoS, local connectivity, many users share same channel, etc.

## Slide 7: GSM-R Development History
UIC - worldwide international organization of the railway sector
  One of the objectives to create new world standards for railways (including common standards with other transport modes)
In late 80-ies Study for selecting of a new digital railway radio communication system
  Primary candidate technologies GSM and TETRA
1990 - UIC adopted GSM technology as a base for a new railway radio system development
  Low risk development path, HW already COTS at the time
  spectrum allocation for the railway purposes was requested
1991 – Development of a new telecommunication system (including radio) required by the European Community Rail Directive
  Requirements:
    Non-proprietary, open, interoperable across Europe
    Voice and data for both general application and train control
    Future proof …

## Slide 8: GSM-R vs. TETRA
GSM-R
Based on GSM upgraded with PMR features
FDMA/TDMA
Modulation scheme Gaussian-Fitered Minimum Shift Keying (GMSK)
200 kHz / carrier
8 timeslots / carrier
Can work in GSM 850/900, 1800, 1900 MHz bands
Data rates
  CSD
    Low protected 14.4 kbps
    High protected <9.6 kbps
  PSD (GPRS)
    ~53 kbps
There is no train control system over TETRA developed yet
TETRA
Based on PMR upgraded with GSM features
FDMA/TDMA
Modulation scheme 4π DQPSK (Differential Quaternary Phase-Shift Keying
25 kHz / carrier
4 timeslots / carrier
Can work in certain parts of 300, 400, 800 and 900 MHz bands
Data rates
  CSD
    Low protected 7.2 kbps
    Low protected 4.8 kbps
    High protected 2.4 kbps
  PSD
    Same as with CSD
It wasn’t proven and commercially available at the time of the decision

## Slide 9: GSM-R Development History
EIRENE (European Integrated Radio Enhanced Network) project
  UIC along with Railway companies
  FRS and SRS
  Started in 1992, first draft specs in 1995.
MORANE (Mobile Oriented Radio Network)
  EC, UIC, Railways, GSM suppliers
In 2000 – FRS/SRS ver. 4/12
  Current ver. 7.1/15.1; 8/16 expected

## Slide 10: Broad Railways Commitment to GSM-R
  EU commitment through legal and financial support
    EU directives from 1996 for High Speed lines and from 2001 for conventional lines require ETCS and GSM-R implementation
  UIC MoU, commitment by the railways to focus Radio Communication systems investments only to GSM-R
    In 1997 signed by 32 railways, current status 37 railways

## Slide 11: GSM-R Frequency Range
Spectrum has been allocated by the relevant EU and national authorities in 800/900 MHz so called “native” GSM-R bands
  876-880 for uplink paired with 921-925 MHz for downlink
Extended GSM-R bands (on-going requests in EU)
  873-876 paired with 918-921 MHz
E-GSM bands in China are used
1800 MHz GSM bands in Australia
  1710-1785 paired with 1805-1880 MHz

## Slide 12: GSM-R standardization stack
GSM standard functionalities
(based on ETSI 2+ Release 99)
GSM enhancements for
railways (by ETSI 3GPP)
EIRENE - railway
specific functionalities
Optional
/Implementation specific
- QoS to support ETCS and high availability voice comms
High mobility – up to 500 kph
Functional Adressing
LDA - Location Dependent Addressing
Railway Emergency Calls …
ASCI – Advanced Call Speech Items functionalities:
Enhanced Multi Level Precedence and Pre-emption
Voice Broadcast Service
Voice Group Call Service …
All GSM 2+ features can be used for GSM-R
Some EIRENE features enhanced
SMS to Functional Number …

## Slide 13: Train Control over GSM-R
ETCS project started in 1992 by UIC/ERRI
Specifications for a new digital train control to satisfy all the needs for conventional and high-speed train lines
Mandated in EU for newly built and system upgrades on major corridors
ETCS levels 2 and 3 are radio communication based
Installed in China for high-speed trains, modified to CTCS
Proven, multi-vendor, open standard systems for conventional and high-speed trains
Uses CSD

## Slide 14: GSM-R implementation status
Europe
      All EU member countries are in the implementation phase
      Many countries have already deployed GSM-R system on major corridors
        Finland, Norway, Germany, Italy, Netherlands, Sweden, Spain (in operation ~64,000 km and ~140.000 mobile units)
      Only where ETCS L2 is deployed also GSM-R is used for as train control system bearer
      Overall European railway network ~220,000 km
      Planned to be eqquiped with GSM-R ~150,000 km (~66%) and more then 300.000 mobile users

## Slide 15: GSM-R implementation status
World-wide
  In operation
    China, India
  In Construction and Contracted
    Turkey, Saudi Arabia, Australia, Morocco, Algeria, Russia
  Considered
    Kazakhstan, South African Republic, Brazil, Argentina … and USA

## Slide 16: Current Issues with GSM-R
Lack of capacity in dense traffic areas
  solutions: migration to ETCS over GPRS and/or extending the RF spectrum
Interference issues with UMTS 900 and LTE systems in adjacent bands
  solutions: better protection by regulation, sw/hw solutions

## Slide 17: Potential Implementation in the US
The challenge to implementing ETCS or any other PTC system over GSM-R is the lack of available RF spectrum for GSM-R throughout the US
For some railroads the challenge might be relatively higher costs in compare to the existing solutions

## Slide 18: References
www.uic.org
www.fra.dot.gov
www.tsd.org

## Slide 19: Q&A