## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title:[Update on Priority Access – Distribution of Priority Channel Access Slots over the Superframe]
Date Submitted: [May 14, 2012]
Source:[Jussi Haapola]
Company [Centre for Wireless Communications / University of Oulu]
Address [P.O. Box 4500, FI-90014 University of Oulu, Finland]
Voice: [+358 40 8363 018], FAX: [+358 8 553 2845], E-Mail: [jhaapola@ee.oulu.fi]
Re:[Progress and MAC work]
Abstract:[Update of Discussion slides for March 25 MAC subgroup conference call]
Purpose:[Refine and complete technical content of draft]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Priority Access in Beacon Enabled PAN – Spreading of Slots over Long Superframes
Problem, Discussion and Refinement

## Slide 3: Basic Scheme in a nutshell
Reserve time at the start of the Contention Access Period for priority access
Normal traffic waits until after this time to start slotted CSMA or Slotted Aloha
Thus priority traffic has less contention and has a chance to win over normal traffic every superframe

## Slide 4: How we specify it now
Reserve the first 2 time slots of the CAP in every superframe
Observations:
  Dedicating two entire time slots at the beginning of the CAP to Priority channel access may be overkill.
  As the superframe duration can become excessively long with high beacon orders and long symbol durations, it is better to have shorter priority channel access slots, but more often.
Slot duration = 2macSuperframeOrder × aBaseSlotDuration
aBaseSlotDuration = 60, macSuperframeOrder = 0 to 14
Superframe Duration = [960, …, 15.728.640) symbols.
Maximal MAC SAP symbol duration ~2.5 ms FSK, much longer for DSSS
-> Superframe duration can be 11 hours or more in DSSS case.
-> in case of DSME extension (and CAP reduction), BI can be 116 days.

## Slide 5: What we need
Having two aMinCAPLength (2*440 = 880 symbols) duration for every priority channel access allocation would be sufficient for contention and transaction of maximum of two priority message MPDU fragments.
Priority messages usually have a delay tolerance. In the case of energy distribution networks that tolerance is about 30 seconds.
As a safety margin, if we allocate at least one priority channel access every 15 seconds, many critical event scenarios can be served.

## Slide 6: The Allocation
SD = 2macSuperframeOrder × aBaseSlotDuration x 16 x MAC-SAP-symbol-rate [seconds]
(SD = superframe duration in seconds)
If superframe duration is less than 5 seconds
  Priority channel access allocation at least once every \floor(5/SD) superframes
  2 for SO = 0, SymDur 2.5 ms, 195 for SO = 0, SymDur 26.67 us.

## Slide 7: The Allocation (cont.)
If 5 s < SD ≤ 15 s
  Priority channel access allocation at least once every superframe.
  Priority channel access occupation of the SD
    FSK: Worst case 46 %, minimal case 0.16 %
If SD > 15 s
  Priority channel access allocation at least \ceil(SD/15) times per superframe
  Priority channel access occupation of the SD
    FSK: Worst case 29 % (SymDur 2.5 ms), minimal case 0.15 %

## Slide 8: The Allocation (cont.)
If SD or multi-superframe duration (temporal) > 15 s, there is a problem with CFP and DSME
  CFP precludes allocation of group access slots
    General priority channel access slots precluded
    Proposal: Allocate priority channel access slots evenly throughout the superframe, but omit the ones coinciding with CFP.
  DSME allows for CAP reduction
    If no CAP in most superframes, no priority channel access slots either.
    Proposal: if Priority channel access enabled and multi-superframe duration > 15 s, macCAPReductionFlag must be always set to FALSE.

## Slide 9: Summary of Changes
Priority Channel Access (PCA) MAC PIB attributes:
  macPriorityChannelAccess; Boolean; True/False, default False
    Priority channel access enabled or disabled
  aPCAAllocationSuperRate; Boolean; True/False; default True
    Priority channel access allocation rate.
    True indicates one or more allocations per superframe
    False indicates less than one allocation per superframe
  aPCAAllocationRate; Integer; Implementation Dependent; default 1
    If aPCAAllocationSuperRate is True number of allocations per superframe is the value of aPCAAllocationRate
    If aPCAAllocationSuperRate is False number of superframes per priority channel access allocation is aPCAAllocationRate
  macCriticalMessageDelayTolerance (mCMDT); Double; Implementation Dependent; default 15.0
    Minimum allocation rate, in seconds, for priority channel access allocations
Each priority channel access allocation is 880 symbol durations
When macPriorityChannelAccess is True and a PCA Allocation occurs the value of aMinCAPLength shall be 1320 or (2macSuperframeOrder × aBaseSlotDuration x 16) symbols, whichever is smaller.

## Slide 10: Summary of Changes (cont.)
When PCA allocation occurs, it occurs at least a number of times per superframe equal to:
where SDur = 2macSuperframeOrder × aBaseSlotDuration x 16 x MAC-SAP-symbol-rate in seconds and indicate floor and ceiling functions, respectively.
The first allocation occurs in the beginning of the superframe, immediately after the beacon.
Subsequent PCA allocations in the same superframe are evenly distributed, in time.
  Should a priority channel access allocation, apart from the first one, coincide with a CFP allocation the priority channel access allocation is omitted.
    With DSME, if macCAPReductionFlag is TRUE and multi-superframe duration > mCMDT, then macPriorityChannelAccess is must be set to FALSE.