## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Miscellaneous MAC fix suggestions
Date Submitted: [Sept 16, 2011]
Source:[Benjamin Rolfe]
Company [Blind Creek Associates]
Address []
Voice: [+1.408.395.7207], FAX: [None], E-Mail: [ben @ blindcreek.com]
Re:[Progress and MAC work]
Abstract:[more MAC fixes]
Purpose:[Refine and complete technical content of draft]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Additional MAC work
Simplified SF specification that can be transmited un-fragmented always
  Work in progress
Fragment Transaction Setup
  I-ACK Policy specification revision
  Fragment Size should be PHY dependent Parameter
Missing fragment link quality report

## Slide 3: I-ACK Policy - Now
Currently we define an I-ACK Interval
  Uses 5 bits to specify to I-ACK after each nth fragment
  Problems:
    Not clear in some re-transmission cases
    Not clear what to do at end in all case
    Not clear why we need this resolution
      (we started with “every one” or “at the end”)

## Slide 4: I-ACK Policy – Fix suggestions
I-ACK interval => I-ACK Policy field
  ACK every fragment cell
  ACK/NACK based on time – repeat last ACK if nothing heard within (configurable) timeout.
  ACK the ‘last outstanding’ fragment cell (i.e. highest number in retries)
  ACK after n good received
    Can overload MPDU size to be the number of fragments that defines “done”.

## Slide 5: Fragment Size should be PHY dependent Parameter
DSSS using Fixed PPDU size – fragment size already known
Finally have something to put in the PHY dependent field

## Slide 6: Missing fragment link quality report
Origionally had a link quality indication in the I-ACK as feedback
  Can be used (by upper layer, implementation specific) for link adjustment
Need 3-bit field in each fragment and I-ACK
Appropriate SAP change