## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Thoughts on Peer Discovery]
Date Submitted: [5 November 2012]
Source: [Seung-Hoon Park, Kyungkyu Kim, Chiwoo Lim, Hyunseok Ryu, Daegyun Kim and Won-il Roh] Company [Samsung Electronics]
Address [416, Maetan-3Dong, Yeongtong-Gu, Suwon-Si, Gyeonggi-Do, 443-742, Korea]
Voice:[+82-10-9349-9845], FAX: [+82-31-279-0813], E-Mail:[shannon.park@samsung.com]
Re: [.]
Abstract: [Clarification and necessity of peer discovery]
Purpose: [To discuss and clarify peer discovery]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Thoughts on Peer Discovery
November 5, 2012
Samsung

## Slide 3: 802.15.8 PAC PAR
5.2 Scope:
  This standard defines PHY and MAC mechanism for Wireless Personal Area Networks (WPAN) Peer Aware Communications (PAC) optimized for peer to peer and infrastructureless communications with fully distributed coordination. PAC features include: discovery for peer information without association, discovery signaling rate, typically 100 kbps, the number of devices in the discovery, scalable data transmission rates, typically 10 Mbps, group communications with simultaneous membership in multiple groups, typically up to 10, relative positioning, multihop relay, security, and operational in selected globally available unlicensed/licensed bands below 11 GHz capable of supporting these requirements.

## Slide 4: Background
Why “discovery for peer information without association”?
  Over-the-top proximity discovery
    Who are in 1 km range from me?
    Find the nearest coffee shop
    Refer 15-11-0744-01-wng0 : CLICK

## Slide 5: Trend
Peer-Awareness support
  FlashLinQ
    Qualcomm proprietary
  802.15.8 PAC (Peer-Aware Communications)
  802.11 SG PAD (Pre-Association Discovery)
    Related to works at Wi-Fi Alliance
    (Social Wi-Fi, Neighborhood Area Network, etc.)
  3GPP ProSe (Proximity Service)
    Under discussion on R12 study item

## Slide 6: PAC Biz. Positioning
To Wi-Fi
  More efficient system
    higher throughput & low power consumption
  Network scalability
    Wi-Fi can not guarantee a hundred of devices to be discovered or communicated.
To cellular (LTE)
  Unlicensed band
    The cellular-based peer discovery is limited due to each cellular band of an operator is different.
    PAC can expand network to diverse devices including consumer electronics, sensors, M2M, as well as cell-phones.

## Slide 7: Common Feature
Peer discovery
  Discovery of application-level information
    shannon.park@facebook
    sale.event@starbucks
  Prior to link establishment
    Get peer information without much burden
      User experience aspect and system aspect
      Over-the-top discovery is not well commercially succeeded
    Try to connect peer based on directly exposed and identified information

## Slide 8: Peer Discovery
Definition
  Discovery of peers in proximity
  Discovery of peers through peer identity information sent from PDs in proximity
  Peer identity information
    e.g. user(membership) ID + application ID
Why peer discovery?
  an essential function to support PAC distinctive use-cases such as social network or gaming

## Slide 9: Peer Discovery Procedure
User A
User B
Facebook App initialize user profile into Peer Identity (User ID, App ID)
Facebook initialize user profile into Peer Identity (User ID, App ID)
Setup for Peer Discovery procedure
Setup for Peer Discovery procedure
Peer Discovery procedure
(broadcasting and monitoring )
Peer Discovery procedure
(broadcasting and monitoring )
Match the same App ID
Notify matched Peer Identity from User B to Facebook App
User A decides to chat with User B and responds to Facebook App
Facebook App request
link establishment
Peering procedure
(Link establishment)
Peering procedure
(Link establishment)

## Slide 10: Device & Service Discovery (Conventional)
Device discovery
  Discovery of devices through scanning (beacon or probe response)
  Discovery of device ID (e.g. MAC address)
Service discovery
  Discovery of service protocol
    High layer protocol (UPnP, bonjour) is followed
  Discovery of service category
    SNS, game, broadcast, multicast, public safety, etc.

## Slide 11: Why Not Only Device ID for Peer Discovery?
Case 1
  A user may use multiple devices.
    Smart-phone, tablet, note-PC, etc.
Case 2
  A device may be shared by multiple users.
    Traveling agency borrows proximity guard devices to a traveling group. Members log in the guard application with their membership ID.
Case 3
  A user may use several membership IDs per different applications when using single device.

## Slide 12: Why Not Only Device ID for Peer Discovery?
Inconvenience
  User can not determine which device is what my friend is using at now.
  User can not know which device can provide service matched to my current interest.
    imagine hundreds of device ID being displayed!

## Slide 13: Why Not Only Device ID for Peer Discovery?
Link-to-stranger problem
  A device establishes link to unknown user’s device.
  Vulnerable to hacking (like Wi-Fi)
Relaying problem
  A device may deliver data from unknown user’s device.

## Slide 14: Why Not Only Service ID for Peer Discovery?
Categorization limitation
  User can not recognize multiple applications in the same service ID.
  A future application after 802.15.8 is published can not be recognized.

## Slide 15: Conclusion
PAC discovery
  Device/Service/Peer/Group discovery
  There is a proper combination of 4 discovery types depending on the requirement of use-case
    Device ID + Service ID
    Device ID + Peer ID
    Peer ID + Group ID
    Service ID + Peer ID
    Device ID + Group ID
    Other combinations
  PAC shall be designed flexibly to support different types of discoveries with the minimum overhead.