## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Status of P802.1Qbz and P802.11ak
Date Submitted: 15 Jan 2013
Source: Norman Finn Company: Cisco Systems
Address: 170 W. Tasman Dr., San José CA 95134 USA
Voice: +1.408.526.4495 , E-Mail: nfinn@cisco.com
Re: IGL2R
Abstract: Early progress on integrating 802.11 as a medium for bridges
Purpose: For information to L2R interest group – no action expected
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Status of P802.1Qbz and P802.11ak
Integrating 802.11 media into 802.1 bridging

## Slide 3: Disclaimer
This deck is not advocating a course of action for IEEE 802.15 L2R.
It is not claiming a position for Cisco Systems or IEEE 802.1.
This is a long-time advocate of 802.1 technologies presenting the capabilities of bridging.
If the shoe doesn’t fit, don’t hurt your feet!

## Slide 4: Both PARs have essentially the same scope
P802.1Qbz scope: This standard specifies protocols, procedures, and managed objects to allow IEEE 802.11 media to provide internal connections within bridged networks, as well as access to bridged networks.

## Slide 5: Reference diagram used frequently in pre-PAR discussions
The Access Points and their co-resident bridging functions become integrated AP bridges (AP/Bs).
Devices with non-AP station capability(ies) and wired connections become “non-AP station bridges” (S).
Of course, not all stations are bridges. (The diamonds are non-bridge non-AP stations.)
Each wireless connection appears, to the bridge functions of the system, to be a separate instance of the MAC service.
AP/B1
AP/B2
S
S
S
Some protocol, perhaps spanning tree or IS-IS, runs in every bridge as a distributed topology control algorithm.

## Slide 6: Possible diagram relevant to 802.15.4:
Coord/B 1
Coord/B 2
Coord/B 1
Coord/B 2
Coordinator/bridges connect to each other, to other media (wired, Wi-Fi, etc.), and to 802.15.4 stations.
This is not a constellation of twinkling stars; the coordinator/bridges shine steadily!

## Slide 7: 802.11 vs. 802.15.4 needs
802.11 needs Access Points that are also Bridges. A wireless connection from the AP to another AP or to a non-AP station is, for the purposes of data forwarding, just like a wired connection.
802.15.4 could probably utilize a similar capability in a coordinator. A coordinator/bridge would forward frames among non-802.15.4 links, connections to stations, or connections among coordinators.

## Slide 8: 802.11 vs. 802.15.4 needs
802.11 needs to bridges with some ports that are wired and some that are non-AP stations, attached to (perhaps different) Access Points.
802.15.4 may not need end stations that are wired bridges.

## Slide 9: 802.11 vs. 802.15.4 needs
802.11 needs to support wireless links among access points.
802.15.4 could probably use wireless links among coordinators.

## Slide 10: Wireless links are dynamic
Wireless links can come up and go down frequently.
Wireless links can vary in speed over short time frames.
Stations can go to sleep for many seconds to conserve power.
Wireless stations can be very mobile.
Bridges were invented to use wired connections that do none of the above.

## Slide 11: Are all problems solved by .1Qbz/.11ak? NO!
The problem of relay points that only wake up occasionally are not addressed by .1Qbz/.11ak. Relay points (bridges) are always available and always exchanging control messages (~ 1 Hz, 1k bytes per link, much more when the topology changes).

## Slide 12: Are all problems solved by .1Qbz/.11ak? NO!
You cannot have a bridge-to-bridge link flapping; frequent topology changes will keep the topology control protocols in turmoil, and disrupt connectivity throughout the network.
Heuristics must be applied—either a flapping link is always present (causing high packet loss and/or delay) or always absent (preventing connectivity). Pick your poison.
Similarly, the network cannot be updated as link speeds change.

## Slide 13: Are all problems solved by .1Qbz/.11ak? NO!
  At least, flapping links to end stations do not disrupt the network; connectivity is simply unreliable.
  All wireless links are represented to the network protocols as being very slow, so that the network will always prefer wired links, where connectivity permits.

## Slide 14: The problem that .1Qbz/.11ak can solve
IF the network is stable enough that heuristics can bring network topology changes down to a maximum of 1/min. (per network – not per link!) without causing excessive packet loss (due to claiming links are up when they’re not);
THEN a bridged network can work.

## Slide 15: If the goal is Big-I Internet connectivity:
If a bridge cannot deliver a frame within one second, it must discard it, because L3 and higher protocol timers start to kick in around this time frame.
This requirement can be relaxed at the very edge of the network, but a station connecting via standard protocols to the big-I Internet just can’t go to sleep for minutes at a time.
The capability of handling any protocol (via EtherType), not just a selected few, is required.

## Slide 16: 48-bit vs. 64-bit vs. short MAC addresses
The bridging standards only work on 48-bit MAC addresses.
There is no inherent reason for this, except lack of demand for a 64-bit version.
One can conceive of ways for a network to allocate 48-bit locally-administered MAC addresses to devices with 64-bit native addresses (or devices with no MAC address) to enable current bridging.
Any such plan would have problems when networks are concatenated.
This is an off-the-top-of-my-head idea, not a proposal for a work item.

## Slide 17: Bottom line
Bridging is a screwdriver.
If you need a box wrench, a screwdriver won’t help you.
But, if you can use a screwdriver, buy one at the hardware store—don’t mill your own from bar stock and discover, the hard way, why the blade is tapered.