## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed resolutions for CIDs 14, 15, 16, 17, 18, 19, 20, 21, and 22
Date Submitted: March, 2013
Source: Youngae Jeon, Sangjae Lee, and Sangsung Choi (ETRI), Soo-Young Chang (SYCA)
Contact: yajeon@etri.re.kr
Voice: +82 42 860 6497, E-Mail: yajeon@etri.re.kr
Re: [802.15 TG4m]
Abstract: This document provides proposed resolutions for CIDs 14, 15, 16, 17, 18, 19, 20, 21 and 22 of LB#87.
Purpose: To provides proposed resolutions for CIDs 14, 15, 16, 17, 18, 19, 20, 21 and 22 of LB#87
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comments for Sub-clauses 4.3.2 and 4.5.1.5
CID 14 (Editorial)
CID 15 (Editorial)
CID 16 (Editorial)
CID 17 (Technical)
CID 18 (Editorial)
CID 19 (Editorial)
CID 20 (Editorial)
CID 21 (Technical)
CID 22 (Editorial)

## Slide 3: CIDs 14, 15, and 20 (Editorial)
Comment
  CID 14: "...is a form of a cluster tree network…"
  CID 15: 1st instance and def. of TMCTP acronym occur above in 4.2.
  CID 20: Long sentence - would be easier to understand if 2 shorter sentences
Proposed Change
  CID 14: Redundant "a" - replace with "...is a form of cluster tree network…“
  CID 15: Remove acronym definition.
  CID 20: Replace with "A TVWS multichannel cluster tree PAN (TMCTP) is a form of cluster tree network where the SPC is the overall PAN coordinator providing synchronization services to other PAN coordinators in the cluster. The SPC also has access to the geo-location database (GDB) server to provide TVWS channel availability information to the other PAN coordinators.
Proposed Resolution
  (from) A TVWS multichannel cluster tree PAN (TMCTP) is a form of a cluster tree network where the SPC is the overall PAN coordinator providing synchronization services to other PAN coordinators in the cluster and has access to the geo-location database (GDB) server to provide TVWS channel availability information to the other PAN coordinators.
  (to) A TMCTP is a form of cluster tree network where the SPC is the overall PAN coordinator providing synchronization services to other PAN coordinators in the cluster. The SPC also has access to the geo-location database (GDB) server to provide TVWS channel availability information to the other PAN coordinators.
CS: A

## Slide 4: CIDs 16, 18, and 19 (Editorial) CID 17 (Technical)
Comment
  CID 16: "Each TMCTP-parent PAN coordinator including the SPC.." needs commas (otherwise the sense is "each parent PAN coordinator which contains the SPC")
  CID 17: "...during the active portion of the TMCTP-parent PAN coordinator…" doesn't make sense
  CID 18: "…beacon only period…"
  CID 19: 1st instance and def. of acronym BOP occur above in 4.2.
Proposed Change
  CID 16: Replace with "Each TMCTP-parent PAN coordinator, including the SPC,…“
  CID 17: Clarification required
  CID 18: Change to "…beacon-only period…" throughout document
  CID 19: Remove acronym definition.
Proposed Resolution
  (from) Each TMCTP-parent PAN coordinator including the SPC may communicate with its TMCTP-child PAN coordinators during the active portion of the TMCTP-parent PAN coordinator and receives beacon frames of TMCTP-child PAN coordinators on a dedicated channel during the dedicated beacon slots (DBS) assigned to them in the beacon only period (BOP), as shown with an asterisk (*) in Figure 2a.
  (to) Each TMCTP-parent PAN coordinator, including the SPC, may communicate with its TMCTP-child PAN coordinators during the CAP or CFP of the TMCTP-parent PAN coordinator and receives beacon frames of TMCTP-child PAN coordinators on a dedicated channel during the dedicated beacon slots (DBS) assigned to them in the BOP, as shown with an asterisk (*) in Figure 2a.
CS: A

## Slide 5: CID 21 (Technical)
Comment
  Not sure what the sentence means when it says "TMCTP increases the coverage area with controlled message latency and reduced collisions between coordinators" - does this mean that the use of TMCTP reduces message latency and collisions with the result that the coverage area is increased?
Proposed Change
  Clarification required
Proposed Resolution
  (from) The use of TMCTP increases the coverage area with controlled message latency and reduced collisions between coordinators, and allows independent operations of each cluster simultaneously.
  (to) In the TMCTP, collisions between clusters can be reduced because each cluster uses its own channel and coverage area is increased through the TMCTP parent-child structure.
CS: AP

## Slide 6: CID 22 (Editorial)
Comment
  1st instance and def. of TMCTP and BOP acronyms occur above in 4.2.
Proposed Change
  Remove acronym definitions.
Proposed Resolution
  (from) This standard allows the optional use of a superframe structure in a TVWS multichannel cluster tree PAN (TMCTP) that is extended by the addition of a beacon only period (BOP) to the active portion of the superframe.
  (to) This standard allows the optional use of a superframe structure in a TMCTP that is extended by the addition of a BOP to the active portion of the superframe.
CS: A