## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Preliminary NICT PHY Proposal (Part A) ]
Date Submitted: [ May 6th, 2013]
Source: [ Marco Hernandez, Huan-Bang Li, Igor Dotlić, Ryu Miura ]
Company: [ NICT ]
Address: [ 3-4 Hikarino-oka, Yokosuka, 239-0847, Japan ]
Voice:[+81 46-847-5439] Fax: [+81 46-847-5431] E-Mail:[]
Re: [In response to call for technical proposals to TG8]
Abstract: [ ]
Purpose: [Material for discussion in 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline
General PHY description
Physical Channels
Modulation Parameters
PHY Layer Procedures (Discovery)
PHY Measurements

## Slide 3: Common mode PHY Description

## Slide 4: Physical Channels
Frequency bands of operation are:
  Sub-GHz, 2.4 GHz and 5.7 GHz bands.
Those are selected because they do not require operation license. Hence, implementers only comply with local regulations. Moreover, those bands cover all PAC applications in terms of mobility and operational distance.

## Slide 5: Proposed frequency band allocations
Channelization of 5.7 GHz band
  Such frequency band ranges from 5.725 GHz to 5.875 GHz, which is divided into 14 channels of 10 MHz. By regulation, the maximum transmit power at the input antenna is 1 W. The central frequencies are given by
  fc = 5735 MHz + 10n for n = 0, 1, ..., 13
Channelization of 2.4 GHz band
  Such frequency band ranges from 2.4 GHz to 2.5 GHz, which is divided into 9 channels of 10 MHz. By regulation, the maximum transmit power at the input antenna is 1 W. The central frequencies are given by
  fc = 2410 MHz + 10n for n = 0, 1, ..., 8

## Slide 6: Physical Channels
Channelization of 920 MHz band (Japan)
  Such frequency band ranges from 915.9 MHz to 929.7 MHz. However, this frequency band is divided according to the maximum power at the input antenna and maximum bandwidth allowed by regulations.
  Option 1: frequency band ranges from 915.9 MHz to 928.1 MHz and divided into 61 basic channels of 200 kHz. The bandwidth rule tolerance: 200 n kHz, where n=1,2,3,4,5. Therefore, the maximum bandwidth is 1 MHz.
  Option 2: The frequency band ranges from 928.1 MHz to 929.7 MHz and divided by 16 basic channels of 100 kHz. The bandwidth tolerance: 100 n kHz, where n=1,2,3,4,5. Therefore, the maximum bandwidth is 500 kHz.

## Slide 7: Physical Channels
The basic channelization by regulations in Japan is summarized in the following table:
  1bandwidth rule tolerance: 200 n kHz, where n=1,2,3,4,5.
  2bandwidth rule tolerance: 100 n kHz, where n=1,2,3,4,5.

## Slide 8: Physical Channels
Proposed channelization

## Slide 9: DFT-S OFDM
Parameters
is constant and equal to 15 KHz.
Maximum FFT size M=1024
Sampling time
Timing based on a common clock at

## Slide 10: DFT-S OFDM
Frame structure (FDD)
One slot contains 7 DTF-S OFDM symbols.
Tslot=7680Ts=0.5 msec

## Slide 11: DFT-S OFDM
Cyclic prefix
73Ts=4.75 usec

## Slide 12: Resource Block
RB is a set of time-frequency slots enabling multiple access

## Slide 13: Resource Block
BW is obtained by concatenating RBs
(2 upper and lower subcarriers are empty)
DFT-S OFDM symbols

## Slide 14: Resource Block
Proposed bandwidths

## Slide 15: Reference signals
Considering a maximum speed of v=100 Km/h (27.78 m/s)
Doppler spread: fd=fc v/c
Min. sampling time to reconstruct the channel: Tc=1/2fd
Slot time Tslot=0.5 msec. Then, one reference symbol per slot is needed in the time domain to estimate the channel correctly.

## Slide 16: Reference signals
Considering 90%, 50% coherence bandwidth:
  where is the RMS delay spread.
Outdoor RMS delay spread is estimated as:
If then freq. selective fading and FDE is needed.
  We propose that the spacing between 2 reference symbols in frequency in a RB is 30 KHz to resolve frequency variations.
d=500m

## Slide 17: Aid for Coherent Detection, FDE, Synchronization, Random Access and Scheduling
Preambles or beacons and reference signals (RSs) are formed with Zadoff-Chu (ZC) sequences of length N.
  Constant-amplitude zero-correlation (CAZAC) sequences
where WN is a primitive nth root of unity, r is a relative prime to N, sequence index k = 0, 1, ...,N-1and q is any integer.

## Slide 18: ZC sequences
ZC sequences have constant amplitude and so its N-point DFT.
  This limits the PAPR and simplifies implementation as only phases have to be generated and stored, besides of bypassing the FFT at transmitter for DFT-S OFDM.
ZC sequences have ideal cyclic autocorrelation, i.e., the correlation with its shifted version is a delta function
  Thus, a [large] set of orthogonal preambles or reference signals is possible to generate.

## Slide 19: Common mode Discovery
Peer aware communication networks are aimed to operate without central control:
  Hence, transmission for initial discovery or re-discovery among peers is asynchronous.
Thus, a preamble sequence is required for time and frame synchronization at start up or when re-synchronization is required for discovery or communication.

## Slide 20: Common mode Discovery
We propose to use a discovery preamble (DP) based on a ZC sequence and a discovery resource block (DRB) from a modified DTF-S OFDM signal.
  The DP and DRB formed the Discovery Signal (DS).
Moreover, we propose to use one channel (from the proposed channelization for sub-GHz, 2.4 GHz and 5.7 GHz bands) for only discovery of devices.
  PAC devices can either transmit or receive the DS in this unique channel asynchronously.
Such unique channel for discovery is named Shared Discovery Channel (SDCH).

## Slide 21: Common mode Discovery
The discovery signal (DS) sent over a discovery shared channel (DSCH):
The DS consists of a preamble sequence plus a DRB formed by Nfs frequency slots and Nts time slots.
Once synchronized, a receiver knows the location of the discovery resource block (DRS) to scan for possible peers or to pick time-frequency slots to transmit its DS.

## Slide 22: Proposed ZC sequence for timing synchronization
The proposed ZC sequence for initial synchronization during discovery (or communication mode) is a ZC sequence with the following parameters:
  Sequence length N = 63, relative prime r = 62 and q = 0.

## Slide 23: Proposed ZC sequence for timing synchronization
Such ZC sequence is mapped onto 62 sub-carriers
  The first subcarrier and the DC subcarrier are empty.

## Slide 24: DRB structure
Contiguous subcarriers are orthogonal.
The DS is transmitted with a predefined duty-cycle (see NICT MAC pre-proposal).

## Slide 25: DRB structure
From upper layers, terminals pick time-frequency slots in the DRB to transmit the DS.
A set of 24 symbols are transmitted per time slot:
  such frame contains information about a given peer (peer ID, service ID, application ID, etc.) and which channel is used for association (different from the SDCH).
The number of frequency slots Nfs =1024 (IFFT size) and the number of time slots Nts is chosen as 20.
Consequently, the DRB can support up to NfsxNts=20,480 users for discovery in a Group.

## Slide 26: Discovery algorithm parameters
Devices are in three possible states:
  RDM –receiving discovery mode,
  TDM –transmitting discovery mode,
  Sleep -idle.
  Also, devices are equipped with clear channel assessment (CCA).

## Slide 27: Discovery Algorithm
  1) At start up or after idle or after command, a device enters into receiving discovery mode (RDM) and listens for a DS.
    Synchronization subsystem detects the preamble (and hence the position of the DRB in time) and detection subsystem scans the DRB for DRB usage and detection of peer ID, service ID, etc. Go to Sleep mode.
  2) After command, a device enters into transmitting discovery mode (TDM)
    Device chooses a free time-frequency slot to transmit its DS over the next DRB transmission. Go to Sleep mode.
  Of course, there are intermediate steps like time-out for DRB scanning, miss detection, etc. Here, we present the core algorithm only.

## Slide 28: Discovery-Association
Notice that the first terminal to start a discovery session, will set the discovery signal duty cycling for other terminals to follow, no matter if it stops transmitting afterwards. There is not central control.
Also, such terminal will set the channel for association (communication link) named Association Channel (ACH). Although, it may change afterwards.
For association, intended devices that want to establish a communication link, request that through a random access preamble transmitted in the ACH.

## Slide 29: Association Preambles
The random access association preambles are named Random Access Preambles (RAPs).
Such RAPs are formed with ZC sequences as well.
Hence, a pool of orthogonal RAPs is formed
  in order to reduce interference from competing terminals for random access.
A unique RAP is assigned to every device in a Group.
Such unique RAP is used for fine synchronization and control messages (how a communication link is granted).

## Slide 30: RAP structure
The RAP signal is illustrated as
  GI is guard interval
  In MAC lingo, it is known as beacon.

## Slide 31: Random access procedure
Once initial synchronization and decoding of discovery RB are achieved by Terminal 2 over Terminal 1:
  Terminal 2 requests association by a random access procedure based on an orthogonal RAP.

## Slide 32: Random access procedure
The process is initiated and control by upper layers.
1) Terminal 2 sends RAP over the ACH.
  It is randomly selected from a pool of orthogonal ZC sequences.
  It contains finer frequency granularity for Terminal 1 to acquire fine time and frequency synchronization of Terminal 2, plus information about the resources needed to transmit in 3).

## Slide 33: Random access procedure
2) Terminal 1 replies with RA response message.
  It contains timing information (round-trip delay), RAP-ID, RB grant to transmit in 3), Group identifier, etc.

## Slide 34: Random access procedure
3) Scheduling request
  It contains scheduling request information for transmission.
  If this message is successfully detected in Terminal 1, still contention remains unsolved for other terminals. A quick resolution is needed.

## Slide 35: Random access procedure
4) Contention resolution
  Terminal 1 echoes Terminal 2 ID contained in 3)
  Terminal 2 detects its ID and sends ACK (RA terminated) a communication link is scheduled and established.
  Terminal 2 detects another ID (RA terminated, starts a new one)
  Terminal 2 fails to detect ID (RA terminated, starts a new one)

## Slide 36: Last but not least
An optional and very low power PHY based on 2FSK modulation is contemplated for the sub-GHz band.