## Slide 1
Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks(WPANs)
Submission Title: Comment for FEC method NRNSC
Date Submitted: May 2013
Source: Matthew Gillmore (ITRON)
Contact: matthew.gillmore@itron.com
Voice: +1.517.745.7350
Re: LB90 Comment on FEC
Abstract:
Purpose: Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Doc: IEEE 15-13-0288-02-004m

## Slide 2: FSK FEC in 4M
Current draft, Section 20.1.2.4, supports one optional FEC method from 802.15.4k
This submission proposes to add the optional NRNSC FEC method from 802.15.4g, as follows
  Replace Section 20.1.2.4 line 49
    “The NRNSC FEC scheme shall be according to sub-clause 18.1.2.4 or the NRNSC FEC in sub-clause 19.1.2.4. The use of the FEC scheme shall be controlled by the PIB attribute phyTVWSFSKFECScheme, as defined in 9.3.
  Add a new PIB attribute phyTVWSFSKFECScheme in clause 9.3, Table 71, with the following description:
      “A value of zero indicates that the NRNSC FEC scheme in 18.1.2.4 is employed, with an interleaving scheme as define in 18.1.2.5. A value of one indicates that the NRNSC FEC scheme in 19.1.2.4 is employed, with an interleaving scheme as define in 19.1.2.5.”
      “The attribute is only valid for the TVWS-FSK PHY”.
Doc: IEEE 15-13-0288-02-004m

## Slide 3: Technical Justification
FEC as mentioned in section 18.1.2.4 is less complex than method suggested in section 19.2.2.4
  Constraint length K=4 versus K=7
    Lower power consumption
    Lower implementation complexity
These schemes are complementary
  Scheme defined in 19.2.2.4 has better range at the expense of throughput
  Scheme defined in 18.2.2.4 has better throughput at the expense of communication range
Systems designers can pick the one that better fits their application requirements
Millions of devices will support the method from 18.1.2.4 by the time 15.4m is approved
Doc: IEEE 15-13-0288-02-004m