## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: ETRI Technical PHY proposal for IEEE 802.15 TG8 PAC Standard
Date Submitted: July xx, 2013
Source: Kapseok Chang (ETRI), Byung-Jae Kwak (ETRI), Moon-Sik Lee (ETRI), and Sunggeun Jin
(Daegu University)
Company: ETRI and Daegu University
Address: 218 Gajeong-ro, Yuseong-gu, Daejeon, 305-700, Korea
Voice: +82 42 860 1639 Fax: E-Mail: {kschang, bjkwak, moonsiklee}@etri.re.kr, sgjin@daegu.ac.kr
Re: TG8 Call for Proposal (CFP: IEEE P802.15-13-0069-05-0008)
Abstract: This document presents technical proposals for IEEE 802.15. TG8 PAC standard.
Purpose: Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline
PHY Frame Formats
Preamble Design
  Requirements
  Basic STF Sequence Design
  Proposed Preamble Structure
Text Proposal

## Slide 3: PHY Frame Format (1/3)
The transmitted RF signal is generated by modulating the baseband signal.
The baseband signal is composed of multifarious fields. The fields and the timing boundaries between them, that is, general PHY frame format, are composed as following:
  Preamble field consists of short training field (STF) and long training field (LTF). It is used for automatic gain control (AGC), packet detection, timing/frequency synchronization, channel estimation, and collision detection.
  Optional Beam Jitter field is used for SSF (Self Spatial Filtering)

## Slide 4: PHY Frame Format (2/3)
Discovery in visible range (1/2)
  Frame formats for Self Spatial Filtering (SSF) [8], [10]
  SSF request frame
    A broadcast or multi-cast frame
    The MPDU consists of MAC header, payload, and FCS. The MAC header indicates this is a SSF request frame, and the payload includes IE that contains the threshold for the correlation level. The threshold is used by other PDs to decide whether they shall send a response frame or not.
    Beam Jitter field includes a pre-defined beam-jittered sequence. The beam-jittered sequence is used to calculate the correlation level, which is used in Self Spatial Filtering [1], [8], [10].

## Slide 5: PHY Frame Format (3/3)
Discovery in visible range (2/2)
  SSF response frame
    A unicast frame
    A SSF Response frame is transmitted by a PD which received a SSF request frame. Upon receiving an SSF request frame, a PD calculates the correlation level and transmits SSF response if the correlation level exceeds the threshold.
    The MPDU consists of MAC header, payload, and FCS. The MAC header indicates this is an SSF response frame, and the payload includes IE that contains the calculated correlation level.

## Slide 6: Preamble Design (1/12) : Requirements
R1: Robustness against Frequency offset (FO)
  Symbol timing synchronization (STS) shall be acquired in case of start up, discovery, or communication in the absence of knowledge about initial carrier FO in the received signal.
  The STS performance is very sensitive to FO.
R2: Good autocorrelation property
  It is pivotal to minimize timing error.
R3: Lower complexity of preamble detector
R4: Low peak to average power ratio (PAPR)
R5: Implicit indication on which transmission mode among SC and OFDM is employed to support multi-mode coexistence

## Slide 7: Preamble Design (2/12) : Basic STF Sequence Design
Focus on design
  Requirements R1 (FO), R2 (STS) should be fully satisfied.
  Regarding R3 (receiver complexity), it is at least identical to the detector complexity of the base Zadoff-Chu (ZC) sequence.
  Regarding R4 (PAPR), it is at least comparable to that of the general ZC sequence.
Key ideas
  K1: Combination of base ZC sequence and its modified sequence in frequency domain
  K2: Combination of FO-immune sequence and excellent correlation sequence in time domain

## Slide 8: Preamble Design (3/12) : Basic STF Sequence Design
Base ZC sequence bu,P[]
  Length-P ZC sequence that has the zero autocorrelation property [2], [11]
      where u is the root index of base ZC sequence, odd P is the sequence
      length, and the sequence element index m = 0, 1, ..., P-1.
    It has been adopted in the 3GPP Long-Term Evolution (LTE) standard [11].
    The optimal P for PAC is FFS.

## Slide 9: Preamble Design (4/12) : Basic STF Sequence Design
K1-based first modified ZC (MZC1) sequence
  A distribution of the based ZC sequence and its negative [3]
  At odd m, Length-N MZC1 sequence Su,N[m]
  At even m, Su,N[m]

## Slide 10: Preamble Design (5/12) : Basic STF Sequence Design
K1-based second MZC (MZC2) sequence
  A concatenation of the base ZC sequence [2] and its complex conjugate [4]
  Length-N MZC2 sequence Su,N[m]

## Slide 11: Preamble Design (6/12) : Basic STF Sequence Design
K2-based Gold Sine Wave (GSW) sequence (1/2)
  So as to achieve robustness against FO
    Half sine wave window function sin(n/N) is introduced.
  So as to achieve good autocorrelation
    Gold sequence Wu(n) is introduced.
    For low-complexity detector, binary sequence is preferable.
    It is noted that a length-P pseudo-noise sequence can be used as Wu(n). Thus, exact sequence is FFS.
  GSW sequence is a multiplication of half sine wave by gold sequence [5].

## Slide 12: Preamble Design (7/12) : Basic STF Sequence Design
K2-based Gold Sine Wave (GSW) sequence (2/2)
  Length-N GSW sequence su,N[n]
    G1 and G2 are m-sequences corresponding to the generator polynomials x5+1 and x5+x4+x+1, respectively.
    [z]N returns the modulo-N value of the integer z.
    u is the index of GSW sequence.
    2(N-2)/N is applied to maintain the same average-power as MZCs.

## Slide 13: Preamble Design (8/12) : Basic STF Sequence Design
PAPR comparison
  In case of N=64 with P=31 (MZC1, MZC2, GSW) or P=63 (Base ZC)
  GSW outperforms other sequences
  Base ZC provides the highest variance of PAPR, and its max PAPR is much more higher than that of random data field, which indicates that the careful selection of sequence index is required.
  On the other hand, MZCs are acceptable since their max PAPR is lower over the random data field.
PAPR | Base ZC | MZC1 | MZC2 | GSW
Average [dB] | 5.8011 | 5.9403 | 6.6069 | 3
Min [dB] | 1.8080 | 5.0235 | 4.3880 | 3
Max [dB] | 13.2950 | 7.0014 | 9.3670 | 3
Variance [dB] | 5.9027 | 0.4969 | 1.7983 | 0

## Slide 14: Preamble Design (9/12) : Basic STF Sequence Design
Detector complexity comparison
  The time-domain MZC1 is a complex sequence, so that the computational complexity of MZC1 is identical to that of base ZC.
  The time-domain MZC2 and GSW are not complex but real sequences, so that the computational complexities can be reduced by a factor of ½ over that of base ZC if cross-correlation based detectors [3]-[5] are employed.
  If auto-correlation based detector [6] is employed, there is no complexity difference.

## Slide 15: Preamble Design (10/12) : Basic STF Sequence Design
Evaluation parameter and condition
  Parameter (compliant to LTE [11] and PAC-recommended channel model)
    Carrier frequency of 2 GHz, system bandwidth of 1.25 MHz (i.e. N=64, P=31 or 63), subcarrier spacing of 15 kHz, FFT/IFFT size of 64, CP duration of 10, a pair of source and destination stations, no transmit diversity, two branch equal gain combining received diversity, channel model of TU-6 [7] with mobile velocity of 3 km/h, the root indices of MZCs and GSW are set to be 1 [3], [4] and 5 [5], respectively, and the root index of the base ZC sequence is set to be 25 from among 25, 29, and 34.
  Condition
    When evaluating the detection error rate (DER) of STS, a correct detection is declared if the detected sample timing is within half the CP duration.
    The transmitted power for the STF signal is the same as that of the data signals.
    The detection scheme for STS is based on cross-correlation for full-length correlation [3]-[5].

## Slide 16: Preamble Design (11/12) : Basic STF Sequence Design
Comparison of robustness to FO
Effective mean correlation output (EMCO) vs. FO with static TU6 channel [7] and no noise
EMCO means the sum of mean correlation outputs at sample timing offsets within half the CP duration.
 is the FO normalized to a subcarrier spacing of the effective OFDM symbol.
  For example, =1 means that one subcarrier spacing is shifted.
All proposed sequences are robust to FO.
EMCO vs. normalized FO

## Slide 17: Preamble Design (12/12) : Basic STF Sequence Design
DER performance
DER vs. SNR per received antenna with =0 and =2/3 in the TU-6 channel with 3 km/h
There are no significant DER performance differences among STS sequences for =0.
All of the proposed sequences provide high STS accuracies even for =2/3.
The ZC used in LTE shows very poor DER performance when =2/3
DER vs. SNR

## Slide 18: Proposed Preamble Structure I (1/3)
Time-domain structure
  The 1st symbol of STF is used for automatic gain control (AGC).
  The 2nd symbol of STF is used for packet detection, initial time/frequency synchronization, and implicit transmission-mode indication by positive/negative number of the correlator output.
    E.g., if the correlator output is positive, it indicates OFDM. Otherwise, it indicates SC.

## Slide 19: Proposed Preamble Structure I (2/3)
Time-domain structure
  The first symbol of the LTF is used for refined time/frequency synchronization and channel estimation.
  We propose MZC1, MZC2, or GSW is used in STF. (TBD)
  We propose MZC1, MZC2, GSW, or Base ZC is used in the 1st symbol of LTF. (TBD)
  Auto-correlation based detection technique [6] can be used to reduce implementation complexity.

## Slide 20: Proposed Preamble Structure I (3/3)
Collision Detection
  The second symbol of the LTE is used for collision detection (CD) [9].
  CD algorithm description
    A PD who wants to transmit data using Random Access selects two random sub-carriers, one from the upper half and another from the lower half of the sub-carriers.
    The PD transmits a busy tone in the selected sub-carriers of the second symbol of LTF.
    When a receiver sees more than one tone in either of the two sub-carrier blocks.
Prob{collision detection failure} = 1/P2

## Slide 21: Proposed Preamble Structure II (1/2)
Time-domain structure
  The structure of STF is the same as Proposed Preamble Structure I. We propose either of MZC1 or MZC2 is used for STF.
  The LTF consists of a long CP followed by two periodic sequence. The LTF is used for refined time/frequency synchronization and channel estimation. We propose Base ZC is used for LTF.
  Auto-correlation based detection technique [6] can be used to reduce implementation complexity.
  The STF and LTF are also used for collision detection.

## Slide 22: Proposed Preamble Structure II (2/2)
Collision Detection
  A PD selects random root ZC sequences to generate STF and LTF.
  Assuming # sub-carriers = 64, this gives ≈16 choices for STF, and ≈ 64 choices for LTF, resulting in ≈ 1024 possible combinations.
  On the receiver side, the collision detection procedure is shown in the below figure.

## Slide 23: Discussion on Preamble Structure
Proposed preamble structure I
  Simple collision detection
Proposed preamble structure II
  More reliable collision detection
  Superior channel estimation
  Superior timing/frequency sync
The preferred preamble structure is “II”.
The preamble sequences and the preamble structures must be evaluated in terms of the requirements R1 ~ R5.
Further study with evaluation results will be presented at the next meeting.

## Slide 24: Text Proposal

## Slide 25: References
ETRI, “Technical pre-proposal for IEEE 802.15 TG8 PAC standard,” IEEE 802.15-13-0271-01-0008, May 2013.
NICT, “Preliminary NICT PHY proposal (Part A),” IEEE 802.15-13-0272-00-0008, May 2013.
K. Chang and Y. Han, “Robust replica correlation-based symbol synchronisation in OFDM systems,” Electronics Letters, vol. 44, no. 17, pp. 1024-1025, Aug. 2008.
K. Chang, P. Ho, and Y. Choi, “Signal design for reduced complexity and accurate cell search/synchronization in OFDM-based cellular systems,” IEEE Transactions on Vehicular Technology, vol. 61, no. 9, pp. 4170-4175, Nov. 2012.
K. Chang, S.C. Bang, and H. Kim, “Replica correlation-based synchronization with low complexity and frequency-offset immunity,” ETRI Journal, Oct. 2013, to be appeared.
T.M. Schmidle and D.C. Cox, “Robust frequency and timing synchronization for OFDM,” IEEE Transactions on Communications, vol. 45, no. 12, pp. 1613-1621, Dec. 1997.
3GPP TR25.943 v8.0.0, Technical Specification Group Radio Access Networks: Deployment Aspects, Dec. 2008.
ETRI, “Response to the Call for Applications: Look-and-Link Communication,” IEEE 802-12-0227-01-0008, May 2012.
ETRI, “A Feasible and Efficient Channel Access Scheme for PAC Networks,” IEEE 802.15-13-0374-0x-0008, July 2013.
ETRI, “Self Spatial Filtering Scheme for PAC,” IEEE 802.15-13-0375-0x-0008, July 2013.
TS36.211 v10.0.0, Physical channels and modulation (Release 10), 3GPP TSG RAN1, pp. 92-96, Dec. 2010.