## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Suggestion of synchronization categorization
Date Submitted: September 10th, 2013
Source: Jinyoung Chun, Suhwook Kim, Han Gyu Cho (LG Electronics)
Address: LG R&D Complex 533, Hogye-1dong, Dongan-gu, Anyang-shi, Kyungki-do, Korea
Voice: +82-31-450-1901, FAX: +82-31-450-4049, E-Mail: jiny.chun@lge.com
Re:
Abstract:
Purpose: Proposal for discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary of email discussion
From Shannon
: categorization based on network synchronization
  Centralized approach (timing reference is decided by signal from single PD)
    NICT : Initiator PD sends broadcast signal and Joiner PDs refers it (Note. NICT named the idea as "Distributed temporary group synchronization".)
    ETRI (SS Joo) : Master-clock capable PD transmits peer network synchronization frame and other PDs refers it. (C. Arguable assumption: master-clock refers from out-of-band.)
    InterDigital : Super-beacon, common beacon or peer beacon is refered for synchronization. (C. Determination procedure of super-VL or VL is missing.)
  Distributed approach (timing reference is decided by signals from multiple PDs)
    Samsung : Each PD decides timing by adjusting oscillator phase corresponding to the reception of sync-signals from multiple PDs
    ETRI (SC Chang) : Pulse-based PHY-level synchronization.
  No network synchronization (asynchronous)
    LG : Only link-level synchronization during peering is presented for slot timing basis. However link-to-link synchronization is required for the proposed slot hopping.

## Slide 3: Summary of email discussion
From Suhwook
: categorization based on synchronization timing
  Pre-sync system: Sync first, and then discovery/peering
    Samsung
    ETRI (SC Chang)
  Post-sync system: Discovery/peering first, and then sync
    NICT
    ETRI (SS Joo, BJ Kwak, WC Jeong)
    InterDigital
    LG
  Note that UWB (NICT, Decawave) and Relay, Groupcast (CAU) have different domain.
: Comment from Marco
  Samsung’s proposal is contention-free access. So that a global synchronization mechanism is required. NICT’s proposal is a combination of contention and contention-free access, but it does not require a global synchronization mechanism. Some people called it asynchronous access.
: Response from Suhwook
  What I want to mean is MAC level sync. In pre-sync type, every PD should sync its phase first.(ex. Discovery, Peering, Data..)However, in post-sync type, a PD has each phase first, and they sync the phase after discovery. Multiple access also can be good criteria. But many proposals have both of contention-free and contention access.

## Slide 4: The first suggestion
  I think high-level categorization is a good start point of technical discussion.
  Based on the categorizations from Shannon and Suhwook, we can categorize to two groups: one is Samsung, ETRI (SC Chang) and other one is NICT, ETRI (SS Joo, BJ Kwak, WC Jeong), InterDigital, LG(excluded in Shannon’s).
  If everyone agreed the categorization of the two groups, we can make descriptions whatever the categorization names are called as below.
High-level categorization about synchronization
  Group1
    Companies: Samsung, ETRI (SC Chang)
    Description
      TBD
  Group2
    Companies: NICT, ETRI (SS Joo, BJ Kwak, WC Jeong), InterDigital, LG
    Description
      TBD

## Slide 5: The first suggestion
  If we agree the categorization in slide 4, then we suggest the following detailed description. Please give us comments or new description.
High-level categorization about synchronization
  Group1 (named such as PHY sync, Pre-sync, Distributed sync, Sync)
    Companies: Samsung, ETRI (SC Chang)
    Description
      It’s a fine sync based on the physical sequence for all neighbor PDs. PDs know Tx/Rx timing without contention after the sync.
      Timing reference is decided by signals from multiple PDs.
      There is no MAC level sync based on MAC message.
  Group2 (named such as MAC sync, Post-sync, Centralized sync, Async)
    Companies: NICT, ETRI (SS Joo, BJ Kwak, WC Jeong), InterDigital, LG
    Description
      It’s a MAC-level sync based on MAC message.
        The message is Beacon by NICT, InterDigital and discovery/peering message by LG.
      It’s for knowing PD’s phase configuration. PDs know the period for Tx/Rx with contention.
        The phase is the period of each TB, CFP, CAP by NICT, the period of each Beacons by InterDigital, and the period of discovery, peering, communication by LG.
      Timing reference is decided by signal from single PD. The single PD is an initiator PD by NICT, InterDigital and the discovered PD by LG.

## Slide 6: The second suggestion
  After 2nd conference call, I revised my categorization.
Categorization of synchronization
  Synchronization before discovery
    Centralized synchronization
      Timing reference is decided by signal from single PD.
      Companies: InterDigital, NICT(Marco, Huan-bang) *I’m not sure about NICT.
    Distributed synchronization
      Timing reference is decided by signals from multiple PDs.
      Companies: Samsung, ETRI (SC Chang)
  Discovery without synchronization
    There is no time reference before discovery.
    Companies: LG, ETRI (SS Joo, BJ Kwak, WC Jeong)
   There are 3 high-level categorization of synchronization. The sync mechanism might impact on the design of PAC procedures such as discovery, peering and communication. Therefore we also can make some categorization of other procedures related to the categorization.