## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Cross-Layer Context Management]
Date Submitted: [12 March 2014]
Source: [Chonggang Wang, Qing Li, Hongkun Li, Zhuo Chen, Tao Han]
Company [InterDigital Communications Corporation]
Address [781 Third Avenue, King of Prussia, PA 19406-1409, USA]
Voice:[610-878-5695], FAX: [610-878-7885], E-Mail:[Qing.Li@InterDigital.com]
Re: [ Call for Preliminary Contributions]
Abstract: [This document presents cross-layer context management for 802.15.8 TG]
Purpose: [To discuss technical feasibility of the proposed cross-layer context management for 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Content
IEEE 802.15.8 Reference Model
Context Management Use Case
Proposed Cross-Layer Context Management Architecture
Proposed Cross-Layer Context Management Interaction
Primitives for HLCM SAP
Primitives for PLCM SAP

## Slide 3: IEEE 802.15.8 Reference Model
PAC Framework Document [1]

## Slide 4: Context Management Use Case
Intra-PD Context Management
  The higher layer requests the MAC layer to discover a particular PD (e.g. a friend) in proximity.
  The MAC layer indicates to the higher layer of new PDs occurring in proximity.
Inter-PD Context Management
  A PD indicates its service/application/user context to a group of other PDs in proximity.

## Slide 5: Cross-Layer Context Management Architecture
Context Manager
(CM)
as an
MAC
Function
HLCM SAP: High Layer to Context Manager SAP
PLCM SAP: PHY Layer to Context Manager SAP

## Slide 6: Cross-Layer Context Management Interactions
Interactions | Requester | Receiver | HLCM SAP | PLCM SAP
Context Retrieval | High Layer | CM | √ | 
Context Subscription | High Layer | CM | √ | 
Context Notification | CM | Higher Layer | √ | 
Context Report | PHY or High Layer | CM |  | √
Table 1. Examples of Context Management Interactions

## Slide 7: Primitives for HLCM SAP
High Layer Retrieves Context – An Example

## Slide 8: Primitives for PLCM SAP
PHY Layer Reports Context – An Example

## Slide 9: Conclusion
IEEE 802.15.8 Reference Model
  Context Management (CM), i.e. PD Management Entity
Context Management Use Case
  Inter-PD and intra-PD context exchange
Proposed Cross-Layer Context Management Architecture
  Context Manager as an MAC function
Proposed Cross-Layer Context Management Interaction
  Primitives between high layer and CM, primitives between PHY layer and CM
Primitives for HLCM SAP
  Context retrieval
Primitives for PLCM SAP
  Context report

## Slide 10: References
[1] PAC Framework Document (doc.: IEEE 802.15-14-0085-01-0008)