## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Application of digital signal processing in high speed OCC system]
Date Submitted: [March, 2014]
Source: [Nan Chi]
[Fudan University]
Address [Shanghai, China]
Voice:[86-021-65642983], FAX: [86-021-65642983], E-Mail:[nanchi@fudan.edu.cn]
Re: []
Abstract: [Application of digital signal processing in high speed OCC system]
Purpose: [Contribution to IEEE 802.15.SG7a OCC]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15-14- 0166 -00-007a
Notes: doc.: IEEE 802.15-09-0117-00-0007
<month year>

## Slide 2
Background & Research Motivation
VLC
Light Wave
Radio Wave
LED lighting in the global marketing
Visible light communication utilizing available and unregulated spectrum
Wireless information transmission via light, simultaneously supporting illumination and communication
electromagnetic interference free
Complementary to radio for wireless access
doc.: IEEE 802.15-14- 0166 -00-007a

## Slide 3
 | White channel |  |  | White channel + equalization |  |  | Blue channel |  | 
Number of Channels | 4 | 16 | 36 | 4 | 16 | 36 | 4 | 16 | 36
Bit rate(Mbit/s) | 48 | 192 | 432 | 120 | 480 | 1080 | 160 | 640 | 1440
Diameter of Lens (cm) | 0.2 | 0.44 | 0.71 | 0.44 | 0.8 | 1.38 | 1.6 | 3.6 | 7.14
Size of Detector (cm) | 0.74 x0.74 | 1.68 x1.68 | 3.05 x3.05 | 1.65 x1.65 | 3.08 x3.08 | 5.91 x5.91 | 6.0 x6.0 | 13.7 x13.7 | 31.4 x31.4
Simulation Results
——adopting MIMO techniques
doc.: IEEE 802.15-14- 0166 -00-007a

## Slide 4
    Schematic of VLC System
Visible light transmission
LED
coding
modulation
Pre-equalization
O to E
Tx Module
LED Modulation
Rx Module
AD
AD
Demodulator
Decoder
Baseband
Q
I
Phase
Signal processing
doc.: IEEE 802.15-14- 0166 -00-007a

## Slide 5: 32-order FIR Filter for different modulation formats
QPSK
8QAM
16QAM
64QAM
128QAM
512QAM
doc.: IEEE 802.15-14- 0166 -00-007a

## Slide 6: Channel equalization
Pre-equalization
  Obtain the channel knowledge(H) at the RF domain
  Make pre-equalization Tx*1/H at the baseband
Post-equalization
Pilot-aided phase estimation
LS estimator according to the pilot information
Original spectrum
Received spectrum
doc.: IEEE 802.15-14- 0166 -00-007a

## Slide 7
Downlink: Green and Red, the BER is within the FEC limit at a distance of 66cm Uplink: P-LED, the BER performance almost remained the same at the bi-directional envionrenment.
Bi-directional transmission based on WDM
doc.: IEEE 802.15-14- 0166 -00-007a

## Slide 8
Uplink: RGB LED (Blue)
Downlink: RGB LED (red green blue)
Data rate: 875-Mb/s downstream and 125-Mb/s upstream transmission
Bi-directional transmission based on WDM and SCM
doc.: IEEE 802.15-14- 0166 -00-007a

## Slide 9: Conclusions
Blue phosphor LED maximum bitrate up to 225Mb/s
RGB LED maximum bitrate up to1Gb/s
Both pre-equalization and post equalization are applied
Challenge on nonlinearity at Tx and Rx to further increase the transmission speed
doc.: IEEE 802.15-14- 0166 -00-007a