Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Overview of 802.15.3
Date Submitted: March 2014
Source:	James Gilb
Contact: James Gilb
E-Mail: last name at ieee dot org
Re:	IEEE Std 802.15.3-2003
Abstract: Overview of the 802.15.3 standard
Purpose: 802.15.3d PAR
Notice:	This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release:	The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide
Slide
[Speaker Notes: Mar 18, 2014 Page]

---
TG4i recirculation
Introduction

---
History
- Initial project started March 2000
  - New MAC/PHY combination
  - Completed 2003
- First amendment failed to complete
  - UWB PHY, but unable to get 75% approval
- Second amendment to fix MAC issues
- Third amendment added mmWave alternative PHY
  - Supports beam forming, aggregation

---
MAC history
- Original version for traditional PHY
  - “Omni-directional” coverage
- Updates to fix problems and add some new features
- Some modifications made to support the mmWave PHY
  - Structured to support particular beam forming protocol
  - 3 different aggregation formats

---
Glossary
- DEV – a device that implements 802.15.3
- Piconet – network of DEVs that communicate wirelessly
- PNC – piconet coordinator
  - Controls admission to piconet
  - Sets timing by sending beacons
- Superframe
  - Basic timing in the piconet.
  - Fixed duration, but can be changed with warning.
- Beacon
  - Signals starts of the superframe
  - Describes the structure of the superframe.

---
Glossary (2)
- DEVID – one octet address assigned to DEV that identifies it.
- PNID – one octet number that identifies the piconet.
- Stream index – assigned by the PNC to identify a specific request for channel time
- Channel Time Allocation (CTA) – time allocated during the superframe for a particular purpose and potentially to a specific pair of DEVs

---
Architecture

---
FCSL
- Attempt to handle multiple upper-layer protocols
- Adopted 802.2 because 802.11 did
  - Thought it was the required method
  - Option to use SNAP header for Ethertype

---
Superframe structure
Superframe for original PHY
Superframe for mmWave PHY (time starts on right)

---
Types of CTAs

---
Addressing
- 64 bit addresses are used to uniquely identify devices (called a DEV address)
- This address is not used in an address field of the frame
  - DEVs are assigned a short ID for the piconet (DEVID)
  - DEVIDs are used for addressing
  - The FCSL maps DEV addresses to DEVIDs

---
Addressing (cont.)
- Addressing in 802.15.3 is for the immediate link
  - Required because it is a shared medium
  - Does not have to do with the “ultimate” source and destination.

---
MAC frame format
- Short addresses are used
- PNID is used to identify the piconet
- PNID & DEVID pair should be unique
- PNID collision causes new PNID to be selected.

---
Suggestion
- Change addressing to be 48 bit
- Option 1:
  - Define that the first 2 octets of all data frames contain EtherType and subsequent octets are interpreted according to that.
- Option 2:
  - Define that the Data Payload field of a Data frame contains an Ethernet frame, i.e., Source Address, Destination Address, Length/Type field

---
Questions
- Should we have length limit for frames that is similar to Ethernet?
- What happens if an incoming MSDU is fragmented? Do we replicate the EtherType?