## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: ETRI PHY Proposal for PAC
Date Submitted: May 5, 2014
Source: Kapseok Chang, Byung-Jae Kwak, and Moon-Sik Lee and Byung-Jae Kwak (ETRI)
Company: ETRI
Address: 218 Gajeong-ro, Yuseong-gu, Daejeon, 305-700, Korea
Voice: +82 42 860 1639 Fax: E-Mail: {kschang, bjkwak, moonsiklee}@etri.re.kr , bjkwak, moonsiklee}@etri.re.kr,
Re: TG8 PAC Call for Contributions (CFC), 15-14-0087-00-0008, Jan 23, 2014.
Abstract: This document presents a fully distributed, synchronized PHY proposal for PAC.
Purpose: Proposal and Discussion
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: ETRI PHY Proposal for PAC
May 2014
Kapseok Chang, Byung-Jae Kwak,
and Moon-Sik Lee

## Slide 3: PHY Proposal Overview
Supporting transmission mode
  Orthogonal Frequency Division Multiplexing (OFDM)
Providing more precise synchronization compared to IEEE 802.11 [1]
Supporting collision detection in receiving mode
Supporting frame timing-offset indication in receiving mode
Supporting contention-window indication in receiving mode
Supporting coexistence with other 2.4GHz and 5GHz
  Different presentation (IEEE 802.15-14-0249-00-0008)
Supporting data transmission rates up to 54 Mbps: up to 64QAM
Supporting physical-layer security
  Different presentation (IEEE 802.15-14-0252-00-0008)
Supporting discovery with spatial filtering
  Different presentation (IEEE 802.15-14-0133-00-0008)

## Slide 4: OFDM Parameters
Parameter | Value
Carrier frequency | 2.4 GHz, 5 GHz
Channel bandwidth | 20 MHz
FFT Size | 64
Number of data subcarriers | 48 (excluding dc)
Number of preamble subcarriers Number of timing-offset indication field (TOIF) subcarriers Number of contention-window indication field (CWIF) subcarriers Number of collision detection field (CDF) subcarriers | 52 (excluding dc)
Number of pilot subcarriers | 4
OFDM sampling time | 0.05 us
Subcarrier frequency spacing | 312.5 kHz
Cyclic Prefix | 16ts = 0.8us
OFDM symbol duration | (16+64)ts = 4 us

## Slide 5: MAC Frame Structure
Synchronization interval [TBD]
Sync slot
  Providing timing reference, timing-offset indication (TOI), collision detection (CD), and contention-window indication (CWI)
Discovery slot
  Different presentation (IEEE 802.15-14-0254-00-0008)
Data slot (CAP, CFP)
  Different presentation (IEEE 802.15-14-0254-00-0008, IEEE 802.15-14-0249-00-0008)

## Slide 6: Sync Slot Format
Backoff slots
  see IEEE 802.15-14-0249-00-0008.
Preamble
  Consists of short training field (STF) and long training field (LTF).
  Preamble is used for automatic gain control (AGC), carrier sensing, packet detection, time/frequency synchronization, and channel estimation.
  Preamble is common regardless of any slot defined by MAC layer.
Timing-Offset Indication Field (TOIF)
  Contains timing offset information in order for receiving PD to acquire frame boundary, i.e. arrival time+timing offset.
  see IEEE 802.15-14-0249-00-0008.
Contention-Window Indication Field (CWIF)
  used for broadcasting current CW information of transmitter.
  see IEEE 802.15-14-0249-00-0008.
Collision Detection Field (CDF)
  used for detecting a collision caused by multiple PDs in physical layer.
  see IEEE 802.15-14-0249-00-0008.
Guard time
  TBD

## Slide 7: Preamble Format (1/4)
STF
  It is used for carrier sensing, AGC, packet detection, coarse time/frequency synchronization, and partial fine time/frequency synchronization.
  It consists of a set of 5 repetition signals (Ds), where D occupies 32 samples.
LTF
  It is used for final fine time/frequency synchronization and channel estimation.

## Slide 8: Preamble Format (2/4)
STF [2]-[5]
Base sequence
  Modified sequence
  V is set to be 1. The time-domain signal of an effective OFDM symbol is real, which make the complexity of a detector for fine synchronization low by a factor of 2 [4].
  The time-domain signal is inherently immune to carrier frequency offset [4].

## Slide 9: Preamble Format (3/4)
STF
  What is transmitted is signalled using the STF pattern as shown below
    Set (D,D,D,D,D) is configured in the beginning of the Preamble for each of sync slot, request to send (RTS), clear to send (CTS), and acknowledgement (Ack).
    Set (D,D,D,D,-D) is configured in the beginning of the Preamble for data packet.
  Specifically, the discovery indication subslot (see IEEE 802.15-14-0249-00-0008.) comprises the STF pattern (D,D,D,D,D) alone.
  If we perform carrier sensing (CS) based on single auto-correlation method with length-64 (corresponding to three Ds), CS performance can be improved by 6 dB compared to single auto-correlation method with length-16 (e.g. IEEE 802.11a), which is verified by simulation.
    CS capability is pivotal to reduce the hidden node problem that is well known.

## Slide 10: Preamble Format (4/4)
Slide 10
LTF [2]-[5]
Base sequence
  Modified sequence
  Z is set to be 25.
  The time-domain signal is inherently immune to carrier frequency offset [4].

## Slide 11: TOIF Format
Based on tone-hopping
  Z, Y, X, and W are groups of the subcarriers shown in the right figure. Each group is in range of 0 to 12.
  The TO ID is mapped into the codeword (Z,Y,X,W). The total # TO IDs needed is 32.
    Code words shall be selected such that Hamming distance ≥ 3
  Hopping procedure in transmitting mode
    Carry busy tones to the four subcarriers corresponding to current TO ID.
    Each busy tone is transmitted with a quarter of total power.
  Merit
    Low peak to average power ratio (PAPR)
    Diversity gain
      Even when any busy tones fall into deep fading, the TO ID can be successfully detected thanks to other busy tones.

## Slide 12: CWIF Format
Based on tone-hopping
  Z, Y, X, W, Z’, Y’, X’, and W’ are groups of the subcarriers shown in the right figure. Each group is in range of 0 to 12.
  The CW ID is mapped into the codeword (Z,Y,X,W,Z’,Y’,X’,W’). The total # CW IDs needed is 289.
    Code words shall be selected such that Hamming distance ≥ 6 (or 7)
  Hopping procedure in transmitting mode
    Carry busy tones to the eight subcarriers corresponding to current CW ID.
    Each tone is transmitted with a quarter of total power allocated to each symbol.
  Merit
    Low peak to average power ratio (PAPR)
    Diversity gain
      Even when any busy tones fall into deep fading, the CW ID can be successfully detected thanks to other busy tones.

## Slide 13: CDF Format
Based on random 4-tone [4]
  Procedure in transmitting mode
    Select four random subcarriers, one from each group of the subcarriers. Each group is in range of 0 to 12.
    Carry busy tones to the four randomly selected subcarriers.
    Each busy tone is transmitted with a quarter of total power.
  Procedure in receiving mode
    When a receiver sees more than one tone in any of the groups of subcarriers, collision occurs.

## Slide 14: PPDU Format
Preamble/CWIF/CDF
  same as that in sync slot.
Header
  used for describing the content of the packet data as well as the protocol used to transfer it.
  employing one robust MCS to guarantee reliable reception
PSDU Field
  used for the information intended for the receiver
  employing diverse MCSs to support scalable data rates
Beam Jitter (BJ) Field
  used for Look and Link (LnL)
  see IEEE 802.15-14-0133-00-0008.

## Slide 15: Header
Bit-level scrambling
  Shall be specified.
  Specific method is TBD.
Channel encoding
  Convolutional encoder shall be specified.
  The specification of channel encoder is TBD.
Modulation schemes applied
  Spread BPSK (SBPSK)/Spread QPSK (SQPSK)
    TBD

## Slide 16: PSDU Field
Bit-level scrambling
  Shall be specified.
  Specific method is TBD.
Channel encoding
  Convolutional encoder shall be specified.
  The specification of channel encoder is TBD.
Supports data rates up to ~ 54 Mbps
  Modulation formats: SBPSK, SQPSK/BPSK, QPSK, 16-QAM, and 64-QAM
  Convolutional Coding: rates 1/2(base code rate), 3/4, 5/8
  MCS table corresponding to scalable data rates will appear in next slide.

## Slide 17: MCS Table
MCS index | Modulation | Code Rate | NBPSC | NCBPS | NIBPS | Data Rate (Mbps)
1 | SBPSK | 1/2 | 0.5 | 24 | 12 | 3
2 | SQPSK/BPSK | 1/2 | 1 | 48 | 24 | 6
3 | SQPSK/BPSK | 3/4 | 1 | 48 | 36 | 9
4 | QPSK | 1/2 | 2 | 96 | 48 | 12
5 | QPSK | 3/4 | 2 | 96 | 70 | 17.5
6 | 16-QAM | 1/2 | 4 | 192 | 96 | 24
7 | 16-QAM | 3/4 | 4 | 192 | 144 | 36
8 | 64-QAM | 5/8 | 6 | 288 | 180 | 45
9 | 64-QAM | 3/4 | 6 | 288 | 216 | 54
Info bits per OFDM symbol
coded bits per OFDM symbol
coded bits per subcarrier
* The above MCS sets are changeable according to ensuing evaluation result

## Slide 18: SBPSK/SQPSK Modulation and Mapping
Concatenated spreading:
Phase shifting to suppress PAPR increasing caused by above spreading:
  Specific phase shifting is TBD.
FYI, the data rate of MCS index 1 is identical to that of BPSK with code rate ¼. However, if we adopt BPSK with 1/4, additional encoder and decoder are needed, which makes battery drain higher.

## Slide 19: Performance Evaluation
Preamble considered
  Preamble1 (P1): proposed preamble comprising STF and LTF, where STF pattern is [D,D,D,D,-D].
  Preamble2 (P2): proposed preamble comprising STF and LTF, where STF pattern is [D,D,D,D, D].
  Preamble3 (P3): 802.11a preamble, where STF pattern is [B,B,B,B,B,B,B,B,B,B].
  Preamble4 (P4): modified 802.11a preamble, where STF pattern is [B,B,B,B,B,B,B,B,-B,-B].
    Time and frequency synchronization (TFS) is performed by cross-correlation using [B,B,-B,-B] in this preamble, which is called cross-correlation based TFS (CCbTFS).
    This preamble is introduced in order to observe frequency immunity compared to P1 employing cross-correlation using [D,-D].
Synchronization acquisition scheme
  Frequency synchronization (FS) scheme applied
    Single auto-correlation based FS (ACbFS) method with length-16, -32, and -64
  Time synchronization (TS) scheme applied
    Product cross-correlation based TS (CCbTS) method: multiplication of CC out using STF and that using LTF

## Slide 20: Performance Evaluation
Performance measure and setting
  Detection error rate (DER) vs. Es/N0
    If estimated sample time offset is out of ±4 samples, an error is declared.
  Mean carrier-sensing (CS) output vs. Es/N0
    CS output is normalized by 16.
  FER vs. Es/N0 and PAPR vs. Es/N0
    In this evaluation, BPSK and SBPSK are simulated. The FER and PAPR results regarding SQPSK will be provided at the next meeting.
  Collision probability vs. Es/N0(PD1)
    False alarm in the absence of PD2 and missing in the presence of PD2. This evaluation results will be provided at the next meeting.

## Slide 21: Performance Evaluation
Simulation parameters
Parameter | Value
Carrier frequency / bandwidth / FFT Size | 5 GHz / 20 MHz / 64
Number of data subcarriers | 48
Number of preamble subcarriers Number of timing-offset indication field (TOIF) subcarriers Number of contention-window indication field (CWIF) subcarriers Number of collision detection field (CDF) subcarriers | 52
Number of pilot subcarriers | 4
OFDM sampling time | 0.05 us
Subcarrier frequency spacing | 312.5 kHz
Cyclic Prefix | 16ts = 0.8us
OFDM symbol duration | 4 us
Channel model: ETSI BRAN | Model A: Office

## Slide 22: Performance Evaluation
DER vs. Es/N0
Proposed preambles outperforms IEEE 802.11a.
To observe the frequency-offset immunity over preamble, we employ CCbTFS. As a result,
  Even though we consider the highest frequency offset, i.e. 40 ppm, the proposed STF and LTF sequences is still working, while the 11a does not work.

## Slide 23: Performance Evaluation
Mean CS output vs. Es/N0
Mean CS output with length-32 outperforms that with length-16 by 3 dB.
Mean CS output with length-64 outperforms that with length-16 by 6 dB.

## Slide 24: Performance Evaluation
FER vs. Es/N0
Three SBPSK MCSs provide same FER performances.
PAPR vs. Es/N0
The first two SBPSK MCSs provide 1.1dB PAPR loss over the last SBPSK MCS proposed.

## Slide 25: Conclusions
Providing more precise synchronization
Supporting collision detection
Supporting frame timing-offset indication
Supporting contention-window indication
Supporting data transmission rates up to 54 Mbps: up to 64QAM
Supporting coexistence with other 2.4GHz and 5GHz
Supporting physical-layer security
Supporting discovery with spatial filtering

## Slide 26: References
IEEE Std 802.11, “Part 11: Wireless LAN medium access control (MAC) and physical layer (PHY) specifications,” IEEE Computer Society, 2012.
K. Chang and Y. Han, “Robust replica correlation-based symbol synchronisation in OFDM systems,” Electronics Letters, vol. 44, no. 17, pp. 1024-1025, Aug. 2008.
K. Chang, P. Ho, and Y. Choi, “Signal design for reduced complexity and accurate cell search/synchronization in OFDM-based cellular systems,” IEEE Transactions on Vehicular Technology, vol. 61, no. 9, pp. 4170-4175, Nov. 2012.
ETRI, “ETRI technical PHY proposal for IEEE 802.15 TG8 PAC standard,” DCN: IEEE 802.15-13-0373-01-0008, July 2013.
ETRI, “Collision detection based PHY Proposal for PAC,” DCN: IEEE 802.15-14-0132-00-0008, March 2014.
ETRI and Samsung, “MAC proposal for PAC,” DCN: IEEE 802.15-14-0254-00-0008, May 2014.
ETRI and Samsung, “Performance Evaluation of Fully Distributed Synchronization Mechanism for PAC,” DCN: IEEE 802.15-14-0249-00-0008, May 2014.