## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Power Control for PAC]
Date Submitted: [5 May 2014]
Source: [Qing Li, Chonggang Wang, Hongkun Li, Zhuo Chen, Tao Han]
Company [InterDigital Communications Corporation]
Address [781 Third Avenue, King of Prussia, PA 19406-1409, USA]
Voice:[610-878-5695], FAX: [610-878-7885], E-Mail:[Qing.Li@InterDigital.com]
Re: [ Call for Final Contributions]
Abstract: [This document proposes power control schemes for 802.15.8 TG]
Purpose: [To discuss technical feasibility of the proposed power control schemes for 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PAC Requirements
Excerpt from IEEE 802.15.8 PFD [1]
  5.12 Interference management: Interference among multiple links is managed by the threshold level.
  5.13 Transmit power control: A PD may perform transmit power control based on channel measurement status.
Excerpt from IEEE 802.15.8 TGD [2]
  6.7 Interference Management: IEEE 802.15.8 shall provide the functionality to mitigate interference from other PDs.
  6.8 Transmit Power Control: IEEE 802.15.8 shall support the functionality for PDs to control the transmit power to minimize interference and power consumption.

## Slide 3: Conventional Power Control
  Open-loop or closed-loop power control based on path-loss.
  Provide similar QoS to all the UEs in the cell no matter what kind of applications or services that the UEs are engaged, i.e. chat on social network, or video conference.
Increase power
Decrease power
UE1
UE2

## Slide 4: Context-aware Power Control
  Different applications or services [3] require different power control schemes
         Application-aware or Context-aware

## Slide 5: Inter-P2PNWs Power Control
  Many P2P networks (P2PNWs) coexist within a short radio range of each other without a central controller to manage the transmission power among the P2PNWs, therefore inter-P2PNWs power control is needed.
    For examples:
    What’s the initial transmitting power for a PD when it enters the proximity?
    Is the “Video Conference Meeting” too loud to affect the other P2P communications in proximity?
    What’s the transmitting power that a PD may use if participates in “Chatting” as well as “Gaming”.

## Slide 6: Examples of Context and Power Control Information
Application | Context Info | Power Control Info
Video Conf. Meeting | Service Power Category: e.g. Cat1 – very high data rate & low error rate QoS: 1-to-N group based -- guaranteed or best effort to all PDs Service Range: medium | Max. Tx Power: medium Power Control Interval: long Measurements at Rx: SINR, CQI, etc. Info from Tx: Tx power level, location, etc.
Gaming | Service Power Category: e.g. Cat2 - high data rate & low error rate QoS: distributive group based -- guaranteed to all PDs Service Range: small | Max. Tx Power: medium Power Control Interval: long Measurements at Rx: SINR, CQI, etc. Info from Tx: Tx power level, location, etc.
Chat | Service Power Category: e.g. Cat3 - low data rate & high error rate QoS: average | Power Control Interval: medium Measurements at Rx: SINR, RSSI, etc. Info from Tx: Tx power level, speed, etc.
Keep Alive | Service Power Category: e.g. Cat4 - very low data rate & high error rate QoS: low | Measurements at Rx: RSSI, etc. Info from Tx: Tx power level, speed, etc.

## Slide 7: Context-aware Power Control for PAC

## Slide 8: Examples of CPCI
Notes: Add simplified contents from the power control papers.

## Slide 9: Context-aware Power Control -- CPCI Detection (1/2)

## Slide 10: Context-aware Power Control -- CPCI Detection (2/2)
Notes: Add simplified contents from the power control papers.

## Slide 11: Context-aware Power Control Procedure - Inter-P2PNWs Power Control (1/2)

## Slide 12: Context-aware Power Control - Inter-P2PNWs Power Control (2/2)
Notes: Add simplified contents from the power control papers.

## Slide 13: Context-aware Power Control Procedure - Intra-P2P Power Control (1/2)

## Slide 14: Context-aware Power Control - Intra-P2PNW Power Control (2/2)
Notes: Add simplified contents from the power control papers.

## Slide 15: Context-aware Power Control – Multi-App (1/2)

## Slide 16: Context-aware Power Control - Multi-App (2/2)
Notes: Add simplified contents from the power control papers.

## Slide 17: Simulation Performance of Context Aware Power control

## Slide 18
Test Case 1:
  For short range application (e.g. game) with high data rate and low error rate requirement, context aware power control keeps the same Tx power when a peer moves out of service range.
  Distance between peer 0 and 1: 20m increases to 80m

## Slide 19: Test Case 1: Simulation Parameters
Parameters for Game Application | Value
Initial Tx Power | 0 dBm
(Max, Min) Tx Power | (30, -20) dBm
MCS | 64QAM, ¾ Coding rate
SINR threshold | 13 dB
Mapped PER | 1.03e-4
Service Range | 30 meters
Bandwidth | 10 MHz
Physical Data Rate | 27 Mbps
Power Adjustment Step | 0.1 dB
Slot Length | 1 ms
Close Loop Power Control Interval | 100 ms
Traffic Model | full buffer
Simulation Time | 20 s

## Slide 20: Test Case 1: Simulation Result Results
Context aware power control maintains the same Tx power level when peer 1 moves out of the service range for the short range game application.
Conventional power control continues increasing the Tx power considering only distance.

## Slide 21
Test Case 2:
  Context aware power control differentiates the QoS requirement for different applications, and applies different power control schemes accordingly.
  For example, chatting application is high error tolerable and low data rate requirement; game application requires low error rate and high data rate.

## Slide 22: Test Case 2: Simulation Parameters
Parameters for Chat Application | Value
Initial Tx Power | 0 dBm
(Max, Min) Tx Power | (30, -20) dBm
MCS | QPSK, ¾ Coding rate
SINR threshold | 5 dB
Mapped PER | 2.51e-3
Bandwidth | 10 MHz
Physical Data Rate | 9 Mbps
Power Adjustment Step | 0.1 dB
Slot Length | 1 ms
Close Loop Power Control Interval | 50 ms
Traffic Model | Bursty traffic (arrival probability=0.1)
Simulation Time | 20 s

## Slide 23: Test Case 2: Simulation Results
Context aware power control treats different applications with different QoS requirements
Conventional power control is not aware of different requirements of applications.

## Slide 24
Test Case 3:
  Context aware power control reduces the overall interference among different P2P networks (i.e. applications). It adjusts the power not only considering the interference within a P2P network also the interference among P2P networks.
  Parameters follows those used in test 1 and 2 for game and chat applications, respectively.
  Peer 0 and 4 is moving toward to 1 and 5 respectively to the shortest distance at 10 seconds, and then move away.

## Slide 25: Test Case 3: Simulation Results (1/2)
Context aware power control limits to increase Tx power for chat application (low data rate and high error tolerable) by considering not to generate too strong interference to the game application, which requires high data rate and low error rate.

## Slide 26: Test Case 3: Simulation Results (2/2)
Context aware power control achieves higher efficiency ratio of power consumption by mitigating the interference among P2P networks, i.e. using less power for successfully receiving a packet.

## Slide 27: Conclusions
Context-aware
  Different P2PNWs, formed for different applications or services, conduct different Power Control schemes optimized with different Context and Power Control Information (CPCI).
  A peer participated in multi-applications may conduct different power control schemes based on the CPCI.
Co-existence
  Optimized the transmitting power level not only for the individual transmitter or receiver, but also for over all P2PNWs in proximity, i.e. inter-P2P power control to reduce interference to other PDs in proximity.
Infrastructure-less
  No central controller to specify the initial power level and the max. power level, etc.
     CPCI detection in proximity
     Cooperation among PDs in proximity, i.e. Inter-P2PNWs power control

## Slide 28: References
[1] PAC Framework Document (PFD) 15-14-0085-01
[2] Technical Guidance Document (TGD) 15-12-0568r9
[3] Application Matrix 15-12-0684r0
[4] Power Control for PAC – Final Contribution Doc, IEEE 15-14-0266-00-008.

## Slide 29: Thank You!
Any Questions?
 Qing.Li@InterDigital.com