## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Transmission performance of short-range MIMO in 60-GHz band
Date Submitted: 13 May, 2014
Source: Ken Hiraga, Kazumitsu Sakamoto, Tomohiro Seki, Toshimitsu Tsubaki, Hideki Toshinaga and Tadao Nakagawa
Company: NTT corporation
Address: Hirarinooka 1-1, Yokosuka Japan
Voice:+81-46-859-3474, FAX: +81-46-855-1497, E-Mail: hiraga.ken@lab.ntt.co.jp
Re: []
Abstract: This document describes the calculated transmission performance of short-range MIMO for the kiosk downloading. Influences on BER by displacement are shown.
Purpose: To discuss the MIMO setting in the 60-GHz kiosk model.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: 15-14-0300-00-003d-transmission-performance-of-short-range-mimo-in-60-gHz-band

## Slide 2: Contents
“Real touch-and-get” of the kiosk system by 802.15.3d
100G transmission rates using 60-GHz band
  Motivation for MIMO transmission at 60-GHz band
100 Gbit/s performance estimation

## Slide 3
“Real touch-and-get” of the kiosk system by 802.15.3d
“Real touch-and-get” within 1 sec (with initial link setup) download with toll-gate
  With 100 Gbit/s rate, data sizes of up to a DVD (4.7 GBytes) are downloaded within 0.5 sec.
4 newspapers
1 Magazine
1 CD
1-hr Video
(MPEG2)
1 DVD
Transmission rate [Gbit/s]
Max. file size [GBytes]
2
4
40
100
10
400
1000
1
0.1
10
100
100Gbit/s
Blu-ray Disc
Maximum file sizes transmitted within 0.5 seconds
15-13-0684-00-0thz

## Slide 4
Modulation | No. of frequency channels | MIMO | Rate | Data transmission time for a DVD (4.7 GBytes)
16QAM | 1 | - (SISO) | 4.5 Gbit/s | 8.4 sec
64QAM |  |  | 6.8 Gbit/s | 5.5 sec
64QAM | 4 |  | 27 Gbit/s | 1.4 sec
256QAM |  |  | 36 Gbit/s | 1.0 sec
1024QAM |  |  | 45 Gbit/s | 0.84 sec
16QAM | 2 | 16x16 | >100 G bit/s | <0.4 sec
64QAM | 1 |  |  | 
100G transmission rates using 60-GHz band
IEEE802.11ad OFDM PHY
MCS#17: 2.1 Gbit/s (QPSK, Code rate=3/4)
MCS#21: 4.5 G bit/s (16QAM,Code rate=13/16)
MCS#24: 6.8 G bit/s (64QAM,Code rate=13/16)
100G rates are attainable using MIMO over 60 GHz
・
・
・
・
・
・
TX
RX
#1
#2
#M
#1
#2
#M
Line-of-sight
environment
Short-Range MIMO
(SR-MIMO)
Frequency channels
66 GHz
57 GHz
Ch1
Ch2
Ch3
Ch4
60.48
62.64
Notes: 256QAM:
6.8 Gbit/s * 4/3 = 9.1 Gbit/s
1024QAM:
6.8 Gbit/s * 5/3 = 11.3 Gbit/s

## Slide 5
100 Gbit/s performance estimation
d
d= 4.1 mm
D = 10 mm
Electromagnetic simulation model of transmission channel
Tx array
Rx array
OFDM transmission simulation
Parameter | Value
Frequency channel | Ch2 (fc=60.48 GHz), Ch3 (fc=62.64 GHz)
No. of branches | 16 x 16
Transmission distance | D = 10 mm
Element spacing | d = 4.1 mm = 0.82 λ0 (Optimized for this transmission distance)
MIMO detection | Zero Forcing (ZF)
No. of data subcarriers | 336
Subcarrier spacing | 5.15625 MHz
Modulation | QPSK, 16QAM, 64QAM
Frequency channels in 60-GHz band
66 GHz
57 GHz
Ch1
Ch2
Ch3
Ch4
60.48
62.64
Microstrip antenna
23mm
Originally presented in 15-13-0684-00-0thz

## Slide 6
  Over 100 Gbit/s is attainable with 16x16 MIMO using small (23 mm x 23 mm) antenna arrays that can be installed on portable devices.
100 Gbit/s performance estimation
Frequency channels in 60-GHz band
Ch1
Ch2
Ch3
Ch4
60.48
62.64
[GHz]
Modulation | No. of frequency channels | Transmission rate
QPSK | 1 | 33 Gbit/s
 | 2 | 67 Gbit/s
16QAM | 1 | 72 Gbit/s
 | 2 | 144 Gbit/s
64QAM | 1 | 108 Gbit/s
 | 2 | 216 Gbit/s
Transmission rates with each modulation
16 x 16 MIMO
Simulated bit error rate (BER)
Originally presented in 15-13-0684-00-0thz

## Slide 7
Influences by antenna displacements
D = 10 mm
Electromagnetic simulation model of transmission channel
Tx array
(Kiosk)
Rx array (Terminal)
OFDM transmission simulation:
Same as the simulation shown above
BER is averaged for two channels
Microstrip antenna
d
d= 4.1 mm
Δx
Antenna Displacement

## Slide 8: Influences by antenna displacement (1) QPSK
Chart: SNR [dB]
| 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
0 | 0.000432 | 0.000105 | 1.3e-05 | 2e-06 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0.000875 | 0.000241 | 3.7e-05 | 9e-06 | 3e-06 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | 0.002545 | 0.00098 | 0.000289 | 7.7e-05 | 1.8e-05 | 1e-06 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
3 | 0.008622 | 0.004264 | 0.001814 | 0.000681 | 0.00019 | 5.4e-05 | 6e-06 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4 | 0.027174 | 0.016587 | 0.009762 | 0.00499 | 0.002231 | 0.000929 | 0.000279 | 8.2e-05 | 1.5e-05 | 4e-06 | 0 | 0 | 0 | 0 | 0 | 0
5 | 0.068471 | 0.049327 | 0.035344 | 0.023419 | 0.014522 | 0.008466 | 0.004486 | 0.002016 | 0.000789 | 0.000268 | 6.9e-05 | 1.8e-05 | 0 | 0 | 0 | 0

## Slide 9: Influences by antenna displacement (2) 16 QAM
Chart: SNR [dB]
| 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
0 | 0.077129 | 0.050635 | 0.03067 | 0.016719 | 0.008153 | 0.003282 | 0.001165 | 0.000327 | 7e-05 | 1.2e-05 | 2e-06 | 0 | 0 | 0 | 0 | 0
1 | 0.080682 | 0.054118 | 0.033728 | 0.019502 | 0.010239 | 0.004677 | 0.001898 | 0.000647 | 0.000176 | 4.3e-05 | 6e-06 | 3e-06 | 0 | 0 | 0 | 0
2 | 0.092967 | 0.06591 | 0.04405 | 0.027742 | 0.016335 | 0.0089008 | 0.0043957 | 0.0018921 | 0.00068464 | 0.00021177 | 5.7215e-05 | 6.4014e-06 | 0 | 0 | 0 | 0
3 | 0.12219 | 0.092736 | 0.067167 | 0.046751 | 0.031579 | 0.019772 | 0.011543 | 0.006372 | 0.00302 | 0.001311 | 0.000461 | 0.000143 | 2.6e-05 | 6e-06 | 0 | 0
4 | 0.16862 | 0.13661 | 0.10632 | 0.080998 | 0.061013 | 0.043943 | 0.030021 | 0.020116 | 0.012062 | 0.007024 | 0.003654 | 0.001669 | 0.000635 | 0.000232 | 5.7e-05 | 1e-05
5 | 0.2355 | 0.20022 | 0.16523 | 0.13453 | 0.10868 | 0.086043 | 0.066209 | 0.050489 | 0.036447 | 0.0258 | 0.017105 | 0.010796 | 0.006215 | 0.003326 | 0.001493 | 0.00062
More than 5 mm displacement is allowed for BER < 10^-2

## Slide 10: Influences by antenna displacement (3) 64 QAM
Chart: SNR [dB]
| 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
0 | 0.23668 | 0.20096 | 0.16694 | 0.13474 | 0.10427 | 0.077356 | 0.054058 | 0.035398 | 0.020908 | 0.011244 | 0.005386 | 0.002292 | 0.000746 | 0.000224 | 5.6e-05 | 1.2e-05
1 | 0.25688 | 0.2201 | 0.18556 | 0.15218 | 0.12079 | 0.092363 | 0.067425 | 0.046514 | 0.029592 | 0.017523 | 0.009302 | 0.00443 | 0.001779 | 0.000646 | 0.000191 | 4.5e-05
2 | 0.26918 | 0.23163 | 0.1967 | 0.16282 | 0.13155 | 0.10268 | 0.077249 | 0.055964 | 0.03802 | 0.024375 | 0.014528 | 0.008099 | 0.004062 | 0.001796 | 0.000704 | 0.000212
3 | 0.30082 | 0.2621 | 0.22527 | 0.19018 | 0.15779 | 0.12747 | 0.10036 | 0.077343 | 0.056743 | 0.040126 | 0.026973 | 0.017331 | 0.010316 | 0.005639 | 0.002856 | 0.001225
4 | 0.35 | 0.31128 | 0.27255 | 0.23572 | 0.20055 | 0.16769 | 0.13763 | 0.11235 | 0.088278 | 0.067833 | 0.050808 | 0.037141 | 0.025846 | 0.017216 | 0.010809 | 0.006264
5 | 0.41504 | 0.37722 | 0.33764 | 0.29941 | 0.26214 | 0.22646 | 0.193 | 0.16419 | 0.13586 | 0.11129 | 0.089595 | 0.071289 | 0.055508 | 0.042133 | 0.031181 | 0.021891

## Slide 11: Conclusions
MIMO transmission in the line-of-sight environment is necessary for 100 Gbit/s transmission in 60-GHz band.
Influences on BER by antenna displacement are clarified.
  More than ±5 mm displacement is allowable in the 16-QAM transmission
  Against further displacements, compensetion method for them will be required.
Modulation | No. of frequency channels | MIMO | Rate
16QAM | 1 | - (SISO) | 4.5 Gbit/s
64QAM | 1 |  | 6.8 Gbit/s
64QAM | 4 |  | 27 Gbit/s
16QAM | 2 | 16x16 | >100 G bit/s
64QAM | 1 |  |