## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Input to Technical Guidance Document: Structuring of System Requirements
Date Submitted: 16 Jul 2014
Source: Dietmar Eggert
Company: Atmel
Address: Koenigsbruecker Str. 61, 01099 Dresden, Germany
E-Mail: dietmar.eggert@atmel.com
Re: Technical Guidance Document
Abstract: This presentation helps to facilitate a discussion on aspects of the Technical Guidance Documents
Purpose: Progress TGD
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Reminder: The Scope of the Group
This amendment integrates wireless ranging techniques and technologies, including those existing within IEEE 802.15.4 and new to IEEE 802.15.4, into a consistent, standardized method addressing the needs of a wide range of applications and PHYs and enabling the interoperability of devices by different vendors using this method. Additionally, the amendment defines necessary MAC and PHY extensions which enable common radio based distance measurements.
Given that various regions and applications are served by numerous frequency bands following different regulatory rules, modulations, and data rates; complexity and confusion can only be avoided if ranging data is made available to higher layers in a consistent manner for location determination mechanisms. Hence there is a need for a Real Time Locating System (RTLS) which works with the diverse PHYs of IEEE 802.15.4.

## Slide 3: Application Scenario Specifics affecting Propagation Characteristics
Devices are fixed or mobile (speed of movements matter)
The environment is stationary or non-stationary, any movement in the environment may matter
Regulatory Requirements (spectrum availability and power density limitations)
Assumptions about propagation environment reflected in channel models

## Slide 4: Application Scenario Specifics affecting Network Layer and above
Point-2-Point, Point-2-MultiPoint, MultiPoint-2-Point, MultiPoint-2-MultiPoint
Many uncoordinated Initiators, Few Sector/Group-Initiator  level of synchronization and related limitation imposed by Network Standard (e.g. BT,..)
Point, where range information is consolidated (initiator, reflector or both)
Point, where position information is consolidated (Tag, Centralized Server controlling the anchor network, or both)

## Slide 5: Application Scenario Specifics affecting Network Layer and above
Security/Protection of
  Measurement Data
  Datacom,
  Security for Range Information,
  Security for Positioning Information
Access to Geolocation Database
  Dependent and independent devices

## Slide 6: Application Related Requirements (Measurement centric)
Range from 10m to several km
Accuracy
  Distance from cm to several 10’s of meters
  Angle up to 10’s of degrees
  Leading to an measurement accuracy of
    Signal Time from ps to us
    Signal Phase up to 10’s of degrees
Circular Error Probability (CEP), CDF
Resolution from mm to m
Airtime
Measurement Time
Latency
Proximity/Presence Support/Geofencing

## Slide 7: Application Scenario Specifics affecting Propagation Characteristics
Relative Accuracy (Accuracy rel. to Distance measured)
Update Rate
Rate of Motion (max. Velocity supported)
  Ability to accurately locate objects at velocity X
Group Requirements enforced by Positioning
  Time for one position
  Time for x number of positions
  Support for x number of Tags
  Time to determine position for x number of Tags
Location/Ranging Measurements per second...ms...
Constraint by air capacity vs. constraint processing capacity

## Slide 8: Radio Measurements: The bottom Layer
Basic Principles
  RSSI,
  Time (Time-of-flight, RTT – Round Trip Time)
  Time-Difference (TDoA,..)
  Angle (AoA, AoD, ...)
  Phase Differences
  Multi-Frequency
Radio/PHY Parameters
  Modulation, Spreading, Coding, frame structures
Single Radio, Multi-Antenna (Beam-forming), Multi Radio

## Slide 9: Single Radio Signal Parameters and Related Radio Measurement
Reference Signal | Radio Measurement | Critical System Parameter
Any radio signal characterized by its power | RSSI | Resolution and Accuracy of radiated TX Power; Resolution and Accuracy of Rx RSSI Measurement,…
Continuous RF Chirps (CSS) | Frequency, Phase & Time offsets | Crystal Tolerance, Signal Quality Error,…
Discrete RF Chirps | Frequency, Phase & Time offsets | Crystal Tolerance, ….
UWB Pulse | Pulse Arrival Time | Crystal Purity, Crystal Offset,…
UWB OFDM | Frequency, Phase & Time offsets | Crystal Tolerance, Signal Quality Error,…