## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Agreed Discovery Procedure]
Date Submitted: [September 17, 2014]
Source: [Huan-Bang Li] Company [NICT]
Address [3-4 Hikarino-oka, Yokosuka, Kanagawa, Japan]
Voice:[+81 468475104], FAX: [:[+81 468475431], E-Mail:[lee@nict.go.jp]
Re: [Response to call for contribution of 15.8 PAC
Abstract: [Discovery Procedure for IEEE802.15.8]
Purpose: [This document is to provide a MAC mechanism]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Agreed Discovery Procedure
TG8 Group

## Slide 3: Discovery Procedure 1
Advertisement (One way discovery) :
  A PD broadcasts Discovery Request message during discovery period.
  A PD may scan during discovery period. After receiving the Discovery Request message, the PD sends it to higher layer.

## Slide 4: Illustration of Discovery Procedure 1
Discovery Request message
PD_2
PD_1
PD_3
PD_4
Discovery Request message
Discovery Request message

## Slide 5: Discovery Procedure 2
Publish/Subscribe (Untargeted two-way discovery) :
  A PD broadcasts Discovery Request message during discovery period.
  A PD may scan during discovery period. After receiving the Discovery Request message, the PD sends it to higher layer.
  Upon the higher layer indication received, the PD responds to the sender PD with a Discovery Response message.

## Slide 6: Illustration of Discovery Procedure 2
PD_2
PD_1
PD_3
PD_4
Discovery Request message
Discovery Request message
Discovery Request message
Discovery Response message
Discovery Response message
Discovery Response message

## Slide 7: Discovery Procedure 3
Query/Reply (Targeted two-way discovery):
  A PD broadcasts Discovery Request message during discovery period.
  A PD may scan during discovery period. After receiving the Discovery Request message, the PD sends it to higher layer.
  Upon the higher layer indication received, the queried PD responds to the sender PD with a Discovery Response message.

## Slide 8: Illustration of Discovery Procedure 3
PD_2
PD_1
PD_3
PD_queried
Discovery Request message
Discovery Request message
Discovery Request message
Discovery Response message