## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for MAC Peering Procedure]
Date Submitted: [14 September, 2014]
Source: [Qing Li]
Company [InterDigital Communications Corporation]
Address [781 Third Avenue, King of Prussia, PA 19406-1409, USA]
Voice:[610-878-5695], FAX: [610-878-7885], E-Mail:[Qing.Li@InterDigital.com]
Re: [ ]
Abstract: [This document proposes the key features for MAC Peering Procedure]
Purpose: [To discuss technical key features for MAC Peering Procedure]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Motion15: Peering Procedure
The peering procedure is initiated by sending a peering request message including peering information.
Responder shall send a peering response message to requestor to indicate whether the peering request is accepted or rejected.
The response message may include peering information if the request is accepted.

## Slide 3: Peering Procedure
Peering procedure may include the following:
Optional: Authentication & Authorization (full validation)
Communication link parameters are TBD, such as link ID, device capability (i.e. #antenna, MIMO), QoS, channel band, transmission power, round trip delay, etc.
Establish the link.

## Slide 4: One-to-One Peering Procedure
MAC
PD1
1. PEER_REQ.request
2. Peering Request
4. PEER_REQ.indication
5. Optional: Authentication & Authorization (TBD)
Higher Layer
Higher Layer
PD2
MAC
9. PEER_REQ.confirm
7. Peering Response
6. PEER_REQ.response
10. Establish link
8. ACK
3. ACK

## Slide 5: Peering Procedure (Marco’s comments)
Communication session parameters:
Estimate of the transmission power of the PD requesting peering, channel band used for peering and RAP-ID (random access preamble-ID).
Establish the link connection
PD2 sends a RAP to PD1 requesting peering, which is contention based. It is randomly selected from a pool of orthogonal ZC sequences that belong to the RAP Group supported by PD1. Moreover, such RAP contains finer frequency granularity for PD1 to acquire fine time and frequency synchronization of PD2, plus information about the resources needed to transmit in 3).
PD1 replies with a RA response message. It is broadcast and contains timing information (round-trip delay), RAP-ID of PD2, plus resources, like time slot or time-frequency slot, to transmit in 3), etc.
PD2 sends a scheduling request (note that it is contention free). It contains scheduling request information for transmission. If this message is successfully detected in PD1, still contention remains unsolved for other terminals.
Contention resolution. PD1 echoes PD2 ID contained in 3) PD2 detects its ID and sends ACK (RA terminated) a communication link is scheduled and established. PD2 detects another ID (RA terminated, starts a new one) PD2 fails to detect ID (RA terminated, starts a new one).

## Slide 6: Motion16: Re-peering Procedure
Re-peering procedure is similar to peering procedure. The main differences are:
  1) some of the previous peering information may not be included in request and response messages;
  2) the PD receiving the re-peering request validates re-peering information with the corresponding peering information before it accepts the re-peering request.
  TBD: parameters for validation may be Peering IDs, or Link IDS, etc.

## Slide 7: Re-peering Procedure
Re-peering procedure may include the following:
Optional: Authentication & Authorization update (light validation)
Update communication link parameters - TBD.
Re-establish the link

## Slide 8: One-to-One Re-peering Procedure
MAC
PD1
1. RE-PEER_REQ.request
2. Re-peering Request
4. RE-PEER_REQ.indication
5. Optional: Authentication & Authorization update (TBD)
Higher Layer
Higher Layer
PD2
MAC
9. RE-PEER_REQ.confirm
7. Re-peering Response
6. RE-PEER_REQ.response
10. Optional: Re-establish link
8. ACK
3.ACK

## Slide 9: Motion17: De-peering Procedure
De-peering procedure starts with a de-peering request. De-peering response is optional.

## Slide 10: De-peering Procedure
De-peering procedure may include the following:

## Slide 11: One-to-One De-peering Procedure
MAC
PD1
1. DE-PEER_REQ.request
2. De-peering Request
4. DE-PEER_REQ.indication
Higher Layer
Higher Layer
PD2
MAC
8. DE-PEER_REQ.confirm
6.De-peering Response
5. DE-PEER_REQ.response
7.ACK
3. ACK
9. Disconnect the link

## Slide 12: Back Up

## Slide 13: Link Update Procedure
Link Update procedure may include the following:
(not currently mentioned in Peering section in PFD, but we may discuss if it’s needed)
Update communication session parameters, such as QoS, channel, time interval, etc.
Update or refresh the link
Removed from Peering Procedure.
Maybe revisit for the Link Management

## Slide 14: One-to-One Link Update Procedure
MAC
PD1
LINKUP_REQ.request
LinkUp Request (air)
LINKUP_REQ.indication
Higher Layer (?)
Higher Layer(?)
PD2
MAC
LINKUP_REQ.confirm
LinkUp Response (air)
LINKUP_REQ.response
Optional: Update link
ACK
ACK
Removed from Peering Procedure.
Maybe revisit for the Link Management