## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal to create a new Task Group 15.3e]
Date Submitted: [21 October 2014]
Source: [Andrew Estrada, Keiji Akiyama, Hiroyuki Matsumura, Itaru Maekawa, Ko Togashi, Kiyoshi Toshimitsu, Ichiro Seto, Ken Hiraga and Masashi Shimizu]
Company: Sony, JRC, Toshiba and NTT
Address [16530 Via Esprillo MZ 7032 San Diego, California 92127]
Voice:[858-942-5483], FAX: [], E-Mail:[Andrew.Estrada@am.sony.com]
Re: []
Abstract: [Discussion for the proposal to create a new Task Group ]
Purpose: [Discussion on creating a new Task Group for Close Proximity P2P applications]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Andrew Estrada, Sony

## Slide 2
Proposal to create a new
Task Group 15.3e
WNG session
IEEE802.15
November 2014

## Slide 3: Why we need an enhanced MAC
Usage focus: kiosk downloading and toll gate use cases
Objectives of MAC enhancements:
  Maximum throughput
  Quick link setup
  Quick link release
Touch motion indicates user’s intention
to make or break the connection
Close Proximity Communication Systems

## Slide 4: Issues with the current 802.15.3 MAC for kiosk usage
Support for multiple DEVs
Capable of covering several meters
Capable of supporting various traffic types
Connection-oriented network
Data transfer must finish within wicket passage time
Must be able to initiate transfer to next device immediately after completion of previous transfer
Spatial density: Must support many independent proximity pairs in the same local area
Download services impractical where
time restrictions or delays exist
New proposed touch model
802.15.3c kiosk downloading model
Up to several
meters away
Close proximity “touch” or “swipe”

## Slide 5: Use case enables key assumptions
A proximity pair is only established to complete a single transaction
A proximity pair consists of a single link between 2 devices
Every link has full access to all the network bandwidth

## Slide 6: Touch-based usage model
Conventional network-based connection steps:
  Search
  Discover
  Select
  Connect
  Reserve bandwidth
  Start traffic
New close proximity steps:
  Touch
  Start traffic
“Touch and Get”
Human
a few cm

## Slide 7: Limitations of 802.15.3 MAC
Required 802.15.3e MAC items
Legacy 802.15.3 MAC spec
65 msec + α
Sequential paired P2P access (not multiple simultaneous P2MP access)
MAC-level data integrity
Connection setup time comparison:
2 msec (kiosk usage only)
2
1
3
4
5
6
7
Touch!
kiosk
Enhancements

## Slide 8: Kiosk Use Case = Transaction Density
kiosk
Touch!
kiosk
Touch!
kiosk
Touch!
kiosk
Touch!
kiosk
Touch!

## Slide 9: Maximize effective throughput
To fulfill these requirements, one must:
  Operate in P2P (point-to-point) mode
    Limit communications to close proximity range
      Place upper limit on EIRP or field strength
    Remove redundant processes not essential for P2P connectivity
      Remove DEVID  Simplify association step
      Beacon not required after establishment of connection
      Only CAP is required (CTAP not needed)
      etc.
  Guarantee data integrity at MAC level
    Maintain throughput even when errors occur during aggregation
    Reordering buffer not required  Reduce buffer size

## Slide 10: Quick link setup and release
Keep Superframe duration short before link setup
  Ex.: under 200usec
  Limited by mMinSuperframeDuration (over 1msec at present)
Simplify Association process
  Eliminate DEVID
  Reduce amount of frame exchanges
    Response to Association Request (ACK, Association Response) not required
  Include mechanism to complete connection setup within MAC level (no need to query upper layers)
To enable quick release:
  Preferably an explicit release scheme not dependent on timeouts
    Connection shutdown after sending Disassociation
Include mechanism to avoid a DEV to re-associate with the same device immediately after disassociating
  MAC level solution preferred. Method other than timer may be needed.

## Slide 11: Current and proposed setup procedure
Current procedure:
Proposed new simplified procedure:
Omitted
steps
Omitted
steps
Eliminated steps are shown in shade

## Slide 12: Summary of Beacon enhancements
Purpose of Beacon
  Search (not needed after establishment of P2P session)
  Sync (no need to manage traffic)
Short beacon interval before connection; No beacon after connection
  Eliminate notice of Beacon interval change
  Provide method to infer that DEV is no longer sending Beacons
  Remove Beacon-lost procedure from DEV

## Slide 13: Questions
Should changes be made as options to the current standard?
  Optional would be a challenge
  Alternative would be a stand-alone amendment
  Should arrange a pre-mtg with James Gilb before WNG session
    Favorable to get his recommendations and support
Sunday, Thomas indicates this item to be on the agenda
WNG presentation on Wednesday (straw poll)
Within .15 WG Thursday mtg: formal motion
  Taken to EC on Friday
For next week’s .3d conf call
  No need for much discussion
  Informative may be helpful if time permits