## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Frequency channel selection]
Date Submitted: [November 4, 2014]
Source: [Huan-Bang Li, Marco Hernandez, Igor Dotlic, and Ryu Miura] Company [NICT]
Address [3-4 Hikarino-oka, Yokosuka, Kanagawa, Japan]
Voice:[+81 468475104], FAX: [:[+81 468475431], E-Mail:[lee@nict.go.jp]
Re: [Response to call for contribution of 15.8 PAC
Abstract: [Frequency channel selection procedure for IEEE802.15.8]
Purpose: [This document is to provide a MAC mechanism]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
<November 2014>

## Slide 2: Frequency Channel Selection (FCS)
November 4, 2014

## Slide 3: Frequency Band and Channels
  TG8 deals with several frequency bands including sub-GHz (900MHz), ISM band (2.4GHz and 5GHz), and UWB band (3.1-10.6GHz).
  Each of these frequency band provides a number of frequency channels, the number and bandwidth of which are to be specified.
  When specify frequency channels, requirements of local regulations must be taken into consideration.

## Slide 4: Unit Channel and Bundle of Unit Channels
  In most regulations, a unit channel is defined while simultaneous occupancy of several unit channels is allowed.
  If it is not specified, a channel could be either a unit channel or a bundle of unit channels.
  As a result, a list of available channel candidates for each frequency band can be decided. The list is provisioned to all PDs.

## Slide 5: Needs For FCS
  At the beginning of each of the following procedures
    Discovery
    Peering
    Communication
  PDs need to select a channel (a unit channel or a bundle of unit channels) for operation.
  The above three procedures may or may not select the same channel for operation.

## Slide 6: What To Do With FCS
  Using pre-assigned channel when installing the system
    Regulation limitations
    Relatively stable network
  Contention based channel selection with channel scanning
    Energy detection
    Clear channel assessment with carrier sensing
    Periodical channel scanning to select optimal channels
  Random channel selection
    ALOHA

## Slide 7: Suggested FCS - Discussion
    The frequency channel selection (FCS) shall be performed by higher layers in cooperation with MAC and PHY. FCS methodologies might include the following.
    Pre-assigned FCS at the time of system installation
    Contention based FCS with CCA. CCA might use energy detection (ED), carrier sensing, or other techniques.

## Slide 8: Suggested FCS - Discussion
    The channel to start discovery procedure should be pre-specified when contention based FCS is performed. Discovery and emergency message are given the highest priority to use this channel (starting channel).
    It is also desired to specify the order of following channels to conduct discovery in case that the starting channel reaches its accommodation capacity.
  Explanation: By specifying the order of FCS, the discovery latency could be made as small as possible.

## Slide 9: Suggested FCS - Discussion
    When the contention based FCS is applied in peering procedure, the information of selected frequency channel must be shared among PDs involved in peering.

## Slide 10: Suggested FCS - Discussion
    When contention based FCS is applied in communication procedure, the information of selected frequency channel must be shared among all joined PDs.
    Channel hopping must be enabled for coexistence purpose.
    Communication procedure should avoid using the starting channel as maximumly as possible.

## Slide 11: Summary
Background information.
General description
Suggested text
Some discussions