## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG agreed text for frequency channel selection]
Date Submitted: [November 6, 2014]
Source: [Huan-Bang Li] Company [NICT]
Address [3-4 Hikarino-oka, Yokosuka, Kanagawa, Japan]
Voice:[+81 468475104], FAX: [:[+81 468475431], E-Mail:[lee@nict.go.jp]
Re: [Proposed text for drafting 15.8 PAC]
Abstract: [proposed text of channel selection procedure for IEEE802.15.8]
Purpose: [This document is to provide a MAC mechanism]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
<November 2014>

## Slide 2: TG agreed Text For Frequency Channel Selection
November 6, 2014

## Slide 3: Agreed Text (1)
    The frequency channel selection shall be performed by higher layers in cooperation with MAC and PHY. Frequency channel selection methodologies may include the following.
    Frequency channel selection could be pre-assigned.
    Contention based frequency channel selection with CCA. CCA might use energy detection (ED), carrier sensing, or other techniques used for channel measurements and detections.

## Slide 4: Agreed Text (2)
    The information of selected frequency channel for peering shall be shared among the PDs involved in peering prior to the peering.
    The information of selected frequency channel for communication shall be shared among the PDs involved in communication prior to the communication.

## Slide 5: Agreed Text (3)
    To minimize discovery latency, the channel to start discovery procedure may be pre-specified when contention based channel selection is performed. Discovery and emergency message are given the highest priority to use this channel (naming of the channel is TBD: i.e. TBD channel).
    To minimize discovery latency, it may specify the order of candidate channel list for discovery if the TBD channel is not available, e.g. reaching its accommodation capacity or failing the required QoS, etc.

## Slide 6: Agreed Text (4)
    Channel hopping shall be enabled for coexistence or other purposes. The manner of channel hopping is TBD.

## Slide 7: Motion
Motion: To approve “TG agreed text for frequency channel selection” (DCN: 14-0679-01-0008) and include it in the Standard Draft v0.5.
      Moved: Huan-Bang Li
      Second: Marco
      Yes: 5
      No: 0
      Abstain: 0