## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Vigilance of Spectrum Resource Usage in private facilities for network stability and security]
Date Submitted: [13 Jan. 2015]
Source: [Shusaku Shimada] Company [Schubiquist Technologies Guild]
Address [1-28 Nishiarai, Chuo-shi, Yamanashi, 409-3802 Japan]
Voice:[+81-55-274-1266], FAX: [+81-3-468-0625], E-Mail:[shusaku@ieee.org]
Re: [15-14-06570-00 “Call for Contributions”]
Abstract: [To maintain the stable and secured operation of a wireless network in private facilities like an industrial plant or a large hospital, the vigilant management including monitoring of radio spectrum occupation and detecting the anomaly event of Radio Resource Measurement (RRM) notified by each node in sub-networks, is becoming more important.]
Purpose: [To support the creation of Technical Guidance Document in IEEE802.15.4s.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Vigilance of Spectrum Resource Usage
in private facilities for network stability and security
Date: 2015-01-13
Author:

## Slide 3: Summary
Monitoring the adequate spectrum usage through a set of radio resource measurements by each node in co-existing networks is becoming more important to ensure the stable and secured operation of overall wireless networks, especially in private facilities like an industrial plant or a large hospital.
The vigilant management of recent wireless environment often requires both monitoring of spectrum resource occupation and collecting the information of detected anomaly events in radio resource measurement results at each node.

## Slide 4: Radio Resource Measurement (RRM) for monitoring adequate spectrum usage
< Shared RRM Information >
Spectrum Resource Management
Entity
Common Media or
Co-located on board plural wireless networks
RRM Report
RRM
Request
Media Agnostic
Media Agnostic
Media Agnostic
Media Agnostic

## Slide 5: Spectrum Resource Usage management by shared information
Spectrum Resource Usage management is becoming more important by sharing each information of co-existing network in same area, e.g. hospitals, social facilities and industrial plants using un-license bands, e.g. 2.4GHz and 915MHz ISM band.
RRM request and report scheme facilitates arbitrating, controlling and managing the spectrum resource usage by each sub-network, in time, frequency and spatial domains.
Media agnostic approach to share the RRM information is preferred to achieve the stable and secured network operation as well as efficient spectrum resource usage, whatever information sharing scheme is employed, e.g. conventional centralized human intervention based on areal policy, or partial or fully adaptive management at the central or common management entity.

## Slide 6: Example of anomaly detection
< Shared RRM Information >
Vigilance of Spectrum Resource Usage
by Common Management Entity
Detection
Notification
  Noise energy increase
  Carrier sense of alien 15.4 device
IEEE802.11 BSS
IEEE802.15.4e
(ISA100.11a network)
Detection Notification
  Noise energy increase
  Carrier sense of alien OBSS of IEEE802.11 device
Moving in
IEEE802.11 OBSS or 15.4 alien device

## Slide 7: Examples of anomaly detection
Co-existing networks, e.g. IEEE802.11 and 15.4e (ISA100.11a), are able to share the alien system information each other.
  Increased noise energy using energy detection
  Overlapping network activity using carrier sense
Jabber or jamming node may be detected.
  Suspicious behavior or ordinary mobile demeanor of alien node can be estimated.
  Sometimes notification storm has to be suppressed, e.g. mobile worker carrying wireless gadgets.
Security threat may be alleviated, for instance;
  detection of “replay attack” node
  detection of “active spoofing” node

## Slide 8: Suggestion for TGD of IEEE802.15.4s
Vigilance of Spectrum Resource Usage should be facilitated by 15.4s standardized RRM functions, e.g. statistical record of parameters.
RRM functions may include the parameters to detect anomaly behavior of alien node and notification of such situation, for example, Jabber node or jamming activity.
Anomaly notification may be initiated by end nodes in accordance of its performed result of RRM functions and pre-defined policy, e.g. threshold of noise energy or prohibition of alien existence.
However, it has to be considered to prevent the storm of anomaly notification even in the situation in which Spectrum Resource Usage is seriously degraded.

## Slide 9
References
[1] 15-14-0555-02-004s-tg4s-technical-guidance-document
[2] 15-14-0175-05-0sru-working-draft-of-sg-sru-csd
[3] PAR of IEEE P802.15.4s