## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Fast Beam Searching Concept for Indoor Terahertz Communications
Date Submitted: 10 Match 2015
Source: Bile Peng Company TU Braunschweig
Address Schleinitzstr. 22, D-38102 Braunschweig, Germany
Voice:+495313912405, FAX: +495313915192, E-Mail: peng@ifn.ing.tu-bs.de
Re: n/a
Abstract: A precise angle of arrival (AoA) estimation is necessary for the implementation of the directive antenna. We introduce a fast and practical concept for the AoA estimation in 2 steps. In the first step, a preliminary estimation is carried out at a lower frequency via exhaustive scanning. After that, the precise angle is estimated at the actual frequency for the data transmission. The evaluation shows a satisfactory estimation precision.
Purpose: Contribution towards developing a wireless data center channel model for use in IG THz
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Fast Beam Searching Concept for Indoor Terahertz Communications
Bile Peng, Sebastian Priebe, Thomas Kürner

## Slide 3: Contents
Introduction
Angle-of-Arrival Estimation in Two Steps
  Preliminary Estimation at 2.4 GHz
  Precise Estimation in Terahertz Band
Protocol Concept
Conclusion

## Slide 4: Challenge of the THz Communication
According to the Friis law, the path loss grows quadratically with the carrier frequency.
The huge path loss due to the extremely high carrier frequency must be compensated by a high antenna gain.
A high antenna gain result in a high directional selectivity, i.e. Tx and Rx must know exactly, where the counterpart is.
The beam searching becomes a challenge in the THz communication.
A compromise between precision and efficiency must be achieved.
(dB)
Path loss
Antenna Diagram

## Slide 5: Contents
Introduction
Angle-of-Arrival Estimation in Two Steps
  Preliminary Estimation at 2.4 GHz
  Precise Estimation in Terahertz Band
Protocol Concept
Conclusion

## Slide 6: The Phased Array and Its Adaption
A phased array consists of several identical antenna elements. Half-wave dipoles are used as antenna elements.
By means of phase shifting before transmission (at Tx) or after receiving (at Rx), the angle of the constructive interference can be adapted. The phase shifting is called beamforming vector (for Tx) and combining vector (for Rx).

## Slide 7: Ray Tracing Simulation for Concept Demonstration
We choose a simple room for the simulation scenario to demonstrate our concept.
Tx and Rx are positioned in two corners of the room, an obstacle is placed at the room center to block the LOS propagation path. Only reflections on the wall are considered.
The electromagnetic wave propagation can be approximated by the geometric optics provided that the frequency is high enough.
The ray tracing simulator is a solid approach for the geometric optics simulation.
6 rays are identified in this scenario.
Tx
Rx
6 m
4 m

## Slide 8: Angle-of-Arrival Estimation in Two Steps
An exhaustive search is the most straightforward idea. However, it takes too long time.
A preliminary search with lower resolution seems hopeful for an acceleration, but the high path loss does not allow a low gain antenna.
The THz system is equipped with a frontend at 2.4 GHz for initialization and fallback solution, which can be applied for the preliminary estimation.
  Assumption: the propagation paths at low and high frequencies are similar.
Preliminary estimation via low frequency
Precise estimation in the THz band
Optimal beamforming and combining vectors
2.4 GHz | 300 GHz
Low path loss | High path loss
Low antenna gain | High antenna gain
Wide main lobe | Narrow main lobe
Low resolution | High resolution

## Slide 9: Step 1: Preliminary Estimation at 2.4 GHz
We use the spherical coordinate system (elevation,azimuth) for the direction description.
It is possible to use directive antenna only at Rx to detect signal at the low frequency (Quasi-omni antenna at Tx).
  To the contrary, this is impossible at the THz band.
Resolution: 36° at low frequency and 12° at high frequency.
The spatial distributions of the received power at low and high frequencies shows enough similarity.
The search region in the second step can be determined using the peak (local maximum) finding algorithm (marked with red rectangles).
Low frequency with noise
High frequency without noise
High frequency with noise

## Slide 10: Step 2: Precise Estimation in the Terahertz Band
By exchanging roles of Tx and Rx, the search range for both sides can be determined in step 1.
In the second step, it is possible to try every combination of beamforming and combining vectors in the search range without too much searching time.
  Each big “pixel” in step 1 contains at most 9 small “pixels” in step 2.
  For each searching range pair, there are at most only 81 combinations of beamforming/combining vectors.
  Without step 1, there would be 20164 combinations in total.
Low frequency
High frequency

## Slide 11: Contents
Introduction
Angle-of-Arrival Estimation in Two Steps
  Preliminary Estimation at 2.4 GHz
  Precise Estimation in Terahertz Band
Protocol Concept
Conclusion

## Slide 12: Protocol
Tx sends
Rx scans
Obtain AoA distributions
Rx sends
Tx scans
Obtain AoD distributions
Pair search ranges
Tx sends
Rx scans
Obtain AoA distributions
Rx sends
Tx scans
Obtain AoD distributions
Select best b/c vector pairs
Exchange role
Directional antenna
2.4 GHz, total range
300 GHz, selected range
Exchange role

## Slide 13: Contents
Introduction
Angle-of-Arrival Estimation in Two Steps
  Preliminary Estimation at 2.4 GHz
  Precise Estimation in Terahertz Band
Protocol Concept
Conclusion

## Slide 14: Conclusion
The high path loss is a main challenge of THz communications. A highly directive antenna is a possible counter measurement.
An AoA estimation is required for a directive antenna.
This paper presents a fast beam searching concept in 2 steps
  Preliminary estimation at a low frequency
  Precise estimation in THz band.
This approach achieves a compromise between precision and efficiency. It should be tested in more complicated and realistic scenarios in the further studies.