## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: The THz Channel Model in Wireless Data Center
Date Submitted: 10 Match 2015
Source: Bile Peng Company TU Braunschweig
Address Schleinitzstr. 22, D-38102 Braunschweig, Germany
Voice:+495313912405, FAX: +495313915192, E-Mail: peng@ifn.ing.tu-bs.de
Re: n/a
Abstract: This contribution presents some preliminary THz channel modeling results in the future wireless data center scenario. A series of ray tracing simulations are conducted for different channel types. The RMS delay spread and the RMS angular spread are employed as the metric of the multipath richness. A stochastic channel model is developed based on the simulation results and is validated by the ray tracing simulation results.
Purpose: Contribution towards developing a wireless data center channel model for use in TG 3d
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: A Stochastic THz Channel Model in Wireless Data Centers
Bile Peng, Thomas Kürner
TU Braunschweig

## Slide 3: Contents
Motivation
Ray Tracing Simulation Results
Stochastic Channel Model
Conclusion

## Slide 4: Motivation
    The data center link is responsible for the cooperation between computers and must achieve very high data rates.
    The data center link is prevailingly wired. However, the wireless link has some significant advantages [1]:
      More flexibility
      Less maintenance cost
      More space for cooling
    The high data rates of Terahertz (THz) communications makes it a competitive candidate.
    This report is a preliminary PHY layer feasibility study of the application of the THz communication in the data center wireless backhaul.

## Slide 5: Radio Wave Propagation Paths [2,3]
Reflector
Ceiling
Type 1: LoS
Type 2: NLoS
Type 3: Adjacent casings

## Slide 6: Selection of Propagation Path Type (1/2)
If transmitter and receiver are on the same or adjacent casings, they can be positioned lower than the casing roof to reduce the interference.
Reflector

## Slide 7: Selection of Propagation Path Type (2/2)
If transmitter and receiver are close enough, we use the NLoS path with reflection on the ceiling.
  The short distance compensates for the reflection loss.
  The AoD/AoA elevations are far from the horizonal direction, which reduces the interference on the LoS paths.
Criterion: the elevation (θ) is at least 2 times Half-Power-Beamwith away from the horizontal direction.
Otherwise we select the LoS path.
Ceiling
θ1
θ2

## Slide 8: Simulation Environment
Transmitter
Receiver
Casing
Wall
Propagation path
Typical data center (source: http://www.enterprisetech.com/wp-content/uploads/2014/11/SIO_DataCenter_Rows1.jpg)
Ray tracing simulation

## Slide 9: Contents
Motivation
Ray Tracing Simulation Results
Stochastic Channel Model
Conclusion

## Slide 10: Statistical Characteristics With Type 1/2
Type1/2: LoS/nLoS channels between 2 nonadjacent casings
Multipath richness metric: RMS delay spread with omniantenna
Parity pattern due to reflections on the casing roof
Tx
Tx

## Slide 11: Impact of Directive Antenna
Antenna: 4x4 phased array
The directive antenna reduces the RMS delay spread significantly.
Omniantenna
Directive phased array

## Slide 12: Statistical Characteristics With Type 1/2
Type1/2: LoS/nLoS channels between 2 nonadjacent casings
Multipath richness metric: RMS angular spread with omniantenna
Parity pattern due to reflections on the casing roof
Tx
Tx

## Slide 13: Impact of Directive Antenna
Antenna: 4x4 phased array
The directive antenna reduces the RMS angular spread significantly as well.
Omniantenna
Directive phased array

## Slide 14: Statistical Characteristics With Type 3
Type 3: channels between 2 adjacent casings
Randomly generated adjacent Tx and Rx
The RMS delay spread is lower than the in type 1/2 because of the limited propagation space.
Omniantenna
Directive phased array

## Slide 15: Statistical Characteristics With Type 3
Type 3: channels between 2 adjacent casings
Randomly generated adjacent Tx and Rx
The RMS angular spread is lower than the in type 1/2 because of the limited propagation space.

## Slide 16: Contents
Motivation
Ray Tracing Simulation Results
Stochastic Channel Model
Conclusion

## Slide 17: Stochastic Channel Model
Determine number of paths.
Determine delay for each path.
Determine pathloss according to delay.
Determine angles.
Generate uniformly distributed phases.
Generate frequency dispersions (Friis law).
Generate polarisations.

## Slide 18: Numbers of Paths
LoS |  |  |  |  | 
Number of paths | 1 |  |  |  | 
Probability | 100% |  |  |  | 
Reflections |  |  |  |  | 
Number of paths | 17 | 18 | 19 | 20 | 21
Probability (%) | 27 | 35 | 22 | 15 | 1
Type 1/2, Tx 1 (in corner)

## Slide 19: Numbers of Paths
LoS |  |  |  |  |  | 
Number of paths | 1 |  |  |  |  | 
Probability | 100% |  |  |  |  | 
Reflections |  |  |  |  |  | 
Number of paths | 16 | 17 | 18 | 19 | 20 | 21
Probability (%) | 32 | 29 | 12 | 16 | 8 | 3
Type 1/2, Tx 2 (in center)

## Slide 20: Numbers of Paths
LoS |  |  |  |  |  |  |  |  | 
Number of paths | 1 |  |  |  |  |  |  |  | 
Probability | 100% |  |  |  |  |  |  |  | 
Reflections |  |  |  |  |  |  |  |  | 
Number of paths | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Probability (%) | 22 | 13 | 8 | 15 | 8 | 17 | 8 | 6 | 3
Type 3 (Adjacent casings)

## Slide 21: Delay Distribution: type 1/2, Tx 1
Path | Distribution | Parameters
LOS | Normal distribution | µ=2.26e-8, σ=8.76e-9
NLOS | Negative EXP | λ=4.26e7

## Slide 22: Delay Distribution: type 1/2, Tx 2
Path | Distribution | Parameters
LOS | Normal distribution | µ=1.20e-8, σ=4.56e-9
NLOS | Normal distribution | µ=2.98e-8, σ=1.79e-8

## Slide 23: Delay Distribution: type 3
Path | Distribution | Parameters
LOS | Normal distribution | µ=1.80e-8, σ=8.60e-9
NLOS | Negative EXP | λ=4.92e7

## Slide 24: Delay-Pathloss Correlation: type 1/2, Tx 1
Path | Deterministic part | Random part (Norm.)
LOS | p=-20log10(d)-71.52 | σ=0
NLOS | pr=-0.294dr-17.44 | σ=4

## Slide 25: Delay-Pathloss Correlation: type 1/2, Tx 2
Path | Deterministic part | Random part (Norm.)
LOS | p=-20log10(d)-71.52 | σ=0
NLOS | pr=-0.385dr-17.95 | σ=4

## Slide 26: Delay-Pathloss Correlation: type 3
Path | Deterministic part | Random part (Norm.)
LOS | p=-20log10(d)-71.52 | σ=0
NLOS | pr=-0.429dr-30.3 | σ=6

## Slide 27: Pathloss-Angle Correlation
Since we want to reduce the multipath effect by highly directive antenna, the propagation paths with low pathloss and similar Angle of Arroval (AoA) to LOS path has a negative impact on the system design.
There is no appropriate distribution to describe the relation, therefore we use the correlation matrix.

## Slide 28: Stochastic Channel Example
Channel impulse response
Pathloss-angle distribution
LoS path

## Slide 29: Validation via RMS Delay Spread
Ray Tracing simulation
Stochastic channel model

## Slide 30: Validation via RMS Angular Spread
Ray Tracing simulation
Stochastic channel model
The similar distribution of RMS delay/angle spreads validate the stochastical model.

## Slide 31: Contents
Motivation
Ray Tracing Simulation Results
Stochastic Channel Model
Conclusion

## Slide 32: Conclusion
The THz communication is a competitive solution for the next generation wireless data center.
A ray tracing simulation environment is set up to investigate the channel characteristics.
The multipath propagation is a major hurdle of the high speed error free data transmission and the RMS delay/angular spread is used as metric of the multipath richness.
A stochastic channel model is developed according to the ray tracing simulation results.

## Slide 33: List of References
T. Kürner, “Literature review on requirements for wireless data centers” doc.: IEEE 802.15-13-0411-00-0thz_Literature Review
Zhang W et. al, „3D beamforming for wireless data centers”, in Proceedings of the 10th ACM Workshop on Hot Topics in Networks. 2011
K. Ramchadran„60 GHz Data-Center Networking: Wireless Worry less?“, 2008