## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resource slot request command text]
Date Submitted: [ April 21st, 2015 ]
Source: [Marco Hernandez, Huan-Bang Li, Igor Dotlić, Ryu Miura ]
Company: [NICT]
Address: [3-4 Hikarino-oka, Yokosuka, 239-0847, Japan]
Voice:[+81 46-847-5439] Fax: [+81 46-847-5431] E-Mail:[]
Re: [In response to call for technical contributions TG8]
Abstract: [ ]
Purpose: [Material for discussion in 802.15.8 TG]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: ReS request command text
5.3.9 GTS ReS request command
  The GTS ReS request command is used by an associated device a peered PD that is requesting the allocation of a new GTS ReS or the deallocation of an existing GTS ReS. from the PAN coordinator. Only devices PDs that have a short address less than 0xfffe shall send this command. TBD
  This command is optional.
  The GTS ReS request command shall be formatted as illustrated in the table:
  *MHR=MAC header.
X octets | 1 octet | 1 octet
MHR* fields | Command identifier | ReS characteristics

## Slide 3: ReS request command text
5.3.9.1 MHR fields: Destination addressing mode field, Source addressing mode field, Frame pending field, Source PAN PAC identifier field, Source address field, and AR field (acknowledgment request).
  The Destination Addressing Mode field shall be set to indicate that destination addressing information is not present, and the Source Addressing Mode field shall be set to indicate short addressing (extended addressing) TBD.
  *source or destination.
*Addressing mode | Description
00 | PAC identifier and address fields are not present
01 | Reserved
10 | Address field contains a short address (16 bit) TBD
11 | Address field contains an extended address (64 bit) TBD

## Slide 4: ReS request command text
  Frame pending field shall be set to zero and ignored upon reception, and the AR field shall be set to one.
  The Source PAN PAC identifier field shall contain the value of macPACId TBD, and the Source Address field shall contain the value of macShortAddress (macExtendedAddress) TBD.

## Slide 5: ReS request command text
5.3.9.2 ReS characteristic field
  The GTS ReS characteristics field shall be formatted as illustrated in the table:
  The GTS ReS length field shall contain the number of superframe slots being requested for the GTS ReS.
  The GTS ReS direction field shall be set to one if the GTS ReS is to be a receive-only GTS ReS. Conversely, this field shall be set to zero if the GTS ReS is to be a transmit-only GTS ReS. GTS ReS direction is defined relative to the direction of data frame transmissions by the device PD.
Bits | 0-3 | x-y | x-y | x-y
Attribute | ReS length | ReS direction | Type | Reserved

## Slide 6: ReS request command text
  The Characteristics Type field shall be set to one if the characteristics refer to a GTS ReS allocation or zero if the characteristics refer to a GTS ReS deallocation.